## Slide 1: GROUP #4 Chris Carmichael Ismael Rivera Journey Sumlar Warayut Techarut
T-100 WATCHDOG

## Slide 2: Project Goals
Autonomous Vehicle
  System Integration
  Motor Control
  Computer Vision
  Wireless Communication
  Power Control

## Slide 3: Requirements
Fully Autonomous
Object Detection within Range
Wireless Communication Capable
  Utilize Thermal Camera

## Slide 4: Specifications
Feature | Measurement
Dimension | 11” x 6”
Operating Range | 12 ft
Power Supply Voltage | 15 v
Maximum Weight | 20 lbs
Minimum Acceleration | 1 ft/s2
Maximum Speed | 3 ft/s
Battery Life | 3 hrs
Recharge Time | < 8 hrs

## Slide 5: Block Diagram

## Slide 6: System on Chip (SoC)

## Slide 7: Microcontroller & Development Board
ARM Cortex A8
TI Sitara AM3359
BeagleBone Black

## Slide 8: Microcontroller & Development Board

## Slide 9: Operating Systems
Angstrom
  Included onboard
ArchLinux|ARM
  Most Lean
Windows Embedded
  Most Integrated

## Slide 10: Proximity Sensors

## Slide 11: Proximity Sensors
Features | Measurement
Working Voltage | DC 5 v
Working Current | 15 mA
Working Frequency | 40 Hz
Max Range | 4 m
Min Range | 2 cm
HC - SR04
45 mm
15 mm

## Slide 12: Object Avoidance

## Slide 13: Object Avoidance

## Slide 14: Wi-Fi

## Slide 15: Wi-Fi
Edimax EW-7811Un
  IEEE 802.11b/g/n
  Compatible with Linux
  Small size
  Internal Antenna
  WEP/WPA/WPA2/WPS Compatible
7.1 mm
14.9 mm
18.5 mm

## Slide 16: Computer Vision - OpenCV

## Slide 17: Computer Vision - OpenCV
  Detect movement
  Recognize and track a moving person
OpenCV 2.4.2
  Optimized computer vision functions and algorithms
  Built-in Object Detection and Tracking functions
  ARM Support
  Performance varies on functions being utilized.
Motion
  Detect any movement
  Works together with OpenCV

## Slide 18: Computer Vision State Diagram

## Slide 19: Server & Streaming

## Slide 20: Server & Streaming
Node.js
  Enable internet HTTP communication
  Web GUI (Optional)
  Lightweight on resources under load
TCP (Transmission Control Protocol)
  JAVA Implementation (Android Compatible)
  Always listening for incoming commands from mobile phone
  Very lightweight on resources
  Port specific
Chart: Server Benchmark
| Apache | Open LiteSpeed | Nginx | Node.js
 | 42.4 | 47.1 | 25.3 | 12.1

## Slide 21: Server & Streaming
MJPEG Streamer
  Streams images from a folder over the internet
  Stream and Snapshot functions available
  Android compatible stream
  Low Resource

## Slide 22: Streaming State Diagram

## Slide 23: Difficulties
Port Forwarding not possible at UCF
  Solution – Use No-IP for Dynamic IP. Overwrite client rule to utilize Local IP instead of External IP

## Slide 24: Webcam

## Slide 25: Webcam
Logitech - HD Webcam C270
  USB 2.0 Connectivity
  Linux Compatible
  Multiple picture/video resolutions available
8.3 cm
5 - 15 cm
Notes: Compare with others

## Slide 26: Thermal Camera

## Slide 27: Thermal Camera
DRS Tamarisk 320
  Automatic Image Calibration
  320 x 240
  40° Field of View (FOV)
  Low Power (< 1.0 W)
  Shock/Vibration Resistant
28 mm.
24 mm.

## Slide 28: Difficulties
Analog Video Input
  Solutions:
    DRS BlackBox – requires a computer/laptop with special serial card and cable. Not compatible with our current setup.
    Analog-to-USB frame grabber – convert the analog input to USB.

## Slide 29: Analog-to-USB Frame Grabber

## Slide 30: Analog-to-USB Frame Grabber
Sabrent USB-AVCPT
  Converts Analog to USB
  Compatible with the Thermal Camera
  Low Cost
  Picture quality is not affected
  Size: 7 L x 1.2 W inches

## Slide 31: Difficulties
Compatibility Issues - Linux recognizes device but picture is black with green lines at the bottom.
  Solution- multiple beta drivers on GitHub, currently testing them.

## Slide 32: Mobile Application

## Slide 33: Mobile Application
  Support Android 4.0 and newer versions
  SQLite Database to store user credentials
  Control vehicle remotely
  View a live video feed
  Store snapshot on the device
  Ability to call 9-1-1

## Slide 34: Mobile Application State Diagram

## Slide 35: Mobile Application
Registration Section
  Allow user to register a username/password combination.
  Store cell phone for SMS and MMS alerts.
    Supports: AT&T, Sprint, T-Mobile, Verizon, MetroPCS, Boost Mobile, Straight Talk.
  Store email for email alerts.
  Send SMS, MMS, and Email address to external server via PHP Post method.

## Slide 36: Mobile Application
Login Section
  Allows user to register/login
  Only authorized users will have access
  Performs an Internet Check

## Slide 37: Mobile Application
Control Section
  View live video feed
  Control robot with virtual joystick
  Store snapshot
  Call 9-1-1

## Slide 38: Motor Controller, Motors, & Wheels

## Slide 39: Mecanum Wheels
Notes: Add Diagrams

## Slide 40: Mecanum Wheels
Notes: Add Diagrams

## Slide 41: Mecanum Wheels
Notes: Add Diagrams

## Slide 42: Mecanum Wheels
Vex Robotics Mecanum Wheels
  Affordability
    $59.99 4 pack
  Diameter: 4 in.
  Thickness: 2 in.

## Slide 43: Platform
Perforated Aluminum – Lightweight
2 pounds with wheels included
Easily Adjustable
12 in.
8 in.

## Slide 44: Motor
VEX 2-Wire motor 393
VEX 2-Wire motor 393 | Requirements | Specs-Low Speed | Specs- High speed
Price | < $20 | $14.99 | $14.99
RPM’s | 130 | 100 | 160
Torque | 1.3 Nm | 1.67 Nm | 1.04 Nm
Weight | < .5 lbs | .2 lbs | .2 lbs
Stall current |  | 4.8 A | 4.8A
Max Power | All measured at 7.2 V | 34.56 W | 34.56 W
2 in.
1.5 in.
1 in.

## Slide 45: H-Bridge Circuit

## Slide 46: H Bridge Components
IRF 9530 P-Channel | IRF 530 N-Channel | BC547
100 Vds | 100 Vds | 47 V Breakdown
12 A | 14 A | 100 mA
$1.29 | $1.03 | $ 0.20
10 K OHM Current Limiting Resistors

## Slide 47: Controller Budget
Component | How many | Price per unit | Total
MSP430G2552 | 4 | 2.79 | 11.16
IRF9530 | 8 | 1.29 | 10.32
IRF530 | 8 | 1.03 | 8.24
BC547 | 64 | 0.20 | 12.80
Capacitor(100nF) | 4 | .05 | 0.20
Resistor (10k) | 40 | .04 | 1.60
Total: (without pcb) |  |  | 44.32

## Slide 48: Motor Controller- PCB
Specifications
3”x3”
Thick Traces for high current lines
2 layer
$33- 60 square inches 4pcb.com

## Slide 49: Testing
Tests
Digital Signal controls Motor Direction.
Analog signal from 0-3 V controls duty cycle of PWM from 0-100% in steps of 1.61%
3.6 A continuous through MOS-FET’s without noticeable heat production

## Slide 50: Difficulties
Heat Dissipation with PCB
  Solution-Add a heat sink if we have heat dissipation issues
Current Capabilities of PCB
  Solution – remake PCB utilizing thicker traces

## Slide 51: USB Power Hub

## Slide 52: USB Power Hub
Beagle Bone Black only has 1 USB port
2.0 USB Ports
Input voltage is 3-5V
Constant power to each USB port
Weight 8 oz.
6 in.
.5 in.
1 in.

## Slide 53: Power Management & Battery

## Slide 54: Single Power Supply or Multi Power Supply?
  Single power supply to power all components
  Battery Characteristics
    High discharge Rate
    No/low Memory Effect
    Light Weight
    High Capacity
    Price Effective
    High Nominal Voltage

## Slide 55: Battery Specifications
Top three candidates for batteries
Most important aspects are Capacity, Discharge Rate, and Voltage
Model | 31604 | 11427 | 18650
Brand | Tenergy | Tenergy | Supower
Capacity (mAh) | 1600 | 2000 | 2200
Voltage (V) | 7.4 | 9.6 | 7.4
Weight (Ib) | 0.2 | 0.52 | 0.2
Discharge Rate (C) | 20 (32 A) | 10 (20 A) | 2.5 (5.5 A)
Price ($) | 24.5 | 19.99 | 17.99
Chemistry | Lipo | NiMH | Li-on

## Slide 56: Battery Selection
Tenergy 7.4V 1600mah
Two Lithium Polymer Ion Batteries in Series
Expected Battery Life needs to be at least 3 Hours
Model | 31604 | 11427 | 18650
Brand | Tenergy | Tenergy | Supower
Capacity (mAh) | 1600 | 2000 | 2200
Voltage (V) | 7.4 | 9.6 | 7.4
Weight (Ib) | 0.2 | 0.52 | 0.2
Discharge Rate (C) | 20 (32 A) | 10 (20 A) | 2.5 (5.5A)
Price ($) | 24.5 | 19.99 | 17.99
Chemistry | Lipo | NiMH | Li-on

## Slide 57: Battery Charger
Tenergy Airsoft Battery Charger
  LIPO tends to overheat easily
  Built in Balancer
  Price $19.99
  Powers both Lion and LIPO batteries.

## Slide 58: Power Requirements
Items | Voltage input needed | Current input needed
BeagleBone Black | 5 V | 2 A
Motor Controllers | 12 V | 16 A
Thermal Camera | 3-5.5 V | <600 mA
Conventional Webcam | 3 V | <500 mA
Proximity Sensors | 4 V | 15 mA
MSP 430 | 3 V | .5 mA
Wi-Fi Adapter | 3 V | <500 mA
USB Power Hub | 3-5 V | 1.5 A

## Slide 59: Voltage Regulator Motor Controllers
Needs to be able to provide 12V and 16A to power all four of the motor controllers
Provide 3.3 V to power the MSP 430
Name | Type of Regulator | Footprint | Efficiency | BOM Count | BOM Cost
LM27402 | Buck Controller | 419 | 97 | 28 | $3.81
TPS40304 | Buck Controller | 318 | 94 | 24 | $3.85
TPS40305 | Buck Controller | 305 | 98 | 24 | $4.35

## Slide 60: Project Milestones
Chart: 
| Pickup Parts | Software Integration | Hardware Unit Testing | Order Motor Controller PCB | Order Power PCB | Prototype | Integration Testing | Completed Project
POSITION | -10 | 10 | 20 | -10 | -10 | 10 | 20 | 25
DATE | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 61: Work Breakdown
Task | Ismael Rivera | Warayut Techarut (Wye) | Journey Sumlar | Chris Carmichael
Motor Controller |  |  |  | X
Power Management |  |  | X | 
Server | X |  |  | 
OpenCV | X | X |  | 
Object Avoidance |  | X |  | 
Mobile Application | X |  |  | 

## Slide 62: Budget & Finance
Part Name | Quantity | Price (each) | Total
HC-SR04 Proximity Sensor | 4 | $1.33 | $5.32
Tamarisc 320 | 1 | $0.00 | $0.00
Wi-Fi USB Adapter | 1 | $5.99 | $5.99
MicroSD Card | 1 | $7.99 | $7.99
USB Power Hub | 1 | $7.99 | $7.99
Motor | 4 | $14.99 | $59.96
Mecanum Wheels | 1 | $59.99 | $59.99
Drive shaft pack | 1 | $5.49 | $5.49
Shaft Collar 16 pack | 1 | $7.99 | $7.99
Motor Controller Parts | 4 | $20.00 | $80.00
PCB Motor Controller | 1 | $33.00 | $33.00
PCB Power | 2 | $33.00 | $66.00
Batteries and Charger | 1 | $80.00 | $80.00
Microcontroller | 1 | $45.00 | $45.00
 |  | Total | $464.72
Chart: Budget
| Total | Left
 | 464.72 | 160.65

## Slide 63: Current Progress
Chart: Subsystem Completion Status
| Server | Mobile App | OpenCV | Motor Controller | Power | Integration | Research | Prototype
Column2
Series 2 | 90 | 90 | 70 | 35 | 50 | 30 | 90 | 30
Column1

## Slide 64: GROUP #4 Chris Carmichael Ismael Rivera Journey Sumlar Warayut Techarut
Questions?