## Slide 1
Acoustic Pinger Locator Sponsor: Robotics Club at UCF
Group 19
Cassondra Puklavage
Jonathan Mohlenhoff
Zhen Cai
<number><number>
<footer>Group #19
Critical Design Review
March 1, 2010

## Slide 2
AUVSI and ONR’s 13th International Autonomous Underwater Vehicle Competition
AUV Tasks
Facility and Competition Layout
AUV must complete several missions
Path Planning
Obstacle Avoidance
Vision Tasks
Pinger Challenge
<number><number>
<footer>Group #19
Notes: AUVSI (Association for Unmanned Vehicle Systems International)
Host several student competition each year
Competitions include ground, air and water robots
ONR (Office of Naval Research)
Co-host several competitions with AUVSI
Provide military and industry judges for competitions
<number><number>

## Slide 3
Robotics Club at UCF
History
Past UCF Vehicle
Participation
Have entered AUVSI competitions for the past 10 years
Have entered the AUV competition for the past 6 years
  2006 Fifth Place
  2009 Fourth Place
Top 3 AUVs completed pinger challenge
<number><number>
<footer>Group #19

## Slide 4
Locate single pinger in underwater environment
7ms pulse every 2 seconds
Frequencies range from 20KHz to 40KHz
Difficulties
Multiple Pingers in the water
Echoes
Signal interference and attenuation
Low-Power signal
<footer>Group #19
<number><number>
Pinger Challenge

## Slide 5
Develop acoustic pinger locator system for AUV team
This component will be integrated into this year’s AUV
Black box approach
  Acquires pinger location independently of AUV
  Provides location information to host AUV computer
Group 19 Goals
<number><number>
<footer>Group #19

## Slide 6
Provided by AUVSI competition rules and AUV Team
Pinger frequency selection from 20KHz to 40KHz
Powered through unregulated 22.2V Li-Po Batteries
Serial interface to AUV computer
Easy physical integration with AUV
  7.5” diameter tube, allocated 6” length
  Hydrophone array externally mounted
    Actual AUV integration will depend on AUV Team
Heading accuracy to within 10 degrees of pinger location
Specifications
<number><number>
<footer>Group #19

## Slide 7
Technical Design
Analog
Analog
  Filters for specific frequency
  Amplifies hydrophone signals
  Condition signal for A/D
Digital
Digital
  A/D Capturing
  Mathematics for acoustic localization
  Control analog hardware: filters and amplifiers
  Digital signal processing
AUV Host
AUV Host
  Send commands to APL: pinger frequency
  Queries pinger location
  Connects to APL
<number><number>
<footer>Group #19

## Slide 8
Incoming signal
Less than 10mV
Amplification
Needed for the ADC and digital processing
Voltage range from 0 to 3.3V for the ADC
Noise Removal
Filtering
  Bandpass
Minimal distortion
Especially between hydrophones
Phase
<footer>Group #19
<number><number>
Analog Hardware Specifications

## Slide 9
<footer>Group #19
<number><number>
Analog Hardware

## Slide 10
<footer>Group #19
<number><number>
Hydrophone: Reson TC4013
Decision
  Meets all requirements
  Previously acquired
  Cost

## Slide 11
<footer>Group #19
<number><number>
Pre-Amp Parts: MAX414
Quad Op-Amp
  Used for initial low gain stage, separate signal

## Slide 12
<footer>Group #19
<number><number>
Group #19
<number>
Pre-Amp Parts: AD605
Analog Controlled Variable Gain Amplifier
  Used for first main gain stage

## Slide 13
<footer>Group #19
<number><number>
AD605 Configuration

## Slide 14
<footer>Group #19
<number><number>
Group #19
<number>
Group #19
<number>
Pre-Amp Parts: DS1803
Digital Potentiometer
  Controls the VGA through I2C implemented on the FPGA

## Slide 15
<footer>Group #19
<number><number>
DS1803 Configuration

## Slide 16
<footer>Group #19
<number><number>
Pre-Amp Stage Schematic

## Slide 17
<footer>Group #19
<number><number>
Group #19
<number>
Group #19
<number>
Group #19
<number>
Filter Parts: MAX268
Programmable Filter
  Controlled through clock line and pin settings

## Slide 18
Center Frequency Calculation
Based on fclk/fo ratio
  32 steps
Higher ratios are more accurate
Equation: fclk/fo = pi(N+13)
  N is set through Fo-F4 pins
Example: fo = 25kHz, large ratio
fclk = fo*pi(31+13) = 3455751
fclk should be 3.45MHz to set a fo of 25kHz
<footer>Group #19
<number><number>
MAX268: Setting fo

## Slide 19
BW and Q relationship
Q = fo/BW > BW = fo/Q
Higher Q results in smaller acceptance BW around fo for the bandpass filter
Filter will have Gain = Q
Chip allows for 128 Q steps
Provided Equation:
Q = 64/(128-N)
  Q programmed through Q0-Q6 pins
Example: Set Q of 32 when fo = 25kHz
BW around fo = fo/Q = 781.25Hz
<footer>Group #19
<number><number>
MAX268: Set Q

## Slide 20
<footer>Group #19
<number><number>
Filter Stage Schematic
Configuration
+5V
Pins set by FPGA
Output A fed into input B to create a 4th order filter bandpass filter

## Slide 21
Final gain or attenuation stage using the same VGA and DP configuration
Use the MAX414 in an adder circuit to adjust the signal into the 0 to +5V range
Feed signal through a potentiometer to scale to 3.3V for the ADC
<footer>Group #19
<number><number>
Signal Conditioning Stage Schematic

## Slide 22
FPGA Signal Output
0 to 3.3V
Filter Input Range
0 to 5V
NPN Transistor
Pull up resistor to 5V
Ground connected by transistor when logic on
  Inverts logic
<footer>Group #19
<number><number>
FPGA Control signals

## Slide 23
<footer>Group #19
<number><number>
Power Usage

## Slide 24
<footer>Group #19
<number><number>
Group #19
<number>
Group #19
<number>
Group #19
<number>
Group #19
<number>
Voltage Regulator: JCK1524D05
Voltage Regulator
  Provide power to the analog hardware board

## Slide 25
<footer>Group #19
<number><number>
Single Signal

## Slide 26
<footer>Group #19
<number><number>
Signal Representation
Hydrophone Signal
Pre-Amplification
Filtering
Signal Scaling
Signal Conditioning
Post-Amplification

## Slide 27
<footer>Group #19
<number><number>
Full Schematic

## Slide 28
The digital hardware selection is an important stage of the project
Controls some of the analog hardware
Samples analog signals
Processes data
Various options to consider for our design
The analog signals need to be converted into a digital format to further be processed
The design needs to utilize the Nyquist Sampling Theorem to fully reconstruct the analog signal
<footer>Group #19
<number><number>
Digital System Overview

## Slide 29
Square wave PWM to select center frequency of analog filters, 500 KHz to 5 MHz
I2C Interface for controlling digital potentiometer
SPI for interfacing with high speed ADCs
UART for interfacing with AUV Host PC
Support large volume of data
4 Channels * 1.5 Bytes * 1 MSPS = 6 MB/S
Digital System Specifications
<number><number>
<footer>Group #19

## Slide 30
Hardware Choices
<number><number>
<footer>Group #19

## Slide 31
Development board provides ease of prototyping and interface to FPGA
Built in programmer via USB
PMOD Digilent Standard interface
Size fits within requirements
100 pin connector for high speed I/O
Built in switches and buttons for user input
LEDs and 7 Segment Displays for user output
<footer>Group #19
<number><number>
Digilent Nexys 2

## Slide 32
<footer>Group #19
<number><number>
A/D Converters

## Slide 33
PmodAD1
<number><number>
<footer>Group #19
Made by Digilent Inc.
2-Pole Sallen-Key Filters cutoff at 500 KHz for anti-aliasing
Two simultaneous A/D conversion channels using successive approximation
1 MSPS at 12 bits (0 to 4095)
Analog Input Range: 0V to 3.3V
Low power consumption:
  3.3V @ 0.6mA ≈ 2 mW * 2 = 4 mW
Small Dimensions: 0.95” x 0.80”
SPI Interface over PMOD, VHDL Interface and sample code provided by Digilent

## Slide 34
Xilinx ISE Design Software
Cost is free
Designed to be used with the Spartan 3E FPGA
Full featured for both VHDL and Verilog Hardware Descriptor Languages (HDL)
<footer>Group #19
<number><number>
Development Software

## Slide 35
HydrophoneControl
  ASampleComp
    AD1RefComp
      i2cComponet x2
    AD1RefComp
      i2cComponet x2
    dcCalc
      i2cComponet x2
    pkToPk
      i2cComponet x2
    pingDectect
      i2cComponet x2
    Adder x4
      i2cComponet x2
    Pwm
      i2cComponet x2
    RS232RefComp
      i2cComponet x2
    ds1803Interface x2
      i2cComponet x2
    Rs232RefComp
      i2cComponet x2
  ChannelComp
    AD1RefComp
      i2cComponet x2
    AD1RefComp
      i2cComponet x2
    dcCalc
      i2cComponet x2
    pkToPk
      i2cComponet x2
    pingDectect
      i2cComponet x2
    Adder x4
      i2cComponet x2
    Pwm
      i2cComponet x2
    RS232RefComp
      i2cComponet x2
    ds1803Interface x2
      i2cComponet x2
    Rs232RefComp
      i2cComponet x2
  Max268Comp
    AD1RefComp
      i2cComponet x2
    AD1RefComp
      i2cComponet x2
    dcCalc
      i2cComponet x2
    pkToPk
      i2cComponet x2
    pingDectect
      i2cComponet x2
    Adder x4
      i2cComponet x2
    Pwm
      i2cComponet x2
    RS232RefComp
      i2cComponet x2
    ds1803Interface x2
      i2cComponet x2
    Rs232RefComp
      i2cComponet x2
  SampleFreqInterface
    AD1RefComp
      i2cComponet x2
    AD1RefComp
      i2cComponet x2
    dcCalc
      i2cComponet x2
    pkToPk
      i2cComponet x2
    pingDectect
      i2cComponet x2
    Adder x4
      i2cComponet x2
    Pwm
      i2cComponet x2
    RS232RefComp
      i2cComponet x2
    ds1803Interface x2
      i2cComponet x2
    Rs232RefComp
      i2cComponet x2
  ArbiterComp
    AD1RefComp
      i2cComponet x2
    AD1RefComp
      i2cComponet x2
    dcCalc
      i2cComponet x2
    pkToPk
      i2cComponet x2
    pingDectect
      i2cComponet x2
    Adder x4
      i2cComponet x2
    Pwm
      i2cComponet x2
    RS232RefComp
      i2cComponet x2
    ds1803Interface x2
      i2cComponet x2
    Rs232RefComp
      i2cComponet x2
  MCUPRT
    AD1RefComp
      i2cComponet x2
    AD1RefComp
      i2cComponet x2
    dcCalc
      i2cComponet x2
    pkToPk
      i2cComponet x2
    pingDectect
      i2cComponet x2
    Adder x4
      i2cComponet x2
    Pwm
      i2cComponet x2
    RS232RefComp
      i2cComponet x2
    ds1803Interface x2
      i2cComponet x2
    Rs232RefComp
      i2cComponet x2
  dPotControllerInterface
    AD1RefComp
      i2cComponet x2
    AD1RefComp
      i2cComponet x2
    dcCalc
      i2cComponet x2
    pkToPk
      i2cComponet x2
    pingDectect
      i2cComponet x2
    Adder x4
      i2cComponet x2
    Pwm
      i2cComponet x2
    RS232RefComp
      i2cComponet x2
    ds1803Interface x2
      i2cComponet x2
    Rs232RefComp
      i2cComponet x2
  rawDataInterface
    AD1RefComp
      i2cComponet x2
    AD1RefComp
      i2cComponet x2
    dcCalc
      i2cComponet x2
    pkToPk
      i2cComponet x2
    pingDectect
      i2cComponet x2
    Adder x4
      i2cComponet x2
    Pwm
      i2cComponet x2
    RS232RefComp
      i2cComponet x2
    ds1803Interface x2
      i2cComponet x2
    Rs232RefComp
      i2cComponet x2
  pingTimerInterface
    AD1RefComp
      i2cComponet x2
    AD1RefComp
      i2cComponet x2
    dcCalc
      i2cComponet x2
    pkToPk
      i2cComponet x2
    pingDectect
      i2cComponet x2
    Adder x4
      i2cComponet x2
    Pwm
      i2cComponet x2
    RS232RefComp
      i2cComponet x2
    ds1803Interface x2
      i2cComponet x2
    Rs232RefComp
      i2cComponet x2
<footer>Group #19
<number><number>
VHDL on FPGA
Hierarchal Component Structure in FPGA
Notes: <number><number>

## Slide 36
<footer>Group #19
<number><number>
HydrophoneControl Logic Overview
Track max and min of analog signal
Adjust analog gain accordingly
Rx Commands from AUV Host PC
Perform directed action
  Report status
  Select filter frequency

## Slide 37
Microcontroller Unit Library supports messaging from an MCU to PC
Developed and maintained by the Robotics Club at UCF
Hosted on public server at SourceForge.net in the Zebulon Code Bank
Supports standard messages and allows expandability
Cross platform support on PC and architectures for MCU: ARMite, PIC, Rabbit
<footer>Group #19
<number><number>
MCU Library

## Slide 38
<footer>Group #19
<number><number>
MCU Packet Format

## Slide 39
Provides communication from FPGA to the Host AUV PC.
Includes a RS232RefComp component for using the RS232 Protocol. Encompasses all code to perform RS232 communications with simple interface.
<footer>Group #19
<number><number>
MCUPRT (Packet Rx and Tx)

## Slide 40
waitForStartBytes
getHeader
getDataByte0
getDataByte1
getDataByte2
getDataByte3
  If valid ->
processChecksum
  Else ->
RxProcess
Finite state machine for receiving a valid MCU Packet
Retrieves the Command and Data bytes and puts it on the external port
<footer>Group #19
<number><number>
MCUPRT (cont.)

## Slide 41
TxProcess
Finite state machine for transmitting a valid MCU Packet that is placed on the components external ports
Encompasses start byte sequence and checksum calculations to module
<footer>Group #19
<number><number>
MCUPRT (cont.)
waitForPacket
txStartByte1
txStartByte2
txCommand
txDataByte0
txDataByte1
txDataByte2
txDataByte3
txChecksum

## Slide 42
<footer>Group #19
<number><number>
Supported Message Set

## Slide 43
Required to control the analog filter’s center frequency.
Must be a 50% duty cycle PWM wave at varying frequencies.
Simple interface for selecting appropriate frequency
Performs calculation to scale from 50 MHz FPGA clock to mapped frequency for filter.
<footer>Group #19
<number><number>
FilterFreqSelect

## Slide 44
A data register is used to store the value for the counter
The Up/Down Counter is loaded with a new value from the data register when the counter reaches its terminal count;
When the data value is first loaded, the counter begins to count down from the data value to 0.
When the counter transitions through 0, the terminal count is generated and it triggers the Toggle Flip-flop to drive the PWM signal High
The data value is re-loaded and the cycle repeats.
*Counter direction is controlled by output signal:
  count down when low / count up when high
<footer>Group #19
<number><number>
PWM (Attempt 1)

## Slide 45
Designed PWM to meet the requirements of a continuous square wave with a varying frequency
Simple approach
F = 50 MHz / [2 * (1 + Input) ]
<footer>Group #19
<number><number>
PWM

## Slide 46
Finite state machine for capturing the four channels simultaneously
Contains two AD1RefComp modules for interfacing with the two PmodAD1 over SPI
<footer>Group #19
<number><number>
ASignalInterface (VHDL)
Wait for Conversion
Store Conversion
Start Conversion
AD_done = 1
AD1RefComp Interface
AD_done = 0

## Slide 47
<footer>Group #19
<number><number>
Hardware interface to PmodAD1
Physical connections made from Nexys2 FPGA to the PmodAD1 peripheral modules

## Slide 48
The DS1803 is a digital potentiometer used for varying the gain in the analog system
Uses the I2C communication protocol
Allows multiple chips to be on the same bus, unique addresses
FPGA will act in master mode
DS1803 in slave mode
<footer>Group #19
<number><number>
DS1803 Interface (VHDL)

## Slide 49
VHDL I2C Module will be utilized to conform to I2C Standard
Create our own simple I2C module
Use an open source module that implements full standard, more complicated
<footer>Group #19
<number><number>
I2C
Custom I2C Module FSM

## Slide 50
Trilateration
Multilateration
Input / Output Data Mapping
All Require Timing Acquisition
Acquiring synchronized and accurate timing data from the hydrophones is necessary for acoustic localization of pinger.
Methods:
  Counter Method
  Frequency Domain Analysis
  Cross Correlation
The different methods are used for differences in hydrophone distances
<footer>Group #19
<number><number>
Localization Techniques

## Slide 51
Time of Arrival (ToA) technique requires the receivers to be synchronized with the source
Solves the intersection of three spheres
Not applicable for our situation
<footer>Group #19
<number><number>
Trilateration

## Slide 52
Hyperbolic positioning of Time Delay of Arrival (TDoA) using a reference receiver
Equations formed results in 3D hyperboloids
Intersection of 3D meshes is the solution, the pinger’s location
Nonlinear system, prone to input error
Initial simulations showed that input with < 1% error resulted in output error > 10%
Tolerances may not be achievable with the system
<footer>Group #19
<number><number>
Multilateration

## Slide 53
Map data elements between two separate and distinct sets
Input pinger timing information from each hydrophone
Output pinger heading and distance information
A technique to attempt to linearize the system about some nonlinear function to reduce error within some specified tolerance
<footer>Group #19
<number><number>
Input / Output Data Mapping
Pinger
Pinger

## Slide 54
Requires high speed counter
Susceptible to noise
Compared to reference signal
Hydrophones need to be spread out as far as possible
<footer>Group #19
<number><number>
Counter Method

## Slide 55
<footer>Group #19
<number><number>
Frequency Domain Analysis (Relative Phase Shift)
Hydrophones have to be placed within half a wavelength
FFT is performed
Assumes pure sine wave
Error due to ‘spill over’ in DFT
Time Domain
Frequency Domain

## Slide 56
Measures the similarity between two waveforms as a function of time-shifting
Minimum and maximum range of input time and resolution is based on maximum distance between hydrophone pair
<footer>Group #19
<number><number>
Cross Correlation

## Slide 57
<footer>Group #19
<number><number>
Budget

## Slide 58
<footer>Group #19
<number><number>
Budget
Total Cost: $6579.00
Total AUV Team Cost: $1385.92
Total Out-of-Pocket Expense: $0.00
Percent Purchased: 70%

## Slide 59
<footer>Group #19
<number><number>
Progress

## Slide 60
<footer>Group #19
<number><number>
Timeline

## Slide 61
Questions?
<footer>Group #19
<number><number>