Group #3
RC Ghost Rider
Adolph Arieux (EE)
James Russick (EE)
Paul Shimei (EE)
Sponsored by: Workforce Central Florida
Mentor: Richard Barrett - ITT

---
Project Description
A small vehicle that is...
  - Controlled remotely by the Cockpit
  - Equipped with sensors to provide feedback to the cockpit concerning the vehicle's displacement
  - Equipped with a camera to provide the end user with optical sensory input

---
Project Description
A Cockpit that...
  - Is an apparatus mounted on an actuating platform in which the user will operate in a seated position
  - Utilizes a steering wheel and pedals to gather information to remotely control the vehicle
  - Tilts depending on acceleration of the RC Car in the directions parallel to the ground plane
  - Jolts proportionally based on obstacles RC Car obstacles
  - Has a display relaying the image from the camera
  - Safe, comfortable, and easy for the user to operate

---
Goals and Motivation
- For the user to have a realistic and interactive simulation experience (as well as safe)
- To challenge ourselves with an extensive and in depth project
- Responsive remote controlled car
- Effective feedback control from the RC Car and the Cockpit

---
Vehicle Specifications
- Dimensions less than 24'' x 24''
- Total weight less than 5 lbs
- Remote Controlled from a distance of at most 300 feet from the Cockpit
- Speed up to 10MPH
- Battery rated at more than 24 WH

---
Cockpit Specifications
- Max Operator Weight Limit: 300lbs
- Angular Velocity greater than 8 deg/s (Along both X/Z plane rotating to Y axis)
- Independent pitch and roll: +/- 15 deg
- Less than 1200W power consumption
- To be operated within 4 feet clear of obstructions

---
Overall System Diagram

---
Vehicle Physical Design

---
Cockpit Physical Design
Base Top View

---
Cockpit Physical Design
Base Side View

---
Cockpit Physical Design
Floorboard Side View

---
Cockpit Physical Design
Steering Column Side View

---
Vehicle Components
- Micro-controller - MSP430
- Transceiver – Xbee
- Control Feedback – An Accelerometer and/or	Potentiometers
- Video Communication - Q-See QSWLMCR video surveillance kit
- Drive Motor - Redcat Racing E012 RC Motor
- Turning Motor – Tower Hobbies Servo Motor

---
Vehicle Hardware Design

---
Vehicle Feedback Subsystem

---
Vehicle Control Subsystems

---
Vehicle Communication Subsystems

---
Vehicle Software Overview

---
Cockpit Components
- Netduino Processing Platform
- Seat: 1992 Nissan 240 SX driver's seat
- Display screen: Sharp 19 inch 720p HDTV
- Steering wheel: 1992 Nissan 240 SX
- Pedals: 1992 Nissan 240 SX pedals
- 3 DC actuators
- 24V Power Supply: DuraComm RM-5024 Unipolar Switching Supply rated for 50A

---
Servo City DC Thrust Actuators
450 lb thrust
6”extension
Operates at 6 - 12 VDC
Operating speed (12V) No load: 2.90in/sec Max load: 1.89in/sec
Static load capacity: 1,011 lbs
Equipped with a 10k potentiometer
Recommended Fuse: 20A (15A fuse will be used)
Three will be utilized

---
Netduino
48MHz Atmel 32-bit Microcontroller
6 analog input pins
14 GPIO Digital pins (of which, 4 are PWM)
Utilizes C#
Open Source

---
Cockpit Hardware Design

---
Cockpit Transceiver Subsystem

---
Operator Controls Subsystem

---
Actuator Control Subsystem
PWM input at 500Hz: 0-14% Duty Cycle
Sign Bit Pin Input (Right): Determines Direction
Output: ~69 values in each direction (-14V to +14V)

---
Cockpit Software Overview

---
Budget and Financing
RC Car
Parts	Quantity	Price	Total
Accelerometer	1	$5.00	$5.00
Potentiometers	4	$4.00	$16.00
Turning Servos	1	$13.00	$13.00
DC Motor	1	$40.00	$40.00
Battery	2	$30.00	$60.00
Voltage Regulators	2	$2.00	$4.00
Car	1	Free	Free
MCU	3	$6.00	$18.00
Transceiver	1	$45.00	$45.00
PCB Fabrication	1	$100.00	$100.00
Misc. Parts	1	$50.00	$50.00
Camera/Transmitter	1	$80.00	$80.00
		Subtotal =	$427.00

---
Budget and Financing
Parts	Quantity	Price	Total
Seat	1	$95.00	$95.00
Pedals	2	$50.00	$100.00
Display	1	$100.00	$100.00
Adjustable Seat Platform & Mounting Brackets	2	$100.00	$200.00
Potentiometers	6	$8.00	$48.00
Steering Wheel	1	$45.00	$45.00
Ball and Socket Joints	10	$50.00	$500.00
Platform	1	$50.00	$50.00
Linear Actuators	3	$400.00	$1,200.00
Raised Platform	1	$95.00	$95.00
Transceiver	1	$45.00	$45.00
Fabrication	1	$200.00	$200.00
MCU	1	$80.00	$80.00
Misc. Parts	1	$100.00	$100.00
		Subtotal =	$2858.00
		Total =	$3285.00

---
Budget Analysis
Total Sponsored Funds $3,200.00
Total Estimated Cost $3,285.00
Balance	-$85.00

---
Work Distribution (%)

---
Progress

---
Potential Pitfalls
- Structural/Mechanical Stability
- User Safety
- High current circuitry
- Over-Engineering

---
Milestones
Completed
- Documentation, Research and Design
- Control Circuit tested and working
- Hardware Parts Aquisition

---
Milestones
To be completed by:
- Feb 14th - PCB submitted to manufacturer
- Feb 25th - Subsystem Interfacing
- March 1s - Cockpit Fabrication
- March 15th - Software Fine-Tuning
- March 20th - Car and Cockpit Interfacing
- April 5th – All testing Completed

---
Questions?