Group #3
RC Ghost Rider
Adolph Arieux (EE)
James Russick (EE)
Paul Shimei (EE)
Sponsored by: Workforce Central Florida
Mentor: Richard Barrett - ITT

---
Project Description
A small vehicle that is...
  - Controlled remotely by the Cockpit
  - Equipped with sensors to provide feedback to the cockpit concerning the vehicle's displacement
  - Equipped with a camera to provide the end user with optical sensory input

---
Project Description
A Cockpit that...
  - Is an apparatus mounted on an actuating platform in which the user will operate in a seated position
  - Utilizes a steering wheel and pedals to gather information to remotely control the vehicle
  - Tilts depending on acceleration of the RC Car in the directions parallel to the ground plane
  - Jolts proportionally based on obstacles RC Car obstacles
  - Has a display relaying the image from the camera
  - Safe, comfortable, and easy for the user to operate

---
Goals and Motivation
- For the user to have a realistic and interactive simulation experience (as well as safe)
- To challenge ourselves with an extensive and in depth project
- Responsive remote controlled car
- Effective feedback control from the RC Car and the Cockpit

---
Vehicle Specifications
- Dimensions less than 24'' x 24''
- Total weight less than 5 lbs
- Remote Controlled from a distance of at most 300 feet from the Cockpit
- Speed up to 10MPH
- Battery rated at more than 24 WH

---
Cockpit Specifications
- Max Operator Weight Limit: 300lbs
- Total Angular Offset (both Pitch and Roll) of 15 degrees totals
- Less than 1200W power consumption
- To be operated within 4 feet clear of obstructions
- Cockpit's should be easy to operate and feature component attachment that allows to be changed in a timely manner

---
Overall System Diagram

---
Vehicle Physical Design

---
Cockpit Physical Design
Base Front View

---
Cockpit Physical Design
Right Side View

---
Cockpit Physical Design
Front View

---
Vehicle Components
- Micro-controller – Atmega 328P
- Transceiver – Xbee
- Control Feedback – An Accelerometer and	Potentiometers
- Video Communication – 1.2 GHz Transmitter and Reciever
- Drive Motor - Redcat Racing E012 RC Motor
- Turning Motor – Tower Hobbies Servo Motor

---
Vehicle Hardware Design

---
Vehicle Software Overview

---
Cockpit Components
- Netduino Processing Platform
- Seat: 1997 Dodge Ram driver's seat
- Display screen: Sharp 19 inch 720p HDTV
- Steering wheel: Sega Saturn Gaming Controller
- Pedals: Self-fabricated from Diamond Plate Aluminum
- Power Supply: Ericson 16 Volt 50 Amp
- Actuators: 3 (Explained in Detail in the following slide)

---
Cockpit Components
- Seat
  - Elimination of Forward/Backwards Seat Movement
  - RCI - 5 point harness
- Television Tree
  - Steering Wheel
  - Television
- Pedals
  - Mounting
  - Potentiometer Connection

---
Servo City DC Thrust Actuators
450 lb thrust
6”extension
Operates at 6 - 12 VDC
Operating speed (12V) No load: 2.90in/sec Max load: 1.89in/sec
Static load capacity: 1,011 lbs
Equipped with a 10k potentiometer
Recommended Fuse: 20A (15A fuse will be used)
Three will be utilized

---
Netduino
48MHz Atmel 32-bit Microcontroller
6 analog input pins
14 GPIO Digital pins (of which, 4 are PWM)
Utilizes C#
Open Source

---
Cockpit Hardware Design

---
Cockpit Transceiver Subsystem

---
Operator Controls Subsystem

---
Actuator Control Subsystem (Old)
PWM input at 500Hz: 0-14% Duty Cycle
Sign Bit Pin Input (Right): Determines Direction

---
Cockpit Software Overview

---
Budget and Financing
RC Car
Parts	Quantity	Price	Total
Accelerometer	1	$5.00	$5.00
Potentiometers	4	$4.00	$16.00
Turning Servos	1	$13.00	$13.00
DC Motor	1	$40.00	$40.00
Battery	2	$30.00	$60.00
Voltage Regulators	2	$2.00	$4.00
Car	1	Free	Free
MCU	3	$6.00	$18.00
Transceiver	1	$45.00	$45.00
PCB Fabrication	1	$100.00	$100.00
Misc. Parts	1	$50.00	$50.00
Camera/Transmitter	1	$80.00	$80.00
		Subtotal =	$427.00

---
Budget and Financing
Parts	Quantity	Price	Total
Seat	1	$45.00	$45.00
Pedals	2	$25.00	$50.00
Display	1	$100.00	$100.00
Potentiometers	6	$8.00	$48.00
Steering Wheel	1	$30.00	$30.00
Heim Joints	2	$25.00	$50.00
Hardware	1	$10.00	$10.00
Linear Actuators	3	$400.00	$1,200.00
Transceiver	1	$45.00	$45.00
Fabrication/Materials	1	$1,100.00	$1,100.00
MCU	1	$80.00	$80.00
Misc. Parts	1	$100.00	$100.00
		Subtotal =	$2858.00
		Total =	$3285.00

---
Budget Analysis
Total Sponsored Funds $3,200.00
Total Estimated Cost $3,285.00
Balance	-$85.00

---
Work Distribution (%)

---
 Problems Encountered
- Structural and Mechanical Stability
- Materials Acquisition
- High current circuitry
- Over-Engineering
- User Safety
- Other Classes

---
Vehicle Specific Issues
- Two Battery Design
- Push pull motor controller
- Accelerometer Jitter
- Synchronization
- Camera and receiver issues

---
Cockpit Specific Issues
- High Current Motor Controlling
- Unstable Potentiometer Readings

---
Questions?