## Slide 1
Team 1 – Sleep Management System
Anthony Bharrat
Facundo Gauna Ryan Murphy
Bartholomew Straka

## Slide 2
KnightTime attempts to monitor sleep cycles through the use of three peripherals.
The peripherals contain biomedical sensors.
They transmit data back to the mobile application.
Wristband
Mask
Base Station

## Slide 3: Motivation
To improve the quality of people’s sleep by informing them of their:
  Movement
  Heart rate
  Ambient Measurements
    Light
    Humidity
    Noise
  Sleep Cycles
*Image by Mikael Häggström via Wikimedia Commons

## Slide 4: Goals and Objectives
The system is:
  Modular
  User-Friendly
  Low-Cost
  Power-Efficient
User-Friendly
Low-Cost
Modular
Power-Efficient

## Slide 5: Requirements
Be able to measure:
  Skin Temperature
  Body Movement
  Ambient Temperature
  Ambient Humidity
  Heart Rate
  Ambient Sound
Be able to sound an alarm at:
A particular time based on measured physiological cues.
At a user-defined time.

## Slide 6: Specifications
Power Supply Voltage (Base Station) | Standard USB (5V DC, 1+ A best for charging)
Wearable Device Battery Life | 6 Hours+
Wearable Device(s) Weight | < 5 lbs.
Temperature Sensor Accuracy | ± 25%
Heart Rate Accuracy | ± 25% when acquired
Humidity Sensor Accuracy | ± 25%
Audible Alarm | 30+ dB
Functional Temperature Range | 5-35° Celsius (intended for indoor sleeping)
Minimum Wireless Range | 5 Feet
Battery Recharge Time | < 12 Hours for 100%

## Slide 7: Concept of Operation

## Slide 8: Smart Alarm
The system attempts to wake the user during a lighter stage of sleep. This reduces sleep inertia.

## Slide 11: Smart Alarm
The peripherals allow the system to continue an alarm until the user shows significant signs of wakefulness such as a math problem.
Additional tasks may be added in the future.

## Slide 12: Data Review
After fully awake, the user can review the data collected throughout the night.
The user is able to see when the alarm was triggered.
They will be able to improve their sleep habits by reviewing the data.

## Slide 13: Implementation

## Slide 14
Vibrator
Light Array
MSP430
Pulse Oximeter
Battery
Bluetooth Module
Skin Temperature
MSP430
Bluetooth Module
Ambient Light
Ambient Noise
Ambient Temp
Ambient Humidity
Charging Module
IMU
Bluetooth Module
Battery
MSP430
Hardware
Block Diagram
Wristband
Base Station
Headband

## Slide 15: Microcontroller (MCU) Selection

## Slide 16: MSP430
MSP430 provides a good balance of features with low power consumption.
Useful for testing sensors in the same development environment.
MCU from board to socket
ICSP (In-Circuit Serial Programming) is easy: only 2 pins required.

## Slide 17: Communication Module Selection

## Slide 18: Bluetooth Module
The Bluetooth module chosen is the RN-42.
Features:
  Easy to Configure
  Readily available on cheap breakout boards
  Auto discovery/pairing
  Error correction
  Integrated antenna
  Small

## Slide 19
Vibrator
Light Array
MSP430
Pulse Oximeter
Battery
Bluetooth Module
Skin Temperature
MSP430
Bluetooth Module
Ambient Light
Ambient Noise
Ambient Temp
Ambient Humidity
Charging Module
IMU
Bluetooth Module
Battery
MSP430
Wrist Peripheral

## Slide 20: Wrist Peripheral
The wrist peripheral functions as an actigraph unit.
Actigraphy is a non-invasive way of monitoring rest and activity through measuring movement.
Offers high agreement with professional sleep studies.
The unit consists of:
  MCU
  Bluetooth Module
  Battery
  Vibration Motor
  IMU (Inertial Measurement Unit)

## Slide 21
Wristband Schematic

## Slide 22: IMU (Inertia Measurement Unit)

## Slide 23: MPU 6050
Inexpensive breakout board (~$10)
Small size
Reasonable power draw
High sensitivity
16-bit Digital values over I²C (Inter-Integrated Circuit) Communication Protocol

## Slide 24: Vibration Motor
This is to help wake the user or notify them of such customizable event.
Precision Microdrives 310-101
Widely available and inexpensive: $4.95 from SparkFun
Powerful: 0.8 G Vibration Amplitude

## Slide 25: Vibration Motor Circuit
Pulse Width Modulation (PWM) from MCU to base of MOSFET controls vibration
Schottky ‘Flyback’ Diode prevents inductive kickback from motor
Capacitor reduces noise generated by motor

## Slide 26
Vibrator
Light Array
MSP430
Pulse Oximeter
Battery
Bluetooth Module
Skin Temperature
MSP430
Bluetooth Module
Ambient Light
Ambient Noise
Ambient Temp
Ambient Humidity
Charging Module
IMU
Bluetooth Module
Battery
MSP430
Mask Peripheral

## Slide 27: Mask Peripheral
The Mask peripheral will contain:
  Skin temperature sensor
  LED light array (to simulate sunrise)
  Pulse rate monitor
  Battery
  Bluetooth Module
  Buzzer alarm near ears

## Slide 29: Selection of Skin Temperature Sensor

## Slide 30: Skin Temperature: MLX90614DAA
Infrared thermometer for non contact temperature measurements.
DAA version intended for medical applications
Key features include:
  17-bit ADC and powerful DSP
  Power saving mode
  Resolution of 0.02°C

## Slide 31: Light Array
An array of LEDs will gradually increase in brightness to simulate the sun rising
Exposure to light 30 min prior to waking reduces sleep inertia
Optional

## Slide 32: Heart Rate Sensor
Pulse is a helpful sleep indicator.
Forehead is a viable location.
Use reflectance of oxygenated blood cells (reflectance pulse oximetry)
Chosen: TCRT1000 Infrared Proximity Sensor
Sensor combines infrared LED with NPN phototransistor
Units in millimeters

## Slide 33
Signal Conditioning for Heart Rate

## Slide 34: DC offset cancellation
“Servo feedback” technique without capacitor signal path
Actively removes DC component with 2nd order filters
Simplifies band-pass filter creation since frequencies of interest are very close (0-3 Hz)

## Slide 35: Low-Pass Filter
Generalized Immittance Converter Structure
Cutoff frequency at 4.8 Hz
Minimizes component sensitivity and spread
Important since small area of interest for frequency response: 0-5 Hz
Simplified design
Butterworth response by modifying one resistor:

## Slide 36: Heart Rate Prototyping
Excellent slew rate
Digital logic level response to detected pulse
Oscilloscope picture taken after heart rate acquired
Circuit takes a few minutes to adjust to the signal input due to active DC offset cancellation

## Slide 37
Vibrator
Light Array
MSP430
Pulse Oximeter
Battery
Bluetooth Module
Skin Temperature
MSP430
Bluetooth Module
Ambient Light
Ambient Noise
Ambient Temp
Ambient Humidity
Charging Module
IMU
Bluetooth Module
Battery
MSP430
Base Station

## Slide 38: Base Station
The base station will contain the following:
Ambient light sensor
Ambient temperature sensor
Ambient humidity sensor
Ambient noise sensor
Bluetooth Module
Charging Module for peripherals

## Slide 40: Ambient Light
An ambient light sensor was selected (Vishay TEPT5600)
Sensor is an NPN phototransistor adapted to human eye responsivity
User can compare quality of sleep to amount of light present.
Potential to kill lights, shut blinds, sound alarm, etc.

## Slide 41: Ambient Light Circuit

## Slide 42: Ambient Temp and Humidity: RHT03
RHT03 is a low cost humidity and temperature sensor
Already calibrated - no external components
1-wire proprietary digital signal; code provided by manufacturer (MaxDetect)
Ambient temperature vs. body temperature
Sleep quality vs. environment

## Slide 43: Ambient Noise: AOM-4544P-2-R
A microphone was selected to detect snoring.
Most snoring occurs at low frequencies: 20 - 500 Hz
AOM-4544P-2-R range from 20 Hz - 20 KHz
Chosen for low price, sensitivity, and omnidirection

## Slide 44: Battery
A polymer lithium-ion (LiPo) battery with 850mAh was selected
Higher energy density compared to standard lithium-ion batteries
Small size and decent capacity.
Rechargeable
Built-in over- and under-voltage protection

## Slide 45: Charging and Power
Dock provides USB ports for peripheral charging
Uses Texas Instruments TPS2074 Four-Port USB Hub Power Controller
AC power supply also USB (5V 1A)
Each peripheral uses a LDO (low-dropout linear regulator)

## Slide 46
TPS2074 USB Power Controller Setup

## Slide 47: Charging and Voltage Regulator
TPS7A4501 Low-Dropout Regulator
Can supply up to 1.5 A with a dropout voltage of 300 mV
Much lower dropout at lower current: 85 mV at 100 mA, 170 at 500 mA
Adjustable

## Slide 48: Charging and Voltage Regulator
MCP73831 Li-Polymer Charge Management Controller
500 mA charger
Chosen for price and ease of use
Available on convenient breakout module
Not placed on peripheral PCBs to reduce footprint

## Slide 49
Vibrator
Light Array
MSP430
Pulse Oximeter
Battery
Bluetooth Module
Skin Temperature
MSP430
Bluetooth Module
Ambient Light
Ambient Noise
Ambient Temp
Ambient Humidity
Charging Module
IMU
Bluetooth Module
Battery
MSP430
Mobile App

## Slide 50: Mobile Application
The application will implement the:
  Monitoring Algorithm
  Network Messaging System
  A database to store acquired data
It was developed using Mono for Android™ framework.
  It allows the developer the use of C#/.NET and Visual Studio™
  It links the assemblies to Java binaries
C#

## Slide 51: Messaging System
1
2
3

## Slide 52: Data Presentation
The mobile application presents collected data by:
  Graphing the collected data
  Sorting stored data by run
Real-time
  Provides real-time plotting for movement messages

## Slide 53: Administrative Content

## Slide 54: Distribution of Work
Facundo (CpE)
Embedded Software
Mobile App
Anthony (CpE)
Embedded Software
Wireless
Bart (EE)
Power
Sensors/PCBs
Ryan (EE)
Power
Sensors/PCBs

## Slide 55: Bill of Materials

## Slide 56: Questions?