## Slide 1
Team 1 – Sleep Monitoring System
Anthony Bharrat
Bartholomew Straka
Facundo Gauna Ryan Murphy

## Slide 2
KnightTime monitors sleep cycles through the use of three peripherals.
The peripherals contain biomedical sensors.
They transmit data back to the mobile application.
Wristband
Mask
Base Station

## Slide 3: Motivation
To improve the quality of a person’s sleep by informing them of their:
  Movement
  Heart rate
  Ambient Measurements
    Light
    Humidity
    Noise
  Sleep Cycles
*Image by Mikael Häggström via Wikimedia Commons

## Slide 4: Goals and Objectives
The system should be:
  Modular
  User-Friendly
  Low-Cost
  Power-Efficient
User-Friendly
Low-Cost
Modular
Power-Efficient

## Slide 5: Requirements
Be able to measure:
  Body Temperature
  Body Movement
  Ambient Temperature
  Ambient Humidity
  Heart Rate
  Ambient Sound
Be able to sound an alarm at:
A particular time based on measured physiological cues.
At a user-defined time.

## Slide 6: Specifications
Power Supply Voltage | AC 110-230 V
Wearable Device Battery Life | 6 Hours+
Wearable Device(s) Weight(total) | < 5 lbs.
Temperature Sensor Accuracy | ± 25%
Pulse Oximetry Accuracy | ± 25%
Humidity Sensor Accuracy | ± 25%
Audible Alarm | 30-90 dB
Functional Temperature Range | 5-35 Celsius°
Minimum Wireless Range | 5 Feet
Battery Recharge Time | < 24 Hours from 100%

## Slide 7: Concept of Operation

## Slide 8: Smart Alarm
The system tracks the user's stage of sleep to wake them at the best time.

## Slide 9: Smart Alarm
The peripherals allow the system to continue an alarm until the user shows significant signs of wakefulness such as high movement or heart rate.

## Slide 10: Data Review
After fully awake, the user can review the data collected throughout the night.
The user will be able to see when the alarm was triggered.
They will be able to improve their sleep habits by reviewing the data.

## Slide 11: Implementation

## Slide 12
Vibrator
Light Array
MSP430
Pulse Oximeter
Battery
Bluetooth Module
Skin Temperature
MSP430
Bluetooth Module
Ambient Light
Ambient Noise
Ambient Temp
Ambient Humidity
Charging Module
IMU
Bluetooth Module
Battery
MSP430
Hardware
Block Diagram

## Slide 13: Micro Controller Selection

## Slide 14: MSP430
MSP430 provides a good balance of features with low power consumption.
Useful for testing sensors in the same development environment.
No ICSP required. MCU from board to socket

## Slide 15: Communication Module Selection

## Slide 16: Bluetooth Module
The Bluetooth module chosen is the RN-42.
Features:
  Easy to Configure
  Auto discovery/pairing
  Error correction
  Integrated antenna
  Small

## Slide 17
Vibrator
Light Array
MSP430
Pulse Oximeter
Battery
Bluetooth Module
Skin Temperature
MSP430
Bluetooth Module
Ambient Light
Ambient Noise
Ambient Temp
Ambient Humidity
Charging Module
IMU
Bluetooth Module
Battery
MSP430
Wrist Peripheral

## Slide 18: Wrist Peripheral
The wrist peripheral functions as an actigraph unit.
Actigraphy is a non-invasive way of monitoring rest and activity through measuring movement.
Offers high agreement with professional sleep studies.
The unit consists of:
  MCU
  Bluetooth Module
  IMU
  Battery
  Vibration Motor

## Slide 19: IMU (Inertia Measurement Unit)

## Slide 20: MPU 6050
Inexpensive breakout board (~$10)
Small size
Reasonable power draw
High sensitivity
16-bit Digital values (over I2C)

## Slide 21: Vibration Motor
This is to help wake the user or notify them of such customizable event.
iPhone 4S Vibration Motor
Widely available + cheap

## Slide 22
Vibrator
Light Array
MSP430
Pulse Oximeter
Battery
Bluetooth Module
Skin Temperature
MSP430
Bluetooth Module
Ambient Light
Ambient Noise
Ambient Temp
Ambient Humidity
Charging Module
IMU
Bluetooth Module
Battery
MSP430
Mask Peripheral

## Slide 23: Mask Peripheral
The Mask peripheral will contain:
  Skin temperature sensor
  LED light array (to simulate sunrise)
  Pulse rate monitor
  Battery
  Bluetooth Module
  Buzzer alarm near ears

## Slide 24: Selection of Skin Temperature Sensor

## Slide 25: Skin Temperature: MLX90614DAA
Infrared thermometer for non contact temperature measurements.
Key features include:
  17-bit ADC and powerful DSP
  Power saving mode
  Resolution of 0.02°C

## Slide 26: Light Array
An array of LEDs will gradually increase in brightness to simulate the sun rising.
Exposure to light 30 min prior to waking reduces sleep inertia.
Optional.

## Slide 27: Heart Rate Sensor
Pulse is a helpful sleep indicator.
Forehead is a viable location.
Similar to pulse oximetry
Use reflectance of oxygenated blood cells
Chosen: TCRT1000 Infrared Proximity Sensor

## Slide 28: Signaling Condition for Heart Rate

## Slide 29: Heart Rate Schematic

## Slide 30: Heart Rate Prototyping

## Slide 31
Vibrator
Light Array
MSP430
Pulse Oximeter
Battery
Bluetooth Module
Skin Temperature
MSP430
Bluetooth Module
Ambient Light
Ambient Noise
Ambient Temp
Ambient Humidity
Charging Module
IMU
Bluetooth Module
Battery
MSP430
Base Station

## Slide 32: Base Station
The base station will contain the following:
Ambient light sensor
Ambient temperature sensor
Ambient humidity sensor
Ambient noise sensor
Bluetooth Module
Charging Module for peripherals

## Slide 33: Ambient Light
A photoresistor was selected to detect ambient light in the room.
User can compare quality of sleep to amount of light present.
Potential to kill lights, shut blinds, etc.

## Slide 34: Ambient Light Circuit + Equation

## Slide 35: Ambient Temp and Humidity: RHT03
RHT03 is a low cost humidity and temperature sensor
Already calibrated - no external components
Ambient temperature vs. body temperature
Sleep quality vs. environment

## Slide 36: Ambient Noise: AOM-4544P-2-R
A microphone was selected to detect snoring.
Most snoring occurs at low frequencies: 20 - 500 Hz
AOM-4544P-2-R range from 20 Hz - 20 KHz
Chosen for low price, sensitivity, and omnidirection

## Slide 37: Battery
A polymer lithium-ion (LiPo) battery with 850mAh was selected.
Higher energy density compared to standard lithium-ion batteries.
Small size and decent capacity.
Rechargeable.

## Slide 38: Charging and Power
Dock provides USB ports for peripheral charging
AC power supply also USB (5V 1A)
Regulator and charger IC's

## Slide 39: Charging and Voltage Regulator
TPS650250 Power Management IC for Li-Ion Powered Systems
3.7 V battery, 5 V USB --> 3.3 V Step-down converter
97% efficiency, up to 1.6A

## Slide 40: Charging and Voltage Regulator
MCP73831 Li-Polymer Charge Management Controller
500 mA charger
Chosen for price and ease of use

## Slide 41: Charging and Voltage Regulator
MCP73831 Li-Polymer Charge Management Controller
500 mA charger
Chosen for price and ease of use

## Slide 42
Vibrator
Light Array
MSP430
Pulse Oximeter
Battery
Bluetooth Module
Skin Temperature
MSP430
Bluetooth Module
Ambient Light
Ambient Noise
Ambient Temp
Ambient Humidity
Charging Module
IMU
Bluetooth Module
Battery
MSP430
Mobile App

## Slide 43: Mobile Application
The application will implement the:
  Monitoring Algorithm
  Network Messaging System
  A database to store acquired data
It is being developed using Mono for Android™ framework.
  It allows the developer the use of C#/.NET and Visual Studio™
  It links the assemblies to Java binaries
  Provides very little overhead and performance hit.
C#

## Slide 44: Messaging System

## Slide 45: Administrative Content

## Slide 46: Performance
Chart: 
| Research | Design | Software | Hardware | Test
Progress | 90 | 70 | 20 | 20 | 5
Left | 10 | 30 | 80 | 80 | 95

## Slide 47: Distribution of Work
Facundo (CpE)
Embedded Software
Mobile App
Anthony (CpE)
Embedded Software
Wireless
Bart (EE)
Power
Sensors/PCBs
Ryan (EE)
Power
Sensors/PCBs

## Slide 48: Bill of Materials

## Slide 49: Problems
TI I2C library did not work with MPU 6050
How to package in while keeping the device small/comfortable
Full system tests could take up to 10hrs.
We must provide power for at least 8 hrs. with minimal battery size.
Initially the base station was going to implement the Monitoring Algorithm.
    The Bluetooth connection (Master/Slave) complicated the chain of command.

## Slide 50: Questions?