## Slide 1: Project AUGI
UCF Augmented Navigation System

## Slide 2: Motivations
To develop an improved and more open navigation experience.
Make it accessible to a broad audience through Android devices.
To improve upon traditional 2D maps and voice turn-by-turn navigation.
Notes: *Introduce yourself, Project Name
*Current navigation aids require the user to be able to read a map, match what they see to the map (cross streets, landmarks)
* Better to just provide a virtual line for them to follow to their destination.

## Slide 3: What is Project AUGI?
Android based augmented reality navigation application.
  Includes:
    Android Application
    Hardware/Software Interface
    Expansion Sensor board
Notes: *Three main focus areas to this project: Software application, Sensor Board, hardware/software communication layers
*

## Slide 4: Platform Choices
iOS vs. Android vs. Windows Phone 8
Which platform is the most open and familiar to the team?
  SDK features
  Programming Language familiarity
  Interfacing with Hardware
  Map Features

## Slide 5: Base Development Platform
Panda Board ES vs Beagle Board-xM
 | Panda Board ES | Beagle Board-xM
CPU | Dual-Core ARM A9 1.2 Ghz | Single Core ARM Cortex A8 1.0 Ghz
RAM | 1 GB | 512 MB
Video | Imagination SGX540 | Texas Instruments DM3730
Connectivity | WLAN bgn, Bluetooth, 10/100 Ethernet | 10/100 Ethernet
Video out | DVI-D, HDMI | DVI-D
Price | $162 | $149

## Slide 6: Base Development Platform
Panda Board ES + Chipsee Expansion
7 inch LCD 800 x 400
5-point Capacitive Touch
5 User Keys (useful for Android OS)
Linaro Android OS 4.0.3

## Slide 7: Application
2 Basic parts to the Application:
Navigation Activity
  Basic Google Maps functionality
  Some custom functionality
AUGI Lens Activity
    Augmented Landmark detection
  Augmented Navigation
Notes: Adam

## Slide 8: Navigation
Basic Google Maps GPS based functionality:
  Landmark Searching
  Destination Routing
  Zooming and panning
Added functionality:
  Custom landmark creation
  (locally stored)
  Bounded by UCF’s campus limits
Sensor Polling:
GPS (location)
Notes: Adam
-Search Queries will be performed across both Google’s DB and local custom landmarks

## Slide 9: AUGI Lens
Augmented Landmark Layer:
Going to detect, in real time, the landmarks that you are facing using the camera preview.
Ability to detect landmarks through
obstruction and display name
preview.
If a landmark is selected,
Augmented navigation will
initiate.
Sensor Polling:
GPS (location)
Gyroscope (orientation)
Magnetometer (find North)
Notes: Adam

## Slide 10: AUGI Navigation
Augmented Navigation Layer:
Initiated within AUGI Lens activity
User will be navigated to selected
landmark via augmented on-screen
route lines.
Sensor polling:
GPS sensor(location)
Magnetometer (find North)
Gyroscope (orientation)
Barometric sensor (altitude)
Notes: John

## Slide 11: Class Diagram
Notes: John

## Slide 12: Controller Software Interface
Java code Libraries integrate with Eclipse
Plug and Play Android Driver
I2C Communication Protocol
Sensor Loop Class

## Slide 13: IOIO Software Interface
Establish Connection
Data Packet Format

## Slide 14: IOIO Software Interface
Send, Receive, Process

## Slide 15: Hardware Diagram
Custom Board

## Slide 16: Microcontroller Selection
MSP430
Advantages:
CHEAP
Arduino:
Advantages:
WELL DOCUMENTED
Parallax Propeller:
Advantages:
EIGHT PROCESSERS(COGS)

## Slide 17: Winner: IOIO Board (Yo-Yo)
Provides robust connectivity to an Andriod device via a USB/bluetooth connection.
Fully controllable from within an Android application using a simple and intuitive Java API
Talks to the PandaBoard ES via USB Directly!

## Slide 18: IOIO Pin Out
Based on PIC24 Chipset with 48 pins
Analog input/output
Digital input/output((3.3v or 5v open drain mode)
I2C (3 module), UART, SPI
Supplies 3.3v and 5V

## Slide 19: IOIO Connections
PandaBoard ES
GPS
Magnetometer
Barometer
IMU
USB
3.3v
Battery
I2C clock
GND
I2C data
UART TX
UART RX

## Slide 20: Power Supply Requirements
Pandaboard ES 5v
IOIO Board 5 – 15v

## Slide 21: Battery
Polymer Lithium Ion Battery
Output: 3.7v
6000mAh (Long Battery Life)

## Slide 22: Step Up
Input: 1 – 4 v
Output: 5v or 3.3v
Max Current: 200 mA.

## Slide 23: Power Diagram
Polymer Lithium Ion Battery
3.7v, 6000mAh
Battery Charger
3.7v
3.7v
5v
5v
Step-up 1-4v to 5v
IOIO Board
PandaBoard ES
START HERE

## Slide 24: GPS-11058
Features:
Up to 20Hz update rate
-165dBm tracking sensitivity
3.5 second TTFF with AGPS
1 second hot start
2.5m accuracy
Multipath detection and suppression
Jamming detection and mitigation
67mW full power navigation
Works directly with active or passive antenna
Single 2.7-3.3V supply

## Slide 25: Antenna GPS Embedded SMA
Features:
Gain 26dB
VSWR <2.0
Voltage 3.3V +/- 0.5V
Current 12mA
Weight 18g

## Slide 26: Barometric Pressure Sensor - BMP085
Features:
Digital two wire (I²C, TWI, "Wire") interface
Wide barometric pressure range
Flexible supply voltage range (1.8V to 3.6V)
Ultra-low power consumption
Low noise measurements
Factory-calibrated
Includes temperature sensor
Low-profile with a small footprint

## Slide 27: Accelerometer & Gyro MPU-6050 IMU
Features:
I2C Interface
Input Voltage: 2.3 - 3.4V
Tri-Axis angular rate sensor (gyro) with full scale range ±250dpi to ±2000dpi
Tri-Axis accelerometer with a programmable full scale range of ±2g, ±4g, ±8g and ±16g
Digital Motion Processing™ (DMP™) engine offloads complex MotionFusion, sensor timing synchronization and gesture detection
Embedded algorithms for run-time bias and compass calibration. No user intervention required

## Slide 28: Triple Axis Magnetometer HMC5883L
Features:
Simple I2C interface
2.16-3.6VDC supply range
Low current draw
5 milli-gauss resolution

## Slide 29: Project Sponsor and Budget
U.S. Army Simulation and Training Technology Center: DARPA Cell
Item | Cost
Panda Board ES | $162
Panda Expansion Board | $250
5MP Camera + Adapter | $100
IOIO Board | $50
CY8CKIT PSOC | $100
Propeller Chip | $8
Step-Up | $6
GPS + Antenna | $62
Sensors | $80
Battery | $40
Shipping | $54
Total | $912
Total Allotted Budget: $2,000
Expenses to date: $912

## Slide 30: Work Allocation and Progress
Group Member | Project Task
Jonathan Pedrosa : BSPE | Primary: Sensor Board Software Interface Secondary: Augi Application Development, Tablet Housing
Adam Ilter : BSPE | Primary: Augi Application Development Secondary: Sensor Board Software
Phillip Lee : BSEE | Primary: Sensor Board Circuit Design and Manufacture Secondary: Sensor Integration with IOIO
Zulkafil Ahamed : BSEE | Primary: Sensor Integration with IOIO Secondary: Sensor Board Circuit Design
Application Sensor
Writing Software
25%
25%
Sensor Project
Board Total
50%
33%
February 22, 2013

## Slide 31: Questions?