## Slide 1: ABEC Autonomous Brilliantly Engineered Cooler
Marc Bianco
Andrew Boyles
Chris Echanique
Garrett Lee
Group #23

## Slide 2: Description
ABEC is, in essence, an autonomous cooler on wheels that addresses the common tailgating issues such as transporting heavy loads across long distances
It features a GPS tracking system to track the user’s smart phone and directs its path according to the user’s position
It uses motion sensors to handle object interferences by rerouting the station’s path
Its sustainable energy framework uses a solar panel to provide renewable energy to the vehicle

## Slide 3: Requirements
Shall sync with phone via Bluetooth
Shall track user through cell phone and onboard GPS
Shall follow user autonomously
Shall be able to switch to remote control via mobile application
Shall avoid obstacles as necessary
Shall recharge battery using solar panels or wall outlet

## Slide 4: Specifications
Carry up to 130 lbs.
Move at least 2 mph
Must detect obstacles at least 5 feet away
Max range of up to 50 feet from user
GPS tracking accurate to 15 feet
Operate for up to 2 hours on one charge

## Slide 5: Block Diagram

## Slide 6: Power Supply For Motors
Uses 30 watt mono-crystalline solar panel
12V sealed lead acid battery
9.5 Ah capacity
Responsible for supplying power to motors and motor controller

## Slide 7: Charge Regulation
Solarix MPPT 2010 charge controller
A charge controller will be used in the solar panel interface to charge the battery more efficiently
Monitors batteries voltage
Controls the charging process
Controls connection of loads connected to the load output

## Slide 8: Secondary Power Supply
9V lithium ion battery
350 mAh capacity
Supplies power to both microcontrollers and ultrasonic sensors
Total power consumption of components is roughly X

## Slide 9: Voltage Regulators
TLV70450 5V voltage regulator
Max Vin: 24V
Max Vout: 5V
TLV70433 3.3V regulator
Max Vin: 24V
Max Vout : 3.3V

## Slide 10: Chassis
A Fisher Price Power Wheels will be used as the chassis.
130 pound weight limit.
5 mph max speed
45”L x 33”W x 28”H

## Slide 11: Advantages of Power Wheels
Save a considerable amount of time by not having to build it ourselves.
Guarantee a sturdy chassis, which has a specified weight limit.
The Power Wheels came with motors, which are already mounted on the back wheels.
Comes with a 12 volt battery and charger.

## Slide 12: Motor Controller
 | AX1500 | SDC 2130 | RB-Dfr-207
Manufacturer | Roboteq | Roboteq | Infineon
Compatibility | Multiple MCUs | Multiple MCUs | Arduino
Operating Voltage | 12 to 40 Volts | 7 to 30 Volts | 4.8 - 35 Volts
Max Current | 2 x 30 Amps | 2 x 20 Amps | 2 x 15 Amps
R/C Control | Yes | Yes | No
Serial Control | Yes | Yes | Yes
Datasheet/User Manual | Both | Both | Datasheet
Additional Features | RoboRun Software | - | -
4.2”L x 4.2”W x 1.5”H

## Slide 13: Servo System
SPG805A Standard Rotation Servo
Can produce 1,375 oz-in. of torque operating at 4.8V
Arduino Servo Library used to generate servo control signals

## Slide 14: On board GPS
A GPS module will be used in conjunction with a digital compass to obtain the position of the vehicle
The positioning data will be transferred to the microcontroller and the user for tracking
30mm x 30mm
GPS Receiver

## Slide 15: GPS Receiver
 | LS20031 | VPN1513 | IT430
Manufacturer | Locosys | Parallax | Fastrax
Channels | 66 | 20 | 48
Time to First Fix | 35 seconds | 42 seconds | 35 seconds
Operating Voltage | 3 to 4.3 Volts | 4.5 to 12 Volts | 1.8 Volts
Interface | TTL Serial | Serial | I2C, SPI, UART
Position Acuracy | 3 m | 10 m | 2.5 m
Position Information | 5 times a second | 1 time per second | 1 time per second

## Slide 16: 3-Axis Digital Compass
15 Dollars
Operating voltage = 2.16 to 3.6 volts
Low Power Consumption: 100 μA
I2C Interface
Arduino example code available
HMC5883L
17.78mm x 17.78mm

## Slide 17: Obstacle/Gap Detection
Work Outdoors
Upper Range > 5 feet
Lower Range < 12in.
45 degree viewing angle

## Slide 18: Ultrasonic vs. Infrared
Infrared cheaper
Ultrasonic better in weather
Infrared not good in weather
Ultrasonic more expensive

## Slide 19: Ultrasonic Sensor
 | Maxbotix LV-EZ1 | Devantech SRF04
Price | $24.95 | $29.50
Range | 0-256in. | 1.18in.-118in.
Sensitivity | 0.25 in. | 1.18 in.
Current | 2mA | 30mA
Interface | Analog, PWM, Serial | PWM

## Slide 20: Bluetooth vs. Wifi
Bluetooth generally uses less power
Bluetooth is cheaper
Bluetooth is effective at short ranges
Range: Class 1(300 ft.) vs. Class 2(50-60 ft.)

## Slide 21: Bluetooth Receiver
 | RN-42 | WT12
Price | $16 | $25
Version | 2.1 | 2.1
Data Rate | 300Kbps-3Mbps | 2-3Mbps
Interface | UART,USB | UART,USB,PCM
Operating Voltage | 3.3 Volts | 3.2 – 3.4 Volts

## Slide 22: Microcontroller Comparison
 | MSP430G2553 | Atmega328
Price | Free | $2.88
GPIO | 16 | 16
Analog Inputs | 8 | 8
DC Current | 220uA | 40mA
Interface | 1(I2C/UART/SPI) | 2(SPI), 1(I2C/UART)

## Slide 23: User Tracking
Vision-Based Tracking
Ultrasonic Sensors
GPS Tracking
Ultrasonic Sensor
Object
Notes: Vision based tracking

## Slide 24: GPS-Based User Tracking
Easy to implement
Can be done using mobile application
  No external hardware needed
Additional features can be incorporated
  Remote control feature
No limit on distance between devices
Notes: Not as complex as vision based tracking

## Slide 25: Android Application
Java programming language
Abundance of APIs and open source code
No start up costs for SDK
GPS
RC
OFF
a b e c
1
2
3
x
y

## Slide 26: GPS-Based User Tracking
Bluetooth Connection
Notes: GPS chip on the vehicle

## Slide 27: Software Design
Distance and Bearing Equations

## Slide 28: Tracking Error
After Tracking
Vreal
Ureal
VGPS
UGPS
Distance Error (<6m)
Vreal
re
3 m
Ureal
re
3 m
VGPS
UGPS
Calculated Path
Expected Path

## Slide 29: Garmin GLO
Garmin GLO™ Specifications | 
Unit Size WxHxD | .70" x 1.65" x 3.04" (1.78 x 4.19 x 7.72 cm)
Weight | 2.12 oz (60.1 g)
Receiver technology | GPS+GLONASS
WAAS | Yes
Update Rate | 10 Hz
Accuracy | 3 meters (9.54 feet)
Battery Capacity | 1100 mAh
Battery Life | 12 hours
Hot Start Time | 3-5s
Warm Start Time | 35s
Cold Start Time | 60s

## Slide 30: Division of Labor
Power System/Steering Servo/PCB
  Marc Bianco, EE
Motor Control/Chassis/PCB
  Andrew Boyles, EE
Obstacle Avoidance/Integration/PCB
  Garrett Lee, EE
Mobile Application/GPS Tracking
  Chris Echanique, CE

## Slide 31
Part | Projected Cost | Actual Cost
Motor Controller | $350 | $300
Solar Panels | $500 | $179
LED's | $10 | $9.65
Batteries | $75 | $50.13
Charge Controller | $200 | $92.5
Bluetooth | $20 | $16
Power Wheels | $250 | $360.49
Garmin Glo | $100 | $100
GPS & Compass | $100 | $80
Ultrasonic Sensors (3) | $75 | $75
ATMega328P | $5 | $2.88
Servo | $200 | $116
PCB | $66 | TBD
Total | $1951.00 | $1381.65
Budget

## Slide 32: Progress
Chart: 
| Testing | Integration | Research | Parts Acquired
Series 1 | 0.35 | 0.25 | 0.9 | 0.95
Series 2 | 0.65 | 0.75 | 0.1 | 0.05

## Slide 33: Milestones

## Slide 34: Current Issues

## Slide 35: Questions?