## Slide 1: ABEC Autonomous Brilliantly Engineered Cooler
Marc Bianco
Andrew Boyles
Chris Echanique
Garrett Lee
Group #23
Sponsored By

## Slide 2: Description
ABEC is, in essence, an autonomous cooler on wheels that addresses the common tailgating issues such as transporting heavy loads across long distances
It features a GPS tracking system to track the user’s smart phone and directs its path according to the user’s position
It uses motion sensors to handle object interferences by rerouting the station’s path
Its sustainable energy framework uses a solar panel to provide renewable energy to the vehicle

## Slide 3: Requirements
Shall sync with phone via Bluetooth
Shall track user through cell phone and onboard GPS
Shall follow user autonomously
Shall be able to switch to remote control via mobile application
Shall avoid obstacles as necessary
Shall recharge battery using solar panels or wall outlet

## Slide 4: Specifications
Carry up to 130 lbs.
Move at least 2 mph
Must detect obstacles at least 3 feet away
Max range of up to 50 feet from user
GPS tracking accurate to 15 feet
Operate for up to 6 hours on one charge

## Slide 5: Block Diagram

## Slide 6: Power Supply For Motors
Uses 30 watt mono-crystalline solar panel
12V sealed lead acid battery
9.5 Ah capacity
Responsible for supplying power to motors and motor controller

## Slide 7: Charge Regulation
Solarix MPPT 2010 charge controller
A charge controller will be used in the solar panel interface to charge the battery more efficiently
Monitors batteries voltage
Controls the charging process
Controls connection of loads connected to the load output

## Slide 8: Voltage Regulators
LM7805 5V regulator
Max Vin: 15V
Max Vout: 5V
LD117V33 3.3V regulator
Max Vin: 15V
Max Vout : 3.3V

## Slide 9: Chassis
A Fisher Price Power Wheels will be used as the chassis.
130 pound weight limit.
5 mph max speed
45”L x 33”W x 28”H

## Slide 10: Advantages of Power Wheels
Save a considerable amount of time by not having to build it ourselves.
Guarantee a sturdy chassis, which has a specified weight limit.
The Power Wheels came with motors, which are already mounted on the back wheels.
Comes with a 12 volt battery and charger.

## Slide 11: Motor Controller
 | AX1500 | SDC 2130 | RB-Dfr-207
Manufacturer | Roboteq | Roboteq | Infineon
Operating Voltage | 12 to 40 Volts | 7 to 30 Volts | 4.8 - 35 Volts
Max Current | 2 x 30 Amps | 2 x 20 Amps | 2 x 15 Amps
R/C Control | Yes | Yes | No
Serial Control | Yes | Yes | Yes
Datasheet/User Manual | Both | Both | Datasheet
Additional Features | RoboRun Software | - | -
4.2”L x 4.2”W x 1.5”H

## Slide 12: Servo System
SPG805A Standard Rotation Servo
Can produce 1,375 oz-in. of torque operating at 5V
Arduino Servo Library used to generate servo control signals

## Slide 13: Servo Issues and Solution
Problems with servo rotating when it hits resistance
When servo cannot reach its limit it spins freely in the other direction
Solution was to rotate the wheels at different speeds
Motor controller allows each motor to be controlled independently

## Slide 14: On board GPS
A GPS module will be used in conjunction with a digital compass to obtain the position of the vehicle
The positioning data will be transferred to the microcontroller and the user for tracking
30mm x 30mm
GPS Receiver

## Slide 15: GPS Receiver
 | LS20031 | VPN1513 | IT430
Manufacturer | Locosys | Parallax | Fastrax
Channels | 66 | 20 | 48
Time to First Fix | 35 seconds | 42 seconds | 35 seconds
Operating Voltage | 3 to 4.3 Volts | 4.5 to 12 Volts | 1.8 Volts
Interface | TTL Serial | Serial | I2C, SPI, UART
Position Acuracy | 3 m | 10 m | 2.5 m
Position Information | 5 times a second | 1 time per second | 1 time per second

## Slide 16: 3-Axis Digital Compass
15 Dollars
Operating voltage = 2.16 to 3.6 volts
Low Power Consumption: 100 μA
I2C Serial Interface
Arduino example code available
HMC5883L
17.78mm x 17.78mm

## Slide 17: Obstacle Detection
Work Outdoors
45 degree viewing angle
Front Range at least 5 feet

## Slide 18: Ultrasonic Sensor
 | LV-EZ1 | SRF04
Manufacturer | Maxbotix | Devantech
Price | $24.95 | $29.50
Range | 0-256in. | 1.18in.-118in.
Sensitivity | 0.25 in. | 1.18 in.
Current | 2mA | 30mA
Interface | Analog, PWM, Serial | PWM

## Slide 19: Bluetooth Receiver
Bluetooth generally uses less power
Bluetooth is cheaper
Bluetooth is effective at short ranges
Range: Class 1(300 ft.) vs. Class 2(50-60 ft.)

## Slide 20: Bluetooth Receiver
 | RN-42 | WT12
Manufacturer | Roving Networks | Bluegiga
Price | $16 | $25
Version | 2.1 | 2.1
Data Rate | 300Kbps-3Mbps | 2-3Mbps
Interface | UART,USB | UART,USB,PCM
Operating Voltage | 3.3 Volts | 3.2 – 3.4 Volts

## Slide 21: Microcontroller Comparison
 | MSP430G2553 | Atmega328
Manufacturer | TI | Atmel
Price | Free | $2.88
Memory | 16k | 32k
GPIO | 16 | 28
Analog Inputs | 8 | 8
DC Current | 220uA | 40mA
Interface | 1(I2C/UART/SPI) | 2(SPI), 1(I2C/UART)
Operating Voltage | 1.8 – 3.6V | 1.8 – 5.5V

## Slide 22: Arduino Uno
ATmega328P-PU microcontroller was chosen
Used Arduino Uno for programming and testing the microcontroller and individual subsystems
Utilizes C based programming language

## Slide 23: User Tracking
Infrared Sensors
Vision-Based Tracking
GPS Tracking
Notes: Vision based tracking

## Slide 24: GPS-Based User Tracking
Easy to implement
Can be done using mobile application
Additional features can be incorporated
  Remote control feature
No limit on distance between devices
Notes: Not as complex as vision based tracking

## Slide 25: GPS-Based User Tracking
Bluetooth Connection
Notes: GPS chip on the vehicle

## Slide 26: Android Application
Java programming language
Abundance of APIs and open source code
No start up costs for SDK
CONNECT BLUETOOTH
a b e c
REVERSE
FORWARD

## Slide 27: Software Design
Distance and Bearing Equations

## Slide 28: Tracking Error
After Tracking
Vreal
Ureal
VGPS
UGPS
Distance Error (<6m)
Vreal
re
3 m
Ureal
re
3 m
VGPS
UGPS
Calculated Path
Expected Path

## Slide 29: Garmin GLO
Garmin GLO™ Specifications | 
Unit Size WxHxD | .70" x 1.65" x 3.04" (1.78 x 4.19 x 7.72 cm)
Weight | 2.12 oz (60.1 g)
Receiver technology | GPS+GLONASS
WAAS | Yes
Update Rate | 10 Hz
Accuracy | 3 meters (9.54 feet)
Battery Capacity | 1100 mAh
Battery Life | 12 hours
Hot Start Time | 3-5s
Warm Start Time | 35s
Cold Start Time | 60s

## Slide 30: PCB
Created using Eagle PCB CAD software
Manufactured by Advanced Circuits
3” x 3” two layer board

## Slide 31: Major Issues
Steering the vehicle with the SPG805 gearbox
Bluetooth on PCB could not send and receive data through the pins it was traced to
Integrating GPS tracking and remote control on one mobile application
GPS accuracy

## Slide 32: Division of Labor
Power System/Steering Servo/PCB
  Marc Bianco, EE
Motor Control/Chassis/PCB
  Andrew Boyles, EE
Obstacle Avoidance/Integration/PCB
  Garrett Lee, EE
Mobile Application/GPS Tracking
  Chris Echanique, CE

## Slide 33
Part | Projected Cost | Actual Cost
Motor Controller | $350 | $300
Solar Panels | $500 | $179
LED's | $10 | $9.65
Batteries | $75 | $50.13
Charge Controller | $200 | $92.5
Bluetooth | $20 | $16
Power Wheels | $250 | $360.49
Garmin Glo | $100 | $100
GPS & Compass | $100 | $80
Ultrasonic Sensors (3) | $75 | $75
ATMega328P | $5 | $2.88
Servo | $200 | $116
PCB | $66 | $105
Total | $1951.00 | $1486.65
Budget

## Slide 34: Questions?