## Slide 1: K.E.E.S. Keyless Electronic Entry System
Group 17
Chris Condella, EE
Jason Wagner, CpE
Joshua Baxter, CpE
Samuel Demole, CpE
Notes: add picture ?

## Slide 2: Motivation
Home Automation is a trending technology in the commercial market
Improve on home monitoring and surveillance systems
Opportunity to learn and implement multiple hardware and software technologies

## Slide 3: Goals and Objectives
Remote door access and guest management system
Remote control via web interface
Mobile app for real time communications
Enable multiple methods of entry to home
Allow specific guests access to home

## Slide 4: Specs & Requirements
KEES camera module will display a live video feed with no less than 5s delay @ 30 FPS
KEES system will allow the user to save an image of the guest and add to the Face database
KEES system will allow for notifications via Text to be sent with no more than 5s delay
KEES service will listen for a request from the server when the doorbell is pressed and open the App with no more than 10s delay
KEES face recognition will recognize a guest within 3s
KEES RFID module will unlock door instantly upon scanning a valid RF tag from within 3in away
KEES piezoelectric sensor will recognize a custom knock within 3s
KEES system voltage and current will require 5V DC @ ~5A
KEES battery backup will last up to approx. 1-2hrs

## Slide 5: Block Diagram
MCU
SoC
Knock Detector
RFID Reader
Electric Strike
Mic/
Speaker
Browser/App
Server
Camera
Power Supply
Notes: Overview

## Slide 6: State Diagram
Active
Locked
Waiting for Motion
Listen for Unlock request from WebApp
Attempt to Recognize Face
Listen for Door Bell
Listen for Unlock
Request from App
Listen for RFID /
Detect Knock Pattern
Door Unlocked
Motion Detected
Door Bell
Pressed
Face
Recognized
Unlock
via App
Valid
Knock Pattern
Valid
RFID
Unlock
via WebApp
Face not
Recognized &
10 sec Timeout
20 sec
Timeout
6 sec
Timeout

## Slide 7: mcu
MCU
SoC
Knock Detector
RFID Reader
Electric Strike
Mic/
Speaker
Browser/App
Server
Camera
Power Supply
Notes: Overview

## Slide 8: ATMega328 vs Msp430
 | ATMega328 | MSP430F2XX
CPU | 20MHz | 16 MHz
Flash Size | 16 KB | 1–120 KB
GPIO | 28 | 10-48
Power Req. | 3.3-5 V | 1.8-3.6 V

## Slide 9: Electric strike
MCU
SoC
Knock Detector
RFID Reader
Electric Strike
Mic/
Speaker
Browser/App
Server
Camera
Power Supply
Notes: Overview

## Slide 10
Normally Closed (NC)
  Strike is locked when no electric current is applied
  Fail Secure
Normally Open (NO)
  Strike is locked when electric current is applied
  Fail Safe
Types of electric strikes

## Slide 11
 | Lee Electric | Rutherford | Lee Electric
Voltage | 3-6 VDC | 12 VDC | 12VDC
Ohms | ~ 2.7 | 3.5 | 4
Current | ~1.8 A | ~3 A | ~2.5 A
Price | $40 | $50 | ~$33
Electric strike

## Slide 12
LEE Electric Strike

## Slide 13: Rfid module
MCU
SoC
Knock Detector
RFID Reader
Electric Strike
Mic/
Speaker
Browser/App
Server
Camera
Power Supply
Notes: Overview

## Slide 14
ID-Innovations
ID-12LA
RFID MODULE comparison
 | Parallax | ID-12LA
Range | 1 ¾” - 3” inches | 3”- 5” inches
Frequency | 125 kHz | 125 kHz
Power Req. | +5 VDC | +2.8 VDC to +5 VDC
Parallax
#28140

## Slide 15: Rfid reader
Purpose:
Allow Entry through the door
Put system into Programming mode using MASTER key
Add/Remove RFID cards
EM4001 64-bit RFID card compatible
Parameter | ID-12LA
Frequency | 125 kHz nominal
Card Format | EM 4001 or compatible
Read Range ID12 | Up to 12cm
Encoding | Manchester 64-bit, modulus 64
Power Requirement | +2.8 VDC thru +5 VDC @ 35mA ID-12LA, 45mA ID-20LA
I/O Lines | 11
Price | $29.95

## Slide 16
Rfid state diagram

## Slide 17: Knock detector
MCU
SoC
Knock Detector
RFID Reader
Electric Strike
Mic/
Speaker
Browser/App
Server
Camera
Power Supply
Notes: Overview

## Slide 18: Piezo electric sensor
Purpose:
When Piezo material is deformed a charge is sent over terminals
Detect secret knock and allow entry through the door
Add/Remove Secret knocks

## Slide 19
Waiting for Knock
Programming State
Storing Knock Parameter
Update Secret Knock
Storing Knock Parameter
Validating Knock
Unlock Door
Knock detection state diag
Master Card
Swiped
Knock
Detected
Knock
Detected

## Slide 20: soc
MCU
SoC
Knock Detector
RFID Reader
Electric Strike
Mic/
Speaker
Browser/App
Server
Camera
Power Supply
Notes: Overview

## Slide 21: Beaglebone vs raspberry pi
 | BeagleBone Black | Raspberry Pi
Base Price | $45 | $35
Processor | 1GHz TI Sitara AM3359 ARM Cortex A8 | 700 MHz ARM1176JZFS
RAM | 512 MB DDR3L @ 400 MHz | 512 MB SDRAM @ 400 MHz
Storage | 2 GB on-board eMMC, MicroSD | SD
GPIO Capability | 65 Pins | 8 Pins
Peripherals | 1 USB Host, 1 Mini-USB Client, 1 10/100 Mbps Ethernet | 2 USB Hosts, 1 Micro-USB Power, 1 10/100 Mbps Ethernet, RPi camera connector

## Slide 22: MCU – soc communication
Implementing I2C between ATMega and Pi
Character scripting protocol is sent over I2C bus for updating and control

## Slide 23: mic/speaker
MCU
SoC
Knock Detector
RFID Reader
Electric Strike
Mic/
Speaker
Browser/App
Server
Camera
Power Supply
Notes: Overview

## Slide 24
Sound Input/Output
 | USB Sound Card | Microphone | Speaker
Company | Creative | HDE | Veho
Model | Sound Blaster Play! | Mini | VSS-001 360 M1
Features | Stereo 1x Speaker Out (3.5mm) 1x Mic in (3.55mm) 16-bit / 48kHz | Flexible 3.5mm Jack Sensitivity: -54±3dB Freq. Range: 100-5KHz | USB Powered 3.5mm Jack 2.4W Output Size: 50x50mm Weight: 4oz

## Slide 25: Camera
MCU
SoC
Knock Detector
RFID Reader
Electric Strike
Mic/
Speaker
Browser/App
Server
Camera
Power Supply
Notes: Overview

## Slide 26: Raspberry Pi Camera
Supports wide range of video resolutions, up to 1080p
Connects via CSI on Raspberry Pi
Higher frame rate due to reduced latency: uses small amount of CPU
Webcams have higher latency

## Slide 27: IMG Processing & streaming Features
Detect faces
Recognize specified faces
Save snapshot of a face in 320x240
Provide JPEG video stream viewable over the internet

## Slide 28: IMG PROCESSING & Streaming
Raspistill
  Driver captures frames from Raspberry Pi camera
  Source code available
OpenCV 2.3
  Face Recognition and Detection API
  Optimized functions
  Numerous image processing capabilities
MJPEG Streamer
  Capture camera frames as .jpeg
  Sends frames to a specified IP addresss
CMAKE

## Slide 29: Img Processing & Streaming

## Slide 30: Img Processing Class Diagram

## Slide 31: Server & App
MCU
SoC
Knock Detector
RFID Reader
Electric Strike
Mic/
Speaker
Browser/App
Server
Camera
Power Supply
Notes: Overview

## Slide 32: WebApp Features
Lock Status
Unlock Door
View Live Stream
View History
Snapshot/Record
Add/Manage Guests
Manage RFID
Manage Knock Patterns

## Slide 33: WebApp (Frontend UI)
Bootstrap 3.0 framework
  Responsive design
  Numerous HTML/CSS templates
  Cross-platform support
jQuery
  Most popular JS library
  Used by 65% of top 10,000 visited sites
HTML
CSS

## Slide 34: WebApp Responsive design

## Slide 35: WebApp UI

## Slide 36: WebApp (Backend)
Node.js - Webserver
  express
  jade
  Mongoose
NPM - Node.js Package Manager
MongoDB - NoSQL Database
  Admin Credentials
  Event History
  Guest Information
Git - Version Control
Twilio - Notification Service
MJPEG-Streamer
Python Scripts
Lock Control
RFID/Knock Master Control
Dynamic DNS (noip.com)

## Slide 37: WebApp - Node.js
Single threaded, event-driven, non-blocking
High scalability
Lightweight
Pure JavaScript (No Apache/XML/PHP/MySQL)
Google V8 JavaScript Engine
Used by PayPal, Microsoft, LinkedIn, Yahoo!

## Slide 38: WebApp UML

## Slide 39: Android application
Service initialized upon door bell pressed
Provide remote communication with Guest
Similar to iOS FaceTime call
2-Way Audio, 1-Way Video
Door can be unlocked for Guest
Support for Android 4.0 and above
AudioRecord, Movie,
NotificationListenerService APIs

## Slide 40: App / Door Bell Integration
Listener Service on RPi
(Python Script)
Listener on Android Device
App Initialized on Request
Door Bell Pressed
Request Sent to
Android Device
User can
Accept / Ignore
User Accepts Communication with Guest
1. End Communication
2. Send Request to Unlock Door
Forward Unlock
Request to Server
Door Unlocked
Serial Command Sent to MCU

## Slide 41: Power
MCU
SoC
Knock Detector
RFID Reader
Electric Strike
Mic/
Speaker
Browser/App
Server
Camera
Power Supply
Notes: Overview

## Slide 42: Power Requirements
Component | Voltage Required | DC current Draw
Strike | 3-6 VDC | 1.1-2.2 A
RFID | 4.6-5.4 VDC | 30 mA
Atmega328 | 3.3/5 VDC | Per I/O pin ~40mA
 |  | VCC/GND pins ~200mA
Raspberry Pi | 5 VDC | 0.7 – 1 A
Charging Circuit | ~15 VDC | 0.2 - 1A
*The electric strike resistance ~ 2.7 Ω, using V=IR @ 5V, I = ~1.8 A
The entire system will need to be powered with 5VDC @ ~ 4 A or more to be safe. An AC/DC converter will be used to satisfy the 15V charging circuit and 5V regulator to step down the voltage.

## Slide 43: Power Block Diagram
Diode OR
15 V AC/DC Adapter
Battery Charger
Battery Pack
AC Power
5V Regulator
System

## Slide 44: Diode OR-ing
When the 15 VDC source is ON it serves as the main power source for the load.
When the 12 VDC source
is OFF the back up 7.2 VDC source becomes the main power source for the load.

## Slide 45: Device = LM5023MM-NOPB Topology = Flyback Vin = 100 – 240 VAC Vout = 15VDC Iout= 5A
Designed with TI Webench
AC/DC Converter

## Slide 46: LM1084 5A Low Dropout Positive Regulator
5 VDC regulated
Max dropout of 1.5V
6.5V ≤ Vin ≤ 20V
5A of load current
Current Limiting (8A)
Thermal Protection
Vref ~ 1.25V
*Images from LM1084 pdf

## Slide 47: Battery back up
A battery back up will ensure the system will stay powered and active even if main power is lost.
Ideally battery would have an infinite amount of capacity for infinite back up.
1-2 hour back up should suffice for our project.
We will consider certain battery types and properties such as size, price, availability and convenience etc.

## Slide 48: Battery types: rechargeable

## Slide 49: Nimh Rechargeable AA Batteries
* From Energizer NiMH Handbook and App Manual PDF
Charge Time (fully discharged)
(Batt mAh Capacity * 120%)/mA Charge Rate
= Hrs needed to charge
mA Charge Rate | Hrs of Charge
200 | ~43
400 | ~22
500 | ~17
600 | ~14
700 | ~12
900 | ~10
1000 | ~9

## Slide 50: Float Charging circuit
1.2 V per cell
Approx. 2000-2500mA-h per battery
Assuming ~2300mA-h x6 gives 7.2VDC with 13.8A-h total
# of NiMH Cells | Volts Required | R3 Ω | VR1 Ω | R2 Ω | R4 Ω | R5 Ω
6 | 15 | 1.1k | 500 | 240 | 1.2k | 2.7k
Max Current | 200mA | 400mA | 500mA | 600mA
R1 | 1.2 Ω | 0.6 Ω | 0.5 Ω | 0.4 Ω
RCL | 3.3 Ω | 1.5 Ω | 1.2 Ω | 1 Ω

## Slide 51: PCB

## Slide 52
Model

## Slide 53: Prototyping

## Slide 54: Budget
Item | Cost
AC/DC Adapter | $20
Raspberry Pi | $35
ATMega328 | $20
WiFi Module | $15
Electric Strike | $30
Pi Camera Module | $30
RFID Module | $30
PCB | ~ $50
Battery Backup | ~ $20
Piezo Element | $5
USB Sound Card | $15
Speaker & Microphone | $12
Item | Cost
Prototyping Materials | ~$30
Various Electronic Parts | ~$20
NiMH Batteries | $18
Total | ~$350

## Slide 55: Work Distribution
 | Chris | Jason | Josh | Sam
ATMega328 | X | X |  | 
Knock Pattern | X | X |  | 
Face Recognition |  |  | X | 
RPi Software |  |  | X | X
Android App |  |  | X | X
Server / UI |  |  |  | X
Power | X |  |  | 
RFID |  | X |  | 

## Slide 56: Progress
Chart: 
| Research | Design | Prototype | Testing | Total
Completed | 95 | 55 | 20 | 5 | 43.75

## Slide 57: Issues
Piezo Placement/Sensitivity
Face Detection and Face Recognition
Integration
Battery Backup

## Slide 58: Questions?
Notes: add picture ?