## Slide 1: K.E.E.S. Keyless Electronic Entry System
Group 17
Chris Condella, EE
Jason Wagner, CpE
Joshua Baxter, CpE
Samuel Demole, CpE
Notes: add picture ?

## Slide 2: Motivation
Home Automation/Access Control is a trending technology in the commercial market
Improve on home monitoring and surveillance systems
Opportunity to learn and implement multiple hardware and software technologies

## Slide 3: Goals and Objectives
Remote door access and guest management system
Remote control via web interface
Enable multiple methods of entry to home
Allow specific guests access to home

## Slide 4: Specs & Requirements
KEES camera module will display a live video feed with no more than 5s delay @ 2fps
KEES system will allow the user to add a guest to the Face database
KEES system will allow the user to remove a person in the Face database
KEES face recognition will recognize a guest within 5s
KEES RFID module will unlock door instantly upon scanning a valid RF tag from within 3in away
KEES piezoelectric sensor will recognize a custom knock within 3s
KEES system voltage and current will require 5 VDC @ ~5A
KEES battery backup will last up to approx. 8 hrs

## Slide 5: Block Diagram
MCU
SoC
Knock Detector
RFID Reader
Electric Strike
Browser/App
Server
Camera
Power Supply
Notes: Overview

## Slide 6: State Diagram
Active
Locked
Waiting for Face
Listen for Unlock request from WebApp
Attempt to Recognize Face
Listen for RFID /
Detect Knock Pattern
Door Unlocked
Face
Recognized
Valid
Knock Pattern
Valid
RFID
Unlock
via WebApp
Face not
Recognized &
2.5 sec Timeout
10 sec
Timeout
2 sec
Timeout

## Slide 7: mcu
MCU
SoC
Knock Detector
RFID Reader
Electric Strike
Browser/App
Server
Camera
Power Supply
Notes: Overview

## Slide 8: ATMega328 vs Msp430
 | ATMega328 | MSP430F2XX
CPU | 20MHz | 16 MHz
Flash Size | 16 KB | 1–120 KB
GPIO | 28 | 10-48
Power Req. | 3.3-5 V | 1.8-3.6 V

## Slide 9: Electric strike
MCU
SoC
Knock Detector
RFID Reader
Electric Strike
Browser/App
Server
Camera
Power Supply
Notes: Overview

## Slide 10
Normally Closed (NC)
  Strike is locked when no electric current is applied
  Fail Secure
Normally Open (NO)
  Strike is locked when electric current is applied
  Fail Safe
Types of electric strikes

## Slide 11
 | Lee Electric | Rutherford | Lee Electric
Voltage | 3-6 VDC | 12 VDC | 12VDC
Ohms | ~ 2.7 | 3.5 | 4
Current | ~1.8 A | ~3 A | ~2.5 A
Price | $40 | $50 | ~$33
Electric strike

## Slide 12
LEE Electric Strike

## Slide 13: Rfid module
MCU
SoC
Knock Detector
RFID Reader
Electric Strike
Browser/App
Server
Camera
Power Supply
Notes: Overview

## Slide 14
ID-Innovations
ID-12LA
RFID MODULE
 | ID-12LA
Range | 3”- 5” inches
Frequency | 125 kHz
Power Req. | +2.8 VDC to +5 VDC
Card Format | EM 4001 or compatible
Price | $29.95
Purpose:
Allow Entry through the door
Put system into Programming mode using MASTER key
Add/Remove RFID cards
EM4001 64-bit RFID card compatible

## Slide 15
Rfid state diagram

## Slide 16: Knock detector
MCU
SoC
Knock Detector
RFID Reader
Electric Strike
Browser/App
Server
Camera
Power Supply
Notes: Overview

## Slide 17: Piezo electric sensor
Purpose:
When Piezo material is deformed a charge is sent over terminals
Detect secret knock and allow entry through the door
Add/Remove Secret knocks

## Slide 18
Waiting for Knock
Programming State
Storing Knock Parameter
Update Secret Knock
Storing Knock Parameter
Validating Knock
Unlock Door
Knock detection state diag
Master Card
Swiped
Knock
Detected
Knock
Detected

## Slide 19: soc
MCU
SoC
Knock Detector
RFID Reader
Electric Strike
Browser/App
Server
Camera
Power Supply
Notes: Overview

## Slide 20: Beaglebone vs raspberry pi
 | BeagleBone Black | Raspberry Pi
Base Price | $45 | $35
Processor | 1GHz TI Sitara AM3359 ARM Cortex A8 | 700 MHz ARM1176JZFS
RAM | 512 MB DDR3L @ 400 MHz | 512 MB SDRAM @ 400 MHz
Storage | 2 GB on-board eMMC, MicroSD | SD
GPIO Capability | 65 Pins | 8 Pins
Peripherals | 1 USB Host, 1 Mini-USB Client, 1 10/100 Mbps Ethernet | 2 USB Hosts, 1 Micro-USB Power, 1 10/100 Mbps Ethernet, RPi camera connector

## Slide 21: MCU – soc communication
Implementing I2C between ATMega and Pi
State scripting protocol is sent over I2C bus for updating and control

## Slide 22: Camera
MCU
SoC
Knock Detector
RFID Reader
Electric Strike
Browser/App
Server
Camera
Power Supply
Notes: Overview

## Slide 23: Raspberry Pi Camera
Connects via CSI on Raspberry Pi
Higher frame rate due to reduced latency: uses small amount of CPU
Webcams have higher latency
Picamera 1.3
  Python SDK captures frames from Raspberry Pi camera

## Slide 24: IMG Processing & streaming Features
Detect faces
Learn a face within 10 seconds
Recognize specified faces within 5 seconds
Categorize non-guests as ‘unrecognized’
Save snapshot of a frame in 320x240
Provide JPEG video stream viewable over the internet

## Slide 25: IMG PROCESSING & Streaming
OpenCV 2.4.6
  Face Recognition and Detection API
    Local Binary Patterns Histogram
  Optimized preprocessing functions
    Canny and Binary Histogram
  Numerous image processing capabilities
MJPEG Streamer
  Capture camera frames as .jpeg
  Very little CPU usage: only 1%
  Sends frames to a specified IP addresss

## Slide 26: Img Processing & Streaming

## Slide 27: Img Processing Class Diagram

## Slide 28: ServeR / WEBAPP
MCU
SoC
Knock Detector
RFID Reader
Electric Strike
Browser/App
Server
Camera
Power Supply
Notes: Overview

## Slide 29: WebApp Features
Lock Status
Unlock Door
View Live Stream
View History
Add/Remove Guests
System Master Mode

## Slide 30: WebApp (Frontend UI)
Bootstrap 3.0 framework
  Responsive design
  Numerous HTML/CSS templates
  Cross-platform support
jQuery
  Most popular JS library
  Used by 65% of top 10,000 visited sites
HTML
CSS

## Slide 31: WebApp UI

## Slide 32: WebApp (Backend)
Node.js - Webserver
  Express
  jade
NPM - Node.js Package Manager
Logging
  Event History
  Guest Information
Git - Version Control
MJPEG-Streamer
Python Scripts
Listener
Send Command
Add Guest
Dynamic DNS (noip.com)

## Slide 33: WebApp - Node.js
Single threaded, event-driven, non-blocking
High scalability
Lightweight
Pure JavaScript (No Apache/XML/PHP/MySQL)
Google V8 JavaScript Engine
Used by PayPal, Microsoft, LinkedIn, Yahoo!

## Slide 34: WebApp UML

## Slide 35: Power
MCU
SoC
Knock Detector
RFID Reader
Electric Strike
Browser/App
Server
Camera
Power Supply
Notes: Overview

## Slide 36: Operating Characteristics
Component | Voltage Required | DC current Draw
Strike | 3 VDC min | 1.1-2.2 A
RFID | 4.6-5.4 VDC | 30 mA
Atmega328 | 3.3/5 VDC | Per I/O pin ~40mA
 |  | VCC/GND pins ~200mA
Raspberry Pi | 5 VDC | 0.7 – 1 A
Charging Circuit | ~15 VDC | 0.2 - 1A
*The electric strike resistance ~ 2.7 Ω, using V=IR @ 5V, I = ~1.8 A
The entire system will need to be powered with 5VDC @ ~ 4 A or more to be safe. An AC/DC converter will be used to satisfy the 15V charging circuit and 5V regulator to step down the voltage.

## Slide 37: Power Block Diagram
Diode OR
15 V AC/DC Adapter
Battery Charger
Battery Pack
AC Power
5V Regulator
Embedded
System
Rasp Pi
PNP
5V Regulator
Diode OR
Battery Pack
Strike

## Slide 38: Diode OR-ing
When the 15 VDC source is ON it serves as the main power source for the load.
When the 15 VDC source
is OFF the back up 7.2 VDC source becomes the main power source for the load.

## Slide 39
AC Voltage ON
AC Voltage OFF
Or-ing Logic

## Slide 40: Device = LM5023MM-NOPB Topology = Flyback Vin = 100 – 240 VAC Vout = 15VDC Iout= 5A
Designed with TI Webench
AC/DC Converter

## Slide 41: 15 VDC, 8.0 a S AC/DC Power Supply
Part Number: PST-AC1580
Output: 15 Volts DC, 8.0 amps
Output Power: 120 Watts max
Input Voltage: 100-240 VAC, 50-60 Hz
Input Frequency: 50-60 Hz
No-load overhead: 200mW
Excellent Efficiency: 80% at half load
78% at full load
Temperature: 0° to 40° C Operating
Size: Approx(1.5 x 2.5 x 6.7 inch)
Weight: 18 oz., 500 gm, 1.1 lbs
Output connector: 6.3 OD x 3.0 ID mm x 12.5mm
Output Polarity: Center Positive
AC plug: Removable IEC connector
*Courtesy of PowerStream.com

## Slide 42: LM1084 5A Low Dropout Positive Regulator
5 VDC regulated
Max dropout of 1.5V
6.5V ≤ Vin ≤ 20V
5A of load current
Current Limiting (8A)
Thermal Protection
Vref ~ 1.25V
*Images from LM1084 pdf

## Slide 43: Battery back up
A battery back up will ensure the embedded system will stay powered and active even if main power is lost.
8-10 hour back up should suffice for our project.
We will consider certain battery types and properties such as size, price, availability and convenience etc.

## Slide 44: Battery types: rechargeable

## Slide 45: Nimh Rechargeable AA Batteries
* From Energizer NiMH Handbook and App Manual PDF
Charge Time (fully discharged)
(Batt mAh Capacity * 120%)/mA Charge Rate
= Hrs needed to charge
mA Charge Rate | Hrs of Charge
200 | ~43
400 | ~22
500 | ~17
600 | ~14
700 | ~12
900 | ~10
1000 | ~9

## Slide 46: Battery Charging circuit
1.2 V per cell
Approx. 2000-2500 mA-h per battery
2300mA-h x6 gives 7.2VDC with 2.3 A-h
# of NiMH Cells | Volts Required | R1 Ω | R2 Ω | TM1 Ω
6 | ~15 | 1.2 | 1k | 0 - 10
Max Current | 25mA | 50mA | 100mA | 200mA
R1 | 1.2 Ω | 1.2 Ω | 1.2 Ω | 1.2 Ω
TM1 | 4.0 Ω | 3.3 Ω | 1.5 Ω | 1 Ω

## Slide 47
PCB
Schematic

## Slide 49
Model

## Slide 50: Prototyping

## Slide 52: Budget
Item | Cost
AC/DC Adapter | $20
Raspberry Pi | $35
ATMega328 | $20
WiFi Module | $15
Electric Strike | $30
Pi Camera Module | $30
RFID Module | $30
PCB | ~ $50
Battery Backup | ~ $20
Piezo Element | $5
Item | Cost
Prototyping Materials | ~$30
Various Electronic Parts | ~$20
NiMH Batteries | $18
Total | ~$323

## Slide 53: Work Distribution
 | Chris | Jason | Josh | Sam
ATMega328 | X | X |  | 
Knock Pattern | X | X |  | 
Face Recognition |  |  | X | 
RPi Scripts |  |  | X | X
Server / UI |  |  |  | X
Power | X |  |  | 
RFID |  | X |  | 

## Slide 54: Issues
Piezo Placement/Sensitivity
Face Detection
Camera Frames
HW/SW Integration
Electric Strike Current Draw

## Slide 55: Questions?
Notes: add picture ?