## Slide 1: Charge Spot
Group 20
Ryan Johnson
Theophilus Essandoh
Emelio Watson

## Slide 2: Introduction
Increased push for wireless technology
Autonomous Charging System for residential use
Resonant frequency charging system

## Slide 3: Goals and Objectives
Design and implement a wireless charging system
No physical connectivity between the car and system
User friendly with very little user interaction
System Shuts down automatically when battery is fully charged
A fail safe manual over ride shutdown switch
Receiving coil must be properly concealed and not interfere with the normal safe operation of the vehicle
Visual guidance system for proper alignment

## Slide 4: Specifications
Car detected 15 Ft minimum from control panel
Proximity sensor range 5 Ft. minimum
Copper coils less than 2 lbs. each
Measure and display battery temperature to within + 1°C accuracy
Charge current greater than 3 Amps
Battery 12V 18AH
Oscillator resonant frequency > 500 kHz
Battery fully charged within 8Hrs
Efficiency > 40%

## Slide 5: Why We Chose Magnetic Resonance
Inductive Coupling
Requires more power
Coils must be properly aligned for maximum efficiency
Shorter range
Inductive Coupling
Magnetic Resonance

## Slide 6
PARTS

## Slide 7: Microcontrollers
Easy to use/implement
Cheap (including development board)
18 pin minimum of programmable I/O
  5 pins on Car System
    2 Digital, 3 Analog
  18 pin on Ground System
    16 Digital, 0 Analog

## Slide 8: Microcontrollers
TI MSP430 / Launchpad (Code Composer)
  128KB memory, 63 pins, 1.8V-3.5V
ATMega328p / Arduino Uno (Atmel Studio or Arduino IDE)
  32KB memory, 23 pins, 4.5V-5.5V
ATXMega64 / STK600 (Atmel Studio)
  64KB memory, 34 pins, 1.6-3.5V

## Slide 9: Microcontrollers
TI MSP430 / Launchpad (Code Composer)
  128KB memory, 63 pins, 1.8V-3.5V
ATMega328p / Arduino Uno (Atmel Studio or Arduino IDE)
  32KB memory, 23 pins, 4.5V-5.5V
ATXMega64 / STK600 (Atmel Studio)
  64KB memory, 34 pins, 1.6-3.5V

## Slide 10: LED 7-segment
The largest and cheapest we can find
At least 3 characters ( ##°C )
Kingbright BC56-12SRWA

## Slide 11: LED Bar Display
Big enough to read from a distance
8 bars (for simple 4:16 decoder implementation)
At least 2 LEDs per bar (5mm green/red)

## Slide 12: Temperature Sensor
Touching Sensor (Thermistors)
Non-touching Sensor (Infrared, Laser)
Range of 0C – 99C (for battery reading)
Optimal battery operating range (-25C to 30C)
GE ZTP-115M

## Slide 13: Motion Sensor (PIR)
Range >15ft
Low current consumption
ROKONET PIR
HC SR501

## Slide 14: Motion Sensor (PIR)
Range >15ft
Low current consumption
ROKONET PIR
HC SR501

## Slide 15: Proximity Sensor
Either Infrared, Ultrasonic, Laser
Ideal range of 60in
Sharp IR Distance Sensor (Left)
SainSmart Ultrasonic Ranging Detector (Right)

## Slide 16: Proximity Sensor
Either Infrared, Ultrasonic, Laser
Ideal range of 60in
Sharp IR Distance Sensor (Left)
SainSmart Ultrasonic Ranging Detector (Right)

## Slide 17: Wireless Communication
XBee Series 1 (1mW antenna)
300ft max range (clear condition)
Easy sync and communication between 2 XBees
3.3VDC

## Slide 18: Charge Controller
6V, 12V and 24V
Life span optimized
Overvoltage protection
Monitored battery performance
BTY79
  Silicon- controlled rectifier
  Operating Temperature 0C to 125C
  Reverse- blocking Thyristors

## Slide 19: Charge Controller

## Slide 20: Vehicle and Battery
Power wheel, golf cart or go-cart
Price range <$150
12V 18AH Battery

## Slide 21: Power Supply and Distribution

## Slide 22: Oscillator Circuit
Initially Colpitts
Chose ZVS since it handles more power
Stronger Magnetic field

## Slide 23: Coils
  Flat spiral chosen over cylindrical design
  Made of 10 AWG Copper wire
  Approx. 12 inches in diameter
  Covered with Plexiglas for safety

## Slide 24
DESIGNS

## Slide 25: Car System – Block Diagram

## Slide 26: Ground System – Block Diagram

## Slide 27: Car System - Schematics

## Slide 28: Ground System - Schematics

## Slide 29: Ground System – LED Displays

## Slide 30: Ground System – LED Displays

## Slide 31: Ground System – LED Displays

## Slide 32: Logic Flow – Car System

## Slide 33: Logic Flow – Ground System

## Slide 34: Logic Flow – Ground System

## Slide 35: PCB/ Assembly
4PCB
  Price
  Turn-around Time
Eagle files completed by March 1
  Ground System MCU Board
    Microcontroller, XBEE, LED circuitry
  Ground System Power Supply Board
    Power Distribution, Oscillator
  Car Systems Board
    Microcontroller, XBEE, Power Distribution, Charge Controller

## Slide 36: Budget/Finance
Component | Cost | Budget | Difference
Metal Box | $5.00 | $30.00 | $25.00
Proximity Sensor | $22.95 | $10.00 | ($12.95)
Motion Sensor | $0.00 | $10.00 | $10.00
LED Displays | $26.95 | $30.00 | $3.05
Kill Switch | $5.38 | $5.00 | ($0.38)
Fan | $0.00 | $5.00 | $5.00
Power Distributor | $54.03 | $30.00 | ($24.03)
Charge Controller | $32.63 | $30.00 | ($2.63)
Vehicle/Battery | $119.99 | $150.00 | $30.01
Temperature Sensor | $11.88 | $20.00 | $8.12
Microcontroller | $29.39 | $20.00 | ($9.39)
Wireless Module | $45.90 | $20.00 | ($25.90)
Oscillator | $8.82 | $30.00 | $21.18
Wires, Conduit, and Mounting | $43.32 | $60.00 | $16.68
Services | $51.94 | $150.00 | $98.06
TOTAL | $458.18 | $600.00 | $141.82

## Slide 37: Progress
Chart: 
| Research | Design | Parts Acquisition | Programming | Testing | Overall
 | 0.9 | 0.7 | 0.8 | 0.5 | 0.3 | 0.5

## Slide 38: Progress
Acquired and tested power supply
Most sensors tested and programed
Built and tested coils
Most parts ordered
Working Prototype by March 1st
Finalized design by April 1st

## Slide 39: Responsibilities
 | Emelio | Ryan | Theo
Power Distribution | x |  | 
Oscillation Circuitry | x |  | 
Coils/Winding | x |  | 
Charge Controller |  |  | x
Wireless Communication |  |  | x
Motion/Proximity Sensors |  |  | x
Temperature Sensor |  | x | 
Microcontrollers |  | x | 
LED Displays |  | x | 
Prototype Construction | x |  | 
Schematics/PCB |  | x | 
Programming |  | x | 
Budget |  |  | x

## Slide 40: Project Issues
Learning the PCB software
Maintaining fixed coil dimensions
Measure battery capacity while charging

## Slide 41
QUESTIONS?