## Slide 1: ChargeSpot
Senior Design II – Spring 2014
Group 20
Theophilus Essandoh
Ryan Johnson
Emelio Watson

## Slide 2: Introduction
To Wireless Power Transfer through High Resonant Frequency

## Slide 3
Increased push for wireless technology
Autonomous Charging System for residential use
Utilize High Resonant Frequency

## Slide 4: Why We Chose Magnetic Resonance
Requires more power
Coils must be properly aligned for maximum efficiency
Shorter range
Inductive Coupling
Magnetic Resonance
Potentially more efficient
Coils can have greater alignment tolerance for high efficiency
Larger range
Inductive Coupling
Magnetic Resonance

## Slide 5: Goals and Objectives
Design and implement a wireless charging system
No physical connectivity between the car and charging system
User friendly with very little user interaction
System shuts down automatically when battery is fully charged or temperature is not ideal
Include a fail safe manual override shutdown switch
Receiving coil must be properly concealed and not interfere with the normal safe operation of the vehicle
Visual guidance system for proper alignment

## Slide 6: Specifications
Wireless XBee link 50 Ft from control panel
Proximity sensor range 5 Ft. minimum
Copper coils less than 2 lbs. each
Measure and display battery temperature to within + 1°C accuracy
Charge current greater than 1A
Battery 12V 18AH
Battery fully charged within 8Hrs
Efficiency > 20%

## Slide 7: Overview
Of Systems

## Slide 8
Kill Switch implemented at power source
Power is rectified and converted to 24V, 12V, 5V, and 3.3V and supplied to corresponding systems
The MCU controls the oscillator system via a switch that controls the wireless power transfer
Data is sent to the MCU via the XBee and relevant data is displayed via the LED displays
Ground Systems Block Diagram

## Slide 9
Power comes from the receiving coil and is rectified
The buck converter brings the voltage down for the charge controller to charge the battery
The battery powers the car MCU and other related systems
Temperature and voltage data from the battery are sent through the Xbee to the ground MCU
Car Systems Block Diagram

## Slide 10: Designs of Systems
And Hardware

## Slide 11
Ground Systems on EAGLE

## Slide 12
Ground Systems on EAGLE
Power System

## Slide 13
Power comes from the transformer and is rectified through a PMR27K100, outputting 24VDC.
A 250VAC/5A fuse is used for overcurrent protection.
24VDC goes to the Relay, it is also regulated to 12VDC with a LM7812.
12VDC goes to the Relay, it is also regulated to 5VDC with a LM7805.
5VDC powers most of the ICs, it is also regulated to 3.3VDC with a LM3940.
3.3VDC powers the XBee Module.
Power System for Ground

## Slide 14
Power comes from the transformer and is rectified through a PMR27K100, outputting 24VDC.
A 250VAC/5A fuse is used for overcurrent protection.
24VDC goes to the Relay, it is also regulated to 12VDC with a LM7812.
12VDC goes to the Relay, it is also regulated to 5VDC with a LM7805.
5VDC powers most of the ICs, it is also regulated to 3.3VDC with a LM3940.
3.3VDC powers the XBee Module.
Power System for Ground

## Slide 15
Power comes from the transformer and is rectified through a PMR27K100, outputting 24VDC.
A 250VAC/5A fuse is used for overcurrent protection.
24VDC goes to the Relay, it is also regulated to 12VDC with a LM7812.
12VDC goes to the Relay, it is also regulated to 5VDC with a LM7805.
5VDC powers most of the ICs, it is also regulated to 3.3VDC with a LM3940.
3.3VDC powers the XBee Module.
Power System for Ground

## Slide 16
Power comes from the transformer and is rectified through a PMR27K100, outputting 24VDC.
A 250VAC/5A fuse is used for overcurrent protection.
24VDC goes to the Relay, it is also regulated to 12VDC with a LM7812.
12VDC goes to the Relay, it is also regulated to 5VDC with a LM7805.
5VDC powers most of the ICs, it is also regulated to 3.3VDC with a LM3940.
3.3VDC powers the XBee Module.
Power System for Ground

## Slide 17
Power comes from the transformer and is rectified through a PMR27K100, outputting 24VDC.
A 250VAC/5A fuse is used for overcurrent protection.
24VDC goes to the Relay, it is also regulated to 12VDC with a LM7812.
12VDC goes to the Relay, it is also regulated to 5VDC with a LM7805.
5VDC powers most of the ICs, it is also regulated to 3.3VDC with a LM3940.
3.3VDC powers the XBee Module.
Power System for Ground

## Slide 18
Ground System on EAGLE
DPDT Relay

## Slide 19
Omron G2R2 5VDC Relay
  Low coil voltage for our microcontroller
  Current rating of 8A
The Relay takes the 24VDC and 12VDC lines and powers the Oscillator System and Cooling Fans.
The “SWITCH” control line comes from the Microcontroller.
DPDT Relay for Ground

## Slide 20
Ground System on EAGLE
Microcontroller

## Slide 21
Atmel ATMega328p
  Arduino Uno development board
  Arduino IDE
  32KB memory, 23 pins, 5VDC
The ground MCU controls the main logic flow of the systems and the LED displays.
18 Digital I/O pins used
Microcontroller for Ground

## Slide 22
Ground System on EAGLE
XBee Module

## Slide 23
XBee Modules used for Wireless communication because of its compatibility with the ATMega328p.
X-CTU used for programming (to set private channel and optional coordinator/slave)
1mW antenna (300ft max range)
XBee Modules

## Slide 24
Ground System on EAGLE
Shift Registers
Header Pins

## Slide 25
Three 8-bit shift registers needed to drive LED displays (595s). Old design used inverters and 3:8 decoders.
  One 595 is used for our 7-segment display.
  Two 595s are used to drive our LED bar display.
LED Displays

## Slide 26
The 7-segment display is a Kingbright BC56-12SRWA 3-digit display.
Displays numbers upside-down, so we can use the DP as a degree symbol.
This particular display uses a common anode configuration, and is connected as shown below:
LED Displays

## Slide 27
For our LED bar display, nothing we found online suited our requirements and budget, so we made our own.
Initially an ice cube tray, we used bottle caps as our LED housing.
This display shows the distance of the vehicle until proper alignment. Once charging begins, it shows the voltage level of the battery.
LED Displays

## Slide 28
In addition to our LED displays, we also have accessory LEDs for additional notifications of systems’ status.
They indicate:
  Charging mode.
    Is the system is the right mode for charging?
  Temperature error.
    Is the battery too hot or cold for charging?
  XBee connectivity.
    Is data being communicated wirelessly?
  A met proximity condition.
    Is the vehicle in position?
  Charging status.
    Is the oscillator system on, sending power through the coils and thus charging the battery?
LED Displays

## Slide 29
  Initially we used an infrared proximity sensor, but its range was far too short. We switched to this ultrasonic proximity sensor by SainSmart.
  It has a maximum range of 80 inches; powered by 5VDC.
  It is used to determine the vehicle’s distance from the ideal position for proper alignment for optimal efficiency.
  It is also used to determine if the vehicle leaves in order to shut the system down.
Proximity Sensor for Ground

## Slide 30
Oscillator System on EAGLE

## Slide 31
VCC is the 24VDC coming from the Ground Systems’ Relay.
Researched variations of Hartley and Colpitts oscillators, but eventually came across the zero voltage switching (ZVS) driver oscillator
Our variation of the ZVS oscillates at 100kHZ.
Oscillator System

## Slide 32
Oscillator System

## Slide 33
Pictured are coil designs we went through. We finalized our design with 3+3 turns for the transmitting coil (center-tapped) and 5 turns for the receiving coil.
Final coils are made from 10 AWG solid copper and measure 12in and 11in in diameter.
Transmitting and Receiving Coils

## Slide 34
Car Systems on EAGLE

## Slide 35
Car Systems on EAGLE
Power System

## Slide 36
Power comes from the receiving coil and is rectified through a GBU6J bridge rectifier, outputting unregulated DC.
The unregulated DC feeds into the buck converter.
The BAT+ is regulated to 5VDC with a LM7805.
5VDC powers most of the ICs, it is also regulated to 3.3VDC with a LM3940.
3.3VDC powers the XBee Module.
Power System for Car

## Slide 37
Power comes from the receiving coil and is rectified through a GBU6J bridge rectifier, outputting unregulated DC.
The unregulated DC feeds into the buck converter.
The BAT+ is regulated to 5VDC with a LM7805.
5VDC powers most of the ICs, it is also regulated to 3.3VDC with a LM3940.
3.3VDC powers the XBee Module.
Power System for Car

## Slide 38
Power comes from the receiving coil and is rectified through a GBU6J bridge rectifier, outputting unregulated DC.
The unregulated DC feeds into the buck converter.
The BAT+ is regulated to 5VDC with a LM7805.
5VDC powers most of the ICs, it is also regulated to 3.3VDC with a LM3940.
3.3VDC powers the XBee Module.
Power System for Car

## Slide 39
Car Systems on EAGLE
Buck Converter

## Slide 40
Unregulated DC feeds the buck converter and outputs an adjustable output; we adjusted for an output of 16VDC.
The 16VDC feeds the charge controller.
Our design is based around the LM2596 Simple Switcher chip.
Buck Converter for Car

## Slide 41
Car Systems on EAGLE
Charge Controller

## Slide 42
16VDC from the buck converter feeds the charge controller.
Output adjusted to 14VDC.
Maximum power dissipation is 16W
Charge Controller for Car
Purpose for the charge controller:
  Life span optimized
  Overvoltage protection
  Monitored battery performance

## Slide 43
Car Systems on EAGLE
Microcontroller

## Slide 44
Same ATMega328p as Ground System
In the Car System, the MCU is reading TEMP and VOLT; voltage from the temperature sensor and voltage from the voltage divider circuit to determine battery’s voltage level.
Microcontroller for Car

## Slide 45
Car Systems on EAGLE
XBee Module

## Slide 46
Car Systems on EAGLE
Voltage Divider
Header Pins

## Slide 47
This simple voltage divider is used to read the battery’s voltage without damaging the 5V microcontroller.
Voltage Divider for Car

## Slide 48
This ZTP-115M temperature sensor module is an infrared non-contact sensor.
Versatile and easy-to-use with an acceptable range of -40C to 145C and 1C accuracy at room temperature.
However, following its given sensitivity curve, we were getting inaccurate readings, so we had to calibrate.
Temperature Sensor for Car

## Slide 49: Software
And Logic

## Slide 50
Logic Flow Diagram for Car MCU

## Slide 51
Logic Flow Diagram for Ground MCU

## Slide 52
Logic Flow Diagram for Ground MCU

## Slide 53: Project Testing
And Administration

## Slide 54
Voltage Divider
  Red points and line represent collected data from voltage divider of 10k and 4.7k; blue line represents voltage divider equation.
Sensors Calibration
Temperature Sensor
  Red points represent data points taken from stove top measurements using DMM temperature sensor as reference; blue line represents best fit curve.

## Slide 55
Vertical Displacement Test
  Used to determine height from transmitting coil where wireless power transfer efficiency fades.
Wireless Power Transfer Efficiency Tests
Horizontal Misalignment Test
  Used to determine distance from origin where wireless power transfer efficiency fades.

## Slide 56
Voltage Divider
  Red points and line represent collected data from voltage divider of 10k and 4.7k; blue line represents voltage divider equation.
Integrated System Power Efficiency Test
Temperature Sensor
  Red points represent data points taken from stove top measurements using DMM temperature sensor as reference; blue line represents best fit curve.
Measurement Point | Voltage | Current | Power
Ground Systems (Oscillator Off) | 23.8V | 0.12A | 2.86W
Ground Systems (Oscillator On) | 21.8V | 1.32A | 28.78W
Oscillator | 21.6V | 1.30A | 28.08W
Car System at Charge Controller Output | 14.0V | 0.48A | 6.72W

## Slide 57
Budget
Category | Cost | Budget
Metal Box | $5.00 | $30.00
Proximity Sensor | $22.95 | $10.00
Motion Sensor | $0.00 | $10.00
LED Displays | $29.47 | $30.00
Kill Switch | $5.38 | $5.00
Fans | $0.00 | $5.00
Power Distributor | $54.03 | $30.00
Charge Controller | $76.98 | $30.00
Vehicle/Battery | $119.99 | $150.00
Temperature Sensor | $11.88 | $20.00
Microcontroller | $70.30 | $20.00
Wireless Module | $45.90 | $20.00
Oscillator | $50.11 | $30.00
Wires and Mounting | $76.94 | $60.00
PCB and Boards | $103.04 | $100.00
Services | $152.82 | $50.00
TOTAL | $824.79 | $600.00

## Slide 58
Proximity sensor had feedback interference due to mis-angled reflections from non-uniform surfaces.
  Vehicle had to be retrofitted with a uniform surface.
Charge controller MOSFET failures due to circuit sensitivity.
Heat issues; oscillator, voltage regulators, and rectifiers.
  System had to include heat sinks and cooling fans.
Mounting circuit boards to the panel door.
Microcontroller Serial buffer used to sense XBee connectivity.
  Used a timer to determine length of disconnection.
Project Issues

## Slide 59
QUESTIONS?