## Slide 1
3D Laser Range Finder
Group 27
Christian Conrose, Andrew Watson, Jon Ulrich
Notes: Add picture

## Slide 2: LIDAR
LIght Detection And Ranging

## Slide 3: Motivation
AUVSI Competitions for Robotics Club
Augment Computer Vision Capabilities
Mobile 3D range finder
Visually represent range data
Notes: Over the many years of intense competition with a variety of platforms across multiple teams the Robotics Club at UCF has consistently found a need for collecting highly accurate 3D data from the environment. To completely and reliably map a real-world environment however one must consider all dimensions at once to fully construct a true representation. The club has generously offered to donate a fast, long range 2D laser range finder to help in the construction of the proposed system.

## Slide 4: Goals
Create Accuracte 3D Sensor
Indoor/Outdoor Operation
High Update Rate
Longevity
Occams Razor

## Slide 5: Specifications Requirements
Size | Less than 3 cubic feet
Weight | Less than 5 pounds
Power Draw | Less than 36 watts
3D Scan Rate | 2 hertz
Communication Port | Ethernet
Weather Rating | IP45
Notes: Boat photo

## Slide 6: Process
Rotating 2D lidar sensor
Event driven system
Rotation adds 3rd dimension

## Slide 8: Lidar Selection
 | Hokuyo PBS | SICK LMS291-S05 | Hokuyo UTM-30LX
Light Source | IR LED | Laser Diode | Laser Diode
Application | Indoor | Indoor / Outdoor | Indoor / Outdoor
Angular Resolution | 1.8 | 0.25 | 0.25
Scanning Range | 178 | 180 | 270
Detecting Range | 0.2m to 3m | 1.5 - 30m | 0.1m to 30m
Scan Time | 100ms | 75ms | 25ms
Power | 24VDC | 230V | 12VDC
Price | $1,200 | $3,500 | $6,000

## Slide 9: Laser UTM-30LX
30 meter range
Serial Interface
C++ Library
Scan Feedback

## Slide 10: Event
Driven

## Slide 11: Laser

## Slide 12: Motion: Pitch
+Pro:
Immediate Horizon
-Con:
Alternating Directions
Full Scan Latency

## Slide 13: Motion: Yawing Scan
+Pro:
Immediate
Vertical Scan
-Con:
Alternating
Directions
Full Scan
Latency

## Slide 14: Motion: Rolling Scan
+Pro:
Center Focus
Continuous
Rotation
-Con:
Peripheral Vision

## Slide 15: Motor Selection
 | Dynamixel RX-24F | 42BYGHM809 | Dynamixel MX-28
Motor Type | Servo | Stepper | Servo
Resolution | 0.29 | 0.9 | 0.088
Voltage | 12VDC | 3VDC | 12VDC
Price | $139 | $17 | $219

## Slide 16: Motor Selection: MX-28T
Motor Feedback
Highest Resolution
Continuous Rotation
Serial Communication
12V Rail

## Slide 17: 3D Interpolation
Input Output
2D Point 3D Point
Motor Position

## Slide 18: Point Cloud
Visualization

## Slide 19: Microcontroller
 | Raspberry Pi Model B | Beagle Board Black | Pandaboard ES
Price | $35 | $45 | $182
Processor | 700MHz | 1GHz | 1.2GHz Dual Core
RAM | 512MB | 512MB | 1GB
Size | 3.37” x 2.125” | 3.4” x 2.1” | 4.5” x 4”
Max. Drain | 700mA | 470mA | 800mA

## Slide 20: Raspberry Pi
700 MHz ARMv6 ISA
8 GPIO
Smallest physical footprint

## Slide 21: Operating System
Raspbian Debian linux operating system tailored for raspberry Pi
Threaded Application
Onboard development
Libraries

## Slide 22: Communication
TCP Communication
Custom Communication Protocol
Packet Section | # Bytes
Initialization | 2
Action Code | 3
Packet Data | N
Command Name | Command Type | Action Code
Start | System | 0xA01
GetDepthImage | Image | 0xCD1

## Slide 23: Power
Source: 12VDC
Output: 5VDC and 12VDC
Part: TI LMZ14203 Switching Module
Source Input: 6V - 42V
Max Output: 18 Watts
Output Voltage: 0.8V - 6V

## Slide 24: Power
LMZ14203 Switching Module

## Slide 25: Testing
Software Testing
  Laser
  Motor
  Microcontroller
3D Scan Testing
  Indoor/Outdoor
  Day/Night
  Movement

## Slide 26: Division of Labor
 | Andrew | Christian | Jon
Laser | X |  | 
Motor | X |  | X
Mount | X |  | 
Communication |  | X | X
Power |  | X | X
Visualization |  | X | 
Testing | X | X | X

## Slide 27: Budget
Raspberry Pi model B | $35
Hokuyo UTM-30LX | $5,999
Dynamixel MX-28 | $219
Logitech Business Pro 9000 | $65
Mercotac Rotating Connector 830 | $449
PCB | $50
FTDI Chip USB-RS485-WE-5000-BT | $45
Power System | $150
Total Cost | $7,015
TI & UCF Robotics Club Donated Parts | -$7,015
Final Cost | $0

## Slide 28: Progress

## Slide 29: Project Status

## Slide 30: Difficulties
Event Timing
Rotating Platform
Real Time Rendering
Vehicle Movement

## Slide 31
Questions?