## Slide 1: Autonomous firefighting robot
Philip Fritz EE
Dylan Moro EE
Bryanna Saavedra EE Dustin James EE

## Slide 2: Project Description/Requirements
A small autonomous vehicle
Ability to navigate maze autonomously
Fire detection and suppression
Manual drive capability
Lightweight and rugged in design
Notes: A small autonomous vehicle able to navigate a maze and detect fire. After the fire has been detected, the vehicle will approach and extinguish the fire. The vehicle will also have the capability to be manually overridden and controlled via wireless remote with FPV video relayed to a small monitor.

## Slide 3: Motivation
Safer than sending human search and rescues
Can fit into smaller spaces than a person can
A scalable design that could be used in the field
  Fire suppression using more robust methods
  Image processing for human detection
  Chassis could be upgraded to a tank style body
Can go where there is a limited supply of oxygen

## Slide 4: Constraints/Requirements
Environmental constraint: use of chemical extinguishers
School regulations mandate that during demonstrations, flame must be no larger than a tea candle size
Maze must fit in the demonstration area
Robot must have small turning radius
Maze must be easy to assemble and disassemble
Robot must be light enough to carry to the scene
Notes: Edf jet

## Slide 5: Specifications
All components must run off of 12 V or lower
Current draw must not exceed 50 A
Under 20 lbs for portability
Wheel base must be no wider than 18 in
Battery should last more than 15 minutes
Sensors should have approximately 180 degree combined field of view

## Slide 6: Hardware Overview

## Slide 7: Proximity Sensor
Purpose - To detect distance from edge of wall.
Possible solutions
  Image Processing
  LIDAR
  Ultrasonic
  Etc.
Chose Ultrasonic for proximity detection.

## Slide 8: HC-SR04 Ultrasonic Sensor
Operating voltage - 5V
Continuous operating current – 15mA
I/O pins – 2
Max reading distance – 400cm
Min reading distance – 2cm
Cost - $7.95
Total measuring angle (degrees) – 60
Dimensions – 1.3 x 0.4 x 0.1 inches
Procured from – Amazon.com
Notes: Start: brief description of purpose for using ultrasonic Sensor and how it works

## Slide 9: Use of Ultrasonic Sensor
Distance=
Number of Sensors used – 3

## Slide 10: Flame Sensor
Purpose – To detect distance and direction from flame.
Possible solutions
  Image processing
  Temperature sensing
  Infrared/visible signature detection
Chose infrared/visible signature detection

## Slide 11: YW Robot Infrared Sensor
Operating voltage – 5v
Continuous operating current – 20mA
I/O pins – 2
3 adjustable sensitivity settings
Approximately 60 degrees detection angle
Detects light waves between 760 nanometer to 1100 nanometer
Cost- $4.40
Procured from Amazon.com

## Slide 12: 700TVL Wide Angle FPV Camera
Purpose – To assist in manual navigation
Viewing angle – 170 degrees
  Humans binocular view is only approximately 120 degrees
Operating voltage – 9-12v
Continuous operating current – 55mA
Size – 0.6x0.6x0.6 in
Picture resolution – 1280 x 960
Cost - $19.99
Procured from amazon.com

## Slide 13: 7"LCD TFT FPV Monitor
Resolution:480（H） X 234（W）
Operating voltage: DC12V
Rating power:7.5W
Screen size:150mm X 90mm
Size:179mm X 120mm X 20mm
Current draw: 0.625 A
Cost: $49.92
Purchased from: Amazon.com

## Slide 14: Radio Control Transmitter
Purpose – To control robot during manual mode operations
Possible solutions
  2.4 GHz radio frequency
  5.8 GHz radio frequency
  Xbee
  Infrared
  Bluetooth 3.0
Chosen method – 2.4 GHz radio frequency

## Slide 15: Futaba 9c with 2.4 GHz Spektrum Transmitter Module
Easily available (already acquired)
2.4 GHz radio frequency commonly propagates further than other options
Uses the encoding scheme DSM2 to avoid cross interference
2.4 GHz transmitter controllers are generally easy to program
Futaba 9c offers 9channels of operation
Notes: Add picture

## Slide 16: Orange Rx R615X DSM2/DSMX 6CH 2.4 GHz Receiver
6 PWM channels
Operating voltage – 3.7-9.6 volts
Continuous operating current – 40mA
Weight – 3.7g
Size – 19.5x30x10mm
Compatible with DSM2/DSM module systems
Cost-$15
Procured from HobbyKing.com
Notes: Picture needed

## Slide 17: 8CH Boscam Wireless Transmitter Receiver 5.8 GHz
Operating voltage (Rx/Tx) – 7-15v
Continuous operating current (Tx) – 300mA
Continuous operating current (Rx) – 100mA
Operating radio frequency – 5.8GHz
Dimensions (Tx) – 55 x 26 x 17mm
Dimensions (Rx) - 61 x 52 x 13mm
Weight (Tx) – 52g
Weight (Rx) - 120g
Cost - $34
Procured from Amazon.com

## Slide 18: MCU
Chose Atmega 328
Flash: 32 Kbytes
Max I/O pins: 23
CPU: 8-bit
Max operating frequency: 20MHz
Open source libraries
Operating voltage: 1.8-5.5 v
Dimensions: 35.5 x 8.6 mm
Cost: $7.45
Purchased: amazon.com

## Slide 21: Chassis
Dimensions of chassis: 7.5 x 10.5 in
Dimensions of wheels: 4.3 in
Weight: 3.35 lbs
Materials: ABS plastic and aluminum
Benefits:
  Low profile
  Lightweight
  Sturdy
Purchased from: servocity.com
Price: $169.99

## Slide 22: Chassis Motors
142 RPM Precision Planetary Gear Motors
Operating voltage: 3-12 V DC
Rated load: 30.6 ounces per in
No load current: 0.19 A
Max stall current: 4.9 A at 12 V DC
Stall torque: 130.5 oz per in
Gear ratio: 84:1
Weight: 92 g
43.7 x 20 mm
Notes: Add picture

## Slide 23: Chassis Motor Controller
Hobbywing Quicrun 1060 Brushed ESC
Operating voltage: 8.4-12.6 V
Forward continuous/peak current: 60/360 A
Reverse continuous/peak current: 30/180 A
Dimensions: 36.5 x 32 x 18 mm
Weight: 39 g
Benefits:
  Forward/reverse/brake function
  Fail safe protection
  Low voltage protection
  Water and dust proof
Purchsed from: Amazon.com
Price: $22.30
Notes: Add picture

## Slide 24: Power Supply
Turnigy Nanotech 3s LiPo
Capacity: 4000 mAh
Discharge: 35C constant/70C burst
Connector: xt60
Dimensions: 152 x 49 x 21 mm
Weight: 335 g
Purchased from: amazon.com
Price: $36.99

## Slide 25: Power Regulation
RC Servo UBEC
Operating input: 5.5-26 V
Output voltage: 5V
Maximum current output: 3 A
Benefits:
  Lightweight
  Compact
  versatile
Price: $8.28
Purchased: amazon.com

## Slide 26: Software and Algorithm Development
Programming language – C++
Programming environment – Arduino IDE
2 operating modes
  Manual
  Autonomous

## Slide 27: Manual Mode
Purpose
  Realistic design – transport, functionality
  Testing purposes
  If autonomous mode fails and control is lost
Triggered by remote control at any time
Uses pulseIn function from Arduino ide library
  pulseIn(pin,value,timeout)
    Pin – assigns input pin to read PWM
    Value- if value is assigned HIGH the function waits for the pin to go HIGH, starts timing, then waits for pin to go LOW
    Timeout-amount of time waited for pin to go HIGH before timing out

## Slide 28: Manual Mode

## Slide 29: Autonomous Mode
Right hand Rule
  Effective
  Always works if there is one entrance
  Used in real fires when vision is obstructed

## Slide 30: Autonomous Mode

## Slide 31: Testing
Equipment used:
  Ultrasonic sensor
  Flat surface (poster board)
  Bread board
  Ruler
  Serial monitor via USB to laptop
  Arduino UNO MCU

## Slide 32: Testing (Cont.)
Equipment used:
  Fire sensor
  Bread board
  Ruler
  Candle
  Serial monitor via USB to laptop
  Arduino UNO MCU

## Slide 33: Testing Results

## Slide 34: Testing (Cont.)
Maze originally used three rooms
  Reduced to one room for presentation purposes
Multiple tests were conducted with a very high success rate
Programming was constrained to the testing environment
  Such as the type of flooring

## Slide 35: Prototype to Integration
Notes: Old vs new

## Slide 36: Expenses

## Slide 37: Complications
Continuing with maze after extinguishing fire
Smoothing movements with delays
  Caused less interference between pings from ultrasonic sensors
Efficiency of code
Library cross interference
Notes: With the prototype, after the fire was extinguished, it had a hard time going back to the wall
Library cross interference: we've had issues when trying to move servos at the same time as reading a sensor, the same timer is used.

## Slide 38: Division of Labor
 | Sensors | Programming | Packaging | PCB Design | Admin. Content
Philip | S | P | S |  | 
Dylan |  | S |  | P | 
Bryanna | P |  |  |  | P
Dustin |  |  | P |  | S
P = primary
S = secondary

## Slide 39: Questions?