## Slide 1: Electri-Surf
Group 22:
  Alex Amoros – Computer Engineering
  Anthony Higgins – Electrical Engineering
  Ryan Taylor – Electrical Engineering

## Slide 2: Project Goal
Design and implement an electric surfboard controlled with a wireless throttle and powered by a rechargeable battery

## Slide 3: Motivation
To Produce a fun project that people may find interesting
Gain hands on experience
Combine learning with an outdoor hobby

## Slide 4: Project Concept
Jet Drive
G
Phone

## Slide 5: Project Specifications
Ride Time: 30 minutes
Weight: Less than 40 lbs.
Wireless Connection Range: 1-2 m
Battery Durability: 2 recharges per 24 hours
Speed: 5-10 mph

## Slide 6: System Block Diagram

## Slide 7: Power Source
ZIPPY | Flightmax
Type | Lipo
Voltage | 22.2 V
Capacity | 4500 mAh
Configuration | 6 cell
Discharge | 45C - 55C burst
Weight | 789 grams
Length A | 145 mm
Height B | 51 mm
Width C | 52 mm

## Slide 8: Propulsion
Motor - Turnigy | AquaStar
Weight | 508 grams
Max Current | 105 A
Max Voltage | 37 V
Power | 3050 W
Shaft A | 5 mm
Diameter C | 39 mm
Total Length | 103 mm
Jet Drive | Pump Unit
Model | Jet2805
Max RPM | 20,000
Total Length | 171 mm
Diameter | 28 mm
Propulsion | Impeller

## Slide 9: Microcontroller
The microcontroller that we required for our project had a couple of requirements to meet:
Low price
Support PWM(Pulse Width Modulation)
UARTSerial support.
Couple of pins for general LED usage.

## Slide 10: Microcontroller
Our first choice was TI’s TMS320F28062 microprocessor.
We were delighted about the microprocessor and met our requirements and more. The only problem that we ran into our design was the lack of CAD files for the microcontroller.

## Slide 11: Microcontroller
Our second microprocessor that we considered was the ATmega328P. Fewer than the other microcontroller, ATmega328P could still perform the requirements of the project.

## Slide 12: Microcontroller
ATmega328P
TMS320F28062

## Slide 13: Bluetooth Communication
Save time using the a smart phone as the handheld control.
Ideal due to the fact most smart phones have Bluetooth incorporated inside the phones.
Do not have to build, hardware wise, a hand control for the board.

## Slide 14: Bluetooth Communication

## Slide 15: Bluetooth Communication
The Bluetooth module that was chosen for the project was the HC-05. Here’s a comparison of other Bluetooth modules that we compared.
Bluetooth Module | CC2564MODN | BT900 | HC-05
OPERATING VOLTAGE | -.5-4.8 V | 3.6 V | 3.3V DC
Size | 7.1 mm x 7.1 mm x 2mm | 2.5mm x 12.5mm x 19mm | 27mm x 13mm x 2mm
Signal range(m) | 10 | 100 | 1
Data Speed | 2.1 Mbps | 3 Mbps | 3 Mbps
Price USD | 13.97 | 15.35 | 10.68
Complex interface | Easy | Easy | Easy
Max Baud Rate | 9600 | 9600 | 9600

## Slide 16: Mobile App
Android Application
Using Android Studio IDE
Have an option for for Guest and Administrator
Gives total control over the surfboard’s settings for the user

## Slide 17: Mobile App

## Slide 18: Speed Control
Electronic Speed Control (ESC)
Connects directly to motor, PCB, and battery
Regulates current sent to motor
  Programmed through ATmega328p
  Via pulse width modulation (PWM)

## Slide 19: Electronic Speed Control
Using 120A ESC
Contains universal battery eliminating circuit (UBEC)
No need to have a battery power receiver
  Converter inside esc that drops voltage

## Slide 20: Battery Monitoring
DS2438 smart battery
  Maxim Integrated
Designed for max 12V battery
Circuit implemented to widen capable input range
LED representation

## Slide 21: Battery Monitoring

## Slide 22: Battery Monitoring
Calculating true voltage
Measure VAD pin

## Slide 23: PCB Design
EAGLE
No experience
  Not 100% confident in design
  Multiple runs expected
Limited CAD files
  Switched parts

## Slide 24: PCB Schematic

## Slide 25: Difficulties
Parts out of stock
CAD files
Little experience

## Slide 26: Safety Concerns
Rider Safety
  Engine shut off mechanism
  Battery level awareness
Water Hazard – hardware preservation
  Water and electricity don’t mix

## Slide 27: Division of Labor
Member | PCB Design | Mobile App | Bluetooth/ Coding | Waterproofing | Testing | Design Assembly | Administration
Anthony | ✔ |  |  | ✔ | ✔ | ✔ | ✔
Alex |  | ✔ | ✔ |  | ✔ |  | 
Ryan | ✔ |  |  | ✔ | ✔ | ✔ | ✔

## Slide 28: Budget
Part | Cost
Surfboard | TBD
Jet Drive | $69.95
Battery | $68.68
Motor | $69.89
Battery Charger | $23.00
ESC – Electronic Speed Control | $29.28
Battery Monitor | Free
Microcontroller | $13.72
Developmental Board | $25.00
Bluetooth | $5.25
LED’s | Free
Waterproofing Supplies | TBD
PCB | TBD
Current Total | $304.77

## Slide 29: Progress
Chart: 
| Overall | Parts Acquisition | Android App | Programming | PCB | Testing | Waterproofing
Completion | 0.35 | 0.7 | 0.35 | 0.5 | 0.2 | 0.15 | 0.05

## Slide 30: Future Plans
Ordering PCB ASAP
Test motor response with phone app
Mount to housing unit and waterproofing
Finalize testing/build prototype

## Slide 31: Questions?