## Slide 1: OSN Optical Supplemental Navigation Device
Wilfredo Ortiz | PSE
Joseph Devenport | PSE
Cedric Harper | EE
Henry Schmitz | EE

## Slide 2: Member Responsibilities
 | Wilfredo | Devin | Cedric | Henry
Transmitter | Secondary | Primary |  | 
Receiver | Primary | Secondary |  | 
Optical Module | Primary | Secondary |  | 
Power |  |  | Primary | Secondary
Processing |  |  | Primary | Secondary
Timing |  |  | Secondary | Primary
Haptic Feedback |  |  | Secondary | Primary

## Slide 3: Motivation
Help blind and vision impaired individuals maneuver new and unfamiliar environments
Create an affordable supplement to the cane or guide dog
US: Approximately 1.1 million vision impaired and 200,000 totally blind
Global: 285 million vision impaired and 39 million totally blind
Cane and guide dog limited to 1 meter range
Safety and Confidence

## Slide 4: Current Ultrasonic Technology
 | Range | Price
Ultracane | 2-4 m ground/ 1.5 m chest height | $635.00
Smartcane | 1.5-3 m | $3000.00
iGlasses | 0-3 m | $96.00
Source: Ultracane

## Slide 5: Current Laser Technology
Not many products on the market currently using lidar
Group of Engineers at University of Melbourne currently prototyping a lidar system
Future technology heading towards eliminating cane altogether and using 3D lidar to map out entire rooms
 | Range | Price
Laser Cane N-2000 | 10 m | $2650

## Slide 6: OSN Block Diagram

## Slide 7: LASER
Notes: https://hackaday.com/tag/laser-rangefinder/
https://chmodux.wordpress.com/2012/04/16/range-finding/
http://www.hizook.com/blog/2009/12/20/ultra-low-cost-laser-rangefinders-actualized-neato-robotics

## Slide 8: Methods of Range-Finding: Time of Flight
Pros:
Can measure long distances
Accurate aiming to targets and through gaps (very small beam divergence).
Can measure to target surfaces at any angle.
Can be set to measure through glass or to the surface of glass.
Can be used to create large scale, 3D images by scanning.
Cons:
Can be more expensive
Range is limited particles in the air (dust, rain, etc)

## Slide 9: Specifications
Overall Weight | Less than 2 lbs.
Overall Size | Less than 8in by 5in by 3in (l,w,h)
Overall Cost | Less than $300
Supply Voltage | Less than 12V
Device Range | From 1m to 4m
Laser Diode Wavelength | Near IR, 800-950nm
Photodiode Absorbance | Maximum Near IR, 800-950nm

## Slide 10: Transmitter

## Slide 11: Pulsed Laser Diode
Model: OSRAM SPL LL85
Spectral range: 840 nm-860 nm
Peak Wavelength: 850 nm
Spectral Width: 4 nm
Pulse Width: 28 ns
Peak Output Power: 14 W
Duty Cycle: 0.1 %
Cost: $20
Model: OSRAM SPL PL85
Spectral range: 840 nm - 860 nm
Peak Wavelength: 850 nm
Spectral Width: 4 nm
Pulse Width: 100 ns
Peak Output Power: 13 W
Duty Cycle: 0.1 %
Cost: ~$20
Notes: http://www.osram-os.com/osram_os/en/press/press-releases/ir-devices-and-laser-diodes/2015/low-cost-lidar--a-key-technology-to-enable-autonomous-driving-in-urban-environments/index.jsp?search_result=%2Fosram_os%2Fen%2Fpress%2Fpress-releases%2Findex.jsp%3Faction%3Ddosearch

## Slide 12: Lens Selection
Newport Model: KBX022
Lens Material: N-BK7
Diameter: 12.7 mm
Radius of Curvature: 11.868 mm
EFL: 12.7 mm
BFL: 10.26 mm
Uncoated
Cost: $35
Newport Model: SBX013AR.16
Lens Material: UV Fused Silica
Diameter: 12.7 mm
Radius of Curvature: 10.358 mm
EFL: 12.7 mm
BFL: 9.86 mm
AR Coating (650-1000 nm)
Cost: $210
Notes: www.newport.com

## Slide 13: Collimation
Basically, the diverging source should be placed at the focal length of a positive lens.
Is It that simple?

## Slide 14: Lens Design
BFL: 10.0 mm
BFL: 6.77 mm
Spot Radius: 1.6 mm
Spot Radius: 0.57 mm

## Slide 15: Optical Module

## Slide 16
Custom made for optical alignment of components
Showcases curved design of enclosure

## Slide 18: Narrow Bandpass Filter
8.0mm in diameter
Thickness of 0.55mm
Center wavelength is 850nm+/-5nm
Half-band width is 30nm
Peak transmissivity is >86%
Cut-off percentage is <1%
Mirror-glass material

## Slide 19: Receiver

## Slide 20
Spectral Response: 400 nm - 1050 nm
Peak Wavelength: 820 nm
Active Area: .36 mm^2
Dark Current: 0.5 nA
Terminal Capacitance: 3 pF
Rise Time : 1.8 ns
Cost: $.83
Spectral Response: 400 nm - 1000 nm
Peak Wavelength: 800 nm
Active Area: .3 mm^2
Dark Current: 0.05 nA
Terminal Capacitance: 1.5 pF
Rise Time: .5 ns
Breakdown Voltage: ~150 V
Cost: ~$82

## Slide 21: OPA380 Transimpedance Amplifier
High Speed
Supply Voltage: 2.7 V-5.5 V
Slew Rate: 80 V/us
GBW: 90MHz
700 kohm Rf
3.3 V VCC

## Slide 22: Timing

## Slide 23: Requirement
Affordable
Set threshold for receiver signal
Down convert signal to detect in ns range
SPI communication with MCU
Low power consumption

## Slide 24: TDC7200 TDC7201
Measurement Range:
Mode 1: 12 ns to 500 ns
Mode 2: 250 ns to 8 ms
Low Power Consumption: 0.5 µA
Supports up to 5 Stop Signals
Supply Voltage: 2 V to 3.6 V
Price : $5.06
Package: TSSOP (14)
Measurement Range:
Mode 1: 12 ns to 2000 ns
Mode 2: 250 ns to 8 ms
Low Power Consumption: 2.7 mA
Supports up to 10 Stop Signals
Supply Voltage: 2 V to 3.6 V
Price : $6.09
Package: nFBGA (25)

## Slide 25
Mode 1
Mode 2

## Slide 26: Processing

## Slide 27
Affordable
16MHz clock frequency
Output 1kHz
1-5V Operating Range
SPI communication
Sufficient GPIO Pins
Requirements

## Slide 28
Operating frequency: 25MHz
Operating voltage: 3.6-5V
Memory: 128KB
Cost: $8.06
SPI Communication
40 GPIO Pins
Operating frequency: 16MHz
Operating voltage: 3.6V
Memory: 16KB
Cost: $1.00
SPI Communication
14 GPIO Pins

## Slide 29: Operation: PWM
Output 1kHz square wave, 0.1% duty cycle
Timer A- SMCLK, Up Mode
Output to dual Schmitt-Trigger Inverter (create delayed TTL signal)
Signal fed into laser driver

## Slide 30: Operation: Communicating with Timing Module
Communicates via SPI
Sends configuration to TDC7200
Reads calculated distance
Executes haptic feedback

## Slide 31: Haptic Feedback

## Slide 32
Eccentric Rotating Mass (ERM) or Linear Resonant Actuator (LRA)?
-similar prices
ERM: Small unbalanced mass on DC motor
Pager or coin style?
-more benefit in smaller size for our project

## Slide 33: Power

## Slide 34
Output Voltage: 9V
Larger in Size
Requires 1 for operation
Output Voltage: 3V
Smaller in size
Requires at least 3

## Slide 35
PCB Design

## Slide 37
Notes: PCB - 80%
Testing - 60%

## Slide 38: Sponsors

## Slide 40: ISSUES
Schmitt Trigger
Code for Measurements
New iteration of Optical Module