## Slide 1: Smart Home Blackout Shades
Group 2
Stephen Fryer – CpE
Brian Mora – EE
Priyank Patel – CpE
John Rossi – EE
Sponsored by: Jetsons Living

## Slide 2: Motivation
Smart home appliances are becoming very popular
Voice Assistant Speakers (e.g. Amazon Echo) are becoming very popular
Window shades operation lends itself well to automation
Sponsor wants a cheaper and more feature packed alternative to current available products

## Slide 3: Goals and Objectives
Capable of operating completely wirelessly
Several modes of interaction
  Remote control, web app, motion sensor
Solar powered
Capable of interfacing with Amazon Echo

## Slide 4: Specifications
Parameter | Specification
Installation Time | 15 - 30 min
Response Time | 500 mS
Solar Panel Peak Output Power | 6 W
Motion Detection Range | > 3 m
Average Power Consumption | < 10 W
Dimensional Length | 2 ft - 5 ft
IR Receiver distance | > 10 m
Amazon Echo Skills | 3 skills

## Slide 5: Hardware Design

## Slide 6: Block Diagram
120 Volt AC
AC-DC
Converter
5 Volt
Regulator
PV Panels
3.3 Volt
Regulator
Battery
Battery Charger
MCU and WiFi
LED strip
Motion Detector
IR Remote
Source Select
Motor
Control Line
Power Line
Power
I/O

## Slide 7: Battery
3.7V Li-Ion
Large capacity is most important factor
Simple to charge
Built-in charge protection
Vendor | All-Battery
Part Number | 31908-1
Capacity | 10,400 mAh
Dimensions | 133.5 x 38 x19 mm

## Slide 8: PV Panel
Available 10W panel footprints were too obtrusive
Opted for 5 2W panels in parallel to achieve more desirable footprint
Vendor | SunnyTech
Part Number | B00HQXQOIQ
Max power | 2W
Max voltage | 6V
Max current | 330mA

## Slide 9: Power Board Schematic

## Slide 10: MCP73871
Battery charge management controller
Small footprint
Few external components are required for use
Over-temperature protection
Vendor | Digikey
Part number | MCP73871-2AAI/ML-ND
Charge current max | 1.1A
Battery pack voltage | 4.2V

## Slide 11: Power Board

## Slide 12: Power Board

## Slide 13: ESP-12S
System on Chip solution for WiFi and Microcontroller
Large Memory (4 MB)
Compatibility with Arduino
Inexpensive
Small
Vendor | Adafruit
Price | $6.95
Memory | 4 MB
I/O | 10

## Slide 14: Control Board Schematic

## Slide 15: Control Board

## Slide 16: Control Board

## Slide 17: PIR Board Schematic

## Slide 18: PIR Board

## Slide 19: PIR Board

## Slide 20: IR Remote Control Schematic

## Slide 21: IR Remote Control

## Slide 22: IR Remote Control

## Slide 23: Software Design

## Slide 24: Web Application vs. Native Application
Native Apps | Web Application
Native Apps are built for particular platforms so that apps can take advantage of its operating system and device–specific hardware | Web Applications use web browsers and web technology
Native Apps offer great look and feel as well as also provides higher speed over web applications | Web Applications and responsive websites both satisfy the definition of mobile-friendly
Cost of maintenance of apps is higher. Also, developers usually have to create multiple apps on different platforms for every user | Hard to accommodate every user when many times users are using different web browsers
Both approaches requires both time and money for good products | 

## Slide 25: Top-level Software Design
Server Programming
Server will accept request from (1 and 2)
Server will process request
Server then communicates with PCB
PCB/MCU
PCB waits for input or command from either remote or server
Once input received, perform appropriate action
1) Web Application Functionality
2) Amazon Echo Functionality
3) Physical Remote Control
Our Web application and Amazon Echo will share or communicate directly with our web server to send/ Receive HTTP Requests.
Our Web Server then will accept the request. As well as process the appropriate the request and calls the appropriate Arduino method.
At this stage, appropriate Arduino methods will execute appropriate actions. (i.e. Roll-up Shades, Set Brightness, Change LED Color.)

## Slide 26: Web Application Core Modules
Remote Utility
  Users are able to move shades up/down
Battery Indicator
  Users are able to view real-time battery status
LEDs
  Users can set preferred color
  Users can set preferred brightness
Settings
  Set Wake/bed time
  Add/modify WiFi connection
Web App
Remote Utility
Settings
LEDs
Battery Indicator
Display Battery Level
Up
Down
LED Color Change
LED Brightness Change
Wake
(Open)
Bedtime
(Close)
WiFi Settings

## Slide 27: Software Tools
Model-View-Controller is a software architectural pattern commonly used for developing user interfaces that divides applications into three interconnected parts.
Bootstrap 3 libraries will be used to make the web application a responsive mobile-first website.
Jquery is a JavaScript library, and its syntax is designed to easily create animations and more.

## Slide 28: Class Diagram

## Slide 29: Web Application Progress

## Slide 30: Web Application Mockups

## Slide 31: Amazon Echo Integration
Our product will also include integration with Amazon Echo.
Users are able to verbally communicate with our shades through Amazon Echo Virtual Assistant
Our hope is to create at least three commands that are coherent with our web application
“Alexa, roll up blinds.”
“Alexa, change LEDs to red.”
“Alexa, lift blinds at 7:00am.”

## Slide 32: Wireless Communications
Bluetooth:
  Limited range
  Multiple pairings
  Not as fast
Zigbee/Z-Wave:
  Not necessary to communicate to other smart home devices
  Not as fast (about 0.25 Mbps)
Wi-Fi (IEEE 802.11 b/g/n):
  Fast
  Good range
  Convenient to implement

## Slide 33: Flowchart

## Slide 34: Function Diagram

## Slide 35: Wi-Fi API

## Slide 36: IDEs
Arduino IDE benefits:
  Default IDE
  Support
  Manage upload bit rate
Visual Studio + Visual Micro benefits:
  Debug
  Integrate with web app

## Slide 37: Useful Libraries
Adafruit_DotStar
  Controlling the LED
ESP8266WiFi
  Wi-Fi Scanning
DNSServer
  Helps implement a DNS server
ESP8266WebServer
  Serves the configuration portal
WiFiManager
  Use of the Captive Portal

## Slide 38: Administrative Content

## Slide 39: Work Distribution
 | Stephen Fryer (CpE) | Brian Mora (EE) | Priyank Patel (CpE) | John Rossi (EE)
Power |  | x |  | 
IR Remote |  | x |  | 
Control |  |  |  | x
Housing |  |  |  | x
Web Application |  |  | x | 
Amazon Echo |  |  | x | 
Microcontroller Programming | x |  |  | 

## Slide 40: Financing
Item | Total Cost
Reimbursable Budget | $500
Total R&D Costs to Date | $88
Total Parts Cost to Date | $188.20
Remaining in Budget | $223.80
Chart: 
| R&D | Total Parts to Date | Remaining Budget
Reimbursable Budget | 17.6 | 37.64 | 44.76

## Slide 41: Budget
Item | Supplier | Price | # Units | Total Cost | Item | Supplier | Price | # Units | Total Cost
Power System |  |  |  |  | Control Board |  |  |  | 
AC-DC Converter | Jameco | $13.70 | 1 | $13.70 | ESP-12s MCU | Adafruit | $6.95 | 1 | $6.95
3.7V Li-Ion Battery Pack | All-Battery | $43.99 | 1 | $43.99 | DRV8838 Motor Driver IC | Digikey | $1.35 | 1 | $1.35
PV Panels | Amazon | $7.99 | 5 | $39.95 | LED Strip | Adafruit | $29.95 | 1 | $29.95
LM1085 5V Regulator | Digikey | $2.16 | 1 | $2.16 | IR Reciever | Adafruit | $1.95 | 1 | $1.95
LM1085 3.3V Regulator | Digikey | $2.16 | 1 | $2.16 | Low Noise 12VDC Motor | Digikey | $47.90 | 1 | $47.90
MCP73871 Solar Charger IC | Digikey | $1.90 | 1 | $1.90 | Other External Components | Digikey | $6.12 |  | $6.12
Other External Components | Digikey | $17.71 |  | $17.71 | IR Remote |  |  |  | 
PIR Board |  |  |  |  | Trinket MCU | Digikey | $6.95 | 1 | $6.95
NCS36000 PIR Driver IC | Mouser | $0.86 | 1 | $0.86 | IR LED | Digikey | $0.44 | 1 | $0.44
PIR Sensor RE200B-P | Mouser | $1.25 | 1 | $1.25 | Batteries/Holders (CR2032) | Sparkfun | $1.24 | 2 | $2.48
Fresnel Lens | Fresnel Factory | $1.55 | 1 | $1.55 | Other External Components | Digikey | $1.30 |  | $1.30
Other External Components | Digikey | $11.26 |  | $11.26 | All 4 PCB's | PCBWay | $55.00 |  | $55.00
 |  |  |  |  | Total |  |  |  | $296.88

## Slide 42: Progress
Chart: Progress
| Overall | Hardware Testing | Software Testing | Prototype | Parts Acquisition | PCB Development | Research
Progress | 55 | 30 | 40 | 40 | 60 | 70 | 95

## Slide 43: Issues
Uncertain if motor will be able to move the shades assembly at a desirable speed at 3.3V

## Slide 44: Questions?