## Slide 1: 3D Environment Modeler
Daniel Batista
Aaron Coville
Matthew Cummings
Sean Huskey

## Slide 2: Motivation
No current cheap, room-proximity depth imaging
LIDAR is more accurate than ultrasound
  Ultrasound diverges quickly producing unwanted results
  Collimated light allows for better resolution
Has applications in
  Robot Vision
  Virtual/Augmented reality
  Area survey

## Slide 3: Overall Project Goals
Render a 3D point cloud of the surroundings relative to the device
Wireless data transfer to a computer for rendering
Not too big or heavy
Fast enough for one scan to happen in a reasonable timeframe
Good resolution

## Slide 4: Project Specifications
Metric | Value
Size | 1 ft3
Weight | <10 lb
Scan Speed | <1 hour per total scan
Axial Resolution | ±1.5 cm
Voltage | 12 V
Range | 10 m
Azimuth | 360°
Elevation | 90°
Final Cost | ≤ $400

## Slide 5
Device Block Diagram
Laser System
Detection System
Power
MCU
Wireless Communication
Through-Hole Mirror
Processing unit
Timing
3D Image
360° Stepper Motor
180° Stepper Motor
Mirror
Target

## Slide 6: Sections
Distance Measurement
Mechanical/Electronic Integration
Embedded System
PC Interface
Administrative Material

## Slide 7: Optical Triangulation
Bad resolution at far range
More complicated imaging
Laser
Lens
Sensor
Object 1 & 2 (close to laser)
Object 1 & 2 (far from laser)

## Slide 8: Continuous-Wave Intensity Modulation Time-of-Flight
Suffers from problems with phase-wrapping
Requires high-speed electronics
Outgoing Signal
Returning Signal
Laser
Sensor

## Slide 9: Pulse Time-of-Flight
Send out a laser pulse, the time it takes to get back can be used to determine distance travelled
Requires high-speed electronics

## Slide 10: OSLRF-01
Uses pulsed TOF, but with sequential-equivalent-time-sampling (SETS) to allow for slow-speed LIDAR

## Slide 11: Sequential-Equivalent-Time-Sampling (SETS)
Allows signals to be “slowed down” to speeds that cheaper electronics can process
Relies on taking individual samples of several pulses over a period of time and stitching them together.
Normal sampling:
Original Signal:
Reconstructed Signal:
= sample

## Slide 12: Sequential-Equivalent-Time-Sampling (SETS)
Allows signals to be “slowed down” to speeds that cheaper electronics can process
Relies on taking individual samples of each signal over a period of time and stitching them together.
SETS sampling:
Reconstructed Signal:
Original Signal:
= sample

## Slide 13: Sequential-Equivalent-Time-Sampling (SETS)

## Slide 14: Sections
Distance Measurement
Mechanical/Electronic Integration
Embedded System
PC Interface
Administrative Material

## Slide 15: Optical and Mechanical Design
PCB
Detector
Laser
Aspherical lens
Focusing lens
Mirror
Slip-ring Rotation
Top-down View
Stepper Motor Rotation
Stepper motor
Gear
Slip Ring
Diffusive Surface
Stepper motor
Mirror
Gear
Stepper Motor Rotation
Cylindrical lens
Through-Hole Mirror

## Slide 16: Limitations
Parallax is an issue and will only see one point
Beam splitter
  Original idea but, introduced a large loss being 50/50
Through-hole mirror
  Design implemented with highest return signal but still introduce loss
Slip ring limits return signal irradiance
Beam collimation
  A smaller beam may return more irradiance

## Slide 17: Range Finder Electrical Schematic

## Slide 18: Connections, Power, Laser Driver

## Slide 19: Laser Time Expander

## Slide 20: Receiver Time Expander and Amplifier

## Slide 21: Master Timer

## Slide 22: Range Finder PCB

## Slide 23: Laser Diodes
System chosen was in the IR spectrum
  Reduction of noise
SPL PL 90 was chosen since it is manufactured to be pulsed
  Previously prototyped lasers failed to generate a clean pulse
SPL PL 90
 | HLM6544FM | Laser Dot Diode Module w/ Driver | SPL PL90
Average Power | 50 mW | 30 mW | 0.5 mW
Peak Power | - | - | 25 W
Rise Time | - | - | 1 ns
Fall Time | - | - | 1 ns
Wavelength | 660 nm | 850 nm | 905 nm
Cost | $33.41 | $25.89 | $20.47

## Slide 24: Detectors
Chose SFH 2701 as detector
Detector has 0.4 A/W sensitivity at 905 nm
  Rise/Fall time of 2ns
SFH 2701 allows pulse to be detected fast enough
  Very quick rise time for $1
  Previously used FDS100 detector for $15 that broke
SFH 2701
 | PDV-P9007 | FDS100 | PD15-22C/TR8 | SFH 2701
Wavelength Range | 400-700 nm | 350 – 1100 nm | 400-1100 nm | 400-1050
Peak Wavelength | 570 nm | 980 nm | 940 nm | 820 nm
Responsivity | - | 0.65 A/W | - | 0.5 A/W
Active Area | - | 13 mm2 | - | 0.36 mm2
Rise Time | 60 ms | 10 ns | 10 ns | 2 ns
Fall Time | 25 ms | 10 ns | 10 ns | 2 ns
Dark Current | - | 1 nA | 10 nA | 0.05 nA
Cost | $1.78 | $14.08 | $0.50 | $1.04

## Slide 25: Sections
Distance Measurement
Mechanical/Electronic Integration
Embedded System
PC Interface
Administrative Material

## Slide 26
Responsibilities of the Control PCB
Regulate the power supply to all components and laser system
Sample an analog signal at 32 kHz
Process the samples to calculate a distance
Communicate the calculated distance over Bluetooth
Direct the laser

## Slide 27: Control Schematic

## Slide 28: Control PCB

## Slide 29
Control PCB Components and Design

## Slide 30
Directing the Laser
Laser System
MCU
3.3 v
Reg
Bluetooth
Module
Laser
Control
Switch
12v
Supply
Stepper Drivers
Stepper 360
Stepper 180

## Slide 31
Servos vs Steppers
Servos can’t provide enough precision and control
Swapped servos for NEMA 17 and NEMA 8 stepper motors controlled by EZ Stepper Driver
Stepper Driver provides excellent current regulation and power saving modes

## Slide 32
Sending the Data

## Slide 33
HC-05 Bluetooth Module
Standard Bluetooth protocol
Many online example projects to reference
Pybluez used during development. C++ with Bluez for the final application

## Slide 34
Choosing a Microcontroller

## Slide 35
ATMEGA328P
Just enough I/O Pins
Only 2 interrupt pins required
Cheap and available
Plentiful Documentation
16 MHz to process data
32 KHz sampling rate required
  ADC can be run at a rate of 12 uSec given the fastest configuration

## Slide 36
Addressing Control PCB issues
Handling an unreliable user or wireless connection
  Solved by implementing the Watchdog timer at its longest timeout interval
Issue of losing samples during scanning
  Solved by setting the ADC to one of its fastest settings and calculating distances using signal maximums

## Slide 37: Sections
Distance Measurement
Mechanical/Electronic Integration
Embedded System
PC Interface
Administrative Material

## Slide 38: PC Interface Goals
Provide a sensible, usable interface for human operators to interact with
Establish a wireless connection to embedded system for various purposes
Provide a visual output for laser data

## Slide 39: PC Interface Design Diagram

## Slide 40: PC App Overview
PC app was designed in the Qt C++ framework
Provides native implementations for UI outlines, timing, debugging, and event handling
Additional feature implementations such as Bluetooth functionality and OpenGL rendering present less dependencies due to the C++ base

## Slide 41: PC App – Simulating

## Slide 42: PC App – Talking to Bluetooth

## Slide 43: Networking with Bluetooth
Done through a socket-based networking script embedded directly into the application
Module acts as a server while the laptop acts as the client
In order to communicate, laptop sends commands and requests messages from the module
To the embedded system, Bluetooth is just an I/O destination

## Slide 44: Network Diagram

## Slide 45: Decoding The Data
Message from Bluetooth must first be confirmed as valid before being converted into 3D number
Done by moving through message one character at a time to find a matching format, accounting for partial messages, duplicate messages, and offset messages

## Slide 46: Rendering The Data
Every primitive is rendered using glBegin() and glEnd(), data points are cubes made of GL_QUADS and axes are made of GL_LINES
glBegin and glEnd are used over vertex arrays and buffer objects
  The former is easy to use and the others are more useful in apps which require high graphical performance

## Slide 47: Sections
Distance Measurement
Mechanical/Electronic Integration
Embedded System
PC Interface
Administrative Material

## Slide 48: Budget
Total Spent to Date | Unit cost (In-House) | Unit cost (Out-of-House)
$1,185.05 | $1,531.44 | $432.39
Expenditure | Cost
Electronic Components | $282.37
Mechanical Components | $172.74
Prototyping Parts | $408.28
PCB Boards | $165.00
Shipping Costs | $156.66
Optics (In-House) | $1143.00
Optics (Out-of-House) | $103.13

## Slide 49: Electrical Components
Component | Number Bought in total | Number Used in final design | Unit Price | Total price we paid
8V linear regulator | 10 | 1 | 0.407 | $4.07
3.3V linear regulator | 10 | 1 | 0.382 | $3.82
3.3 V Buck Regulator (DRC) | 5 | 1 | 4.03 | Sample
3.3 V Buck Regulator (DGS) | 5 | 0 | 4.16 | Sample
Laser Driver | 8 | 1 | 1.02 | $8.16
Pulsed Laser Diode | 1 | 1 | 20.47 | $20.47
Laser Diode (NIU) | 2 | 0 | 25.89 | $51.78
Laser Switch | 4 | 1 | 0.69 | $2.76
Diode | 10 | 1 | 0.309 | $3.09
Transimpedance Amplifier | 4 | 1 | 5.84 | $23.36
Sampling Switch | 5 | 1 | 0.42 | $2.10
Sampling Switch | 5 | 1 | 0.32 | Sample
Duel Sampling Switch | 5 | 1 | 0.68 | Sample
Op-Amp Receiver | 5 | 1 | 0.42 | $2.10
Op-Amp Laser | 5 | 1 | 0.61 | $3.05
Photodiode | 10 | 1 | 0.806 | $8.06
Si Photodiode (NIU) | 2 | 0 | 13.8 | $27.60
12 Stage Counter | 5 | 1 | 0.63 | $3.15
D-Flip-Flop Q# (TI) | 5 | 0 | 0.18 | Sample
D-Flip-Flop Q# | 20 | 3 | 0.295 | $5.90
Inverter Gate | 5 | 2 | 0.36 | $1.80
Inverter Gate | 5 | 2 | 0.21 | Sample
D-Flip-Flop Q | 10 | 2 | 0.295 | $2.95
Dual Schmitt-Trigger Buffer | 5 | 1 | 0.42 | Sample
16.369 MHz Clock | 7 | 2 | 3.58 | $25.06
16 MHz Crystal | 4 | 1 | 0.25 | $1.00
Timing Chip (NIU) | 10 | 0 | 1.39 | Sample
Arduino Due Chip (NIU) | 2 | 0 | 9.68 | Sample
Arduino Uno Chip (NIU) | 5 | 0 | 2.2 | $11.00
Surface Mount Arduino Chips | 3 | 1 | 2.2 | $6.60
MOSFET Switch | 5 | 0 | 1.41 | Sample
NPN Transistors | 4 | 0 | 0.55 | $2.20
PNP Transistor | 5 | 2 | 0.21 | $1.05
N-Channel MOSFET | 3 | 1 | 0.36 | $1.08
Blue LED | 10 | 1 | 0.376 | $3.76
Red LED | 10 | 1 | 0.211 | $2.11
121 kΩ Resistor | 100 | 1 | 0.0056 | $0.56
100 kΩ Resistor | 100 | 4 | 0.0063 | $0.63
10 kΩ Resistor | 100 | 11 | 0.0063 | $0.63
1.8 kΩ Resistor | 100 | 4 | 0.0117 | $1.17
1 kΩ Resistor | 100 | 7 | 0.0063 | $0.63
4.7 kΩ Resistor | 100 | 1 | 0.0056 | $0.56
470 Ω Resistor | 100 | 1 | 0.0056 | $0.56
200 Ω Resistor | 100 | 4 | 0.0056 | $0.56
100 Ω Resistor | 100 | 1 | 0.0063 | $0.63
27 Ω Resistor | 100 | 1 | 0.0055 | $0.55
0.5 Ω Resistor | 4 | 1 | 0.45 | $1.80
22 µF Capacitor | 4 | 1 | 0.64 | $2.56
10 µF Capacitor | 12 | 3 | 0.215 | $2.58
1 µF Capacitor | 100 | 3 | 0.0688 | $6.88
1 µF Capacitor (alt.) | 4 | 1 | 0.45 | $1.80
0.1 µF Capacitor | 100 | 2 | 0.0446 | $4.46
100 nF Capacitor | 100 | 14 | 0.026 | $2.60
33 nF Capacitor | 10 | 1 | 0.046 | $0.46
22 nF Capacitor | 20 | 2 | 0.24 | $4.80
1 nF Capacitor | 100 | 8 | 0.0062 | $0.62
120 pF Capacitor | 100 | 1 | 0.0385 | $3.85
100 pF Capacitor | 100 | 3 | 0.0094 | $0.94
22pF Capacitor | 100 | 5 | 0.0223 | $2.23
150 µH Inductor | 4 | 1 | 0.87 | $3.48
Misc. Skycraft Elec. | 1 | 0 | 3.8 | $3.80
Slide Switch | 3 | 1 | 1.65 | $4.95
Component | Number Bought in total | Number Used in final design | Unit Price | Total price we paid
Total Spent to Date
$282.37

## Slide 50: Mechanical Components
Component | Number Bought in total | Number Used in final design | Unit Price | Total price we paid
Slip Ring | 1 | 1 | 42.3 | $42.30
360° Servo | 1 | 0 | 29 | $29.00
Nema 17 Stepper Motor | 1 | 1 | 13.99 | $13.99
Nema 17 Mounting Bracket | 1 | 1 | 6.5 | $6.50
180° Servo | 1 | 0 | 10.89 | $10.89
Nema 8 Stepper Motor | 1 | 1 | 24.95 | $24.95
T50 Gear | 3 | 1 | 5.32 | $15.96
T90 Gear | 3 | 1 | 7.72 | $23.16
Delrin Sheet 0.25'x12'x12' | 1 | 1 | 52.1 | Sample
T50 Gear Mount | 1 | 1 | 5.99 | $5.99
Total Spent to Date
$172.74

## Slide 51: Prototyping Parts
Component | Number Bought in total | Number Used in final design | Unit Price | Total price we paid
Total Spent to Date
$408.28
Male Pin Headers | 1 | 0 | 7.29 | $7.29
Female Pin Headers | 1 | 0 | 5.6 | $5.60
Flux Pen | 1 | 0 | 12.75 | $12.75
Solder Paste | 2 | 0 | 1.95 | $3.90
Solder Wick/Desoldering Pump | 1 | 0 | 7.99 | $7.99
MSSOP-14 Breakout Boards | 2 | 0 | 2.83 | $5.66
SC-70 Breakout Boards | 4 | 0 | 0.6 | $2.40
SC-70-6 Breakout Boards | 4 | 0 | 0.85 | $3.40
0.3 mm Solder | 1 | 0 | 9.99 | $9.99
Battery Holder | 8 | 1 | 0.6 | $4.80
Bluetooth BLE (NIU) | 1 | 0 | 7.99 | $7.99
Bluetooth | 5 | 1 | 9.99 | $49.95
Stepper Motor Driver Board | 3 | 1 | 9.99 | $29.97
IC Chip Socket Adaptors | 1 | 0 | 6.22 | $6.22
Protoboards | 1 | 0 | 9.99 | $9.99
Wires | 1 | 0 | 15.34 | $15.34
Switches (NIU) | 1 | 0 | 8.14 | $8.14
Arduino Due | 2 | 0 | 40.27 | $80.54
Batteries | 1 | 0.25 | 16 | $16.00
USBtinyISP | 1 | 0 | 12.95 | $12.95
Alligator Clips | 1 | 0 | 6.78 | $6.78
Multicolored Dupont Wire | 1 | 0 | 7.86 | $7.86
Nylon Screws/Spacers | 1 | 0 | 8.99 | $8.99
Superglue | 1 | 1 | 10.59 | $10.59
Giftcards | 2 | 0 | 25 | $50.00
Laser Heat Sink (NIU) | 1 | 0 | 6.69 | $6.69
Beamsplitting Cubes | 1 | 0 | 16.5 | $16.50

## Slide 52: Optical Components
Component | Number Bought in total | Number Used in final design | Unit Price | Total price we paid
Aspherical Lens (In-House) | 1 | 1 | 124 | Sample
Cylindrical Lens (In-House) | 1 | 1 | 459 | Sample
Focusing Lens (In-House) | 1 | 1 | 210 | Sample
Mirrors (In-House) | 2 | 2 | 71 | Sample
Beamsplitter (In-House) | 1 | 1 | 279 | Sample
Aspherical Lens (Out-House) | 0 | 0 | 11.23 | $0.00
Cylindrical Lens (Out-House) | 0 | 0 | 39.31 | $0.00
Focusing Lens (Out-House) | 0 | 0 | 17.99 | $0.00
Mirrors (Out-House) | 0 | 0 | 11.82 | $0.00
Beamsplitter (Out-House) | 0 | 0 | 22.78 | $0.00
In-House Cost | Out-of-House Cost
$1143.00 | $103.13

## Slide 53: Group Member Work
Name | Laser System | Detection System | Timing | Signal Analysis | Data Communication | Electrical Design | Mechanical Design | 3D Render | PC app
Daniel | ● | ● |  |  |  | ● | ● |  | 
Aaron |  | ○ | ● | ○ |  | ○ | ● |  | 
Matthew |  |  |  |  | ○ |  |  | ● | ●
Sean |  |  | ○ | ● | ● | ● | ● |  | 
Primary Contributor | ●
Secondary Contributor | ○

## Slide 54: Final Assembly
Range of 1 meter to 2 meters
  Due to power loss
Accurate within 10 cm in the axial direction
  Due to noise in return signal
  Added filters to reduce noise
Precision optics hindered ability to make chassis
Potential heating issue with stepper drivers
Application is unresponsive during device discovery

## Slide 55: Questions?

## Slide 56: Power Loss Due to Slip-ring

## Slide 57: Expected Axial-Resolution

## Slide 58
Programming the ATMega328P
Keeping the system responsive

## Slide 59
Dedicated Testing Circuit

## Slide 60
Qt – Signals and Slots

## Slide 61
Test Results