## Slide 1: Portable Plant Monitor System
Group 4
Alexander Meade: CpE
Syed Bukhari: EE
Nicholas Poidomani: CpE
Kareem Rahounji: EE

## Slide 2: Motivation
Create an environment to monitor plant growth and easily transport it
Provide researchers controlled environments to study plant life
Ability to move the environment without stress to the plant

## Slide 3: Goals and Objectives
Primary Goals
  Provide monitoring for plant growth
  Make the environment portable
  Switch between battery and AC power
Secondary Goals
  Low power consumption
  Exchangeable batteries
  Low cost assembly

## Slide 4: Specifications
Project Area | Design Specification
Temperature Monitoring | Be able to monitor temperatures from 20°C to 40°C
Humidity Monitoring | Be able to monitor up to 70% humidity
Battery Life | Run off battery for a minimum of 6 hours
Portability/Weight | Weight less than 20lbs
Portability/Size | Dimensions within 2ft x 2ft x 3ft dimension (LxWxH)

## Slide 5
House
of
Quality

## Slide 6: Block Diagram
* Means moved to stretch goal scope

## Slide 7: Class Diagram

## Slide 8: Electrical System

## Slide 9: Project Design

## Slide 10: Requirements for CPU
Need a CPU with ability to drive the sensors and communication
Still want to keep power consumption low
Desire for ease of integration of all parts
Potential to expand the scope of sensors used

## Slide 11: CPU Comparisons
 | Atmega 2560 | PIC24FJ128GA010
Architecture | 8 Bit | 16 Bit
Program Memory | 256kB | 128kB
SRAM | 8kB | 8Kb
Clock Speed | 16MHz | 32MHz
EEPROM | 4kB | 64kB
Number of Timers | 6 | 5
JTAG Support | Yes | No
GPIOs | 86 | 100

## Slide 12: MCU Decision
Choice - Atmega 2560
Reasons:
Ease of flashing code into the MCU
Better integration into our PCB due to documentation
Tradeoffs:
Lose of some modules
More limited CPU resources
Limited file handling

## Slide 13: Potential Environment Sensors
Many sensor options but we want the most relevant to growth
  Soil Moisture
  Humidity
  Temperature
  Light Level
  Soil Nutrient
  Accelerometer

## Slide 14: Sensor Type Selection
Soil Moisture
  Dry soil can cause malnutrition
Light
  Light is critical to all plant life
Temperature and Humidity
  Extreme conditions can be damaging to plant growth

## Slide 15: Soil Moisture Sensor SEN-13322
Low cost
High accuracy
Simple interfacing

## Slide 16: Everlight Sensor EAALST05RDMA0
Low cost photoelectric diode compared ambient light counterparts
Threshold levels allow distinction between low and optimal light levels

## Slide 17: Temp and Humidity DHT11
Ultralow cost sensor reads temperature and humidity
Functions wide range of temperatures
Sampling rate of 1HZ
Low power use

## Slide 18: Wireless Technology Comparison
 | Wi-Fi | Zig-Bee | Bluetooth | GSM
Range | Up to 100m | 10m-100m | <100m | Ranges from over 100m to 35km
Cost | ~ $10-$30 | ~ $15-$20 | ~$10-$20 | Most Expensive ~ $150
Power Consumption | High Power Draw | Lowest Power Draw | Low Power Draw | Highest Power Draw
Data Transfer | Up to 55Mbps | 20-250Kbps | 1-3Mbps | 40-50Kbps

## Slide 19: Wireless Module Choice
  SH-HC-08
Transportation protocol chosen was Bluetooth Low Energy
BLE moderate transfer rate, good broadcast distance, and very low energy consumption
SH-HC-08 utilizes UART for communication

## Slide 20: Data Storage
We want the ability to store data locally in case communications are down
Challenged faced is ballooning data size from readings
Solutions options considered EEPROM, NAND flash memory, and external SD card slot

## Slide 21: Implementation SD Slot
  Allows for large storage space for sensors readings
  Ease of integration into the existing design
  Allows for access of data in case of total PCB failure

## Slide 22: Supporting Software
Identify trends that correlate plant growth with environment readings
Organize our data into graphical representations
Ability to identify inconsistencies in the environment
Prefer cross platform tools

## Slide 23: Project Implementation

## Slide 24: DC Power Supply
Keep the PCB running under all conditions
Is powered by an AC to DC adapter
Operational voltage range 5V-12V
Need a method to continue use after disconnecting from AC

## Slide 25: Battery Back-up Circuit
9V battery is the back-up power supply
Allows the circuit to keep running after it is unplugged
Battery take-over features:
  Automated switching
  Easy battery replacement
  Portability
  Long running times

## Slide 26: Closed Switch (Power Supply)

## Slide 27: Open Switch (Battery Backup)

## Slide 28: Enclosure Design

## Slide 29: Enclosure

## Slide 30: PCB Schematics

## Slide 31: Full PCB

## Slide 32: PCB Power Section

## Slide 33: PCB Reset & Stepdown

## Slide 34: PCB MCU, EMU, and Resonator

## Slide 35: PCB Grounded Top Layer

## Slide 36: Administrative Content

## Slide 37: Work Distribution
Name/Section | Kareem | Nick | Alec | Syed
Sensor Programming |  | Secondary | Primary | 
Wireless Communication |  | Primary | Secondary | 
PCB Design | Secondary |  |  | Primary
Power | Primary |  |  | Secondary
Data Logger |  | Secondary | Primary | 
Enclosure Design | Primary |  | Secondary | 

## Slide 38
Chart: Project Progress
| Research | Design | Prototyping | Assembly | Total
Series 1 | 90 | 63 | 45 | 30 | 57

## Slide 39: IEC 60529 Standard
Degrees of protection against water ingress
Protection level at minimum is 2 (Protected against vertically falling water drops when enclosure tilted up to 15°) with a maximum level of 4 (Protected against splashing water )
Degrees of access to hazardous Parts
The level of protection provided for hazardous part protection is a 2, protection of hazardous parts from a finger or a solid foreign objects ≤ 12.5 mm diameter

## Slide 40
Project Projected Budget |  |  |  | 
Expense | Estimated | Actual | Difference ($) | Difference (%)
PCB | $ 50.00 | $ 40.00 | $ 10.00 | 20%
CPU | $ 25.00 | $ 10.00 | $ 15.00 | 60%
Moisture Sensor | $ 80.00 | $ 15.00 | $ 65.00 | 81%
Light Sensor | $ 30.00 | $ 8.00 | $ 22.00 | 73%
Temp/Hum Sensor | $ 30.00 | $ 33.00 | $ (3.00) | -10%
Light Source | $ 40.00 | $ 15.50 | $ 24.50 | 61%
LCD Display | $ 30.00 | $ 20.00 | $ 10.00 | 33%
Enclosure | $ 70.00 | $ 35.00 | $ 35.00) | 50%
Dev Kits | $ 40.00 | $ 34.00 | $ 6.00 | 15%
Batteries | $ 20.00 | $ 14.00 | $ 6.00 | 30%
SS Relay | $ 10.00 | $ 6.00 | $ 4.00 | 40%
Bluetooth Module | $ 20.00 | $ 8.75 | $ 11.25 | 56%
SD Mount | $ 15.00 | $ 9.00 | $ 6.00 | 40%
Unplanned Parts | N.A | $ 45.00 | $ (45.00) | 
Extra |  |  | $ - | 
Total Expenses | $ 460.00 | $ 293.25 | $ 166.75 | 36.25%

## Slide 41
Bill of Material as of 1/22/19 |  |  |  |  |  |  | 
Quantity | Part | Unit Price | Line Total | Quantity | Part | Unit Price | Line Total
2 | 2.1mm Barrel Jack | 1.625 | 3.25 | 2 | 16MHz Resonator | 0.315 | 0.63
2 | 47uF Cap | 1.255 | 2.51 | 2 | 47uF Cap | 1.435 | 2.87
1 | 1A Schottky Diode | 0.31 | 0.31 | 3 | LDO Regulator | 0.4967 | 1.49
1 | 2A Schottky Diode | 0.43 | 0.43 | 10 | 1A Switching Diode | 0.076 | 0.76
3 | 1uF Cap | 0.25 | 0.75 | 1 | MCU ATMEGA2560 | 10.65 | 10.65
10 | .1uF Cap | 0.005 | 0.05 | 1 | SD Card Slot | 6.59 | 6.59
10 | 1uF Cap | 0.105 | 1.05 | 1 | Bluetooth Module | 7.99 | 7.99
4 | LDO Regulator | 0.4025 | 1.61 | 1 | DHT11 Sensor | 5 | 5
10 | 150mA Switch Diode | 0.125 | 0.5 | 1 | SEN-13322 | 5.95 | 5.95
10 | Res Film Array 10k | 0.014 | 0.14 | 1 | EAALST05RDMA0 | 0.6 | 0.6
4 | 1A Schottky Diode | 0.3925 | 1.57 |  | Total | 44.4017 | 55.47
2 | 16MHz Resonator | 0.385 | 0.77 |  |  |  | 

## Slide 42: Issues
PIC24 VS Atmega2560 for PCB
Originally enclosure was going to be 3-D printed but due to fabrication constraints we have to switch to underlayment wood
Deciding which goals fit with our projects paradigms and which had to be pushed to stretch goals
Integration of humidity and temperature readings for accurate timing and integration into system

## Slide 43: To Complete
Fabricate the environmental enclosure
Write MCU logic for SD card slot and Bluetooth
Application interface for accessing of data

## Slide 44: Questions?