## Slide 1: HeadsUP Optical Mobility Aid
Austin Singh (P.S.E.)
Hunter Tanchin (Cp.E.)
Alex Radulescu (E.E.)
Duc-Quy Nguyen (P.S.E.)
Notes: Quy

## Slide 2: The Problem
STOP

## Slide 3: Motivation and Goals
STOP
Notes: Extending Range of Awareness and Detect Mid Level Objects Chest or above waist high

## Slide 4: Specifications
Detection Distance | 0.5 meters ≤ D ≤ 2 meters
Operational Lifetime | 24 Hours
Processing Speed | 250 ms
Distance Resolution | 20 cm
Notes: Reflex Time

## Slide 5: Constraints & Standards
Size | 9 cm x 15 cm Area
Weight | < 2.5 kg
Eye-Safe | MPE = 100 ms 𝜆 = 905 nm Pout = 3.2 mW
Laser Eye Safety Standard IEC 60825
Notes: Austin, this graphic will be referenced later on component selection of laser diode, Talk higher up on y axis the safer it goes

## Slide 6: Working Principle

## Slide 7: Laser Triangulation Principle
Notes: E = 12 cm, F = 1.5 cm, G = 0-2.9 cm, thus giving a minimum D of 40 cm, maximum D theoretically infinity. Depth of Field and Depth of Focus affect our viewing distance though, as well as abberations.

## Slide 8: Hardware

## Slide 9: Laser Transmitter
λ = 904 nm
Pout = 10 mW
Thorlabs L904P010 Laser Diode
MPE
Notes: Explain RGB sensitivity of eye, cost aspect, focusing off the retina, higher MPE is better, all for Class I

## Slide 10: Collimation Optics

## Slide 11: Imaging System
S = 32 V/lx*s
29 mm Active Area
Toshiba TCD1304DG Linear CCD Image Sensor
Thorlabs FL905-10 Bandpass Filter
Notes: Field of View, Depth of Field, Bandpass Filter

## Slide 12: Microcontroller - MSP430F6459
Up to 32 MHz
12-bit Analog-to-Digital Converters
Direct Memory Access Channels
Low-Power Modes
512 kb FLASH
66 kb RAM
Past MSP430 Experience
Notes: Hunter

## Slide 13: Computational Logic
IMAGE SENSOR
Notes: Intensity values let us know where the beam is spatially --> using spatial information to let you know how far away something is, correlate distance

## Slide 14: Software Flow

## Slide 15: Power
Batteries
  Two 3.7V and 2700mAh Li-Ion batteries in parallel
Voltage regulation
  3.7V to 3.3V step-down
  3.7V to 5V step-up
Notes: Alex, talk battery first then talka bout step up and step down voltagges

## Slide 16: Laser Diode Driver (LM317)
Notes: Include diagrams for LM317 and TCD1304DG

## Slide 17: Image Sensor (Toshiba TCD1304DG)

## Slide 18: PCB

## Slide 19: Overall Block Diagram
Notes: Block Diagram

## Slide 20: Bill of Materials
Item # | Name | Manufacturer | Price | Quantity | Total
1 | Laser Diode (L904P010) | Thorlabs | $26.01 | 1 | $26.01
2 | Bandpass Filter (FL905-10) | Thorlabs | $95.88 | 1 | $95.88
3 | Cylindrical Lens | Thorlabs | $56.10 | 1 | $56.10
4 | Plano-Convex Lens (LA1540-B-ML) | Thorlabs | $38.16 | 1 | $38.16
5 | MSP430F6459 | TI | $43.95 | 1 | $43.95
6 | DRV2605 haptics driver | TI | $11.65 | 1 | $11.65
7 | 1304DG Image Sensor | Toshiba | $5.10 | 1 | $5.10
8 | 74HC04D Hex Inverter | Arrow | $0.65 | 1 | $0.65
9 | 2SA1015 Transistor | Arrow | $0.65 | 1 | $0.65
10 | PCB | 4PCB | $33 | 1 | $33
 |  |  |  | Final Price | $311.15
Notes: Show BOM with team
Quy
Estimated vs Actual
Final Model Price

## Slide 21: Administrative Content
Notes: Show Charts with team what category want to add

## Slide 22: What’s Next?
Design/Fabricate Test Housing
Integrate Haptic Feedback
Iterations of the PCB

## Slide 23: Any Questions?