## Slide 1: PEISS Power-Efficient Infrared Security System
Carlos Granja Angulo - Photonics Science Engineering
Matthew Berasa - Computer Engineering
Andrew Forde - Electrical Engineering
Andrew Topliffe - Electrical Engineering
Group 12 Final Demo Spring 2025
Notes: Carlos

## Slide 2: Overall function of the project
Our project is a power-efficient infrared security system that combines photonic technology with traditional security systems to create something more energy efficient and affordable. We're solving the big problems with regular security systems - they use too much power and cost way too much, especially when you want advanced features that need lots of computing power.
We're designing a system that's not just energy efficient but also cost-effective by using photonics. It's perfect for people who want privacy in their offices, classrooms, bedrooms, or other indoor spaces.
The system is simple to use - you control everything through a mobile app where you can arm or disarm it. When someone trips the system, it sets off an alarm at the location, takes pictures of the intruders, and sends you notifications right away. We've also included backup battery power so it keeps working even if the electricity goes out.
Notes: Carlos

## Slide 3: Engineering Requirements and Specifications
Feature | Requirement
Max Detection range | At least 2.5 ft
Object detection accuracy | Accuracy of at least 80%
Response Time | Less than 10 seconds
Power consumption | Less than 5W
Backup Power | Rechargeable Batteries
Mobile Compatibility | iOS and Android
Component | Parameter | Specification
LED | Field of View | Minimum 40°
Wavelength range | 780 - 1000 nm
Photodiode | Field of View | Minimum 40°
Wavelength range | 780- 1000 nm
Filter | Center wavelength | 780 - 1000 nm
Notes: Andrew T