## Slide 1: Smart Safe
Final PRESentation
GROUP 21
Notes: Speaker: Eric
DONE

## Slide 2: Meet the Team
Lakshmi Katravulapalli
Computer Engineering
Nick Brandenburg
Computer Engineering
Alexis Mui
Electrical Engineering
Eric Terry
Electrical Engineering
Alexis (EE)
Notes: Speaker: Everyone
DONE
Our team members are eric

## Slide 3: Motivation and background
Ensuring the security of personal belongings is essential in today’s world
A reliable, secure, and portable storage for valuables
Real-time alerts for unauthorized access attempts or tampering
Create keyless, instant access
Provide awareness of its security status
Customize additional access levels and monitor usage remotely through email notifications
Alexis (EE)
Notes: Speaker: Alexis
-Customize? DONE

## Slide 4: Basic Goals & Objectives
Basic Goals:
Unlock with correct passcode and remained locked with an incorrect passcode
Unlock with a registered fingerprint and remained locked with an unregistered fingerprint
Display readable user prompts during the safe’s operation
Send email notifications to inform the user when the safe is being accessed
Alexis (EE)
Notes: DONE

## Slide 5: Advanced goals & Objectives
Advanced Goals:
Register email to receive notifications on a web interface
Incorporate a battery backup system
Implement motion sensor and notify user
"Lockdown Mode" if four incorrect passcode attempts are made
Stretch Goals:
Tamper detection
Temperature/humidity sensor
User will receive an email in case they forget to close the safe door
Alexis (EE)
Notes: DONE

## Slide 6: Engineering Requirements & Specifications
Specifications | 
*Fingerprint access accuracy | Unlocks safe 90% of the time (unless it’s an unregistered fingerprint)
Motion Sensor distance | Reads an input from >= 6 inches
Status LED accuracy | Is correct 90% of the time
*Email notification duration | Received in under 1 minute 95% of the time
*Lockdown Mode activation | Activates after 4 passcode attempts
Self-Lock Time Limit | Locks after 30 seconds
Safe Size | 18” x 10” x 10”
*These will be our 3 demonstratable specifications
Nick (CpE)
Notes: Speaker: Nick DONE

## Slide 7: Hardware Block Diagram
Eric(EE)
Notes: Speaker: Eric
DONE

## Slide 8: Software BLOCK Diagram/ Flowchart
Nick (CpE)
Notes: Speaker: Nick
Add door sensor or anything else?

## Slide 9: Keypad block Diagram/ Flowchart
Nick (CpE)
Notes: Speaker: Nick
Add door sensor or anything else?

## Slide 10: Final SAFE DESIGN
Nick (CpE)
Notes: Nick
-removed whiteboard pic
-add final pic of physical safe?

## Slide 11: Microcontroller/Microprocessor selection
Final Decision: ESP-WROOM-32
Product | Memory | Processor Speed | GPIO Pins | Operating Voltage | Cost
Arduino Mega 2560 Rev 3 | 256KB(Flash) | 16MHz | 70 | 5V | $48.40
Raspberry Pi 3 Model B+ | 2GB(RAM) | 1.5GHz | 40 | 5V | $45.00
ESP-WROOM-32 | Max of 16MB(Flash) | 2.4GHz | 32 | 3.3V | $9.99(3 pk)
Eric(EE)
Notes: Speaker: Eric
DONE

## Slide 12: Keypad Selection
For our keypad selection we chose the Membrane Keypad because it is user friendly, easy to maintain, and designed to take up minimal space and weight
Final Decision: NEXTION 16 Keys Matrix Keypad 4x4 Membrane Keyboard Module
Type | Technology | Advantages | Disadvantages | Suitability for Safe Design
Membrane | Flexible layers of membranes that are connected | Easier to clean and maintain Resistant to dirt or water Slim profile and lightweight | Limited tactile feedback Less durability for frequent pushing | More suitable for compact design due to slim size Best for safes requiring minimal space or weight
Mechanical | Physical push buttons with tactile feedback | Stronger and withstanding Easy to interface with Debouncing feature | Heavier weight Prone to dust or water | Suitable for robust designs Good for safes requiring long-term durability and user feedback
Touch Sensor | Keys that senses physical human touch | Less likely to physical damage Cannot be damaged by dust or liquid Modern design | Sensitive touch factors Requires cleaning Fewer available products | Ideal for sleek, modern safes Lightweight and tech-forward option, though less common
Lakshmi (CpE)
Notes: Speaker: Lakshmi
DONE

## Slide 13: Fingerprint Sensor Selection
Type | Technology | Advantages | Disadvantages | Suitability for Safe Design
Capacitive | Uses pressure of the fingerprint | Difficult to replicate Fast speed High accuracy Robust | High cost Susceptible to electrostatic discharge damages Sensitive to wet or very dry fingertips | More suitable for compact design due to slim size Suitable for robust designs
Optical | Uses light of the fingerprint | Cost effective Fast speed Easy maintenance Easily available in the market Work well with variety of skin conditions | Susceptible to hacking Not as robust than others Sensitive to dry, oily, or wet fingertips | More suitable for variety of skin conditions like scars Easy integration Fast processing time
Thermal | Uses the heat pattern of the fingerprint | Difficult to replicate Functions effectively when fingertip is dry, oily, or wet Reliable | High cost Requires more maintenance than others Slow speed Sensitive to significant temperature changes in the environment | More suitable for designs with no size constrictions Suitable for varying fingertips in cleanliness, moisture or dryness levels
For our fingerprint scanner selection, we chose the optical fingerprint sensor because of its reliability, fast accuracy, and suitability for a variety of skin conditions like scars
Final Decision: Hangzhou Grow Tech’s GROW R307 Fingerprint Module
Alexis (EE)
Notes: Speaker: Alexis
DONE

## Slide 14: Lock Mechanism Selection
Type | Technology | Advantages | Disadvantages | Suitability for Safe Design
In-Linear Actuator | Converts rotational motion into linear motion using an AC or DC motor | Precise movement Robust Easy integration | Slow speed Complicated integration High levels of noise Expensive Heavy | More suitable for circuit due to precise movement Robust
Stepper Motor | Converts electricity pulses into rotation motion by a fixed number of degrees | Precise movement Cost effective | Chance of slipping Chance of missing steps High levels of noise Susceptible to overheating High current consumption Heavy | More suitable for circuit due to precise movement Cost effective
Solenoid | Converts electrical current into linear motion using electromagnetism | Low power consumption Reliable Fast speed Cost-effective Easy integrations | Limited stroke strength Susceptible to overheating High current consumption | More suitable for circuit due to light weight Low power consumption Cost effective
For our lock mechanism selection, we chose the solenoid due to its quicker response time and low power consumption while provding the same benefits as the other two
Final Decision: Uxcell’s 1240L-12E07
Alexis (EE)
Notes: Speaker: Alexis
DONE

## Slide 15: Motion Sensor Selection
Product | Voltage | Operating Current | Number of pins | Serial Communication | Cost
HC-SR04 | 5V | < 5mA | 4 | I2C | $2.00
URM37 V5 | 3.3-5V | 20mA | 9 | UART | $13.90
TCT-40 | 3.3V | N/A | 4 | I2C | $9.95
Final Decision: HC-SR04
Nick (CpE)
Notes: Nick
DONE

## Slide 16: Display Selection
Product | Voltage | Display Size | Number of pins | Serial Communication | Cost
LCD 1602 Module | 5V | 2 inches | 4 | I2C | $2.00
ESP32 Touchscreen 2.8inch TFT LCD Display | 3.3-5V | 2.8 inches | 4/7 | SPI/UART | $20-$35
HiLetgo 2.42” SSD1309 | 3.3V | 2.42 inches | 4 | I2C | $9.95
Final Decision: HiLetgo 2.42” SSD1309
Nick (CpE)
Notes: Nick
DONE

## Slide 17: Magnetic door sensor
Product | Max Voltage | Max Current | Wire Length | Sensing Distance | Cost
Gebildet NO/NC Magnetic Switch | 100V | 0.5A | 30cm | 10mm – 20mm | $9.99
GAGALOR Heavy Duty Wired Alarm NC | 100V | 0.2A | 34cm | >=50mm | $15.99
VictorsHome Magnetic Reed Switch NC | 36V | 0.1A | 30cm | 10mm – 20mm | $8.99
Final Decision: Gebildet NO/NC Magnetic Switch
Nick (CpE)
Notes: Nick
DONE

## Slide 18: Battery Selection
Type | Technology | Advantages | Disadvantages | Suitability for Safe Design
Alkaline | Converts chemical energy into electrical energy through a chemical reaction | Stable voltage until depleted Light weight Cost-effective Easily available in the market | Short lifespan in storage and in use Lower energy capacity Temperature sensitive | More suitable for circuit due to light weight Easily available in the market
Lithium | Converts movement of lithium ions into electrical energy | Higher energy capacity Longer lifespan in storage and in use Wider temperature range Rechargeable option | Higher energy capacity Longer lifespan in storage and in use Wider temperature range Rechargeable option | More suitable for circuit due to longer lifespan in storage and in use Higher energy capacity
For our battery selection, we chose lithium batteries due to its higher energy capacity, longer lifespan both in storage or during use, and a wider temperature range compared to alkaline batteries
Final Decision: INVERCRIGIL Mini UPS Battery Backup
Alexis (EE)
Notes: Alexis
DONE

## Slide 19: Linear vs Switching regulators
Linear Regulators
Cheap & dependable
Low output voltage ripple & noise
High power dissipation
Simple in design(only need an input & output capacitor)
Switching Regulators
Expensive & versatile
Can act as buck/boost converters, have high noise
Low power dissipation
Complex in design
Final Decision: Linear Regulators
Eric(EE)
Notes: DONE

## Slide 20: Voltage Regulator Selection
Final Decision: AMS1117 & LM7805
Product | Dropout Voltage | Output Voltage Acc. | Output Current | Max Input Voltage | Cost
LD1117V33 | 1.1V | +/-1% | 800mA | 15V | $0.60
HT7333​ | 90mV | +/-3% | 250mA | 12V | $0.65
AMS1117 | 1.2V | 1.5% | 1A | 18V | $0.58
LM7805 | 2V | +/-2% | 1.5A | 35V | $0.33
Eric(EE)
Notes: Eric
DONE

## Slide 21: Relay Selection
Type | Technology | Advantages | Disadvantages | Suitability for Safe Design
Electromechanical | Uses electrical and mechanical mechanisms | Easy integration Good thermal management Separates power between two circuits High current and voltage ratings Easily available in the market Cost-effective | Slow speed Wear out over time because of mechanical mechanism Bulkier than solid state relays | More suitable for circuit due to power isolation between two circuits High current and voltage ratings Good thermal management Cost-effective
Solid State | Uses only electrical mechanisms | Fast speed Robust Compact | Expensive Limited voltage ratings Bad thermal management Can’t separate power between two circuits as well as electromechanical relays | More suitable for circuit due to longer lifespan in storage and in use Higher energy capacity
For our relay selection, we chose the electromechanical relays due to its high current and voltage ratings, thermal management, and popularity
Final Decision: Songle Relay’s SRD-05VDC-SL-C
Alexis (EE)
Notes: Alexis
DONE

## Slide 22: Buzzer Selection
Final Decision: Magnetic Buzzer
Product | Frequency | Operating Voltage | Max current | Price
Electromagnetic Buzzer | 2.73kHz | 4-6V | 60mA | $1.49
Magnetic Buzzer | 2kHz | 2.54-4V | 25mA | $6.99(10 pk)
Piezo Buzzer | 2kHz | 4-8V | 15mA | $0.95
Eric(EE)
Notes: Eric
DONE

## Slide 23: LED SELECTION
Product | Company | Forward Current | Price
Common Anode LED | Shenzhen Fedy Tech | 20mA | $2.00
RGB LED Module | DIYables | 20mA | $9.99(10 pack)
Common Cathode LED | CHANZON | 20mA | $8.99(100 pack)
Final Decision: RGB LED Module
Eric(EE)
Notes: DONE

## Slide 24: Website Technology Selection
Technology | Purpose | Language
ESP32 WebServer (ESP-IDF or Arduino Core) | Performance and asynchronous processing | C++
ESP32AsyncWebServer | Simplicity | C++
MicroPython with uasyncio | Python Development | Python
We decided to go with the ESP32AsyncWebServer because of the many libraries that work with the ESP32 that make it easier to setup IoT dashboards and real-time applications. Since the website currently only asks for an email to input for the safe owner to receive notifications.
Nick (CpE)
Notes: Nick ( mention
DONE async web server library) (mention what the website will be used for aka entering user’s email)

## Slide 25: Email Protocol and Library Selection
Email Protocol | Purpose | Storage method | Use Case Suitability
SMTP | Sends Email from Client to Server | Not applicable; used only for sending | Sending outgoing emails; typically used by email servers and applications
POP3 | Receives emails from one client and downloads to local device | Emails stored locally on the device after download | Suitable for single-device email access with offline storage
IMAP | Receives emails from multiple clients and downloads them across devices. | Stored on the server with optional local caching | Ideal for multi-device access and constant synchronization
SMTP Protocol is the best protocol to use to send email notifications for our project. SMTP is easy to implement and can be used with any service provider.
We will be using the ESP-Mail Client Library which is designed specifically for the EPS32 microcontroller and used with the SMTP Protocol.
Lakshmi (CpE)
Notes: Lakshmi
(maybe add a slide for software libraries if need be)
DONE

## Slide 26: Email Service platform and provider selection
Email Platform | Purpose | Features | Email Sending Limit
Gmail | Widely used email platform | - Spam filtering - User-friendly interface - Advanced security features | 500 emails per day
Outlook | Business-oriented email platform | - Enhanced security - Business-specialized features - Spam protection | 300 emails per day
Yahoo | Established global email service platform | - Spam filtering - Basic encryption - Easy navigation | 100 emails per day
We will use Gmail SMTP Service Provider because it works well with the Gmail Service Platform and provides efficient email delivery
We chose Gmail as our email service platform for users to receive email notifications regarding their safe. Gmail is a user-friendly and reliable email service. It comes with enhanced security protocols like TLS and email authentication
Lakshmi (CpE)
Notes: Lakshmi – mention security protocols, fast email delivery
DONE

## Slide 27: Software and Hardware program selection
Software | Ease of Use | Real-Time testing | Designed For | Debugging Capabilites
Visual Studio Code | High | No | General Purpose, Programming IDE | Limited
Code Composer Studio | Moderate | Yes | Programming TI microcontrollers | High
Platform IO | Moderate | Yes | Embedded Development | High
Arduino IDE | High | Yes | Embedded Development, microcontroller programming | High
Final Decision: Arduino IDE
Hardware | Ease of Use | Designed for
Eagle PCB | Moderate | Used to create and design PCB schematics
KiCad | Moderate | Used to design and create PCB schematics with advanced features
Fusion 360 | High | 3D modeling software used to design and create hardware components
Final Decision: Fusion 360
Lakshmi (CpE)
Notes: DONE

## Slide 28: PCB Design
PCB #1: Main PCB
This board has our ESP-WROOM-32 MCU that is responsible for powering & communicating with our peripherals for the safe
Has a GPIO pin reserved for the operation of our locking mechanism PCB
Eric(EE)
Notes: Eric/Alexis
Update if need be -DONE

## Slide 29: PCB Design(CONT.)
PCB #2: Locking Mechanism
This board contains our safe's entire locking mechanism circuit
The relay controls the locking/unlocking mechanism
The transistor also allows the ESP32 to control the relay indirectly by using a GPIO pin from our main PCB
The transistor also isolates the ESP32 from the relay’s inductive load
Alexis (EE)
Notes: Eric/Alexis
DONE- Update if need be

## Slide 30: PCB Layout
Main PCB
ESP-WROOM-32
3.3V Regulator
Keypad
Fingerprint Scanner
RGB LED
Buzzer
Motion Sensor
Display
Door Sensor
Ext. USB-UART Converter
Eric(EE)
Notes: Eric/Alexis
DONE- Update if need be

## Slide 31: PCB Layout
Locking Mechanism PCB
5V Voltage Regulator
Power Barrel Jack
SPDT Relay
N-Channel MOSFET Transistor
Solenoid
Alexis (EE)
Notes: Eric/Alexis

## Slide 32: Final Main PCB Design
Modifications:
Fingerprint scanner and motion sensor traces are connected to 5V
Scratched off a trace to connect extra pin to GND
Eric(EE)
Notes: For the finalized design of our main PCB, two modifications were made. The first one was soldering a wire to connect the fingerprint scanner trace and motion sensor trace to 5V so that they will receive power. The second change was to scratch off an extra pin that we weren’t using so that we’ll have an extra ground pin that will be used to implement our door sensor stretch goal.

## Slide 33: Final Locking Mechanism PCB Design
Alexis (EE)
Modifications:
Connect the second led indicator to the 5V voltage regulator
Add a pin on the board for the signal pin of the relay
Notes: Alexis
For the finalized design of our locking mechanism PCB, two modifications were made. The first one was soldering a 1k resistor to connect the LED indicator to the 5V voltage regulator. The second change was to add the signal pin of the relay to extra pin we weren’t using so we can use it to control the flow of the current in the circuit to scratch off an extra pin that we weren’t using so that we’ll have an extra ground pin that will be used to implement our door sensor stretch goal.

## Slide 34: Final WEBSITE DESIGN
Lakshmi (CpE)
Notes: Lakshmi
We will host a local server directly using the ESP32 MCU. After connecting to a local Wi-Fi network, the ESP32 will provide a local IP address where we can access the website. We will setup a route to serve the HTML Page and use HTML and JavaScript to design it.
The screenshot shows the final design of our Website. We have a box on the left-hand side where to the user can sign up for emails. After the user enters their email, it will be saved to the ESP32’s memory and they will receive a registration confirmation email. On the right-hand side we have a list of emails informing the users which emails they will receive directly from our safe. We also added our contact info at the bottom including the smart safe email in case the user wishes to contact us.

## Slide 35: Final EMAIL NOTIFICATION SYSTEM
Lakshmi (CpE)
Email for Registration:
Email for Access Attempt:
EEPROM storing User’s Email to ESP32:
Notes: Lakshmi
We will set up email functionality using the Gmail SMTP protocol and authentication credentials. The safe user will receive emails from a special Gmail account created for this project: smartsafesd1@gmail.com.
For our final email notification implementation, on the left we are showing how the EEPROM saves the user’s email into the ESP32’s memory after they enter it from the website. They will then receive an email confirming that they have signed up which is shown on the right. An example email is shown at the bottom informing the user that someone has accessed their safe.
The user will receive the additional emails from our safe which are listed in the previous slide on our website.

## Slide 36: Work DISTRIBUTION
Lakshmi (CpE)
Task | Primary Person | Secondary Person
Main PCB Development | Eric | Alexis
Lock PCB Development | Alexis | Eric
Software Code | Lakshmi | Nick
Component Testing | Nick | Lakshmi
PCB Soldering/Fabrication | Eric | Alexis
Safe Design | Alexis | Nick
Email/Web Server | Lakshmi | Eric
Safe User Interface | Nick | Lakshmi
Notes: DONE
This shows how the work distributed among all team members, ___ primarily worked on ____ and assisted with _____.

## Slide 37: Budget and Bill of Materials
Item | Quantity | Estimated Cost | Total Cost
MCU | 1 | $20 | $15.99
Display | 1 | $18 | $16.99
Keypad | 1 | $3 | $5.95
Fingerprint Sensor | 1 | $24 | $24.27
Ultrasonic Sensor | 1 | $6 | $6.99
Magnetic Sensor | 1 | $10 | $9.99
Solenoid Lock | 1 | $13 | $14.99
LED | 1 | $0.30 | $9.99(10 pack)
Buzzer | 1 | $6 | $7.99
Voltage Regulator | 1 | $5 | $8.19
Relay | 1 | $3 | $7.39
DC Power Connector | 1 | $4 | $5.99
Power Source | 1 | $50 | $59.99
TTL Converter | 1 | $10 | $7.39
Sheet Metal | 6 | $20 | $0
Hinges | 2 | $4 | $7.99
Handle | 1 | $15 | $0
PCBs (with shipping) | 10 | $80 | $125.02
Total |  | $291.30 | $335.11
Alexis (EE)
Notes: Alexis – If too short bring up fingerprint sensor
UPDATE

## Slide 38: FINAL Progress & Plan
Task | Start Date | End Date | Duration
Finalizing PCB Design | 1/6 | 1/16 | 10 days
PCB Ordering | 1/17 | 1/22 | 5 days
PCB Assembly | 1/22 | 1/30 | 8 days
CDR Preparation | 1/25 | 2/19 | 3.5 weeks
PCB Testing | 1/30 | 2/27 | 1 month
Midterm Demo Preparation | 2/19 | 3/8 | 2.5 weeks
System Integration/Testing | 2/27 | 4/3 | 6 weeks
8-Page Conference Paper | 3/10 | 3/17 | 1 week
Final Project Review Preparation | 3/10 | 4/12 | 1 month
Finalize Documentation | 4/14 | 4/22 | 8 days
Practice Final Live Demo | 4/3 | 4/17 | 14 days
Final Live Demo | 4/17 | 4/17 | 30 mins
Alexis (EE)
Notes: Alexis
In this table you can see the timeline of our progress from beginning of SD2. Implementing Wi-Fi and email was our biggest challenge for software and trying to fix our stdio problem on our microcontroller was our biggest hardware challenge, but thanks to everyone's hard work and collaboration, we reached all our milestones and even finished ahead of schedule
(maybe a bullet points list or a timeline instead of a table)
UPDATE FINAL PLAN

## Slide 39
Thank You!