## Slide 1: Automated Lens Metrology
Lens in, Datasheet out.

## Slide 2
Kiva
McCracken
(PSE)
Ollie
Mueller
(PSE)
Zachary Kassner
(EE)
Daniel
Gomez
(CpE)
Illumination & Processing
Lead
Spectral
Processing
Lead
PCB & Electrical
Lead
Integration &
Software
Lead

## Slide 3: Motivation & Background
Notes: Optical laboratories suffer from a chronic lens organization issue. Specifically, it is hard to label and keep track of lenses that perform vastly different tasks because they tend to look very similar. As a result, there are tens of thousands of dollars of unsorted optics in our department that are not utilized effectively.
As optical engineers, many of us have experienced this problem first-hand. A typical sight in our labs is a teaching assistant standing over a set of lenses to compare their focal lengths by the naked eye alone. This is an imprecise and time-consuming sorting method that is not suitable for research. Our design project aims to remedy this issue by autonomously creating a comprehensive datasheet for a given test lens. This design’s intended users are students, researchers, and professors in a lab setting.
The lens metrology systems currently available are generally geared towards production and high-accuracy single data point measurement. Our system serves as a middle ground, providing researchers with data they otherwise might not have about their lenses in a timely and convenient manner. It is designed to work on a macroscopic scale, listing lens characteristics rather than data on quality control.

## Slide 4: Sample Datasheets
Industry (Thorlabs)
Ours
Notes: Typical datasheets in the optics industry take the form of tables detailing the geometric and optical data of a particular lens. While some datasheets are more thorough than
others, most include specifications for diameter, focal length, index of refraction, radii of curvature, lens material, coating, and Abbe number. Many also provide a transmission or reflection graph over the visible spectrum.

## Slide 5: Goals & Objectives
 | Goals | Objectives
Basic | Measure focal length Measure transmissive and reflective spectra Measure geometry | WLS built WLS collimated Single monochromator IAS records an image
Advanced | Data output in plain text format Data output recoverable via flash drive | Calculate optical values based on measured geometry
Stretch | System graphical touch interface Data output in a PDF Data output recoverable via QR code Lens product number estimation | Lens product catalog lookup algorithm
Notes: 2.32 Basic Goals
• The system will measure the focal length of the test lens.
• The system will measure the transmissive and reflective spectra of the test lens.
• The system will manually measure the test lens’ geometric features.
2.33 Basic Objectives
• The white light source will be built.
• The white light source will be collimated.
• The wavelength selection will be done by a single monochromator.
• The image acquisition system will record an image.
2.34 Advanced Goals
• The data produced by the system will be output in a plain text format.
• The data produced by the system will be recoverable with a flash drive.
2.35 Advanced Objectives
• The wavelength selection will be done by a double monochromator.
• The system will derive optical values from the measured geometry.
2.36 Stretch Goals
• The system will have a graphical touch interface.
• The system will generate a datasheet as a PDF.
• The datasheet output by the system will be accessible by QR code or printed
document.
• The code will estimate the test lens’ product number by comparing the specs to a
known product database

## Slide 6: Hardware design / Overview
Show the overall block diagram

## Slide 7: Optical Design Overview

## Slide 8: Optical Design Overview

## Slide 9: WLS Overview/Spec
Capture and project as much 400 to 700nm light as possible in a 10mm diameter collimated beam

## Slide 10: WLS Comparison & Selection
Reflector Material
Collimation Architecture
Source + Relay
Mirror + Source + Relay
Mirror + Source + Asphere + Relay
Small vs. Large Reflector
Source

## Slide 11: Source + Relay
-4%
-4%
-4%
For a lens system of NA = .35 expected loss is about 76% minimum

## Slide 12: Mirror + Source + Relay
-66%
-60%
-32%
-20%

## Slide 13: Mirror + Source + Asphere + Relay
~90% Collection / Collimation

## Slide 14: Small vs. Large Reflector
Small Reflector = Very Small Focal Length = More Divergence
Large Reflector = Larger Focal Length = Less Divergence
Output beam size = exit aperture size
Bigger output = more compression needed = more loss

## Slide 15: The Horrors of Entropy

## Slide 16: The Hope in the Darkness

## Slide 17: WLS Design Matrix
Architecture | Efficiency | Collimation | Complexity | Score
Source + Relay | LOW (+1) | HIGH (+3) | LOW (-1) | +3
Mirror + Source + Relay | MID (+2) | MID (+2) | MID (-2) | +2
Mirror + Source + Asphere + Relay | HIGH (+3) | HIGH (+3) | HIGH (-3) | +3
Large Reflector | HIGH (+3) | HIGH (+3) | HIGH (-3) | +3
Small Reflector | LOW (+1) | LOW (+1) | LOW (-1) | +1

## Slide 18: Blender Sim
WLS as of Feb 13th
WLS Testing

## Slide 19: Monochromator Comparison & Selection
~ 3.5 nm FWHM
Peak wavelength of 671 nm with a linewidth of 3.5 nm
Notes: Gratings, photodetectors, etc...

## Slide 20: Monochromator Design
Notes: Gratings, photodetectors, etc...

## Slide 21: Monochromator Testing
Notes: Gratings, photodetectors, etc...

## Slide 22: Photodiode Testing
Notes: Gratings, photodetectors, etc...

## Slide 23: Datasheet Generation

## Slide 26: IAS Design

## Slide 27
IAS LINEAR GANTRY

## Slide 28: IAS Comparison & Selection

## Slide 29: PCB Design Verification Strategy
Talk about gonig from adafruit like modules for verification to breadbboarding to building those modules and re breadboarding
Find Pre-Built Modules that Accomplish Given Project Objective
Breadboard these Pre-Built Modules to Verify System
Design PCBs to Replace Pre-Built Modules in System
Breadboard New Modules to Verify New PCB Integrity

## Slide 30: PCB Design Main Objective
Talk about primary objective of project is to provide stepper motors interfacable with software that allow for X axis movement and rotational movement around the z-axis
X-Axis
Z-Axis

## Slide 31: Block Diagram for Achieving Objective
Just explain the block diagram really tbh

## Slide 32: Finding Pre-Built Modules to Verify System
Cheap Stepper Driver
From Amazon
Cheap Microcontroller
from Amazon
Cheap DC-DC Convertor
from Amazon
Explain the quick arrangement of a demo Circuit with amazon parts

## Slide 33: Hardware Selection Finding ICs to Make Better Hardware
a4988 Stepper Driver IC
By Allegro MicroSystems
STM8S003F3P6TR
By STMicroelectronics
TPS62932DRLR
By Texas Instruments
Explain the selection of ICs to make better versions of the amazon parts
Stepper Driver
MCU
Switching Regulator

## Slide 34: Why Use that Stepper Driver?
Explain the selection of ICs to make better versions of the amazon parts
Simple STEP/DIR interface (no SPI, UART, or firmware configuration required)
Very low cost compared to newer drivers (DRV8825, TMC2209, etc.)
Massive ecosystem and proven reliability from years of 3D-printer/CNC use
Easy hardware integration
Microstepping set with pins, not registers
Built-in current limiting and chopper control (no external current regulation needed)
Existing Adafruit module makes PCB layout easier
PCB Layout

## Slide 35: Why Use that MCU?
Explain the selection of ICs to make better versions of the amazon parts
Incredibly low price of only $0.40 per MCU
Strong price-to-peripheral ratio. It gives us GPIO, timers, ADC, UART, SPI, I²C, watchdogs, etc. without paying for high-end features we don't need.
Lower firmware complexity than larger MCUs like Arduino and ESP32. With fewer abstraction layers, it becomes easier to write low-level code
PCB Layout

## Slide 36: Why Use that Switching Regulator?
Explain the selection of ICs to make better versions of the amazon parts
Ultra-low quiescent current (~12 µA)
Wide input range (3.8 V–30 V) allows use to use 12-24V to power our project
Spread-spectrum EMI reduction built-in which lowers noise emissions compared to legacy regulators
High duty-cycle capability (~98%)
Peak current-mode control with fast transient response, necessary when steppers cause current spikes
PCB Layout

## Slide 37: Verification
Explain the selection of ICs to make better versions of the amazon parts
Switching regulator PCB has been manufactured but still needs to be assembled
All other PCBs have been verified to work in demo
All that’s left is integration and programming

## Slide 38: What's Next?
Just need to build a PCB to plop all the modules together
The modules will be soldered together permanently.
This will integrate the components in a way that satisfies the SD2 requirements.

## Slide 39: How are they made?

## Slide 40: Laying the front stencil

## Slide 41: placing components

## Slide 42: Hot plate time!

## Slide 43: Quality assurance testing

## Slide 44: Laying the back stencil

## Slide 45: Component placement and soldering... With a twist

## Slide 46: Pin header soldering

## Slide 47: The finished product

## Slide 48: Software Required
ALM Software
STM8 Programming
Raspberry Pi Automation
CSV Data Visualization
In this slide explain the three main uses of Software needed in this project.

## Slide 49: Software Block Diagram
User begins program
Pi controls STM8s via i2C
STM8 peripherals (Sensors, Stepper Driver, etc.)
Pi receives STM8s data
CSV Generation
Data Visualization
Final Datasheet

## Slide 50: Single Pass Measurement Flow

## Slide 51: Gantry Specifications

## Slide 52: Lens Holder Specifications

## Slide 53: Spectral Specifications

## Slide 54: Lens Tested

## Slide 55: IDE Options for the STM8
IDE / Toolchain | Compiler Support | Debugging Support | Ease of Setup | Cost | Pros | Cons
ST Visual Develop (STVD) | Cosmic C, Raisonance, SDCC | Full ST-LINK hardware debugging | Moderate | Free (IDE) | Native STM8 support, strong debugger integration, stable, professional workflow | Requires external compiler install
IAR Embedded Workbench | IAR C Compiler | Excellent debugging | Easy | Expensive (license required) | Very optimized compiler, professional toolchain | High cost, limited free version
PlatformIO (VS Code) | SDCC | Limited STM8 debug support | Moderate | Free | Modern UI, cross-platform | STM8 support is not mature
Eclipse CDT + SDCC | SDCC | Manual configuration | Difficult | Free | Highly customizable | Complex setup, not STM8-specific
Raisonance Ride | Raisonance C | Yes | Moderate | Limited free version | Good integration | License restrictions
This slide here explain how all options were explored and why ST Visual Develop was the better option
ST Visual Develop was the better option because it contains native STM8 support, it was free and compatible with the ST-Link hardware debug functionality.

## Slide 56: Single Board Computer Selection
Raspberry Pi 5 has built in Wi-Fi, more memory, and a faster CPU.
Raspberry Pi 5 CPU is favored for general-purpose computing, while the Jetson Nano CPU is favored for embedded AI projects.

## Slide 57: Raspberry pi peripherals

## Slide 58: STm8 peripherals

## Slide 59: I2C DATA PACKET FORMAT
For programming the stm8 mcus, we plan on programming them via swim. The ST-Link V2 was the best option we went with. While there are cheap clones that can program the stm8, they are susceptible to bricking suddenly. The software we used to program to the stm8 is the ST Visual Programmer. While there are other softwares that can upload to the stm8, this one is natively compatible with the ST-Link V2,
I2C chosen over UART because UART ultimately failed during tests.
Inside each data packet sent contains information on the task the stm8 needs to perform, or data being sent back to the pi.
All stm8s share the same i2c bus, each stm8 has it's own unique address.

## Slide 60: USER INTERFACE

## Slide 61: Dev Mode

## Slide 62: CSV Generation
Sensor data coming from stm8 will be inputted and categorized into csv via a python script
The C spot, D spot, and F spot will also be calculated and inputted into the csv.
This csv will then be inputted into LaTeX to start the datasheet process.

## Slide 63: Electronic Case
The case will act as an enclosure for all the PCBs.
Wire clamps make sure wires are not suddenly yanked from PCBs.
Cooling fan helps regulate temperature for all the electronics.

## Slide 64: Future plans
Have an app that the Pi sends the datasheet to
Improve accounts of grating and photodiode efficiency on data

## Slide 65: Administrative content
 | Hardware | Optics | Electronics | Total
Budget Total | $350 | $350 | $2,500 | $3,200
Budget Spent | $106.97 | $288.38 | $1,934.12 | $2,329.47
Notes: Budget & work distribution

## Slide 66: Our next steps