## Slide 1: Group 10 Final Presentation
Luke Anderson
Computer Engineer
Ethan Dill
Optics & Photonics Engineer
Luke Anderson
Computer Engineer
P.E.G.A.S.U.S. (Pilot Enhanced Guidance and Augmented Sight Utility System)
Frank Murphy
Electrical Engineer

## Slide 2: Motivation & Background
Heads-Up Displays are a tool utilized in vehicle situational awareness across a myriad of industries. In aviation, commercial and military cockpit environments have HUD compatibilities. Civilian HUDs for general aviation are not commonplace.
ED
Notes: Situational awareness is an important part of operation of any vehicle, especially in aviation.
Having more information readily available in a cockpit can ensure a safe operating environment at times when every second counts.
The P.E.G.A.S.U.S. HUD aims to make an accessible, affordable, and robust heads-up display that will serve the general aviation market.

## Slide 3: ***Motivation & Background
The P.E.G.A.S.U.S. Heads-Up Display seeks to increase pilot situational awareness, while remaining a compact and affordable solution for the general aviator.

## Slide 4: Goals & Objectives - Goals
Basic Goals:
Develop a portable standalone Heads-Up-Display (HUD) for aircraft.
Display essential flight data in a Graphical User Interface.
The system be visible in various lighting conditions and portable.
Advanced Goals:
System will contain an adaptive lighting system for comfortable visibility in all settings.

## Slide 5: Goals & Objectives – Basic Objectives
Basic Objectives:
House all optical components and sensors in an optomechanical housing.
Implement an Inertial Measurement Unit (IMU) to calculate three-dimensional attitude data and compass heading data.
Implement an altimeter for altitude data reading.
Incorporate one microcontroller unit (MCU) designated to real-time sensor reading.
Implement a dedicated MCU for data formatting and GUI display control.
The GUI will display attitude (orientation in space) data, altitude, and compass heading.
Display brightness visible through polarized and unpolarized lenses.
ED

## Slide 6: Goals & Objectives – Advanced Objectives
Advanced Objectives:
System displays data for >80% of total flight time with restart technology if an unexpected shut off occurs.
Correct for system aberrations and distortion specifically localized within target eye box area.

## Slide 7: Engineering Specifications
Parameter | Specification | Description | Priority
Accuracy | ~90% | Ensures data is accurately displayed to pilot | High
Total System Power Consumption | <21W | Critical for aircraft electrical load margin | Med
GUI Display Brightness | >750 nits | Ensures HUD visibility in cockpit daylight | High
System Boot Time | < 1 minute | Pilot needs minimal delay at startup | High
Attitude Measurement, Processing and Display Time | <200ms | Ensures prompt reading to ensure accurate display of data | Med
IMU Polling Rate | >9.9 Hz | Smooth sensor readings | Med
GUI Refresh Rate | > 30 FPS | Ensures a responsive GUI | Med
Total System Weight (including housing) | <11 lbs | Keeps system portable and minimizes aircraft load | High
Horizontal Field of View Overlay* | >39° | Provides useful HUD coverage | Low

## Slide 8: Hardware Diagram

## Slide 9: Hardware Comparison & Selection - MCU
Factor | Pi4 + ESP32 | Pi4 + STM32 | ESP32 + STM32
Graphics | Highest | Highest | Lowest
Clock Speed | Low | High | Highest
Latency | Medium | Low | Lowest
Learnability | Highest | Low | Lowest
Feasibility | Highest | Low | Lowest
Pi4 + ESP32 had the highest learnability and development speed with acceptable clock speed and high graphics rendering leading to this being selected for our MCU combination
STM32 has less community support and the most difficulty developing on hence why combinations with it were not selected

## Slide 10: Hardware Comparison & Selection – Altimeter
Part | Pressure | Altitude Capability | Accuracy | Noise/ Vol Consumption | Cost
BMP-390 | 300 -1200hPa | -500m - 9000m | ±0.5hPa | Very Low | Very Low
MS5611 | 10 -1200hPa | -1000m - 11000m | ±1.5hPa | Moderate | Moderate
LPS22HB | 260 - 1260hPa | -1000m - 10000m | ± 0.1hPa | Low | Low
The MS5611 has the best all around capabilities for our project
They are similar enough that the the easy to solder package makes it the clear choice.
Notes: Looking at the specs we can see that the it does not have the widest pressure rannge or altitude capabiltiy it is not as accurate as as the LPS22HB. it does have the lowest noise and voltage consumption. On top of this it is the cheapest and closly allignned typical use for ou project. whcih makes it the most balanced choice

## Slide 11: Hardware Comparison & Selection – IMU
Part | Axes | Noise/ Vol Consumption | Difficulty of Use | Typical Use | Cost
BMI270 | 6-axis(Accel + Gyro) | Very Good | Easy | Modern Low Power Systems | Low
LSM9DS1 | 9-axis(Accel + Gyro + Mag) | Good | Easy | Modern Low Power Systems | Very Low
MPU9250 | 9-axis(Accel + Gyro + Mag) | Moderate | Moderate | Low Power Systems | Low
The IMU needs to have 9 axes
The more easily solderable package makes the MPU-9250 our choice

## Slide 12: Hardware Comparison & Selection – Power Consumption / Communication Protocol
Part | Voltage | Current | Communication Protocol
ESP-32 | 3.3V | 500mA | I2C Compatible
Raspberry Pi4 | 5V | 3A | I2C Compatible
MPU9250 | 3.3V | 4mA | I2C Compatible
MS5611 | 3.3V | 5mA | I2C Compatible
Low power system outside of the Raspberry Pi
Only require a 3.3V and 5V regulator
All I2C Compatible
Notes: Looking at the specs we can see that the it does not have the widest pressure rannge or altitude capabiltiy it is not as accurate as as the LPS22HB. it does have the lowest noise and voltage consumption. On top of this it is the cheapest and closly allignned typical use for ou project. whcih makes it the most balanced choice

## Slide 13: Hardware Comparison & Selection - Regulator
Part | Type | Good for | Vin Range | Iout Max | Downsides
LM-2679-ADJ | Buck | 5V and 3.3V | 5 - 40V | 5A | Complex design
LMR33640 | Buck | 5V | 1.8 - 36V | 4A | Unreliable part
TLV767 | LDO | 3.3V | 2.5 - 16V | 1A | Unreliable part
The LM-2679-ADJ can be used for both
The only difference is its component values

## Slide 14: Hardware Comparison & Selection – Display
ED
Part | Brightness | Driver Board / No Driver Board | Type of Display | Cost | Resolution
NHD-3.5-HDMI-HR-RSXP | 950 Nits | No Driver Board | TFT LCD | Inexpensive (<$120) | 640 x 480
SY049LDM02 | 1500 Nits | Driver Board | Micro-OLED | Expensive ($500+ for whole system with tariffs) | 1920 x 1080

## Slide 15: Hardware Comparison & Selection – Polarizer
ED
Part | Polarization | Ease of Integration | Surface area of polarizing element | Cost
λ/4 Polarizing Film | Circular | More complex, have to design housing | High | Inexpensive ($20) for a 11x8.5” segment of film
λ/4 Waveplate | Circular | Comes with existing housing | Low and cost prohibitive | Expensive ($500+ for small diameter plates)

## Slide 16: Hardware Selection: Petzval Relay Projection System
ED
Diagram and Schematic of Petzval Relay System
PEGASUS V1 Petzval Relay System + Polarizer

## Slide 17: Hardware Selection: Petzval Relay Projection System
ED

## Slide 18: Hardware Selection: Projection and Optical Combination
ED

## Slide 19: Hardware Selection: Optical Combination
ED
We selected a high-transmission 40/60 Dielectric Optical Combiner Glass for the heads-up display.
The optical combiner assists in the elimination of “ghost images” as well as providing a projection medium for our final image.
In addition, the combiner also allows for physical mounting of any add-ons such as self-dimming elements.

## Slide 20: Software Comparison & Selection – ESP32 Programming Languages
Language | Speed | Stability | Ease of Use
Python (MicroPython) | Lowest | Lowest | Highest
C++ | High | Highest | High
C | Highest | High | Lowest
C has the highest processing speed and due to the developer's familiarity with the language, this was the best option for the ESP32 programming language
Python is too slow for our purposes
C++ is overly complicated for sensor reading

## Slide 21: Software Comparison & Selection – GUI Framework
Language & Framework | Ease of Use | Resource Usage | Speed | Boot Time
C++ & Qt | High | Low | High | Low
Python & PyQt | Highest | Highest | Highest | Highest
C & SDL2 | Lowest | Lowest | Highest | Lowest
C++ & Qt offer the widest variety and support of graphics rendering while maintaining a high speed
Python & PyQt are too slow
C & SDL2 offer too little graphics rendering support

## Slide 22: PCB Design - Regulator

## Slide 23: PCB Design-Altimeter

## Slide 24: PCB Design - IMU

## Slide 25: PCB Design – Main PCB

## Slide 27: V1 Final System – PCB / Sensors

## Slide 28: Software Design – Use Case Diagram

## Slide 29: Software Design – System Flow

## Slide 30: Software Design – MCU Integration

## Slide 31: Software Design – UI Spec

## Slide 32: Early Prototyping
Successfully built a benchtop basic projection prototype utilizing:
  Raspberry Pi4 for peripheral integration / GUI
  Quarter Waveplate Polarizer
  Projection Magnification lens System
  Reflective Optics for Packaging Constraints
  Breadboard for electrical integration
ED
Notes: project basic information in a compact and concise manner
P.O.C. utilized a barometric pressure sensor for altimeter calculations and then displayed the calculated altitude onto the micro-display screen. This would then be integrated into our graphical user interface.
our Pi4 system allowed for software integration and flexibility in making and displaying those calculations.
Optical system aimed to provide rough packaging constraints as well as basic projection principles for demonstration and iteration purposes.
Breadboard allowed for electronic integration of the microcontroller, display, and other electronic components.
Overall, the prototype was successful in it's ability to roughly display the desired output but with some caveats.

## Slide 33: Early Prototyping
Test Display Screen outputting sample imagery for our setup
ED
Optical Test Setup with display
Test setup complete with optics and display integration
Notes: The altitude readings were correct and visible to the user in a dimly lit environment. But there were still improvements to be made
brightness needed to be improved,
optics were not housed (free floating)
electronics needed to be refined.

## Slide 34: Benchtop System Prototypig
Notes: Display
Petzval Setup
Positive image formation
Distortion Correction
Fold Mirror
Optical Combiner

## Slide 35: Test Pattern on Benchtop System

## Slide 36: ***Designed Product (P.E.G.A.S.U.S. V1)
Final housing with PCB and optical systems fully integrated
Final GUI overlaid on to pilots FOV with accurate data

## Slide 37: V1 Final System: Internal Components

## Slide 38: Optical Hardware Difficulties Faced
Issue Faced | Solution
Optomechanical Housings and Mounts | Designed optomechanics and utilized additive fabrication techniques (3d printing) to iterate upon mechanical housings
Optical Alignment Challenges | Utilized the optical rail cage system in order to ensure optical axis consistency as well as ease of alignment.
HUD Brightness Improvements | Introduced Optical Attenutation Film to combiner in order to increase GUI contrast
Polarization Cost Improvement | Incorporated cost-effective Circular Polarizing λ/4 film instead of having to buy a costly λ/4 waveplate

## Slide 39: Electrical Hardware Difficulties Faced
Solderable sensors
  Picking the correct package
  Making sure there are no shorts
LSM9DS1
MPU9250
Side Pins
No Side Pins

## Slide 40: Software Difficulties Faced
Issue Faced | Solution
Magnetometer Distortion & Unstable Heading - Magnetic interference and sensor noise caused inconsistent heading readings. | Used a Mahony sensor fusion filter with calibration and correction logic to stabilize heading.
IMU Bias & Drift - Gyroscope and accelerometer biases caused orientation drift over time. | Applied multi-axis calibration to compute and correct sensor offsets.

## Slide 41: Administrative Content - BOM
# | Item / Part No. | Qty | Unit Price (USD) | Line Total (USD) | 
1 | Raspberry Pi 4 Model B (4 GB) | 1 | $55.00 | $55.00 | 
2 | Adafruit Feather ESP32-S3 (STEMMA QT) | 1 | $19.95 | $19.95 | 
3 | MS5611 Chip | 1 | $11.95 | $11.95 | 
4 | MPU9250 9-DoF IMU | 1 | $15.95 | $15.95 | 
5 | Quectel L76K | 1 | $9.90 | $9.90 | 
6 | 25mm Ceramic Patch Antenna | 1 | $4.19 | $4.19 | 
7 | 32GB SDHC Flash MEM CARD | 1 | $6.98 | $6.98 | 
8 | Arducam IMX-219 Wide-FOV Pi Camera (IMX219, 160°) | 1 | $12.09 | $12.09 | 
9 | LM2679-ADJ | 2 | $8.76 | $17.52 | 
10 | 6 Pin Male Header | 3 | $0.36 | $1.08 | 
11 | 6 Pin Female Header | 3 | $0.31 | $0.93 | 
12 | 4 Pin Male Header | 1 | $0.34 | $0.34 | 
13 | 4 Pin Female Header | 1 | $0.17 | $0.17 | 
14 | 0805 100k ohm Resistor | 2 | $0.10 | $0.20 | 
15 | 0805 24.9k ohm Resistor | 1 | $0.10 | $0.10 | 
16 | 0805 500k ohm Resistor | 1 | $0.10 | $0.10 | 
17 | 0805 160k ohm Resistor | 1 | $0.10 | $0.10 | 
18 | 0805 4.7k ohm Resistor | 4 | $0.10 | $0.40 | 
19 | Ceramic X7R 100nF Capacitors | 4 | $0.10 | $0.40 | 
20 | Ceramic X7R 220nF Capacitors | 1 | $0.10 | $0.10 | 
21 | Ceramic X7R 1uF Capacitors | 4 | $0.08 | $0.32 | 
22 | Ceramic X7R 10uF Capacitors | 2 | $0.08 | $0.16 | 
23 | Ceramic X7R 22F Capacitors | 6 | $0.08 | $0.48 | 
24 | Ceramic X7R 0.1uF Capacitors | 3 | $0.08 | $0.24 | 
25 | Ceramic X7R 2.2uF Capacitors | 1 | $0.08 | $0.08 | 
26 | Ferrite Bead 600ohm 100mHz | 1 | $0.10 | $0.10 | 
27 | 8uH Inductor | 1 | $1.23 | $1.23 | 
28 | OLED Display | 1 | $139 | $139 | 
29 | Multi-Order Quarter Waveplate | 1 | $17 | $17 | 
30 | Collimating Lens | 1 | $113 | $113 | 
31 | Reflective Mirror | 1 | $25 | $25 | 
32 | OAP Mirror | 1 | $185 | $185 | 
33 | Magnifying Lens | 1 | $56 | $56 | 
34 | Photochromic Film | 1 | $40.50 | $40.50 | 
35 | Optical Combiner | 1 | $100 | $100 | 
36 |  |  | Total: | 862.04 | 

## Slide 42: Administrative Content – Work Distribution
Computer Engineering | Responsibilities
Luke Anderson | Software Design and Implementation
 | MCU Selection and Implementation
 | Website Design and Management
 | Project Lead
Electrical Engineer | 
Frank Murphy | PCB/PSU Design
 | Hardware Component Selection
Optics Engineer | 
Ethan Dill | Optical Design
 | Component Alignment
 | Optical Component Integration

## Slide 43: Future Changes
Utilize GPS module instead of magnetometer for improved heading
Implement an overlaid navigation feature to allow pilots to navigate using this system
Head / eye tracking for dynamic eye box
Notes: For future improvements, one area we identified is replacing the magnetometer with a GPS-based heading solution. Magnetometers are highly susceptible to environmental interference, so using GPS—particularly course-over-ground data—would provide more stable and reliable heading information during motion.
We also plan to implement an overlaid navigation feature, where real-time directional cues and waypoints are projected directly onto the HUD. This would allow pilots to use the system not just for situational awareness, but for basic navigation as well.
Finally, we’re interested in adding head or eye tracking to enable a dynamic eye box. This would allow the display to adjust based on the pilot’s viewing position, improving visibility and making the system more adaptable across different users and seating positions

## Slide 44: Thank You!

## Slide 45: Questions?

## Slide 46
Trial # | Brightness Measurement (nits)
1 | 980
2 | 910
3 | 920
4 | 930
5 | 960
6 | 960
7 | 980
8 | 930
9 | 910
10 | 920
AVERAGE | 940

## Slide 47: Heading Accuracy
Objective (deg) | Measured (deg) | Accuracy (formula above)
345 | 344.3 | 99.80%
328 | 329 | 99.70%
290 | 288.3 | 99.41%
216 | 203.4 | 94.17%
187 | 173.8 | 92.94%
159 | 151 | 94.97%
115 | 113 | 98.26%
87 | 80.5 | 92.53%
68 | 72 | 94.12%
52 | 47.7 | 91.73%
Average Accuracy = 98.5% > 90% Accuracy Spec

## Slide 48: Attitude Accuracy
Roll (O) | Roll (M) | Pitch (O) | Pitch (M) | Roll (A) | Pitch (A)
25 | 23.9 | 5 | 2.4 | 99.69 | 99.28
15 | 15.2 | 8 | 5.7 | 99.94 | 99.36
6 | 4.7 | 10 | 7.3 | 99.64 | 99.25
-10 | -8.6 | 18 | 17.3 | 99.61 | 99.81
-15 | -14.2 | 17 | 16.5 | 99.78 | 99.86
-19 | -19.0 | -5 | -3.5 | 100.0 | 99.58
-22 | -22.4 | -6 | -4.8 | 99.89 | 99.67
18 | 18.2 | -7 | -6.5 | 99.94 | 99.86
11 | 11 | -10 | -10.3 | 100.0 | 99.92
5 | 4.4 | -13 | -12.8 | 99.83 | 99.94
Average Roll Accuracy: 99.83% > 90%, Average Pitch Accuracy: 99.65% > 90%

## Slide 49: Altitude Accuracy
Altitude Objective (ft) | Altitude Measured (ft) | Accuracy
110 | 115 | 95.45%
100 | 103 | 97.00%
90 | 91 | 98.89%
70 | 72 | 97.14%
71 | 74 | 95.77%
73 | 76 | 95.89%
82 | 84 | 97.56%
83 | 86 | 96.39%
92 | 95 | 96.74%
93 | 95 | 97.85%
Average Accuracy: 96.90% > 90% Accuracy Spec

## Slide 50: Attitude Response Time
Response Time (ms)
80
70
110
90
100
240
70
60
120
Average Response Time: 94ms < 200ms