## Slide 1: LMCO – Swarm Operations and Autonomous Rescue (SOAR)
Critical Design Review
Team 15
Adrian Castillo
Cristian Gomez
Robert Hagerty
Michael Palin
Belle Perry
Kristopher Tellez
Notes: bel

## Slide 2: Meet the team
Belle Perry
Aerospace Engineering
Michael Palin
Computer Engineering
Kristopher Tellez
Computer Engineering
Cristian Gomez
Computer Engineering
Adrian Castillo
Computer Engineering
Robert Hagerty
Aerospace Engineering
Notes: bel

## Slide 3: Topics
Motivation and Background
Goals and Objectives
Engineering Specifications
Comparison of Hardware
Comparison of Software
Hardware Design
Software Design
Prototyping and Testing
Administrative Content, Progression and Plans
Notes: bel

## Slide 4: Motivation and Background
Motivation:
Reduce risk with drone-based operations
Mitigates additional injuries of human teams
Provides safe and reliable tracking to detect human life
Background:
LMCO continuation/sponsored project
Utilizing AI modeling to adapt to search and rescue scenarios
Notes: adrian

## Slide 5: Goals and objectives
Goals:
Create a heterogeneous autonomous drone swarm for search operations
Enable coordinated operation through inter-drone communication
Achieve multi-modal sensing for complementary situational awareness
Demonstrate a proof-of-concept search capability in a defined area
Ensure structural robustness for sustained search-and-rescue missions
Objectives:
Build and configure three flight-ready drones with autonomous flight control
Deploy distinct sensors per drone with live data streaming
Execute a pre-defined cooperative search flight path
Validate simultaneous area coverage (~100 m) by the swarm
Notes: Rob

## Slide 6
Engineering Specifications
Requirement | Target Value & Units | Description
Flight Time | ≥ 10 minutes | The drone swarm shall be able to perform search and rescue operations for a minimum of 10 minutes.
Number of Drones in Swarm | ≤ 3 count | The drone swarm shall consist of three drones, defined by test and safety constraints. Allows for robust swarm communication testing while minimizing system complexity.
Number of Drone Sensors | ≥ 3 count | The system includes one RGB camera, one infrared (IR) sensor, and a LiDAR. Enables multi-modal sensing for object recognition, terrain awareness, and thermal detection.
Drone-to-Ground Communication Range | ≥ 100 meters | Ensures consistent telemetry transmission and command reception from the GCS (Ground Control Station), even in semi-obstructed environments.
Notes: rob

## Slide 7
Hardware Block Diagram
PCB requirement is exempt for our sponsored project, but that means we must use commercial ready products.
Lockheed Martin provides us with their available resources such as NVIDIA Jetson's, flight controllers, camera sensors, etc.
Notes: adrian

## Slide 8
Hardware Cad Design
SolidWorks
Why is it important?
Planning and Proof of Concept
Notes: This slide contains the CAD of the teams’ current and planned implementation of the SOAR project
This model was constructed in SolidWorks
The practice of CAD allows for the team to plan and verify the design before part procurement.

## Slide 9
Notes: This slide contains the CAD Drawing of the SOAR Drone based on the Assembly from the last slide
There are various dimensions listed to define the size and scale of the project and for its replication.

## Slide 10: Hardware and software design and comparison

## Slide 11: Companion Computer Selection
Selected Component: NVIDIA's Jetson Orin Nano
Why Jetson Orin Nano?
Significantly higher AI compute capability
Native CUDA
Capable of running RGB, thermal, and LiDAR real-time detection models
Future-proof for advanced autonomy
Provided by Lockheed Martin
How the connections will be setup for the Jetson Orin Nano:
Notes: Kris
Companion computers are separate on-vehicle computers that are connected to the flight controller, and which enable computationally expensive features like…

## Slide 12
Selected Component: Hex Pixhawk 2.1 Cube Black Flight Controller
Why Cube Black
Triple-redundant IMUs for fault tolerance
Native CAN, UART, I2C support
Proven reliability in autonomous UAV platforms
Strong ArduPilot ecosystem support
Provided by Lockheed Martin
How the connections will be setup for the Cube Black:
Flight controller Selection
Notes: cris

## Slide 13: Electronic Speed Controller (ESC) Selection
Criteria | F55A Pro II 4-in-1 | Lumenier 60A 4-in-1 | SpeedyBee 60A 4-in-1
Continuous Current | 55A | 60A | 60A
Voltage Rating | 3–6S LiPo | 2–6S LiPo | 2–6S LiPo
ESC Protocol | DShot1200 (BLHeli_32) | DShot1200 (BLHeli_32) | DShot600 (BLHeli_S)
Weight | ~18g | 27g | 10.5g
ArduPilot Compatibility | Yes | Yes | Yes
Cost (USD) | ~$129.99 | $84.99 | $75.99
Role in System:
Motor drive control and power distribution
Why F55A Pro II?
55A continuous rating suitable for 6S operation
BLHeli_32 firmware support
Reduced wiring complexity with 4-in-1 design
Proven compatibility with Cube flight controllers
Notes: adrian

## Slide 14: Electronic Speed Controller Diagram Setup
6S LiPo battery supplies high-current power directly to the 4-in-1 ESC
ESC distributes three-phase (U, V, W) power to four BLDC motors
Cube Black sends DShot digital motor control signals to the ESC
ESC returns telemetry and current sensing data to the flight controller
Shared signal ground ensures reliable communication and monitoring
Notes: adrian

## Slide 15
Selected Sensors: LiDAR, thermal camera, and RGB Camera
Purpose of Each Sensor
LiDAR – obstacle/human detection (spin 2D plan to create 3D map) distance mapping
Thermal Camera – human heat signature detection (search & rescue)
RGB Camera – human detection
Why these sensors?
Supports heterogeneous sensing requirements
Enables multi-modal perception for autonomous operation
Provided by Lockheed Martin
Drone Sensor's Selection
Notes: kris

## Slide 16
Criteria | RFD900x Telemetry Radio | SiK Telemetry Radio | 3DR Telemetry
Frequency | 900 / 915 MHz | 915 MHz | 915 MHz
Communication Range | Up to 40 km | Up to 1–3 km | Up to 1–2 km
Data Rate | Up to 200 kbps | Up to 115 kbps | Up to 115 kbps
Reliability | Very High | Moderate | Moderate
MAVLink Compatibility | Full native support | Full native support | Full native support
Real-Time Telemetry Performance | Excellent | Good | Good
Role in System​:
Provides long-range wireless communication between drones and the ground control station, enabling telemetry transmission, command control, and swarm coordination.
​
Why RDF900?
Supports Divide-and-Conquer Swarm Operation
Long-Range and Reliable Communication
High Reliability and Industry Proven
Compatible with Flight Controller and MAVLink
Drone RADIO selection
Notes: michael

## Slide 17
Criteria | Wi-Fi Video Transmission | Analog FPV Transmission | Digital FPV Transmission
Frequency | 2.4 / 5 GHz | 5.8 GHz | 2.4 / 5.8 GHz
Communication Range | 100–300 meters | 500–2000 meters | 1–10 km
Video Quality | 720p / 1080p | 480p | 720p / 1080p
Data Bandwidth | Very High | Low | High
Latency | Moderate | Very Low | Low
Integration with Jetson | Excellent | Requires additional hardware | Requires additional hardware
Integration with Ground Station | Excellent | Limited | Moderate
Budget | $0–$20 | $50–$120 | $150–$400
Power Consumption | Moderate | Low | High
Role in System​:
Provides real-time video transmission from the cameras to the ground control station, enabling visual monitoring, target verification, and situational awareness during search and rescue missions.
​
Why Wi-Fi for Video Transmission?
Direct Integration with Jetson Companion Computer
High Video Quality
Meets System Communication Requirements
Low Cost and Simple Implementation
Video Transmission Selection
Notes: mic

## Slide 18
Criteria | LiPo (Lithium Polymer) | Li-ion (Lithium Ion) | LiFePO₄ (Lithium Iron Phosphate)
Energy Density | High | Very High | Moderate
Current Output | Very High | Moderate | Moderate
Weight | Light | Very Light | Heavy
Discharge Rate | Excellent | Moderate | Moderate
Safety | Moderate | High | Very High
Flight Performance | Excellent | Moderate | Poor
Cost | Moderate | High | High
Role in System
Primary onboard energy source for propulsion, avionics, and sensors
Supplies high burst current to the ESC motor system during takeoff and maneuvering
Supports sustained autonomous flight under varying payload and mission loads
Why LiPo (Selected)
Delivers very high current output required for multirotor propulsion
Excellent discharge rate enables rapid throttle response
Lightweight relative to power capability, improving thrust-to-weight ratio
Provides superior flight performance compared to Li-ion and LiFePO
Moderate cost and wide availability for UAV applications
Battery System Selection
Notes: mic

## Slide 19
Criteria | SunnySky V4010 Brushless DC Motor | T-Motor MN3510 Brushless DC Motor | 3542 Brushless DC Motor
KV Rating | 375 KV | 360 KV | 900–1000 KV
Motor Size & Weight | 40×10 mm, ~120 g | 35×10 mm, 140 g | 64×35 mm, 155 g
Thrust Output | ~2.0–2.5 kg (prop-dependent) | ~2.5–3 kg | ~2 kg
Voltage Range | 4–6S LiPo | 4–6S LiPo | 3–4S LiPo
Current Draw | 30–40 A | 35–45 A | ~52 A
ESC Compatibility | High | High | Low
Durability (Cycle Life) | ~90% integrity after 1000 h | 95% after 1000 h | 75% after 1000 h
Efficiency | ~87% | 88% | 78%
Cost (USD) | ~$49.99 | $79.99 | $31.99
Role in System​:
Provide lift and thrust for multirotor platform.
​
Why the SunnySky V4010 motors?
Optimized for 6S LiPo operation
Longer flight time (~14 min)
Suitable thrust margin for payload capacity
Cost-effective for multi-drone swarm deployment
Drone motor selection
Notes: bel

## Slide 20
Notes: bel

## Slide 21: Propeller Selection
Role in System: Generate lift via pressure differences through rotation.
Why the SunnySky 18x5.5 Carbon Fiber Propellers?
Longer blade creates more thrust
Carbon Fiber is lightweight and durable
Affordable
Design Aspect | HQProp 13x9x3 | SpeedyFPV 18x5.5 | CB2 Pro 16x5.4 | EOLO 15x5.5
Weight (each) | 63.9 | 49g | 18g | 21g
Efficiency | Moderate | High | High | High
Lift | High | High | Moderate | High
Drag | High | Moderate | Moderate | Low
Material | Nylon | Carbon Fiber | Carbon Fiber | Carbon Fiber & Nylon
Stability | Moderate | Moderate | Moderate | Moderate
Price | $42.09 | $36.99 | $49.00 x 2 | $17.99 x 2

## Slide 22
Drone frame selection
Material | 6061 | 7075 | Carbon Fiber | Nylon | ABS | Graphene
Density | 2.70 g/cm^3 | 2.81 g/cm^3 | 1.4-1.8 g/cm^3 | 1.1 g/cm^3 | 1.2 g/cm^3 | 0.77 g/cm^3
Tensile Strength | 310 MPa (T6 Temper) | 572 MPa (T6 Temper) | >350 MPa | 60 MPa | 34 MPa | Dependent
Elastic Modulus | 69 GPa | 71.7 GPa | Dependent on fiber fraction | 1-4 GPa | 2.1-2.27 GPa | 1 TPa
Fatigue | 500 mil cycles | 500 mil cycles | Depends on quality | Poor | Poor | Unknown
Relative Cost | Moderate | High | Moderate-High | Moderate | Moderate | High
Role in System​:
Serve as structure for drone system
Builds two drone frames, four support arms, and four landing gear legs
Carbon Fiber serves as a reliable structure, not easily malleable, affordable, and strong tensile strength
​
Why:
Drone frame responsible for supporting all electronics
Provides overall framing and shape of the drone
Notes: bel

## Slide 23: Comparison of Software

## Slide 24
Overall System Flow
System startup and initialization
Sensor data acquisition (LiDAR, cameras, GPS)
Decision Logic
Obstacle detection and avoidance
Action selection (move, hover, land)
Human detection
Control Execution
Motor commands issued via flight controller
Continuous feedback loop during flight
Communication
Telemetry and data exchange with ground station
End Conditions
Landing procedure
System shutdown
Software flowchart
**One of many Software Diagrams**
Notes: kris

## Slide 25: Autopilot Stacks
Framework | Summary
ArduPilot | A versatile, open-source autopilot software stack that supports a wide range of vehicle platforms. Its open-source architecture enables extensive community participation, resulting in robust documentation, active development, and a large body of user-contributed guides and support resources.
PX4-Autopilot | A high-performance, closed-source autopilot for research, consumer, and industrial drones. It is characterized by the modular structure of its software, consisting of the flight stack and a middleware.
Notes: cris

## Slide 26: Swarming on the drone
Swarm Operation & Coordination
System initializes with synchronized ground station and aerial units
Operator defines mission parameters and objectives at ground station
Roles and operational zones assigned based on drone capabilities and sensors
Drones execute tasks autonomously while performing continuous health checks
Parallel Decision Processes
System Integrity: monitors sensors, communication, and subsystem health
  Fault logging, reporting, and recovery (restart, reconnect, redistribute load)
Mission Progress: evaluates task completion and feasibility
  Reports status, transmits data, or requests reassignment if needed
Closed-loop coordination enables adaptive reconfiguration, fault tolerance, and reliable swarm autonomy
Notes: adrian

## Slide 27: Ground Control Station Software
Framework | Summary
QGroundControl | An open-source Ground Control Station application designed to control and configure unmanned vehicles running PX4 Pro or ArduPilot autopilots. It provides real-time flight monitoring, and advanced mission planning across platforms (i.e. Windows, macOS, Linux, iOS, and Android).
MissionPlanner | An open-source Ground Control Station application designed to configure, tune, and monitor vehicles that are ArduPilot based. It allows for planning and execution of complex autonomous missions using GPS, real-time telemetry, and data logs. It is primarily designed for Windows.
Notes: cris

## Slide 28: Computer Vision Algorithms
Algorithm | Summary
YOLO | Fast, single-stage object detector that balances real-time speed with strong accuracy, making it ideal for dynamic environments like aerial surveillance
SSD | Single-stage detector optimized for speed and efficiency on embedded systems, but it sacrifices accuracy—especially for small or distant objects
R-CNN | Uses a two-stage detection pipeline that delivers very high accuracy and robustness to occlusion, but they are too computationally heavy for real-time embedded use
NanoOWL / YOLO-World | An open-vocabulary, vision-language detector that enables flexible text-prompt–based object detection on edge devices, trading some accuracy for adaptability without retraining
Notes: kris

## Slide 29: Which YOLO version to Use?
YOLOv5 is the best choice because it offers the strongest balance of speed, accuracy, and deploy ability for real-time aerial detection.
Version | Pros | Cons | Summary
YOLOv3 | Simple, fast, low computing cost | Lower accuracy, weaker with small object | Older model; falls short for robust real-time aerial detection
YOLOv4 | Improved accuracy and speed compared | Less optimized compared to newer model | Proven option for drone detection
YOLOv5 | PyTorch implementation; easy to train and deploy | Large models may be too heavy Orin Nano | Well-rounded, great for real-time aerial detection
YOLOv7 | Excellent accuracy and efficient training | Heavier than v5; requiring opt. for embedded system | Best for accuracy versus speed
YOLOv8 | Streamlined training and deployment, supports detection | Less UAV-specific research compared to v5 | Versatile option, but adoption in aerial platforms still emerging
Notes: Kris
It has a proven track record in UAV-specific research, demonstrating reliable performance for detecting humans,vehicles, and objects across varying altitudes and environmental conditions. With scalable model sizes and a mature PyTorchecosystem, YOLOv5 can be efficiently tuned to run on embedded platforms like the Jetson Orin Nano while maintaining robust real-time performance.

## Slide 30: Train Custom YOLOv5 Model
Organizing the dataset structure may seem like an intuitive task, but YOLOv5 requires a very specific folder hierarchy to function correctly. Each dataset must contain two main directories: one for images and one for labels. The image folder should include .jpg or .png files, while the label folder should contain corresponding .txt files where each line defines a bounding box using the structure <class_id> <x_center> <y_center> <width> <height>, with all coordinates normalized between 0 and 1. Maintaining this structure ensures YOLOv5 can efficiently pair images with annotations during training and validation.
Notes: kris

## Slide 31: Prototyping and Testing

## Slide 32: Mechanical Prototyping & Testing
Continuous Process
Test mechanical components
Performance evaluation
Problem and proposed solution
Success
Notes: rob

## Slide 33: Software Prototypes & Testing
The two videos to the right show the results of the RGB human detection model. The model runs smoothly is a variety of lighting and has a range of at least 42 feet. However, the model has trouble detecting a human depending on their orientation.
Overall, the model is a success. For best usage, ensure the camera is placed in a well-lit room.
Notes: cris

## Slide 34: Issues and Solutions
Issues | Solutions
New motors are short; propellers are too close to drone frame. | Spacers implemented to increase propeller height.
Electrical noise affecting sensor readings during high throttle. | Improved cable routing and grounding.
Intermittent communication delays between Jetson and Cube Black. | Adjusted baud rates and prioritized MAVLink message streams.
Limited battery life under full payload conditions. | Optimized power management and reduced unnecessary background processes
Limited wi-fi range with just a wi-fi dongle on drone. | Add a router next to the ground computer as the main hub for the wi-fi and connect all devices to it to increase range.
Notes: mic

## Slide 35: Administrative content, Progression and Planning

## Slide 36: Administrative Content
Item | Price | Quantity | Status | LMCO Property
Drone Tubing | $17.99 | 12 | Ordered | 
Drone Frame |  | 3 | Received | Yes
SunnySky Motors | $59.99 | 8 | Ordered | 
Cube Black Flight Controller | - | 5 | Received | Yes
Jetson Xavier | - | 3 | Received | Yes
Motor Mount Clamp | $42.99 | 2 | Ordered | 
TMC Reciever Modules | $23.98 | 3 | Ordered | 
Wifi Adapter | $24.99 | 3 | Ordered | 
Notes: bel

## Slide 37: Administrative Content
Item | Price | Quantity | Status | LMCO Property
Voltage Regulator | $12.15 | 3 | Ordered | 
Propellors | $36.99 | 2 | Ordered | 
ESC | - | 3 | 2 Received | Yes
RGB Camera | - | 1 | Received | Yes
IR Camera | 1 | 1 | Received | Yes
Power Distribution Board | - | 3 | Received | Yes
Wifi Antenna | - | 4 | Received | Yes
Cables/Connectros | - | Various | Received | Yes
Notes: bel

## Slide 38: Administrative Content
Item | Price | Quantity | Status | LMCO Property
Batteries | - | 3 | Received | Yes
Battery Charger | - | 1 | Received | Yes
Socket Cable | - | 3 | Received | Yes
Long Range Communication | - | 6 | Received | Yes
Total Spent: $1097.40
Remaining: $102.60
Notes: bel

## Slide 39: Administrative Content
Name/Major | Primary Responsibilities | Secondary Responsibilities
Adrian Castillo Computer Engineering | Project Lead Motors and Motor Control Component Installation GPS Selection and Implementation | Power Supply Unit (PSU) Integration PCB Design and Implementation Antenna and Communication Setup Accelerometer Setup
Kristopher Tellez Computer Engineering | Camera Selection and Implementation Sensor Selection and Implementation Website Design and Management AI Software Implementation | MCU Implementation Barometer Integration Peripheral Software Implementation
Michael Palin Computer Engineering | Power Supply Unit (PSU) Integration Antenna and Communication Setup and Integration Accelerometer Setup | Motors and Motor Control Component Installation GPS Selection and Implementation
Name/Major | Primary Responsibilities | Secondary Responsibilities
Cristian Gomez Computer Engineering | MCU Implementation Barometer Integration Peripheral Software Implementation | Camera Selection and Implementation Sensor Selection and Implementation Website Design and Management AI Software Implementation
Belle Perry Aerospace Engineering | Structural Analysis Integration & Test Systems Verification CAD Airframe Administrative Planning Part Purchasing LMCO Primary Contact Drone Construction | Material Selection FEA Analysis Structural Integrity Material Testing Vibration/Shock Analysis Flight Profiling Hardware and Frame Verification
Robert Hagerty Aerospace Engineering | Lift/Drag Analysis Aero Design Propellors Flight Dynamics CAD Airframe Motor Selection and Compatibility Drone Construction | FEA Analysis Deformation Stress and Strain Propeller Calculation Weight Distribution Calculation Propulsion Stability
Notes: bel

## Slide 40: Progression and Plan
Test phases will include assembly of two additional drones, integration into drones, system testing through small scale flights, etc.
This phase will also include mechanical system test such as; shock test, long duration test, structural analysis, etc.
Notes: bel

## Slide 41: Progression and Plan
Finalization stage will include full length requirement testing. These will occur at the Lockheed drone club facility in Palm Bay, where the team will conduct mock search and rescue operations
Assignments and presentations will wrap up and be concluded during this stage. Lockheed presentation requirements will be addressed during this final stage.
Notes: bel

## Slide 42: Thank you -LMCO SOAR TEAM
Notes: bel

## Slide 43: Questions?