## Slide 1: Sit & Chow – Smart Training Dog Feeder Final Presentation
Group 25
Advisor:
Dr. Saleem Sahawneh
Review Committee:
Dr. Shahana Ibrahim
Dr. Truong Nghiem
Dr. Tong Wu

## Slide 2: Group 25 Members
Andres Arzola Computer Engineering | Andrew Balmes Electrical Engineering | Natalie Nguyen Electrical Engineering | Maria Tran Computer Engineering

## Slide 3: Motivation and Background
Traditional automatic feeders only have the convenience of feeding pets consistently at scheduled times. However, these systems do not address behavioral training during feeding.
Problem:
  Some dog owners lack a reliable and consistent way to enforce consistent training during feeding time, especially when they are not physically present. As a result, dogs may develop undesirable behaviors, such as barking or jumping.
Our solution:
  The proposed system combines automatic feeding with behavioral training by requiring dogs to “sit” before food is dispensed by combining an automated feeder with machine learning.

## Slide 4: Goals
Allow for owners to check in with their dog at any point of the day through the mobile app and camera.
5
Provide a reliable, automated feeding solution for dogs.
1
Reinforce obedience training by requiring a dog to sit before eating.
2
Allow for owners to conveniently manage feeding times and portions through a mobile app.
3
Monitor system status and system reliability.
4
Objectives
Develop a food dispensing system that operates on a timer.
1
Incorporate a camera to detect a dog’s posture.
2
Design a mobile app for scheduling feeding times, adjusts portion sizes, logs feeding history.
3
Include sensors to check food supply level and how far a dog is from the system.
4
Include a speaker on the system and add the feature on the app.
5

## Slide 5: Engineering Specifications
Aspect | Specifications
Feeding Schedule Accuracy | Within 3 minutes
Low Food Storage Range | Over 20cm
Depth Sensing range | Up to 2 feet
Sound Output | 60-80 dB
FPS | Up to 15fps
Posture Detection Accuracy | At least 70%
Mobile App Features | Creating and editing feeding schedules, quick feed, feeding logs, low food supply notifications, and user authentication
Data Logging Retention | Minimum 30 days
Food Storage Capacity | Maximum 5 kilograms

## Slide 6: Hardware Comparisons

## Slide 7: ESP32-S3
Why We Chose The ESP32-S3
Native Camera Interface for OV5640
More Memory For image Processing
Able to handle multiple sensors
Built in Wi-Fi and USB
 | ESP32-WROOM-32 | ESP32-CAM | ESP32-S3
Camera Support | None (no DVP/CSI interface) | Built-in OV2640 2MP camera (via GPIO) | Native DVP camera interface (supports OV2640, OV5640)
USB Inferface | Requires external UART adapter | Requires FTDI programmer | Native USB OTG — direct flashing and debugging
GPIO Availability | 30+ usable GPIOs | 6–7 available after camera/SD use | 30+ usable GPIOs (depending on module configuration)

## Slide 8: OV5640 Camera
OV5640
High Resolution
Reliable under varying lighting
DVP interface with ESP32-S3
30 FPS @ 1080p for smooth Capturing
 | OV2640 | OV5640 | Realtek AMB82
Resolution | 2 MP (1600x1200) | 5 MP (2592x1944) | 2 MP (1920x1080)
Frame Rate | 15-30 Fps | 30 fps / 1080p | 30 fps /1080p
Cost | Low | Moderate | High
Ecosystem Support | Large Ecosystem | Good Ecosystem | Less support than the other two cameras

## Slide 9: Motor & Motor Driver
Motor | Pros | Cons | Notes
Stepper (NEMA-17) | Open-loop precision, easy microstepping, stall detect with modern drivers | Higher current draw and heat when holding, more expensive | Best choice for auger metering
DC + gearbox | Low cost, efficient | Requires encoder or feedback loop for precision | Suitable for timed dispensing systems
RC Servo | Simple control set up | Limited torque and shorter lifespan | Ideal for flap gates only
Feature | A4988 | DRV8825 | TMC2209
VMOT Range | 8–35V. | 8.2–45V. | Up to ~28V.
Max Current (typical use) | ~1–2A/phase with cooling. | ~1.5–2.2A/phase with cooling. | 2A RMS, 2.8A peak/phase.
Max Microstepping | 1/16 step. | 1/32 step. | 1/256 (via interpolation).
Noise Level | High (audible whine). | High–moderate. | Very low (StealthChop2).
Special Features | Basic protections. | Strong current regulation, protections. | StealthChop2, SpreadCycle, StallGuard4, CoolStep.
Suitability for Dog Feeder | OK for budget prototypes. | Overkill voltage, too noisy. | Best match: quiet, smart, enough current.
Update: after testing and considering, we decided to switch to DRV8825

## Slide 10: Speaker
We decided 3W 4Ω Speaker is a best balance for what we need: moderate power (3W) suitable for embedded drive, lower impedance (4Ω) to use voltage efficiently, and full range for nice tone. The other options either under-power (1W) or over-spec (5W) potentially wasting cost and driving complexity.
Feature | 1W 8Ω Speaker | 5W 8Ω Speaker | 3W 4Ω Full-range Speaker
Loudness (Sensitivity) | Less efficient and likely quieter than the 4Ω option for the same input voltage. | Less efficient than the 4Ω option. | A 4 Ω speaker can be louder than 8 Ω speaker
Pros | Low power rating means very modest current or drive required. 8Ω is a common safe impedance for small amplifiers (the microcontroller audio driver likely can handle it). Lower cost, smaller size. | Higher power handling given more headroom for louder notifications, which may help in presence of ambient noise. Still 8Ω, which is compatible with many drivers. | 4 Ω impedance draw more current at a given voltage, meaning more available acoustic output for the same voltage – useful in low-voltage system. A full-range speaker covers the tone/frequency band of interest (the dispense chime) without needing separate tweeter/woofer 3W rating is the modest but sufficient for a small feeder environment.

## Slide 11: Amplifier
Features | Class A | Class AB | Class D
Efficiency | ~25% (very low). | ~50-70% (moderate). | >90% (very high).
Heat Dissipation | High, requires a large heat sink. | Moderate. | Low, minimal or no heat sink needed.
Fidelity | Very high, low distortion. | High, with minimal crossover distortion. | High, modern designs offer excellent audio quality.
Advantage | Excellent linearity and low distortion (very little crossover distortion) because the device is always on and in its linear region. Good for high-fidelity audio (audiophile territory). | Good compromise: lower distortion than Class B, better efficiency than Class A. Widely used in home audio stereo amplifiers. | Very high efficiency because the devices are either fully on or off (hence minimal wasted power as heat) Compact size, lower heat sink requirement, good for embedded systems (battery or low-power).
Feature | MAX98357A | PAM8403 | PAM8302
Input Type | I²S Digital | Analog | Analog / PWM
Channels | Mono | Stereo (2 ch) | Mono
Noise & Quality | Clean digital path. Low hiss. Great clarity. | Acceptable for simple tones. Noise depends on analog path. | Can pick up noise. Dependent on analog cleanliness.
Power Output (5V) | ~3.2W into 4Ω | ~3W ×2 into 4Ω | ~2.5W into 4Ω
MCU Compatibility | Native support on ESP32 & similar MCUs | Works with PWM/DAC | Works with PWM or simple DAC
Ease of Use | Moderate. Needs I²S setup but straightforward. | Easy. Many ready boards. | Very easy. Minimal configuration.
We started to work with MAX98357A at first. However, after considering about soldering it on main board because of its size, we decided to switch to a new model which is LM386.

## Slide 12: Programmer
Reliable firmware flashing
Better driver experience
Cleaner hardware design
Cheap
Programmer | CP2102 | FT232RL | CH340
Auto-flash | Easy | Easy | Works but less consistent
Driver issues | Rare | Rare | Sometimes
Cost | Low | High | Very low

## Slide 13: Sensing Storage Capacity
Feature | RCWL-1601 | JSN-SR04T | A02YYUW
Key Features | HC-SR04 protocol but works at 3.3 V or 5 V | Waterproof transducer on cable | Waterproof ultrasonic with digital UART output
Pros | Direct ESP32 compatibility; no level shifting; low cost; compact | Very rugged; moisture/dust resistant; long range | Waterproof; noise-filtered digital output; good accuracy
Cons | Not waterproof; dust may degrade accuracy over time | More expensive; mounting more complex; cable + puck footprint | More expensive; UART parsing required; slower update rate
Suitability for Dog Feeder | Best choice for indoor dog feeder; ideal electrical compatibility | Excellent for outdoor or washable feeders; overkill for indoor use | Good for industrial feeders; more complex than needed
Feature | Load cell Sensor | Infrared Sensor (IR) | Capacitive Sensor | Ultrasonic Sensor
Environment Factors | Mostly immune, especially with hermetic sealing. Sensitive to vibrations if measuring minor | Prone to interference from dust, direct sunlight, and changing ambient light. | Sensitive to temperature, humidity and material build-up on the sensor. | Can be affected by extreme temperature changes, but generally reliable in typical home environments.
Pros | Measures actual weight for precise portion control; Can be very accurate and reliable for batching. | Inexpensive and easy to implement. | Low cost, durable, and suitable for non-conductive materials. | Non-contact method is hygienic and not affected by food type or color; Affordable, widely available, and simple to interface with microcontrollers.
Since we only use it inside the house and check for how much food in storage, we decided RCWL-1601 is the best choice for indoor dog feeder and less complex than others.

## Slide 14: Depth Sensor
Sensor | Features
Time-of-Flight Sensor (ToF) | Works in indoor environments Easy to integrate with I2C connection
High Distance Accuracy: cm-level precision, great for verifying that the dog is within feeding range.
Digital I2C Interface: clean integration with the ESP32-S3. No need for pulse timing measurements like ultrasonic sensors.
Quiet: ToF sensor does not emit any audible sounds that may disturb the dog like ultrasonic waves.
Fur: most sensors are sensitive to reflections and light. The ToF sensor is sensitive to sunlight, but the system must be operated indoors.

## Slide 15: Power Management – Power Supply Type
Power Supply | Advantages | Disadvantages
Bench Power Supplies | Highly accurate voltage regulation. Adjustable current limiting prevents component damage. Ideal for debugging, prototyping, and electrical characterization. | Expensive compared to consumer power sources. Bulky and not portable. Not suitable as a final embedded power solution.
Wall Adapters (AC-DC adapters) | Reliable, continuous 24/7 power. Electrically isolated for safety. Available in many voltage/current ratings. Perfect for stationary appliances. | Requires access to a wall outlet. System loses power during outages unless battery backup is added. Cheap adapters may cause electromagnetic noise.
Battery Packs | No auto-shutoff issues (unlike USB banks). Flexible voltage design (1.2 V–12 V+). Inexpensive and safe. Excellent for backup power. | Heavy and bulky. Voltage decreases as cells discharge. Need periodic replacement or charging.
Switching Power Supplies (SMPS) | Very efficient (>85–95%). Minimal heat generation. Supports high input voltage ranges. Available as ICs or off-the-shelf modules. | Switching noise and EMI. Layout must follow strict rules. Requires additional components (inductor, diode, capacitors).
Simple
Maintain the product with enough power to provide continuous and smooth operation

## Slide 16: Power Management – Wall Adapter
Feature | 12V Wall-Mount Adapter | USB-C PD Charger + PD Sink | Desktop Brick
Complexity on PCB | Very low (just barrel jack & filtering) | High: PD sink IC, CC negotiation, etc. | Low (similar to wall-mount)
Cost & BOM Impact | Low total cost | Higher total (charger + PD sink BOM) | Slightly higher than wall wart
User Familiarity | Very familiar | Also familiar, but expects USB devices | Common for laptops/routers
Feature | Facmogu 12V 3A Adapter | Mean Well GS36U12-P1J ( 36 W) | CUI SMI36-12-V-Px (36 W)
Barrel Connector Fit | Flexible (two barrel sizes) | Specified barrel size | Specified barrel size, known connector
Cost / Availability | Likely lower cost | Slightly higher cost but trade-off in reliability | Slightly higher cost but trade-off in reliability
Simple
Cheap
Easy to use

## Slide 17: Power Management – Voltage Regulators
Feature | Linear Regulators | Non-Synchronous Buck Regulators | High-Current Simple Switcher Buck Regulators | Off-the-shelf Buck Modules
Typical Efficiency (12→5 V) | ~42%. | ~70–85 %. | ~85–92 %. | Similar to IC used.
Current Capability | Up to a few A (with huge heatsink). | Up to ~3A. | Up to 5A. | Often 2–3A typical.
Thermal Behavior | Enormous heat: (12–5)·I, up to 35W at 5A. | Moderate heat, manageable at 2–3A. | Several watts of loss at 5A, heat sinkable. | Depends on module quality.
PCB Complexity | Very simple. | Moderate. | Moderate. | Very easy.
Feature | LM2596 | LM2679 | LM22678
Topology | Non-synchronous buck. | Non-synchronous buck. | Non-synchronous buck.
Vin range | 4.5–40 V. | 8–40 V. | 4.5–42 V.
Vout option | Fixed 5V available. | Fixed 5V available. | Fixed 5V available.
Iout max | 3A. | 5A. | 5A.
Typical efficiency (12→5 V) | ~75–85% (design-dependent). | ~85–92% (design-dependent). | ~85–92% (design-dependent).
Layout difficulty | Low–moderate. | Moderate (comfortable for 2-layer). | Moderate–high (more EMI care).
Fit for 5V at 5A dog feeder | Undersized. | Excellent, recommended. | Excellent, but more layout-sensitive.
Problem: SMD chip is too small and cannot test before doing PCB.
Solution: Use LM2576-ADJ for both 3.3V and 5V.

## Slide 18: PCB Design

## Slide 19: Hardware Design
Wall Adapter
3.3V regulator
5V regulator
ESP32
Amplifier
Speaker
Ultrasonic sensor
Depth Module
Camera
Motor Driver
Motor
Programmer
12V

## Slide 20: Voltage Regulators
Since using LM2576-ADJ, we can use this one for both 3.3V and 5V.
We only have to adjust values of R1 and R2 to get the output we need.
We also need to be careful to decide how much current we draw out for this.
LM2576
12Vin
GND
Vout

## Slide 21: Amplifier
LM386
Speaker
Input from ESP32
LM386

## Slide 22: CP2102 programming
USB-A
Connect to ESP32
CP2102

## Slide 23: DRV8825
Connection to ESP32-S3 PCB
Connection to Motor

## Slide 24: ESP32-S3 PCB
ESP32-S3
Camera
Ultrasonic Sensor
Motor Driver
Amplifier
Depth Module
CP2102
3.3V Regulator
5V Regulator

## Slide 25: ESP32-S3 PCB
CP2102 Programmer
Motor Driver
Connecter
Amplifier Connecter
Depth
Module
Camera

## Slide 26: Changes To The ESP32-S3 PCB
What Changed
Amplifier Peripheral switched from the MAX98257A to the LM386 then it was removed from the ESP PCB and created as its own PCB.
3 extra pins were added to the motor driver header to incorporate the new DRV8825 motor driver peripheral
New Amplifier Connecter
3 New Pins

## Slide 27: Software Comparisons

## Slide 28: Mobile Application Stack - Frontend
Category | React Native | Ionic | Flutter
Language | JavaScript / TypeScript (React) | HTML, CSS, JavaScript / TypeScript (Angular, React, or Vue) | Dart
Learning Curve | Easy if familiar with React/JS | Easiest for web developers (HTML/CSS/JS skills reusable) | Moderate — requires learning Dart and widget-based UI paradigm
Ecosystem & Libraries | Mature, vast NPM ecosystem, backed by Meta | Large plugin base, strong web developer community | Growing rapidly, strong official support from Google
Integration with Backend (Firebase, REST APIs) | Excellent — native Firebase SDKs and REST API support | Good — uses JavaScript SDKs; works well with Firebase | Excellent — first-class Firebase integration and SDKs
Google-Backed & Fast-Growing Ecosystem — Flutter's library support is expanding rapidly with strong official backing, ensuring long-term reliability and frequent updates
First-Class Firebase Integration — Flutter offers the best-in-class Firebase and REST API SDK support, making backend connectivity seamless out of the box
Single Language, Full Control — Dart and Flutter's widget-based paradigm give us a consistent, unified development experience across all platforms
Purpose-Built for Mobile — Unlike Ionic (optimized for web devs) or React Native (JS bridge overhead), Flutter compiles natively for true performance

## Slide 29: Mobile Application Stack - Backend
Category | Firebase | Supabase | AWS Lightsail
Ease of Setup | Easiest setup; no servers to manage; seamless with Flutter and mobile SDKs. | Simple setup with SQL-like structure; integrates quickly with Flutter via REST or SDKs. | Requires manual API and server setup; more configuration needed for databases and hosting.
Real-Time Communication | Built-in real-time sync with Firestore and Realtime DB. | Supports real-time updates using PostgreSQL’s replication features. | Must implement custom WebSockets or MQTT for real-time data.
Database Model | NoSQL (Firestore) and JSON structure; ideal for live sync. | SQL (PostgreSQL) with relational querying and constraints. | Choose any (MySQL/PostgreSQL/MongoDB) — manual setup required.
Cost | Free tier + pay-as-you-go; cost increases with high read/write frequency. | Generous free tier; predictable pricing. | Fixed monthly per instance; predictable but may cost more idle time.
Fast & Beginner-Friendly Setup: Firebase provides native Flutter SDK support and requires no server management, allowing us to deploy quickly without extensive backend experience.
Real-Time Cloud Synchronization: Firestore and the Realtime Database enable instant data updates between devices, ensuring a responsive and seamless mobile app experience.
Integrated Storage & Cost Efficiency: Firebase Storage securely handles images and video snapshots, integrates with Cloud Functions and analytics, and offers a generous free tier with scalable pay-as-you-go pricing.

## Slide 30: Embedded Software
Category | C/C++ with FreeRTOS
Use Case | Low-level embedded control for MCU. Run components concurrently.
Advantages | Direct access to hardware registers and peripherals. Runs efficiently with minimal memory. High performance and timing precision. Real-time scheduling ensures deterministic behavior. Enables parallel task management.
Disadvantages | Manual memory management. Limited abstraction. Longer development cycles. Requires careful task priority tuning. More complex.
Deterministic Real-Time Control: C provides precise timing and predictable execution, ensuring near immediate responses when the dog is detected sitting and the motor, time of flight sensor, or speaker must activate.
Low Memory & High Efficiency: With the ESP32-S3’s limited RAM and processing power, C’s low overhead and direct memory control make it ideal for efficient embedded execution.
Direct Hardware Access: C allows direct interaction with registers, drivers, and peripherals, enabling accurate control of the motor, camera, LEDs, speaker, and Wi-Fi module.

## Slide 31: Cloud Server
No sever management: Google Cloud Run does not require any server management, so no Linux maintenance, firewall configuration, or patching.
Built for HTTPS interface APIs: Allowing for an easy integration with Firebase and request routing is handled automatically.
Auto-scaling: It scales automatically for any future upgrades or multiple feeders, and if camera or audio usage becomes frequent.
Simple deployment: Build a Docker container or connect a Github repository, deploy, and get HTTPS URL.
Other Methods: Require server maintenance and setup while providing less flexibility.
Feature | Google Cloud Run
Setup | Easy
Server Management | None
Auto-Scaling | Yes
Best For | REST APIs
CPU Control | 1-8 vCPU (selectable)

## Slide 32: Detection Model
Feature | YOLO (You Only Look Once)
Real-Time Speed | Enables continuous live detection from camera stream
High Accuracy | Already trained to detected general objects, like dogs
Scalability | Multiple model sizes and variants for device efficiency
Fast, real-time detection.
Has lightweight models, so it can run well on CPU.
Pretrained on object classes, including dogs.
Other models would be too slow, less accurate, and reliable for real-time streaming

## Slide 33: Software Design

## Slide 34: Mobile Application

## Slide 35: Mobile Application – Login and Register
The first page that the user sees is the login and register page
When they register, the information they enter is sent to the Realtime Database in Firebase to authenticate the user in the login process
Note there is also a forgot password function on the login page should the user need to use it
Once they register or login, they are sent to the landing page

## Slide 36: Mobile Application – Schedules
The schedules page displays all of the schedules the user has created
A quick feed option is available to immediately activate the feeder, bypassing the detection model should the user need to do so
The user can create a new schedule, assigning different days, times, food amount, and devices the schedule is assigned to
The user can freely edit or delete the schedules created at any time

## Slide 37: Mobile Application – Feed Logs & Devices
By clicking the history icon on the top right of the schedules page, the feed logs page appears
This page tracks the earlier feeds and the amount dispensed
The device page displays all of the currently linked devices
To link a device, the user will simply click on add device and that will route them to the provisioning page where they can configure the Wi-Fi the feeder is set to
The Device ID is generated using the ESP's MAC ID and will be used during device provisioning
The user can name the device once connected and can then freely edit or delete said device

## Slide 38: Mobile App – Live Camera Feed
The camera page will have the list of devices so that the user can select which device's camera they want to see
They can click on the device's name so that they can look through the camera on that device
Once the live feed page is open, the live feed will activate, and the user will be able to see through the camera
There is an interactable microphone symbol that allows the user to speak through their phone out through the speaker on the dog feeder

## Slide 39: Mobile Application – Settings
On the settings page, the user will be able to change their full name
They will be able to verify their email address
A reset password function is available should the user wish to change their password
They are also able to enable their notifications on this page if they turned it off before
Lastly, they can sign out of their account if they wish to do so, sending them back to the login and register page

## Slide 40: Main Feeding Workflow

## Slide 41: Scheduled Feed Workflow
User Scheduled Feeding Time Occurs
Start
Dog In Range?
(2ft)
Publish Outcome To Logs
Dispense Food
Dog Sitting?
(5s)
Dispense Food After 3 Minutes
End
Camera Turns On To Apply Inference
No?
No?
Yes?
Yes?

## Slide 42: Google Cloud Run Services
2 services are deployed:
WebSocket:
Streams camera frames to the mobile app and calls the machine learning prediction for each frame.
Streams microphone audio to speaker.
Machine Learning:
Holds the detection and classification pipeline.
WebSocket Calls ML Service
YOLO Model Detects Dog
Classification Model
Output Posts To Firebase Database
Dispense Food
Publish Output To App Logs
Scheduled Feeding Time

## Slide 43: Posture Detection and Classification Pipeline
The detection and classification pipeline operates in 5 main stages:
Getting the image
Detecting the dog
Displaying and cropping the bounding box
Classifying the posture
Executing the event
YOLO (You Only Look Once) is a computer vision model that is pretrained on the COCO dataset. Dogs are one of the objects it has learned to detect.
A box will be drawn around the dog, and the image will be cropped around the box.
The new cropped image will be passed through a custom binary classification model to determine if the dog is “sitting” or “not sitting.”
The classifier uses a ResNet-18 backbone with a single-logit output layer and trained on a combination of Stanford Dogs images and images captured the system’s camera.
Image Is Cropped Around Dog
Cloud Server Receives Image
YOLO Model Detects Dog

## Slide 44: Prototyping and Testing

## Slide 45: Hardware
Camera Output: 1st main PCB iteration had hardware connection issues where the output was very distorted, causing problems for the ML to run properly.
GPIO Pins: Two GPIO pins connected to the time-of-flight sensor and one GPIO pin connected to the ultrasonic sensor were accidentally wired to pins held by PSRAM. If we wanted to use PSRAM, we would have to free those pins. We solved this by moving three pins meant to set the microstepping on the motor driver and rerouting the ToF sensor and ultrasonic sensor to those newly freed pins.
CP2102 Programmer: Since the chip is too small to solder, we only have 2 of them that work properly.
Voltage Regulators: work well and don’t have problem
Motor: The connectors are smaller than we expected, we need to solder wires to the pins on the motor driver board to the main board. We need to be careful not break the wire connections.

## Slide 46: Google Cloud Run
Successfully integrated Firebase, the mobile app, and machine learning between 2 services, 1 for machine learning and the other streaming the camera and microphone audio.
Problems:
  Microphone audio output: Mismatched endpoints had to be corrected. 1 endpoint to store the microphone input, and 1 to output the audio to the speaker.
  Deployment: WebSocket Service failed to deploy without the proper environment variables, such as missing dependencies, Firebase credentials, and API key.
  Database output: ensuring the final output is written to the correct location and not overwriting pre-existing mobile app functionalities.

## Slide 47: Machine Learning
Pipeline Performance
  ML pipeline performed well before connecting to the system’s camera. However, there were some struggles classifying the posture when the dog is directly facing the camera, so more training images of that view needed to be added. Standardizing the image size and adding padding and clamping to the cropped images ensures all features within the detection bounding box were seen for the classifier.
  YOLO successfully detected dogs on the system’s camera. Detection accuracy was lower using the system’s camera, but not enough to hinder overall performance.
  Classifier performance struggled with the system’s cropped images for sitting poses. Therefore, “sitting” and “not sitting” images had to be taken with the system’s camera to retrain the classifier.
  The final ML output successfully stored in the database to be accessed by the mobile app and ESP32-S3.

## Slide 48: Administrative Content

## Slide 49: Contributions
Senior Design 2 | 
Hardware | 
Andrew | Main PCB, Motor Driver
Natalie | Power Supply System, Amplifier, Programmer, 3D Model for Case
Software | 
Andres | Embedded Firmware, Mobile Application, WebSocket Service
Maria | Detection and Classification Pipeline, WebSocket Service, Machine Learning Service
All | Full System Integration
Senior Design 1 | 
Andres | Project Description, MCU Selection, Mobile Communications, MCU and Mobile Application Software Design, Case Study, Software Testing
Andrew | Hardware Selection (Camera), Standard Constraints, Hardware Design, PCB
Maria | Introduction, Project Description, Hardware (Depth Module), Detection and Classification Model, Software Constraints, Software Testing, BOM
Natalie | Hardware Selection (Motor, Motor Driver, Speaker, Amplifier, LEDs, Button, Sensing Storage Capacity, Power Management), Case Study, Hardware Design, PCBs, Hardware Testing, BOM, Milestone
All | HOQ, Specification Table

## Slide 50: Budgeting
Component | Quantity | Price Total
Stepper Motor | 1 | 3.33
Motor Driver | 1 | 4.59
Power Adapter | 1 | 9.99
Barrel jack | 1 | 0.65
Camera | 1 | 13.76
Voltage Regulators | 2 | 18.64
Amplifier | 1 | 5.95
Speaker | 1 | 1.95
Programmer (CP2102) | 1 | 8.88
USB Port | 1 | 0.50
Ultrasonic Sensor | 1 | 3.95
Depth Module | 1 | 13.00
ESP32-S3 | 1 | 10.67
PCBs | 5 | 252.83
PLA | 6 | 125.94
Total Cost |  | ~474.63

## Slide 51: THANK YOU!
Group 25 wish to thank for the guidance throughout this senior design project:
Mentor: Dr. Saleem Sahawneh
Review committee:
  Dr. Tong Wu
  Dr. Shahana Ibrahim
  Dr. Truong Nghiem
Lab professor: Dr. Arthur Weeks