## Slide 1: On Board Droid
Vehicle Monitor Control System

## Slide 2: Group Members
Josh Estes CpE
Matthew Huereca CpE
Alex Powell EE
Firoz Umran CpE
Group 9

## Slide 3: What is On Board Droid?
A system that allows users to view critical vehicle data as well as control certain aspects of a vehicle via Android application and On-Board Diagnostics port (OBD-II)
A means to communicate with a Vehicle’s Engine Control Unit (ECU)
A cheaper and more comprehensive version of existing systems

## Slide 4: Objectives
Using Android 2.1 or later:
Allow user to view OBD data
Include capabilities to log data such as gas mileage, speed and air pressure
Allow user to turn vehicle on, turn accessories on and start vehicle engine
Allow user to lock and unlock car, roll windows up and down and pop trunk
Allow user to clear error codes

## Slide 5
OBD Functions
Physical Functions
Timing Advance
Engine RPM
Coolant Temperature
Throttle Position
Fuel Level
Time Since Engine Start
Air Intake Temperature
Speed/ Average Speed
Mass Air Flow
Intake Manifold Pressure
Fuel Pressure
Engine Load
Fuel Economy/ Average Fuel Economy/ Miles to Empty
Battery Voltage
Error Codes
Unlock/Lock
Start Engine
Open Trunk
Panic
Roll up/down Windows

## Slide 6: Specifications
Feature Spec
Starting Car 10 Seconds
Window Control 3 Seconds
Lock Control 3 Seconds
Alarm Control 3 Seconds
Trunk Control 3 Seconds
OBD-II Reading 3 Seconds
Bluetooth Connect 10 Seconds

## Slide 7: Specs Continued
Feature Spec
Range 100 meters
Price, project 300 dollars
Price, system 100 dollars

## Slide 8: High Level Design

## Slide 9: High Level Design

## Slide 10: Wireless Communication
Bluetooth or WiFi?
 | Bluetooth | WiFi (a) | WiFi (b) | WiFi (g)
Standard | 802.15 | 802.11a | 802.11b | 802.11g
Frequency(Ghz) | 2.45 | 5 | 2.4 | 2.4
Speed(Mbps) | 0.72 | 54 | 11 | 54
Range | 10 - 100m | 50m | 100m | 100m
Advantage | Low Cost | Speed | Low Cost | Speed
Disadvantage | Range | Cost | Speed | Cost, Range

## Slide 11: BlueSMiRF Gold
Class 1 Radio Bluetooth Modem
Low Power Consumption: 25mA
Operates on 3.3 Volts – 6 Volts
Operates in harsh RF environments like WiFi, 802.11g, and Zigbee
Encrypted Connection
Frequency: 2.4 GHz – 2.524 GHz

## Slide 12: Arduino UNO
C based programming
Large community of developers
Open source hardware
Well documented programming help
Price: $30

## Slide 13: ATmega328 Microcontroller
Compatible with Arduino development board
16 input/output pins
Operates on 5 Volts
6 Volt – 20 Volt input Limits
32Kbytes of flash memory
Price: $9.51

## Slide 14: ELM 327
Supports all OBD-II protocols and automatically selects correct type
Configurable command set
Power Control with standby mode
28 pin chip

## Slide 15: Schematic Diagram

## Slide 16: MCU Software
Receives serial data from bluetooth chip
Compare data header
  If OBD-II data, pass to ELM 327 and listen for response
  Else, compare data further and turn on corresponding relay

## Slide 17: OBD-II Data
Data requests are sent in a standard format from the diagnostics tool (Android) to the OBD-II port.
The first 3 bytes sent are the header. Then, 1 to 7 data bytes follow.
Lastly, there is a check sum byte

## Slide 18: Data Bytes
First data byte is mode – 9 modes, determines the type of data being requested
Second data byte is the parameter identification (PID) which specifies the data being requested
Any additional bytes are used to further specify

## Slide 19: OBD-II Response
The response sent from the vehicle’s ECU back to the OBD-II port, has a similar structure as the request message
3 header bytes, 7 data bytes
The first of the data bytes represents the mode, second represents PID, and remaining bytes represent actual data
Conversions take place in Android application, not MCU

## Slide 20: Response Conversion
PID | Description | # Bytes | Calculation
04 | Load value percent. | 1, A | A*100/255 = engine load%
05 | Coolant temperature in degrees C | 1, A | Deg = A – 40
06 | Short term fuel percent | 1, A | .7812 * (Byte A – 128)
0A | Fuel pressure in kPa | 1, A | Pressure = A * 3
0B | Intake manifold pressure kPa | 1, A | Pressure = A
0C | Engine RPM | 2, A and B | RPM = .25 * (A*256 + B)
0D | Vehicle speed, in km/h | 1, A | Speed = A
0E | Timing advance in degrees | 1, A | Advance = (.5 * A) – 64
0F | Intake air temperature in degrees Celsius | 1, A | Degrees = A - 40
10 | MAF air flow | 2, A and B | Air flow = .01*(256*A+B)
11 | Throttle position | 1, A | Position % = .3922 * A

## Slide 21: Software

## Slide 22: Connecting Via Bluetooth
Create bluetooth device with name of Device
Create bluetooth socket object and connect()
OutputStream out
  out.write()
InputStream in
  in.read()
  Clear buffer after every read

## Slide 23: Reading Issues
Problem
  The reader would get command but program would not get the response.
  Application would sit in an infinite loop.
Reason
  The data would have already been sent before the thread begins to listen for response.
  Since read() is a blocking command it did not allow the program to continue

## Slide 24: Solution
Create a thread whose sole purpose is to listen for response.
Have that thread start before any data is sent to the Bluetooth Device.
Have a boolean variable to tell when the thread has read data so it may clear the buffer.

## Slide 27: ObdFunction
sendFunc(String func)
  Sends command to bluetooth chip described by func.
setInput(InputStream in)
  Sets inputStream from bluetooth socket
Overloaded
  formatResult()
  getUnit()
  getImpUnit()
  run()

## Slide 28: TempObdFunction
transform()
  Used for all obd functions that deal with temperature:
  - 40 used to offset data for negative temperature
getImpUnit()
.

## Slide 29: PressureObdFunction
formatResult()
  Calls transform(int b)
  Data that comes in is the exact amount except in hex.
transform(int b)
  Just convert hex value to decimal except for fuel pressure

## Slide 30: IntObdFunction
Used for functions with Integer values such as RPM and Speed
Each has its own transform and formatResult method.
Also has its own getImpUnit() method based on what the imperial units are

## Slide 31: Error Codes
First have to run DtcNumFunction() to see if the CEL is on and to see how many error codes.
Gives 3 error codes per line:
  numLines = (num+2)/3
When error codes are received they must be decoded.
Clearing error codes must be done with caution

## Slide 32: Error Code Conversion
1ST Digit | Replace w/ | Description
0 | P0 | Power Train Code – SAE defined
1 | P1 | “ “ – Manufacturer Defined
2 | P2 | “ “ – SAE Defined
3 | P3 | “ “ – Jointly Defined
4 | C0 | Chassis Code – SAE defined
5 | C1 | “ “ – Manufacturer Defined
6 | C2 | “ “ – Manufacturer Defined
7 | C3 | “ “ – Reserved for Future
8 | B0 | Body Code – SAE defined
9 | B1 | “ “ – Manufacturer Defined
A | B2 | “ “ – Manufacturer Defined
B | B3 | “ “ – Reserved for Future
C | U0 | Network Code – SAE defined
D | U1 | “ “ – Manufacturer Defined
E | U2 | “ “ – Manufacturer Defined
F | U3 | “ “ – Reserved for Future

## Slide 33: Fuel Economy
Instantaneous data
  14.7 = grams of air to 1 gram of gasoline, which is the ideal air/fuel ratio of most vehicles
  6.17 = density of gasoline in pounds per gallon (lb/gal)
  4.54 = convert pounds per gallon (lb/gal) to grams per pound (g/lb)
  .621361 = conversion of kilometers per hour (KPH) to miles per hour (mph)
  3600 = seconds per hour
  100 = grams per second (g/sec) for mass air flow (Maf)
  Speed = speed of vehicle, from OBD
  Maf = mass air flow of vehicle from OBD

## Slide 34: Logging
Ability to review data that has been obtained previously and calculate average values.
Create a log object every time data is updated from main activity, with time/date, name and value.
Put that value in a file with “functionname”_log as title.
Use file to calculate average value
Delete older values from file if file gets too big.

## Slide 35: Physical Functions
Function | Header | Data
Unlock | FC | 01
Lock | FC | 02
Pop Trunk | FC | 03
Panic | FC | 04
Windows Down | FC | 05
Windows Up | FC | 06
Start | FC | 07
Will not need to listen for a response from the chip.
Send Header byte along with data to perform desired function using sendFunc() method.

## Slide 36: User Interface

## Slide 37: Main Menu
Can manually start connection
Choose the function desired
Simple, easy to understand

## Slide 38: OBD Reader Gauge View
Custom view had to be written for gauges
Uses Canvas object like traditional Java
Draw circle, use image for background
Scale, numbers and label drawn using rotate() on canvas
Other functions call setHandTarget(float input) to change the value of the gauge

## Slide 39: Customizing The Layout
Long-press on any gauge to change its function
Challenge to be able to update each gauge individually
Had to ensure that each gauge had a proper range of values and label

## Slide 40: OBD Reader Graph View
Single-press any gauge to pull up this screen
Real-time graph and larger gauge

## Slide 41: Keypad
Eventually similar to this:
Current layout:

## Slide 42: Issues With Layout
General layout correct but still looked wrong
Had to fill out the screen. Could hard-code dimensions in pixels, but needs to be resolution independent
Set width to 0, use layout_weight parameter
<Button android:id="@+id/unlock“
android:layout_width="0dip“
android:layout_height="fill_parent"
android:layout_weight="1"
android:text="Unlock"/>

## Slide 43: Logs
Logs will be recorded of each function from the OBD and stored in text files on the user’s SD Card
Values can be averaged or shown on a graph

## Slide 44: Log Graphing
Static graph of the selected log
Only graphs the most recent set of data
Buttons to return to log select screen

## Slide 45: Error Codes
Read error codes from OBD
Able to clear errors from the program
Long-press individual error to find out more information online

## Slide 46: View Design Layout
Design separated into Views and ViewGroups
ViewGroups can be embedded
Sometimes custom Views necessary (gauges, graphs)

## Slide 47: Administrative

## Slide 48: Budget
Subsystem | Percent Acquired | Current Total | Projected Total
Hardware Development | 92% | $232 | $252
Software Development | 100% | $0.00 | $0.00
PCB Board | 0% | $0.00 | $150.00
‘98 Honda Accord | 100% | $0.00 | $0.00
Smart Phone | 100% | $0.00 | $0.00
Total | 78% | $232 | $402

## Slide 49: Progress Graph
Chart: 
| Stages
Research | 0.95
Design | 0.85
Hardware Prototyping | 0.3
Software Development | 0.6
Overall System | 0.45
Testing | 0.25

## Slide 50: Next Step
Hardware
Software
Test on Breadboard
Order PCB
Test starting car and rolling windows
Implement logging and graphing
Error handling
Test handling of multiple gauges
UI tweaks