## Slide 1: Digital Guitar Amplifier
Group 5
Shaun Caraway, EE
Matt Evens, EE
Jan Nevarez, CpE

## Slide 2: Motivation and Value of Project

## Slide 3: Goals
Professional grade audio quality (Low noise, high resolution, etc.)
Able to process a guitar signal in real-time with less than 3 ms of latency
Simple user interface
Model various vacuum tube amplifiers, speaker cabinets, and effects

## Slide 4: Specifications
Less than 3 ms of latency
24 bit 96kHz
Maximum input 2 Vpp
Line level output of 1.228 Vrms
Headphone output impedance less than 50Ω

## Slide 5: Over all System design
DSP
Subsystem
TMS320C6657
Converter Subsystem
DAC/ADC
User Interface Subsystem
Digital
signals
Analog I/O
SPI
Regulated
Voltages
Regulated
Voltages
Power Supply
Subsystem
Regulated
Voltages

## Slide 6: Hardware

## Slide 7: Analog Input

## Slide 8: Analog Output

## Slide 9: ADC and DAC

## Slide 10: Amplifier and speaker cabinet modelling
Power Supply
Preamplifier
Power Amplifier
Speaker Cabinet
Effects

## Slide 11: Reference Amplifier

## Slide 12: User Interface Subsystem
Front of Device
LCD Module
264 by 64 pixel LCD module to display menue
Options to the user.

## Slide 13: User Interface Subsystem
CONTROLS
Front of Device
4 buttons aranged in a dimond for directionnel control
2 buttons for Select and De-Select

## Slide 14: User Interface Schematic

## Slide 15: User Interface Subsystem PCB

## Slide 16: User Interface Subsystem PCB
MCU Board
Will use the MP430G2553
to control the LCD module,
receive input from the user
via external buttons and
send commands to the
C6657 DSP over the SPI

## Slide 17: User Interface Subsystem PCB
Controls Board
Used to implement the user controls

## Slide 18: User Interface Subsystem PCB
Connection for LCD
Module
MSP430G2553
Connection for SPI
Connection for
Control board
14-PIN JTAG
Connection
External Power

## Slide 19: User Interface Subsystem
Having the Buttons mounted on their own board separate from the rest of the user
interface will allow the controls to be placed in various locations once the
housing design has been completed.
Controls Board

## Slide 20: DSP Subsystem
TMS320C6657-2 x Core Digital Signal Processor |  | 
Peripherals | On-Chip Memory | Operating Voltages
2xExternal Memory Interface 16 and 32 bit | L1-Cahe 32KB data and 32KB Program per core | Core Supply 0.9 to 1.1V SmartReflex
32 x General Input Output Pins | L2-Cache 3072 KB | CVDD-1V for internal memory
1x Universal Parallel Port | L3- Shared 1024KB | DVDD-1.8V for LVCMOS buffers and internal PLLs
1x I^2C |  | DVD-1.5V for the DDR3 IP buffers
2x Universal Asynchronous Receiver/ Transmitter |  | 
1xSerial Port interface |  | 
2xPeripherial Component Interconnect Express |  | 
4x Serial Rapid Input Output lanes |  | 
1x Ethernet MAC Subsystem |  | 

## Slide 21: DSP Subsystem
DSP
TMS320C6657
Duel Core
1.00GHz
DDR3 1 G-BIT
NOR-FLASH
NAND FLASH
User Interface Subsystem
Converter Subsystem ADC/DAC
EMIF
SPI
GPIO
MCBSP
Utilized Peripherals | 
Peripheral | Use
EMIFx32 | DDR3
EMIFx16 | NAND Flash for program code storage
SPI | Communication with user Interface
 | Interface with NOR-Flash for boot Image
McBSP | Communication with Converter Subsystem
GPIO | Communication with User Interface
 | Communication with Power Sequence MCU
Power Sequence MCU

## Slide 22: DSP Subsystem
CVDD-1v
CVDD SmartReflex
DVDD-1.8V
CVDD-1.5v
CLOCK GENRATOR
Power Sequencing MCU
Power On Sequencing | 
1 | Enable CVDD
2 | Enable CVDD-1V
3 | Enable Clock Source
4 | Enable DVDD-1.8V
5 | Drive the RESETSTAT pin of the C6657 low
6 | Enable CVDD-1.5V
7 | Drive the RESET pin of the C6657 high
8 | Drive the Power On Reset (POR) Pin of the C6657 high
9 | Drive the RESETFULL pin of the C6657
TMS320
C6657

## Slide 23: DSP Subsystem Schematics

## Slide 24: DSP Subsystem Schematics

## Slide 25: DSP Subsystem Schematics

## Slide 26: DSP Subsystem Schematics

## Slide 27: DSP Subsystem Schematics

## Slide 28: DSP Subsystem Schematics

## Slide 29: DSP Subsystem Schematics

## Slide 30: Power Supply - User Interface

## Slide 31: Power Supply - DSP

## Slide 32: Power Supply - DSP
Notes: Fix units

## Slide 33: Power Supply
Notes: Check this slide out
13.5 -> 12.3

## Slide 34: Power Supply Schematic

## Slide 35: Software

## Slide 36: Software Overview
User Interface
Allow for control
Display Menu Options
Signal Interrupts
DSP Software
Model Amplifiers
Model Effects
Allow for various parameter changes
SPI Bus

## Slide 37: User Interface Subsystem
Writing in C via Code Composer
Push buttons generate interrupts
Generates binary coded commands
Transmits to the DSP over the SPI bus in 4 pin mode as slave

## Slide 38: User Interface Subsystem

## Slide 39: User Interface Subsystem
void initSetup ()
void SPITransmite()
void navigate()
void pushButton()
void menuSetup()
int main()
Main
void SPIConfig()
void sendData()
int main()
SPI
void init()
void interrupt()
int main()
Buttons
void initSetup ()
void leftButton()
void rightButton()
void downButton()
void upButton()
void forwardButton()
void backButton()
int main()
Menu
void initSetup ()
void changeDisplay()
int main()
LCD Controller

## Slide 40: DSP Subsystem
Writing in C via Code Composer
Model Amplifiers/Effects
Communicates to the ADC/DAC through the McBSP
Receives controller codes through SPI bus in 4 pin mode as master
Setup the EMIF16/32 to communicate to NAND Flash and DDR3

## Slide 41: DSP Subsystem
void initSetup ()
void SPIReceive ()
void semaphore()
void modelAmplifier()
void modelEffects()
void McBSPtransmit()
void McBSPreceive()
int main()
Main
void SPIConfig()
void clockConfig()
void receiveData()
int main()
SPI
void initSetup()
void changeGain()
void changeBass()
void changeMid()
void changeVolume()
int main()
Amplifier
void initSetup()
void readData()
int main()
EMIF16/32
void McBSPConfig() void receiveData()
void transmitData()
int main()
McBSP
void initSetup()
void changeWet2Dry()
int main()
Effects

## Slide 42: Administrative

## Slide 43: Current Progress
Notes: Hardware design 55% back off
Add %’s

## Slide 44: Milestones

## Slide 45: Distribution of Responsibilities
Shaun
User Interface Hardware
DSP Hardware
Jan
User Interface Software
DSP Software
Matt
Power Supply Design
Analog to Digital Converter
Algorithms
DSP software Algorithm Simulation
Digital to Analog Converter

## Slide 46: Issues
Multi layer DSP PCB layout
High speed digital signal errors
  Parasitic signals
  Timing with the DDR3
Jitter in data converters
  Loss of signal integrity

## Slide 47: Budget

## Slide 48: Questions?

## Slide 49: Copy this slide
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Vivamus et magna. Fusce sed sem sed magna suscipit egestas.
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Vivamus et magna. Fusce sed sem sed magna suscipit egestas.
Lorem ipsum dolor sit amet, consectetuer adipiscing elit. Vivamus et magna. Fusce sed sem sed magna suscipit egestas.