## Slide 1: Puppy Pal
Group 11
Marshall Smith
Afzal Shafi
Cameron Riesen
Anson Contreras

## Slide 2: The face of innocence?

## Slide 3: The face of destruction

## Slide 4: Causes and Solutions
Causes
  Teething stage
  Boredom
  Nervous energy
Solutions
  Toy Doesn’t move, Dog loses interest 
  Another pet May be bad a influence 
  Puppy Pal Mimics the ideal playmate 

## Slide 5: Puppy Pal’s Job
Should prevent destructive behavior while the owner is away
Should not introduce unsafe situations
Should not be a nuisance to people or the dog
Should allow the dog to sleep without interruption
Should not scare timid dogs or lose interest of hyperactive dogs
Should be durable
Should be capable of autonomous operation and user controlled modes

## Slide 6: Accomplishing the job
Detect motion and presence from dog to activate the ball to allow the dog to sleep
Use a ball with replaceable fabric cover to create a distraction with physical and audible interactive play mimicking real animals
  Ball design minimizes points of failure that could be chewed off
  Replaceable fabric cover mimics appearance of real animals
  Audio system mimics nonthreatening but playful sounds made by real animals to accommodate all dogs from timid to hyperactive or aggressive
Keep ball within user defined play area to keep the dog safe and out of trouble

## Slide 7: Subsystems
Mechanical Housing (ball)
Mechanical Drive
Communications
Android Interface
Autonomous Control
User Control
Motion and Proximity Sensing (of the dog)
Power and Charging

## Slide 8: Puppy Pal’s Three Main Components
Ball
  The moving piece housing the motor control, autonomous control, and audio subsystems, as well as communications connecting to an Android device, the Collar, and the Base Charging Station.
Base Charging Station
  The stationary piece housing the location, proximity, and wireless charging subsystems, as well as communications connecting to the Ball.
Collar
  The piece attached to the dog’s collar, housing the motion detection subsystem as well as communications connecting to the Ball.

## Slide 9: Specifications
10 hour battery life (including time spent in low power)
  A typical work day in America requires 10 hours away from home
    8 hours of work, 1 hour of lunch, 1 hour total commute time
Wireless Charging
  The ball should be fully enclosed to maximize durability
    Wireless charging eliminates cords and connectors that could be chewed
Autonomous Control
  The ball should be capable of distracting the dog without human assistance
    Will require a locating subsystem

## Slide 10: Mechanical Housing
Spherical Shape
  Dogs like playing with balls
Shape brings about problems different from traditional robots
  Internal structure being turned upside down
  Measure of distance traveled is not as straight-forward

## Slide 11: Housing Materials
Plastic
  Light
  Transparent
  Easy to drill holes
  Sturdy enough for dogs to play with

## Slide 12: Internal Structure
Buying a Chassis
  No product suiting our requirements was found
Buying Sphero
  Similar project
  Only has 3 inch diameter
  Doesn’t leave us with much to expand on
Purchase is not an option, so we have to build it ourselves

## Slide 13: Internal Structure

## Slide 14: Internal Structure

## Slide 15: Internal Structure
Materials
  Aluminum
    Light
    Able to withstand powerful forces from a dog
  Plastic
    Light
    Consistent with rest of the design

## Slide 16: Internal Structure
Tamiya gearbox controls two motors
Gear ratio of 58:1
Shaft gave us options for different wheels throughout the prototyping stage

## Slide 17: Driving System
The TB6612FNG, a full bridge driver, drives both motors at once.
Change direction of rotation or apply brakes with digital pins.
Able to operate 6V or 12V motors

## Slide 18: Hardware Block Diagram - Ball
Notes: Change Block diagram

## Slide 19: Hardware Block Diagram – Dog Collar

## Slide 20: Bluetooth Communications
Simple to connect and configure (Pairing, Searching, Switching Roles)
Range is adequate for project application
Reliable connection
Will be used to send commands to the ball from mobile device and dog collar.
Multiple modules will be used for simplicity and in addition so incoming commands will not be disrupted.

## Slide 21: Bluetooth Communications
Collar to ball communications will constantly be updating commands with respect to the dog’s activity (wakes up device)
Mobile device to ball communications will send user commands in RC mode (mode switching, manual control, speed control)
Slave devices on the ball, master devices on collar and mobile phone

## Slide 22: HC-05 Bluetooth Module
Class 2 – 2.5 mW, *approx. 30 feet range
Bluetooth Specification v2.0+EDR
2.4 Ghz ISM band
Bluetooth Serial (Master/Slave)
Operating Voltage : 3.3 to 5 VDC
Integrated antenna
Size : 27mm x 13mm x 2mm
Baud rate : 9600 bps
Auto-connects to last device on power as default
Simple to use ATcommands to configure the module

## Slide 23: HC-05 Bluetooth Module

## Slide 24: Dog Collar
Detects motion from the dog
Sends to “Autonomous Mode “when active threshold has been met, sends system to “Waiting” if not.
Broken down into 3 main components
  Bluetooth Module - HC-05
  Microcontroller – ATmega328P
  Accelerometer - ADXL 345

## Slide 25: ADXL 345
3 –axis (X and Y axis input)
SPI Communications – Acts as slave
2g, 4g, 8g, and 16g ranges
  Used 4g , gave us the most accurate readings and 4g is significantly higher than threshold needed
Supply voltage – 3.3 V

## Slide 26: Dog Collar Schematic

## Slide 27: Dog Collar PCB
Dimensions – 1.58 x 1.79 inches
Advanced Circuits – 4pcb.com
Power Supply – 2 CR2032 Coin Cell Battery ( 3 volts each in series)
  5 V - LM7805 voltage regulator (Atmega328P and HC-05)
  3.3 V – Voltage Divider (ADXL 345)

## Slide 28: Dog Collar Flow Diagram

## Slide 29: Ball Schematic - MCU

## Slide 30: Ball Schematic - MCU
ATmega2560

## Slide 31: Ball Schematic - MCU
UART Ports

## Slide 32: Microcontroller
Name | Atmega2560
Clockspeed | 16 MHz
Flash | 256KB
GPIO | 54 Digital, 16 Analog
6 pins for serial (3 total interfaces)
11 channels for 8-bit PWM

## Slide 33: Puppy Pal Software
C++
GNU Make / avr-g++ / avrdude
No STL
Limited DMA

## Slide 35: Puppy Pal Software
3 Major aspects
  Messaging
  Modeing
  Interfacing hardware

## Slide 36: Puppy Pal Software - Messaging
Not specific to Puppy Pal
  How all components communicate with each other
Contain data fields specific to the message
Each message knows how to pack/unpack itself
Directed to appropriate module through the MessageRouter

## Slide 37: Puppy Pal Software - Modeing
Modes define how the system is operating
  controlled by phone, autonomous, waiting for input, ...
Essentially the “forever” loop of the software
The ModeMachine starts, runs and ends modes
  subscribes to mode change messages

## Slide 38: Puppy Pal Software – Interfacing Hardware
Singleton that provides a global access point to all the hardware
  turning LEDs on and off
  setting duty cycle for PWM pins
  writing to GPIO pins
  checking for and handling incoming Bluetooth messages

## Slide 39: Dog Collar Software
Continuously checks accelerometer values
  When values are past a threshold, sends a message to the Puppy Pal that it should turn on

## Slide 40: Autonomous Control
Preliminary Ideas
  Location sensing and pathfinding with IR, WiFi, GPS
    Not enough information, unreliable, large error margins
  Image recognition on the Puppy Pal
    Physical space constraints, code size constraints

## Slide 41: Power and Charging
Ball will be powered by a 12V NiMH Battery, not yet selected
  Depends upon testing, use measured power consumption to calculate battery requirements to meet battery life specification
The Base Charging Station will be powered by a standard 120V outlet
  Stepped down to 5V and transmitted wirelessly from base station to ball
    Transmitter:
      Input 5V DC at 2A maximum
    Receiver:
      Output 5V DC at 1A maximum
    Wireless power transfer efficiency of approximately 60%

## Slide 42: PCB
2 Layer Design Required
Utilize existing designs from Arduino to minimize design work
Design using Eagle freeware
Using 4PCB’s $33.00 2 layer student deal

## Slide 43: PCB Schematic

## Slide 44: PCB Board

## Slide 45: Work Distribution
 | Marshall Smith | Cameron Riesen | Afzal Shafi | Anson Contreras
Mechanical Design | x |  | x | ●
Motor Control |  | x |  | ●
Android Application |  | ● | x | 
Communication |  | x | ● | 
Location Detection | x | ● |  | 
Motion/Proximity Sensing | ● | x |  | x
PCB | x |  | ● | 
Power System | ● |  |  | x
Embedded Software |  | ● |  | 
● - Key Responsibility | x – Contribution |  |  | 

## Slide 46: Budget – Total
Component | Quantity | Price
Ball Enclosure | 1 | 10.99
Arduino Mega 2560 | 1 | 15.00
Bluetooth Module(s) | 5 | 20.00
DC Motors | 2 | 10.00
Android Device | 1 | Owned
PCB Ball | 1 | 316.00
PCB Dog Collar | 1 | 50.00
Accelerometer | 1 | 5.00
Gear Box | 2 | 12.00
Misc. Mechanical Parts | 1 | 30.00
Misc. Electrical Parts | 1 | 20.00
12 V Battery | 1 | 40.00
Dog Collar Battery | 1 | 20.00
Total | 19 | 548.99