## Slide 1: Puppy Pal
Group 11
Marshall Smith
Afzal Shafi
Cameron Riesen
Anson Contreras

## Slide 2: The face of innocence?

## Slide 3: The face of destruction

## Slide 4: Causes and Solutions
Causes
  Teething stage
  Boredom
  Nervous energy
Solutions
  Toy Doesn’t move, Dog loses interest 
  Another pet May be bad a influence 
  Puppy Pal Mimics the ideal playmate 

## Slide 5: Puppy Pal’s Job
Should prevent destructive behavior while the owner is away
Should not introduce unsafe situations
Should not be a nuisance to people or the dog
Should allow the dog to sleep without interruption
Should not scare timid dogs or lose interest of hyperactive dogs
Should be durable
Should be capable of autonomous operation and user controlled modes

## Slide 6: Accomplishing the job
Detect motion and presence from dog to activate the ball to allow the dog to sleep
Use a ball with replaceable fabric cover to create a distraction with physical and audible interactive play mimicking real animals
  Ball design minimizes points of failure that could be chewed off
  Replaceable fabric cover mimics appearance of real animals
  Audio system mimics nonthreatening but playful sounds made by real animals to accommodate all dogs from timid to hyperactive or aggressive
Keep ball within user defined play area to keep the dog safe and out of trouble

## Slide 7: Subsystems
Mechanical Housing (ball)
Mechanical Drive
Communications
Android Interface
Autonomous Control
User Control
Location Detection (of the ball)
Motion and Proximity Sensing (of the dog)
Power and Charging

## Slide 8: Puppy Pal’s Three Main Components
Ball
  The moving piece housing the motor control, autonomous control, and audio subsystems, as well as communications connecting to an Android device, the Collar, and the Base Charging Station.
Base Charging Station
  The stationary piece housing the location, proximity, and wireless charging subsystems, as well as communications connecting to the Ball.
Collar
  The piece attached to the dog’s collar, housing the motion detection subsystem as well as communications connecting to the Ball.

## Slide 9: Specifications
10 hour battery life (including time spent in low power)
  A typical work day in America requires 10 hours away from home
    8 hours of work, 1 hour of lunch, 1 hour total commute time
Wireless Charging
  The ball should be fully enclosed to maximize durability
    Wireless charging eliminates cords and connectors that could be chewed
Autonomous Control
  The ball should be capable of distracting the dog without human assistance
    Will require a locating subsystem

## Slide 10: Mechanical Housing
Spherical Shape
  Dogs like playing with balls
  Enclosure keeps dog away from the motor and the electronics that would be exposed if we use a rectangular chassis
Shape brings about problems different from traditional robots
  Internal structure being turned upside down
  Measure of distance traveled is not as straight-forward

## Slide 11: Housing Materials
Plastic
  Light
  Comes in variety of colors
  Transparent or oblique
  Easy to drill holes
  Sturdy enough for dogs to play with
  Custom ordered or taken from other products

## Slide 12: Housing Materials
3D printed ABS
  3D printer available on-campus
  Strong
  Impact-resistant
  Gives us the option to print out the internal structure already inside
  Expensive: $7 per cm3
Acryllic
  Can be ordered in any size
  Only comes in hemispheres or as a solid piece with a single opening
  Once hemispheres are sealed closed, we won’t have access to the inside of the robot

## Slide 13: Housing Materials
Alfie Hamster Ball
  Plastic
  Hemispheres can be connected and separated easily
  6 inch diameter
  Two openings with 3 inch diameters
  Allows us to take apart the ball to troubleshoot during testing and construction

## Slide 14: Internal Structure
Buying a Chassis
  No product suiting our requirements was found
Buying Sphero
  Similar project
  Only has 3 inch diameter
  Doesn’t leave us with much to expand on
Purchase is not ideal, so we have to build it ourselves

## Slide 15: Internal Structure

## Slide 16: Internal Structure
Materials
  Aluminum
    Light
    Plenty available in Home Depot and Skycraft
  Wood
    Insulator
    Bulky if not purchased with correct thickness
    Home Depot can cut the wood for us
    Cheap
  Plastic
    Light
    Consistent with rest of the design
    Different colors can give the project more personality
    Constructed with salvaged plastic
    Produced with a 3D printer with mounts for motors, PCB, and batteries already built-in

## Slide 17: Driving System
We are using the Arduino Motor Shield to drive our motors
It uses the L298P, a full bridge driver, to drive both motors at once
Able to operate our 12V and 6V motors

## Slide 18: Progress
We have tested mechanical output of our motors and the amount of current required
Test also showed the effectiveness of the motor shield

## Slide 19: Hardware Block Diagram - Ball

## Slide 20: Bluetooth Communications
Simple to connect and configure (Pairing, Searching, Switching Roles)
Range is adequate for project application
Connection to mobile device
Will be used to send commands to the ball from mobile device and dog collar.
Potentially may be used to receive commands from charging station
Multiple modules will be used so incoming commands will not be disrupted

## Slide 21: Bluetooth Communications
Collar to ball communications will constantly be updating commands with respect to the dog’s activity
Mobile device to ball communications will send user commands in RC mode
Charging Station will update commands with respect to location

## Slide 22: HC-05 Bluetooth Module
Class 2 – 2.5 mW, *approx. 30 feet range
Bluetooth Specification v2.0+EDR
2.4 Ghz ISM band
Bluetooth Serial (Master/Slave)
Operating Voltage : 3.3 VDC
Integrated antenna
Size : 27mm x 13mm x 2mm
Baud rate : 9600 bps
Auto-connects to last device on power as default
Simple to use ATcommands to configure the module

## Slide 23: HC-05 Bluetooth Module

## Slide 24: Mobile Application
User Input
Movement and Speed Control
  Button
  Tilt
Switching Modes
Configure boundaries
Settings

## Slide 25: Audio Output
Ideally will be used to attract the dog to the system
Will play short sound clips
Triggered by the commands received by the collar via Bluetooth (Autonomous Mode)
Triggered by the user in RC mode via mobile application
Potential methods for sound generation
  Modified MP3 Clip Player – cheap, doesn't add too much hardware, not a lot of information.
  VS1053b - References available, Libraries available, requires more hardware

## Slide 26: Audio Decoder - VS1053B
High Performance DSP processor core
MP3, AAC, WMA,MIDI files
Low power operation
Receives input bitstream through the SPI bus
Bass ,treble, and volume controls
Shield available for testing

## Slide 27: Audio Output – Schematic

## Slide 28: Audio Output – Schematic
VS1053B – Audio Decoder

## Slide 29: Audio Output – Schematic
MicroSD card

## Slide 30: Audio Output – Schematic
External
Speaker
Connection

## Slide 31: Ball Schematic - MCU

## Slide 32: Ball Schematic - MCU
ATmega2560

## Slide 33: Ball Schematic - MCU
UART Ports

## Slide 34: Ball Schematic – Motor Driver

## Slide 35: Ball Schematic – Motor Driver
L298P – Motor Driver

## Slide 36: Ball Schematic – Motor Driver
MCU Input Ports

## Slide 37: Ball Schematic – Motor Driver
12 Volt Battery

## Slide 38: Microcontroller
Name | Atmega2560
Clockspeed | 16 MHz
Flash | 256KB
GPIO | 54 Digital, 16 Analog
6 pins for serial (3 total interfaces)
11 channels for 8-bit PWM

## Slide 39: Puppy Pal Software
C++
GNU Make / avr-g++ / avrdude
No STL
Limited DMA

## Slide 41: Puppy Pal Software
3 Major aspects
  Messaging
  Modeing
  Interfacing hardware

## Slide 42: Puppy Pal Software Messaging
Not specific to Puppy Pal
  How all components communicate with each other
Contain data fields specific to the message
Each message knows how to pack/unpack itself
Directed to appropriate module through the MessageRouter

## Slide 43: Puppy Pal Software Modeing
Modes define how the system is operating
  controlled by phone, autonomous, waiting for input, ...
Essentially the “forever” loop of the software
The ModeMachine starts, runs and ends modes
  subscribes to mode change messages

## Slide 44: Puppy Pal Software Interfacing Hardware
Singleton that provides a global access point to all the hardware
  turning LEDs on and off
  setting duty cycle for PWM pins
  writing to GPIO pins
  checking for and handling incoming Bluetooth messages

## Slide 45: Dog Collar Software
Continuously checks accelerometer values
  When values are past a threshold, sends a message to the Puppy Pal that it should turn on
  moar

## Slide 46: Autonomous Control
A few different ideas tossed around
  Location sensing and pathfinding with IR, WiFi, GPS
    Not enough information, unreliable, large error margins
  Image recognition on the Puppy Pal
    Physical space constraints, code size constraints

## Slide 47: Autonomous Control
Finally settled with Xbox Kinect
  Pros
    Powerful, easy to use, acts as an overseer,
  Cons
    Requires the Kinect, requires Windows machine

## Slide 48: User Control
Finally settled with Xbox Kinect
  Pros
    Powerful, easy to use, acts as an overseer,
  Cons
    Requires Windows machine, NEED OTHERS

## Slide 49: Location Detection
Kinect
  Additional Hardware
  Strong Performance
  Limited Range
Embedded or Desktop OpenCV
  Both require additional hardware
  Embedded requires more processing power
  Desktop requires additional hardware
GPS
  Signal strength and accuracy issues when in buildings and urban areas
  Limited accuracy

## Slide 50: Motion and Proximity Sensing of the Dog
The motion and proximity sensing will be handled separately
Motion detection will be accomplished by a collar worn by the dog containing an accelerometer and Bluetooth communications system.
  This allows us to determine if the dog wakes up outside of the play area and will signal the ball to attempt to bring the dog into the play area using sounds.
  ADXL362 digital 3-axis accelerometer for ease of prototyping using an available breakout board
Proximity sensing will be accomplished by the Kinect and a laptop on the Base Charging Station and locations transmitted from to the ball via Bluetooth.

## Slide 51: Collar Block Diagram

## Slide 52: Collar Schematic
Passive: 33
Active: 3

## Slide 53: Power and Charging
Ball will be powered by a 12V NiMH Battery, not yet selected
  Depends upon testing, use measured power consumption to calculate battery requirements to meet battery life specification
The Base Charging Station will be powered by a standard 120V outlet
  Stepped down to 5V and transmitted wirelessly from base station to ball
    Transmitter: BQ500211A
      Input 5V DC at 2A maximum
    Receiver: BQ51013B
      Output 5V DC at 1A maximum
    Expected wireless power transfer efficiency of 60%

## Slide 54: Base Charging Station Block Diagram

## Slide 55: Base Charging Schematic
Passive: 120
Active: 18

## Slide 56: PCB
4 Layer Design Required
  Component Layer, Ground Layer, Routing Layer, Ground Layer
Utilize existing designs from Arduino to minimize design work
Design using Altium, Eagle freeware board size too small
Using 4PCB’s $66.00 4 layer student deal
Try to fit full project on the maximum 30 square inch board

## Slide 57: Work Distribution
 | Marshall Smith | Cameron Riesen | Afzal Shafi | Anson Contreras
Mechanical Design | x |  | x | ●
Motor Control |  | x |  | ●
Android Application |  | ● | x | 
Communication |  | x | ● | 
Location Detection | x | ● |  | 
Motion/Proximity Sensing | ● | x |  | x
PCB | x |  | ● | 
Power System | ● |  |  | x
Embedded Software |  | ● |  | 
● - Key Responsibility | x – Contribution |  |  | 

## Slide 58: Project Progress
Chart: 
| Research | Parts Acquisition | Prototyping | Testing | Overall
Series 1 | 90 | 60 | 30 | 30 | 40

## Slide 59: Budget – Total
Component | Quantity | Price
Arduino Motor Shield | 1 | 26.56
Ball Enclosure | 1 | 10.99
Arduino Mega 2560 | 1 | 15.00
Bluetooth Module(s) | 5 | 20.00
DC Motor | 1 | 5.95
DC Motor2 | 1 | Owned
Kinect | 1 | Owned
Android Device | 1 | Owned
PC | 1 | Owned
PCB | 1 | 66.00
Accelerometer | 1 | 14.95
Audio System | 1 | 10.00
Misc. Mechanical Parts | 1 | 30.00
Misc. Electrical Parts | 1 | 20.00
12 V Battery | 1 | 40.00
Total | 17 | 259.45
Total Spent | 11 | 78.50

## Slide 60: Issues
Location subsystem
  Kinect greatly increases the hardware requirements for this project (Kinect and Computer)
  GPS signal will suffer greatly indoors, and may completely lose connection
  OpenCV also greatly increases the hardware requirements (Camera and Computer or high performance microcontroller)
Mechanical subsystem
  Minimal experience, minimal documentation on similar projects