## Slide 1: Hydroponics with Automated Reporting and Monitoring
Group 15
David Mascenik (Electrical Engineer)
Jon Spychalsky (Electrical Engineer)
James Tooles (Electrical Engineer)
Sponsored by Duke Energy

## Slide 2: What is Hydroponics?
"Growing plants in the absence of soil."
Nutrients and air dissolved in the water, directly absorbed by the plant roots
Sensitive to:
  pH
  Dissolved Oxygen
  Temperature (water and air)
  Contamination (fungi and molds)
Design Choice: Implement the Nutrient Film Technique to cultivate the test plant (tomatoes) for the project.
Figure 1

## Slide 3: Project Motivations And Goal
Motivation 1: Investigate hydroponic science, which has the potential to be:
  Resource Efficient (Nutrients)
  Space efficient (Vertical Growing)
  More Controllable
Motivation 2: Develop skills that will be desirable in the job market:
  Embedded Programming
  PCB Layout Design
Project Goal: Automate the care and maintenance of a hydroponic system.
  Design boards for the MCU, Automation, and Solar Charge Controller.
  Analyze sensor data to on/off control automation subsystems
  Post data to a local server

## Slide 4: Specifications and Requirements
Table 1
Table 2

## Slide 5: Standards and Specifications
RS232 UART
Inter-Integrated Circuit (I2C)
802.11 b/g/n
JTAG Interface (IEEE 1149.1)
C Programming Language (ISO 9899)
Chip Package Types

## Slide 6: Hardware Block Diagram

## Slide 7: Power Distribution

## Slide 8: Solar Panel
HQRP Mono-Crystalline Solar Panel
  50 Watt Power Rating
  12V Operating Voltage
  Mono-Crystalline Solar Panel
  6.07kg (13.4lb) Weight
  53.3cm x 73..66cm x 3.81cm (21in x 29in x 1.5in) Dimensions
Figure 2

## Slide 9: Solar Charge Controller
Specifications
  50W Solar Panel Input
  7V - 14V Adjustable Output
  Dropout Voltage of 1.25V @4A
  4A Maximum Current
  Charging of Sealed Lead Acid
  Reverse Battery Protection
Figure 3
Reference Design: Electroschematics

## Slide 10: Selecting Battery Chemistery
Sealed Lead Acid
(SLA)
20% The Cost of LiFePO4
Low Charging and Discharging Complexity
Wide Operation Temperature Range -40C - 45C
No Battery Memory
Minimal Self Discharge
Lithium Iron Phosphate
(LiFePO4)
75% The Weight of SLA
Higher Charge Density
65% The Volume of SLA
7 Times The Life Cycle of SLA
No Harmful Elements
Minimal Voltage Sag

## Slide 11: Sealed Lead Acid Battery
Odyssey PC925
  12V Nominal Voltage
  28Ah Capacity
  11.8kg (26lb) Weight
  M6 or SAE 3/8" Receptacle Terminals
Figure 4

## Slide 12: Voltage Regulation Goals
Need to Reduce the Voltage from the Battery.
Need to Output Multiple Voltages.
Since linear regulators are inefficient, and efficiency is important for our project, we decided to use switching voltage regulators.
An efficiency of 85% or greater for the regulators is a minimum, but a >90% efficiency is ideal.

## Slide 13: TPS563200 Switching Voltage Regulator Overview
Description | Value
Input Voltage Range | 4.5V – 17V
Output Voltage Range | 0.76V – 7V
Feedback Voltage Accuracy | 1%
Operating Temperature | -40°C – 85°C
Efficiency | Varies (graph on next slide)
Figure 5
Table 3

## Slide 14: TPS563200 Switching Voltage Regulator Efficiency Graph
For 5V Output, Greater than 85% Efficiency at ~5mA, Greater than 90% Efficiency at ~20mA.
For 3.3V Output, Greater than 85% Efficiency at ~15mA, Greater than 90% Efficiency at ~600mA.
Figure 6

## Slide 15: 12V Input to 5V Output Schematic Design
Figure 7
Based on Reference Design: Texas Instruments

## Slide 16: 12V Input to 3.3V Output Schematic Design
Figure 8
Based on Reference Design: Texas Instruments

## Slide 17: Complete Voltage Regulator PCB Design
Figure 9

## Slide 18: Power Switch
Receive TTL Commands to Selectively Engage Hydroponic Automation Subsystems.
Multiplexor to Solid State Relays
  Hold Circuit to Hold MUX Output
  MUX = CD74HC4067
  SSR = S108T02
Modulate
  Water Pump
  LED Light Array
  Solenoid Valves
  Nutrient Tiller
Solid State Relay - SHARP Datasheet
Figure 10a
Figure 10b

## Slide 19: Power Switch Control

## Slide 20: The Microcontroller
Project Requirements:
  Take Sensor Readings From 5 Separate Devices
  At Least 4 GPIO Necessary For Automation Subsystems
  Communicate to Web Server Wirelessly
  Display Sensor Readings Locally on an LCD Display
Summary:
  At Least 1 I2C And 2 SPI Ports
  At Least 1 UART For Debugging Over Serial
  Min. 32kB of Space For User Code

## Slide 21: Microcontroller - Comparisons
Table 4

## Slide 22: Automation Subsystems - Water Pump
Boat Bilge Pump
  500 Gallons per Hour
  12VDC @ 2Amps
  Submersible
  MSRP $30 - Donated to Project
Figure 11

## Slide 23: Automation Subsystems - LED Array
RV LED Lights
  250 Lumens
  12VDC @ 200mA
  Sufficient Spectrum for Plants
  MSRP $8 per Bulb
Figure 12
Figure 13

## Slide 24: Automation Subsystem - Nutrient Tiller
"Archimedes Water Screw" Design
Stepper Motor
  Step Angle = 3.6 deg
  12VDC @ 150mA per Phase
  Auger Bit Mounted to Till Nutrient Solute
Figure 16
Figure 15
Figure 14

## Slide 25: Automation Subsystem - Water Flush
Solenoid Valves Between Water Pump and Hydroponic System Intake
Flush Water Reservoir
  Out of Range Ph Value
  Watchdog Limit: 1 Week
Solenoid Valves
  12V @ 400mA
  Off-State = Valve Closed
  One Valve Active At A Time
Figure 17

## Slide 26: Sensors

## Slide 27: Types of Sensors
Ambient Light Sensor
Ambient Temperature Sensor
Ambient Humidity Sensor
Barometric Pressure Sensor
Water Level Sensor
Water Temperature Sensor
pH Sensor
Dissolved Oxygen Sensor

## Slide 28: Texas Instruments Sensor Hub
Sensirion SHT21
  Humidity Sensor
  Ambient Temperature Sensor
Intersil ISL29023
  Ambient Light Sensor
  Infrared Light Sensor
TMP006
  Non-Contact Infrared Temperature Sensor
Bosh Sensortec BMP180
  Barometric Pressure Sensor
Figure 18

## Slide 29: Water Level Sensor
eTape Continuous Fluid Level Sensor PN-12
  12" Long
  Resistive Output
  0.25mm (0.01") Resolution
  1500Ω (Empty) - 300Ω (Full)
  0.5W Power Rating
  -9C - 65C Temperature Range
Figure 19

## Slide 30: Water Temperature Sensor
Waterproof DS18B20
  Digital Water Temperature Sensor
  3V - 5V Operating Voltage
  9 - 12 bit Selectable Resolution
  0.5C Accuracy
  -10C - 85C Temperature Range
Figure 20

## Slide 31: pH Sensor
Atlas Scientific EZO Embedded pH Sensor
  UART or I2C Protocol
  3.3V - 5V Operating Voltage
  0.001 - 14 pH Range Readings
  0.02pH Resolution
  Waterproof Probe
  0.995mA at 3.3V Sleep Mode
Figure 21

## Slide 32: Dissolved Oxygen Sensor
Atlas Scientific EZO Embedded Dissolved Oxygen Sensor
  UART or I2C Protocol
  3.3V - 5V Operating Voltage
  0 - 20 mg/L Readings
  0.1 mg/L Resolution
  Waterproof Probe
  0.995mA at 3.3V Sleep Mode
Figure 22

## Slide 33: User Interface

## Slide 34: User Interface Specifications
A Web-Based and LCD Touchscreen Based Interface.
View Current Sensor Readings and Threshold Alerts.
Ability to Manipulate Alert Thresholds.
Manually Activate Numerous Parts of the System.
  A Resistive Touch LCD Screen for Control at the Site.
  Beaglebone Black Web Server for Remote Viewing and Control.
Around 5 Minute Sensor Refresh
Ability to Manually Refresh Sensors.
Straightforward and Simple to Use UI.

## Slide 35: Kentec 3.5” LCD Touchscreen Overview
Decent Size.
Can Fit Multiple Elements on Screen Easily.
Touchscreen Allows Ease of Use of Control of the System.
Supported by Texas Instruments’ Graphics Library.
Parallel Data Connection.
Figure 23

## Slide 36: Kentec 3.5” LCD Touchscreen Specifications
 | Value
Operating Voltage | 3.3V & 5V
Resolution | 320 x 240
Interface | 16-bit parallel
Operating Temp. | -20 – 70°C
Figure 24
Table 5

## Slide 37: LCD Touchscreen Flowchart

## Slide 38: Web-based Interface Goals
In Addition, a Similar Featured Web Interface to the LCD Interface.
Adds a Database for History.
Manipulate Alert Thresholds and Control Subsystems.
Can Access the System Remotely, No Need to Be at the Location.

## Slide 39: BeagleBone Black Overview
Open Source Hardware and Tons of Documentation.
69 GPIO Pins, Easy to Interface With.
4GB On-Board eMMC, No Need for a microSD Card.
Low Power Consumption (between 1-2W).
Free from the Innovation Lab.
Large Community.
Built-in Simple to Use Node.js Web Server.
Figure 25

## Slide 40: Wireless Module Goals
Needed a Longer Range Communication Device Between MCU and BeagleBone Black.
Wires Not Practical, a Wireless Approach is Needed.
Should Use Low Power
Should Have 10-15 Meter Range
Should Be Less Than $20
Should Be Easy to Implement

## Slide 41: NRF24L01+ Wireless Transceiver Overview
Uses 2.4 – 2.525 GHz RF
Can Use up to 126 Channels
Range of About 30 Meters
Powered by 3.3V (Same as MCU and Beaglebone Pins)
Uses SPI for Communication
Has an Interrupt Pin
Has an Ultra Low Power Mode
Only About $7 for a Pair
Figure 26

## Slide 42: NRF24L01+ Wireless Transceiver Specifications & Block Diagram
 | Value
Operating Voltage | 1.9 – 3.6V
Maximum Current Draw | 13.5mA
Standby Current Draw | 26µA
Data Rates | 250kbps, 1Mbps, 2Mbps
Operating Temp. | -40 – 125 °C
Figure 27
Table 6

## Slide 43: Camera
TMEZON Outdoor IP Camera
  1.0 Mega Pixels
  720p
  24 IR LEDs
  Night Vision
  Power Over Ethernet (POE)
  Weatherproof
  IP66 Water Resistance
  Self Hosting IP Camera Stream
  WiFi 802.11 b/g/n Compliant
Figure 28

## Slide 44: Administrative Content Progress Chart
Chart: 
| Testing | Prototyping | Software | Design | Research
Percent Complete | 25 | 40 | 20 | 90 | 95

## Slide 45: Administrative Content Work Distribution
 | David | James | Jon
PCB Design | X | X | X
Web Server | X |  | 
Sensor Integration |  | X | 
Control Signals Integration |  |  | X
LCD Screen | X |  | 
Power Distribution | X | X | X
Pump, Tiller, Hydroponics System |  |  | X
Table

## Slide 46: Administrative Content Budget
Device | Device Type | # of Units | Price per Unit
Solar Panel | Power Distribution | 1 | $103.95
Battery | Power Distribution | 1 | $152.95
Sensor Hub | Sensor | 1 | Free (TI Innovation Lab)
Water Level Sensor | Sensor | 1 | $39.99
Water Temperature Sensor | Sensor | 1 | $9.95
pH Sensor | Sensor | 1 | $105.95
Dissolved Oxygen Sensor | Sensor | 1 | $199.95
Camera | User Interface | 1 | $43.99

## Slide 47: Administrative Content Budget (cont)
Device | Device Type | # of Units | Price per Unit
LCD Touch Screen | User Interface | 1 | $33.25
BeagleBone Black | User Interface | 1 | Free (TI Innovation Lab)
Tiva C TM4C1294 | Microcontroller | 1 | Free (TI Sample)
TPS563200 | Voltage Regulator | 2 | Free (TI Sample)
Various passive devices | Passives for Regulator | Multiple | $1.43 for all
Wires | Wires | 1 set of 120 | $9.99 per set
Bilge Pump | Water Pump | 1 | $33.99
nRF24L01+ | Wireless Module | 2 | $3.42
Solid-State Relays | Active Device | 4 | $4.99
LED Bulbs | Light | 2 | $30.99

## Slide 48: Administrative Content Budget (cont)
Device | Device Type | # of Units | Price per Unit
Auger Bit | Hardware | 1 | $11.99
Stepper Motor | Motor | 1 | Free
Solenoids | Active Devices | 2 | $12.99
3/4" Hosing | Hardware | 4 | $3.95
 |  | Total | $803.72
 |  | Duke Funding | $1250.00
 |  | Remaining Funds | $446.28
Table 7

## Slide 49: Constraints
Time (Shorter Semester)
Money (Cost vs Performance)
Practical Experience
Mechanical Design Knowledge
Manufacturing
  No Low Cost Pick and Place
  No Low Cost Reflow Station
  No Low Cost and High Quality PCB Design Software Package

## Slide 50: Difficulties and Successes
Difficulties
  Software Development With Only Electrical Engineers
Successes
  Wireless Communication Between the MCU and BeagleBone Black
  Completed Hydroponic System
  Learning a Large Amount of Practical Design Applications

## Slide 51: Immediate Plans
Finish PCB Designs
Order PCB Designs
Complete Sensor Interfacing
Develop Code for Subsystem Integration
Develop Code for Web Server
Develop Code for LCD Interface

## Slide 52: Figure Sources
Figure 1 - http://hydroponie.fr/mendota-hydroponie-production-local-solution-global/
Figure 2 - http://www.amazon.com/HQRP-Mono-crystalline-Anodized-Aluminum-Warranty/dp/B002OSAB28
Figure 3 - http://www.electroschematics.com/6899/12v-ldo-solar-charge-control/
Figure 4 - http://www.amazon.com/Odyssey-PC925-Automotive-LTV-Battery/dp/B0002ILK72
Figure 5 - http://www.ti.com/product/TPS563200/datasheet
Figure 6 - http://www.ti.com/product/TPS563200/datasheet
Figure 10a - http://cdn.sparkfun.com/datasheets/Components/General%20IC/S108,208T02%20Series.pdf
Figure 11 - www.amazon.com
Figure 12 - www.amazon.com
Figure 13 - http://www.electronicsweekly.com/
Figure 14 - http://www.robosoftsystems.co
Figure 15 - www.fine-tools.com
Figure 16 -
Figure 17 - www.adafruit.com
Figure 18 - http://www.ti.com/tool/boostxl-senshub
Figure 19 - http://www.adafruit.com/products/464
Figure 20 - https://www.sparkfun.com/products/11050
Figure 21 - http://atlas-scientific.com/product_pages/kits/ph-kit.html
Figure 22 - http://atlas-scientific.com/product_pages/kits/do_kit.html
Figure 23 - http://www.kentecdisplay.com/uploads/soft/Products_spec/EB-LM4F120-L35_UserGuide_04.pdf
Figure 24 - http://www.kentec.com.hk/images/UploadFile/20111115190922-7.pdf
Figure 25 - http://www.logicsupply.com/blog/2013/05/23/beaglebone/
Figure 26 - http://web.uvic.ca/~andpol/project5.html
Figure 27 - https://www.nordicsemi.com/eng/content/download/2726/34069/file/nRF24L01P_Product_Specification_1_0.pdf
Figure 28 - www.amazon.com

## Slide 53: QUESTIONS?