## Slide 1: SCAM: Smart charging Automobile Monitor
Group J members:
Nathan Rodriguez EE
Andre Lomans EE
Symone Adams EE
Sponsor: Florida Solar Energy Center

## Slide 2: Motivation and Purpose
Low cost smart electric vehicle charger
Secure access for UCF students/faculty only
Power monitoring capabilities

## Slide 3: Goals and Approach
EV charger will track power
  Build a power monitoring circuit at a low cost. Current ones are expensive.
  Use products and parts that have simple implementation.
Modern Functionalities
  Students/Faculty will track power using a smartphone application.
Limited Accessibility: two verification systems
  Magnetic strip card swiper for UCF ID.
  Keypad

## Slide 4
System Overview
Grid/Power Outlet
EVSE Monitoring System
Mobile Application
Electric Vehicle
Inlet + Charger + Battery
Database

## Slide 5
System Requirements
Operating Voltage: 120-240V
Center Frequency: 50-60 Hz
Output Current: 6-32A
Output Power:
  Level 1: <2.4 kW
  Level 2: <9.6 kW
Weight: 1.5kg/3.3lbs
System Temperature <155°C

## Slide 6
J-1772

## Slide 7
SCAM Main Block Diagram
Power Supply
220V AC at 60 Hz
Wi-Fi Board
Electric Vehicle
Inlet + Charger + Battery
Charging Station
Power Processing Board
System Power Generation Board
External to the System
Internal to the system
Keypad
Android Phone Application
Magnetic Card Reader
Online Database
User Interface Board

## Slide 8
Wi-Fi Board Hardware

## Slide 9
Overall Layout
CC3200 Arm-Based Processor chip
External Flash Memory 8 MB
SPI
Accuracy 32-kHz Crystal
Internal Processor 40-MHz Crystal
Multi-
Purpose Buffer
USB 2.0 Connection
UART
JTAG
LTC3561 Switcher
5.0V
3.3V and 1.85V
50 ohm Co-planar Waveguide
Multi-layer Bandpass Filter
2.54 GHz Antenna Chip
SPI
MSP4305529 Central Processor
Power Processing Board
Resistor Divider
2.5V
3.3V
Infrared Temperature sensor
4um to 16 um range
54 Mb OFDM

## Slide 10
Bandpass Filter

## Slide 11
Oscillators
40 MHz Oscillator
  Used by internal ARM processor and proprietary WLAN system
32.768 KHz clock
  Used for set and rest times, synchronization for phase lock loops, accuracy in timing purposes

## Slide 12
Multipurpose Buffer – FT2232D Dual USB to Serial UART/FIFO IC
Entire USB protocol handled on the chip.
Multi-Protocol Synchronous Serial Engine
  USB to JTAG
  SPI, I2C, JTAG
On chip clock multiplier
  Supporting 6-48MHz operations
Supports full-speed USB 2.0
  12Mbit/s

## Slide 13
Schematics

## Slide 14: LTC3561 Features
Up to 4 MHz switching operation
High Switching current: 1.4A
Uses current mode control for better
  Load response
  Line response
High Efficiency up to 95%
Short Circuit protected
Stable with ceramic capacitors

## Slide 15: LTC3561

## Slide 16
LTC3561 Simulation

## Slide 17: Antenna Selection – RFANT5220110A2T
Parameter | Specification
Frequency Bandwidth | 2.4-2.5 GHz
Typical Gain | 1.9 dBi
VSWR | 3
Efficiency | -1.3dB (73%)
AH316M245001-T
  Taiyo Yuden
  Can be on edge of PCB
RFANT5220110A2T
  Walsim
  Needs to be in corner of PCB
Antennas Satisfy

## Slide 18
Power Processing
Board

## Slide 19: Motherboard (Power Processing Board) Layout
USB HUB and Power Supply for Re-programming
TI eZ-lite Emulation Section
Main Electronics and MCU section

## Slide 20: MSP430F5529
Features
  Integrated USB and PHY supporting USB 2.0
  four 16-bit timers
  High-performance 12-bit analog-to-digital converter (ADC)
  two universal serial communication interfaces (USCI)
  hardware multiplier (32x32),
  DMA (Direct Memory Access),
  a real-time clock (RTC) module with alarm capabilities
  IrDA

## Slide 21: USB-Hub and Power Supply

## Slide 22: USB-Hub, Power Supply, and Emulation

## Slide 23
MSP Main Electronics

## Slide 24: Pilot Signal
1 kHz PWM
Pulse width changes based on current delivered to car.
Duty Cycle = amps/0.6

## Slide 25: ADC configuration

## Slide 26
Wireless Communication

## Slide 27: Wi-Fi Communication
Wi-Fi vs. Bluetooth: One of the goals stated was for communication between station and device to be accessed anywhere on campus.
MCU must have WLAN (wireless area network) access point connection capabilities.
Receive state of charge electric vehicle data through SPI from Main MCU.
Send data using TCP sockets to smartphones.

## Slide 28
CC3100 vs. CC3200: CC3200 is a single-chip wireless MCU.
Interface between two TI products simplifies implementation.
Acts as a station that connects to a network.
IoT (Internet of Things) solution.
CC3200 Wireless MCU
Specifications | 
Input Voltage | 3.3 V
Source Current | 2-6 µA
TCP data rate | 13 Mbps
Wi-Fi standard | 802.11b/g/n
External SPI Interface | 8 simultaneous sockets
Body size | 9 mm x 9 mm

## Slide 29
SPI Flow Chart

## Slide 30
Familiarity with CCS
Compatibility with Texas Instrument products.
C/C++ compiler and debugging applications.
Many resources and references for troubleshooting.
Software: Code Composer Studio

## Slide 31
TCP Flow Chart: Server

## Slide 32
A popular IDE for developing applications on Android devices.
Features include:
  Debugging
  Android Phone Emulator
  Connectivity with real devices through USB
  XML files for layout design
Programming language is Java.
Because of its wide use, there are many resources available.

## Slide 33
Main Features of Application
Sign page that is accessible for only UCF students/faculty.
Database to store NID and password information.
Second screen that displays the state of charge.
Connection using TCP to the wireless MCU.

## Slide 34
Sign-in Page
Simple NID and password sign in familiar to all UCF students/faculty.
On button click, code will compare input to database and respond according to that input.

## Slide 35
Database
For prototyping purposes, a database was created in Android Studio.
NID is set as a unique constraint; new entries are entered based on this. No one with the same NID can be in place.
SQLite Open Helper: A helper class that connects to the Firefox plugin, SQLite Manager.

## Slide 36: Second Screen
When NID and password are correct
On the connect button click, phone will connect to wireless MCU server to receive information.
Information is displayed as percentage on progress bar.

## Slide 37
Android Code Flow Chart

## Slide 38
TCP Flow Chart: Client

## Slide 39
User Interface

## Slide 40
Magstripe Reader Ps/2 Interface
Interfaces directly to MSP430 via Ps/2 wired connector
Provides first line of two verify security system capable of reading 3 tracks. Utilizing 2 track for S.C.A.M
Magstripe

## Slide 41
Chosen for being microcontroller-friendly
Cheap relative to Stripe readers ($59.95)
PS/2 cable allows us to use MSP430 without fabricating USB port most Readers in this price range we're USB operated
Uses a single connector for power and data and two data pins
Bi-directional and outputs data stream in the right order regardless of orientation
Does not write to cards. Operation not needed for S.C.A.M
Notes

## Slide 42
Specifications | 
Input Voltage | 5V
Source Current | 1-2A Max draw
Operating temperature | -40-85 ℃
Life | 1000 cycles
PS/2 Wired Connector

## Slide 43
Additional Specs | 
Baud rate | 9600bps
Data Bit | 8 bit
Check bit | None
Stop bit | 1 bit
PS/2 Wired Connector

## Slide 44
PS/2 Device wiring | 
Green Wire | +5V
Black Wire | Ground
Brown Wire | Data
Yellow Wire | Clock
White Wire(n/a) | Mouse Data for 2-in-1 spliter cables
Red Wire(n/a) | Mouse clock for 2-in-1 splitter cables
PS/2 Wired Connector

## Slide 46
Keypad Switch Circuit

## Slide 47
FCI Part No. SLW8S-5C7LF
8-Pin connection
24V
Requirements

## Slide 48: Power Management

## Slide 49
Power Management

## Slide 51
Specs | 
Startup Current | 25 µA Max
Max Duty Cycle Limiting | 80%
Vin Voltage | 8Min - 30Max
PWM

## Slide 52
Budget
Part | Current Cost | Expected Cost
Magstripe | 59.99 | 
Switching Keypad | 25.25 | 
Msp430(6x) |  | 20
CC3200 |  | 12
Regulators |  | 60
PCB layout |  | 300
J-1772 Connector |  | 160
Phone(Prototyping) | 30 | 
Misc |  | 100
 | 115.24 | 652.00

## Slide 54
Input power
  Level of charging
  110-120 vs 208-240
Software implementation
Part aquisition
RF design
Not standardized
  Japan vs Usa
Challenges

## Slide 55
Work Distribution
 | Hardware | Software | User Interface | Power
Nathan Rodriguez | P | S | S | S
Symone Adams | S | P | S | S
Edwin Lomans | S | S | P | S

## Slide 56: Questions?