## Slide 1: AIV Autonomous Irrigation Vehicle
Sponsor by Guard Dog Valves
Group 4
Joshua Betetta (EE)
Parameswari Chandrasekar (CpE)
Stuart Munich (CpE)
Roberto Santos (EE)

## Slide 2: AIV Motivation
According to the EPA "Depending on the region, homeowners use between 30 and 70 percent of their water outdoors." and Experts estimate that "50 percent of the water we use outdoors goes to waste from evaporation, wind, or runoff due to overwatering."
According to the University of Florida "If you water too much, the roots don't have any incentive to grow deep, so you end up with a lawn that's weak, susceptible to pests, disease and has shallow roots"
We are already exceeding the capacity of the Floridan Aquifer System to supply adequate water to maintain springs health. The only way to restore health to these springs is to greatly reduce our reliance on groundwater from the Floridan Aquifer System.

## Slide 3: Existing Issues with Current Watering System and Objectives
Current Issues
Expensive
Invasive
Frequent Maintenance
User Error
Project Objectives
Effective watering
Monitoring soil
User friendly
  Autonomous movement & obstacle avoidance
  Cost saving
  Durable

## Slide 4: The Benefits
Cost savings
  Modern Sprinkler Head: $50+ annual savings
  Moisture Sensors: $35+annual savings
    Average Yard: $415+ annual savings
  Increased Accuracy of Watering: $15 annual savings
  Energy cost of existing small pump: $30 annual
More effective watering
Low maintenance
Overall healthier yard
Availability for bulk application to communities
  All cost savings would multiply by multiple yards covered

## Slide 5: Specifications
Component | Design Specification
Vehicle Size | 21.10” x 24.13” x 5.55” (L x W x H)
Obstacle Detection Distance | 2 cm to 6 m
Time to Water Designated Area | ≤1 hour per zone
Targeted Rate of Water Flow | 24 Gallons Per Minute
Average Lawn Size | .25 acre (10890 ft^2)
Battery Life | ≤1 hour
Printed Circuit Board Size | 6” x 5” (L x W)

## Slide 6: Drive System: Traxxas Summit 1/16th Scale
4 wheel drive
Durable suspension
Modular for modification of all parts
Proper scale for designed prototype
Relatively low weight
Comes with reliable, rechargeable battery

## Slide 7: Hardware Block Diagram

## Slide 8: LIDAR
Purpose
  Detect long range objects
  Weatherproofing
    LIDAR
    Servo
Manufacturer | Garmin | RPLIDAR
Accuracy | +/- 2.5 cm | +/- 2.5 cm
Range | .05-40 Meters | .2-6 Meters
Power | 4.75-5 VDC | 5 – 10 VDC
Price | $149.99 | $199

## Slide 9: Ultrasonic Range Finder
Purpose
  Weatherproof
  Detect obstacles
Manufacturer | DFRobot | Axe-Tech
Range | 25 - 450 cm | 2-400 cm
Detecting Angle | < 70° | 15°
Power | 5 VDC | 5 VDC
Price | $16 | $3.50

## Slide 10: Microcontroller on PCB
ATMEGA32P-PU
  Open source
  Active community with many resources
PIC16F87A-I/SP
  Low capability
  Low memory capacity
Manufacturer | Atmel | Atmel
Pin Count | 28 | 16
Speed (MHz) | 20 | 1
Power Supply (V) | 1.8 - 5.5 | 2– 5.5
Price | $2.14 | $2.13

## Slide 11: Microcontroller
Arduino
  Control vehicle’s
    Speed
    Acceleration
    Steering
    Breaking

## Slide 12: Computer
Raspberry Pi
  Analyze & processes received data
  Turbot quad-core
    Faster & more powerful
Manufacturer | Raspberry Pi Foundation | Intel
CPU | Broadcom BCM2837 | Intel Atom E3845
RAM | 1 GB | 2 GB
Power | 5V @ 2.5A | 5V @ 4A
Price | $35 | $190

## Slide 13: PCB Schematic
Power Circuit
Microcontroller layout

## Slide 14: PCB Layout
Indication | Color
Device Outline | 
Pin Placement | 
PCB Perimeter | 
Top Layer Traces | 
Bottom Layer Traces | 

## Slide 15: Prototyping
Device | Raspberry Pi | ISP | Servo | Power Jack
Color |  |  |  | 

## Slide 16: SOFTWARE

## Slide 17: Software Flowchart

## Slide 18: Class Diagram
3 main classes
  Midpoints
  Locations
  Sensors

## Slide 19: Use Case Diagram

## Slide 20: Localization
Proximity sensors
Node.js
Calculates the distance using RSSI (Received Signal Strength Indicator) and measured power
JSON (JavaScript Object Notation)
The distance of the sensors is updated each iteration of the AIV's path where the three nearest ones are used to determine the AIV's position on the map.

## Slide 21: Obstacle Avoidance​
LIDAR​
Learning Phase​
Detects objects on terrain ​
Prevent collisions​
Updates two-dimensional array map​
C++​

## Slide 22: MAP PLOTTING
1m represents sensors
2m represents midpoints
Midpoints are to be used as travel destinations
Midpoints will store the id of the sensors at their edges
They also store the number of sensors at their edges that give dry readings
Maximum dryness of a midpoint is two, minimum is zero.

## Slide 23: Map Updating​
Two-dimensional array map​
In map number 9 represent obstacle location ​
Maximum number of adjacent obstacle is 8​
Minimum number of adjacent obstacle is 0​
1m represent sensor​
2m represent midpoints

## Slide 24: Long Path Finding
Builds a list of midpoints between sensors to travel to.
Orders them based on shortest distance and the readings of sensors at their edge.
Begins by looking to the sensors to its left and right to determine which needs more water.
If both have the same dryness, it moves across the center
If neither are dry, it moves to the neighboring midpoint that is the closest to the next dry midpoint.
The purpose of this is to create a linear path for later when the AIV is attached to a hose.

## Slide 25: A* Search
Searches all adjacent locations to current location
Calculates heuristic value for each location.
Compares new heuristic to previous value stored in location.
If new heuristic is less than previous one, it adds it to a queue.
Once the goal is reached, it returns a list of locations to reach the goal.

## Slide 26: Movement Control of AIV
Takes long path midpoint list
Builds a list of locations to get to each midpoint in the long path using A* Search.
The AIV moves in the direction and distance from current location to the next location on its list.
Keeps track of current location of the AIV while it is moving to each location the list to compare with detected location.
Re-calculates its path if new obstacle is detected or if location is detected off course.
From midpoints: 0 -> 1 -> 3 -> 6

## Slide 27: ADMINISTRATIVE CONTENT

## Slide 28: Work Distribution
Name | CPU Interfacing | MCU Interfacing | Communication | Algorithm
Joshua | P | S |  | 
Parameswari |  |  | P | S
Roberto | S | P |  | 
Stuart |  |  | S | P
Primary | P
Secondary | S

## Slide 29: Budget
Component | Estimated Cost | Actual Cost | Vendor
LIDAR | $100.00 | $149.99 | RobotShop
Ultrasonic Range Finder | $5.00 | $16.00 | RobotShop
Battery Pack | $15.00 | $59.99 | Amazon
Raspberry Pi | $35.00 | $36.98 | Amazon
Waterproof Servo | $50.00 | $42.99 | RobotShop
Atmega328P | $4.50 | $4.50 | Amazon
Brackets | $20.00 | $17.90 | RobotShop
Traxxas RC Car | $499.99 | $249.95 | Traxxas
Button & RBG LED | $5.00 | $14.95 | Monk Makes
Total | $734.49 | $593.25 | 
Financed by Guard Dog Valves

## Slide 30: Questions?