## Slide 1: Ion Interactive Robot Assistant
Group 11
Dennis Gebken, CpE
David Jaffie, CpE
Mohammad Rizeq, EE

## Slide 2: Motivation
Combat boredom at the desk
Provide more interaction and a physical embodiment to personal assistant smart speakers
Objective
Produce an all-in-one robotic assistant
  Natural movement and conversation
  Small, lightweight for portability
  Wirelessly utilize the internet to carry out tasks
Meet Peeqo! Made by Abhishek Singh

## Slide 3: Requirements & Specifications
Property | Design Specification
Weight | < 5lb
Size | < 7”x7”x15”
Voice Command Response Time | < 2 seconds
Voice Recognition | 80% of what is spoken
Supported Language | English
Face Recognition | 80% of faces recognized under normal lighting
Power Consumption | < 50W
Development Cost | < $500

## Slide 4: Overall Block Diagram & Tasking
Task | Primary | Secondary
Controller | Dennis | David
Camera & CV | Dennis | David
GUI | David | Dennis
Voice Recognition | David | Dennis
Body Design | David | Dennis
MCU & Servos | Dennis | Mohammad
Power | Mohammad | Dennis
Audio | Mohammad | Dennis
PCB | Mohammad | Dennis
WiFi | Mohammad | Dennis

## Slide 5: David’s Responsibilities
Body Design
Display
GUI
Voice Recognition

## Slide 6: David’s Responsibilities
Body Design
Display
GUI
Voice Recognition

## Slide 7: Body Design
Originally wanted to utilize 3D printing to build a body
Low priority, decided to finish primary tasks related to ECE hardware and software
Basic tubing just to house components while allowing rotation

## Slide 8: David’s Responsibilities
Body Design
Display
GUI
Voice Recognition

## Slide 9: Display
Important factors:
  Cost
  Touch capability - GUI
  Size & Resolution – GUI & multimedia
  Built-in adaptor board
Source: Adafruit

## Slide 10: Pi Foundation Display
Size: 7”
Resolution: 800x480
Liquid Crystal Display (LCD)
  Cheaper, more energy-efficient compared to TFT
Capacitive touchscreen allowing for multi-touch
Attached driver board that handles power and signal processing
Easily integrates with Raspberry Pi
Cost: $80

## Slide 11: David’s Responsibilities
Body Design
Display
GUI
Voice Recognition

## Slide 12: GUI
Secondary means of interaction with the device
Allows the user to:
  View available commands
  Receive notifications on recognized or unrecognized users
  Change various settings
Coded in Python
  Included with Raspbian
  Event-driven language
  Used Kivy library
    Open-source
    Easily integrates with the Raspberry Pi
    Great for multi-touch user interfaces and apps

## Slide 13: GUI User Flowchart

## Slide 14: David’s Responsibilities
Body Design
Display
GUI
Voice Recognition

## Slide 15: Voice Recognition
Primary means of interaction with the device
Works the same as Amazon Echo, Siri, etc.
Looks for a ‘wake-up word’
Records the command that follows the wake up word and utilizes Google Speech API to translate it into a command that Ion can recognize

## Slide 16: Voice Recognition Flowchart

## Slide 17: Dennis’s Responsibilities
Face Detection
Face-the-User System (name TBD)
Facial Recognition
Main Processor selection
Motor Control Unit (MCU)

## Slide 18: Dennis’s Responsibilities
Face Detection
Face-the-User System (name TBD)
Facial Recognition
Main Processor selection
Motor Control Unit (MCU)

## Slide 19: Face Detection
Purpose:
  Detect faces
  Return position of face closest to center (x,y)
  Feedback for Face-the-User (name TBD) system
Language: Python
Library: OpenCV

## Slide 20: Face Detection Algorithm
Reduces capture size
Transforms to grayscale
Blurs
Detects faces
Returns coordinates

## Slide 21: Dennis’s Responsibilities
Face Detection
Face-the-User System (name TBD)
Facial Recognition
Main Processor selection
Motor Control Unit (MCU)

## Slide 22: Face-the-User System
Purpose
  Turn Ion so the screen faces the user
Camera
Raspberry Pi
MCU
Capture image
Image is sent to Raspberry Pi
Detects face
Calculates distance vector to center
Instructs MCU to update position
Changes servo position

## Slide 23: Face-the-User System Challenges
Position vector’s magnitude could be off
  Too large
    Overshoot
    Oscillation
  Too small
    Many minor adjustments
  Both are a waste of power and resources
User may move while position is updated

## Slide 24: Face-the-User System Solutions
Dynamic feedback
  Position change in increments
Variable buffer rectangle
Slow, continuous adjustments
Target rectangle while adjusting position.
Buffer rectangle. The center of the face needs to cross one of its borders to initiate movement.
Position updated until face is centered

## Slide 25: Dennis’s Responsibilities
Face Detection
Face-the-User System (name TBD)
Facial Recognition
Main Processor selection
Motor Control Unit (MCU)

## Slide 26: Facial Recognition
Purpose:
  To identify saved users and greet them
  Notify user when someone else was detected at the desk
Not a true safety feature
  Not accurate enough because of lack of processing speed
Accuracy vs. Speed
  Eigenfaces – fast but unreliable
  Fisherfaces – More reliable but slow
Will only run when a face has not been detected for a while

## Slide 27: Dennis’s Responsibilities
Face Detection
Face-the-User System (name TBD)
Facial Recognition
Main Processor selection
Motor Control Unit (MCU)

## Slide 28: Processor Load
Facial Recognition
Face Detection
GUI & Multimedia
Voice Recognition
OS (Linux-based)

## Slide 29: Single Board Computer (SBC) Choices
Asus Tinkerboard
Beagleboard
Raspberry Pi
Sopine A64

## Slide 30: SBC Comparison
 | Raspberry Pi | BeagleBoard | Asus TinkerBoard | Sopine A64
CPU/SOC | 4-core 1.2 GHz | 1-core 1.0 GHz | 4-core 1.8 GHz | 4-core 1.152 Ghz
Memory (RAM) | 1 GB | 512 MB | 2 GB | 2 GB
Price | $35.00 | $49.00 | $55.44 | $35.00
Component Availability | Readily available | Readily available. CPU can be bought directly for $20 | Prototype board available on Amazon. Components for final design not yet found | Readily available
Interfaces | Everything necessary, except 2nd PWM output | All necessary interfaces available | All necessary interfaces available | Everything necessary, except 2nd PWM output
Final Implementation | Connect Raspberry Computer Module 3 via fixed SODIMM connector to PCB | SBC design to be used as reference to add CPU directly to final PCB | Currently not possible because components have not been found | Connect Sopine A64 via fixed SODIMM connector to PCB

## Slide 31: SBC Choice: Raspberry Pi 3 Compute Module Lite
Performance deemed sufficient
Smaller when added to PCB
Lowest cost
Already own development board and SBC (version 3 B)
Abundant information and tutorials online
Most future-proof
Raspberry Pi Compute Module 3 Lite
WaveShare Compute Module IO Board Plus

## Slide 32: Dennis’s Responsibilities
Face Detection
Face-the-User System (name TBD)
Facial Recognition
Main Processor selection
Motor Control Unit (MCU)

## Slide 33: Motor Control Unit (MCU) Tasks
Rotate servos
RGB LED control

## Slide 34: MCU Main Choices and Comparison
 | Atmel Mega328 | Ti M430
Prototyping Board | Arduino Uno | LaunchPad
Operating Voltage | 1.8-5.5V | 2.0-3.6V
Clock Speed | 20 MHZ @ 4.4+ V | 16 MHz
I/O | 23 GPIO 8 10-bit ADC channels | 15 GPIO 8 10-bit ADC channels
Price | $1.30 | $2.48

## Slide 35: MCU Choice: Atmel mega328
Faster
Cheaper
Can be prototyped on breadboard (see picture)
Already own Arduino Uno and Bootloader

## Slide 36: Mohammad’s Responsibilities
Audio Processing
WiFi System
Input Ports
Power Management
PCB

## Slide 37: Mohammad’s Responsibilities
Audio Processing
WiFi System
Input Ports
Power Management
PCB

## Slide 38: General User-Device Voice Interaction
User issues the device a command; the device responds.
Example:
User: Stream The Beatles from Youtube.
Device: *plays song*

## Slide 39: Initial Design Audio Components

## Slide 40: Electret Microphone
Very common in audio projects.
Specs:
  -44dB sensitivity
  20Hz-20kHz frequency response
  Operating voltage range of 1VDC-10VDC
  Breadboard-friendly
  Downside: Requires filtering and amplifying
Amplifier & Low Pass Filter
Cutoff Frequency: ~4kHz
Gain: 4 V/V

## Slide 41: Speakers
Parameter | Regular Speaker | Thin Speaker
Diameter | 50mm | 40mm
Power Rating | 0.5W | 0.25W
Impedance | 8Ω | 8Ω
Price | $1.95 | $0.95
Quality | Much clearer sound | Sound is noisy and unclear
Thin Speaker
Source: SparkFun
Regular Speaker

## Slide 42: Final Design Audio Components

## Slide 43: Sienoc Mini USB Microphone
Specs:
  Very small: 22.5x18.3x7.1 mm
  100Hz-16kHz frequency response
  Does not require a driver
  Effective distance of 2 meters
Advantages:
  Less PCB space & signal noise
  Can be switched out
  ADC not required
  Amplifier & LPF not needed
Source: Amazon

## Slide 44: USHONK USB Mini Speakers
Regular Speaker
Specs:
  Small: 79.756x30.48x45.212 mm
  Does not require a driver
  0.5W per speaker (2)
Advantages:
  Less PCB space & signal noise
  Can be switched out
  DAC no longer needed
Source: Amazon

## Slide 45: Mohammad’s Responsibilities
Audio Processing
WiFi System
Input Ports
Power Management
PCB

## Slide 46: WiFi Chip
Parameter | Xbee S6B | ESP-12E
Standard | 802.11 b/g/n | 802.11 b/g/n
Frequency Band | 2.4GHz | 2.4GHz
Security | WPA/WPA2/WEP | WPA/WPA2/WEP
Interface | SPI/UART | SPI/I2C/UART
Operating Voltage | 3.12V-3.46V | 3.0V-3.6V
Transmit Power | +/- 16 dBm | +/- 20 dBm
Price | $29.00 | $6.95
ESP-12E WiFi Chip

## Slide 47: Mohammad’s Responsibilities
Audio Processing
WiFi System
Input Ports
Power Management
PCB

## Slide 48: Input Ports
MicroSD Card Socket
Boot drive
Storage
USB Type A
Initial Design: Troubleshooting & Peripherals
Final Design: Mic, Speakers & Peripherals

## Slide 49: Mohammad’s Responsibilities
Audio Processing
WiFi System
Input Ports
Power Management
PCB

## Slide 50: Final Design Power Consumption
Component | Nominal Input Voltage (V) | Nominal Current Draw (mA) | Power Consumed (mW)
Processor | 5 | 700 | 3,500
LCD | 5 | ~200 | ~1,000
Servo Motors | 5 | 200 | 1,000
Motor Control Unit | 5 | 0.2 | 1
WiFi Chip | 3.3 | 80 | 264
Camera | 5 | 250 | 1,250
LEDs | 3.3 | ~20 | ~66
microSD Card | 3.3 | 100 | 330
USB Peripheral | 5 | ~500 | ~2,500
Total: |  | ~2.05A | ~10W

## Slide 51: Final Design Power Connections
LED

## Slide 52: Mohammad’s Responsibilities
Audio Processing
WiFi System
Input Ports
Power Management
PCB

## Slide 53: PCB Schematic Overview
Initial Design
CPU
MCU
WiFi
DSI
&
CSI
microSD
USB
Mic Amp
DAC
Voltage Regulators
DC Jack
LCD & Servo

## Slide 54: Initial Design Disadvantages
Size & price can be reduced
Very complex
MCU is through-hole
Components are very small

## Slide 55: PCB Schematic Overview
Final Design

## Slide 56: Administrative Content

## Slide 57: Budget
Component | Projected Cost ($) | Actual Cost ($)
Microphones | 3.00 | 7.78
Speakers | 6.00 | 15.90
Display | 60.00 | 80.00
Controller | 35.00 | 26.00
Camera | 15.00 | 10.00
PCB(s) | 50.00 | 60.00
Body | 50.00 | 0
Buttons, switches | 10.00 | 1.50
Resistors, capacitors, etc | 10.00 | 50.00
LEDs | 10.00 | 5.90
MCU | 20.00 | 7.52
Servo(s) | 30.00 | 6.99
WiFi Modules | 32.00 | 11.95
Mono Audio Amplifier | 8.00 | 7.95
DAC Breakout Board | 5.00 | 4.95
Battery | 20.00 | 0
Voltage Regulators | 15.00 | 12.58
Total | 494.00 | 309.02

## Slide 58: Ion Unit Cost
Component | Cost ($)
Voltage Regulators | 1.29
Speakers | 12.00
Display | 80.00
Controller | 26.00
Camera | 9.99
PCB | 2
Body | 0
Resistors, capacitors, etc | 13.05
LED | 0.10
MCU | 1.88
Servo | 6.99
WiFi Modules | 5.00
USB Hub | 6.99
Microphone | 5.88
Ball Bearing | 5.95
Total | 177.12

## Slide 59: Issues
Final PCB’s USB port is not working:
Error code: “Warning – TX status read failed -71”
Possibly Differential pair (mismatched or wrong impedance)
Could also be hardware driver
But, we had a plan B prepared
Kivy and Pi didn’t get along as well as we hoped
Python library to embed browser wasn’t compatible with ARM processors
Window provider for Pi always kept Kivy on top – couldn’t launch browser in front of it
Complex widgets resulted in lag

## Slide 60: Questions?