## Slide 1: SMART CHAIR Group 7
Rudy Ramjas - EE
Mackenson Jean - EE
Annavay Kean - CpE
Thien Nguyen - CpE

## Slide 2: Goals & Objectives
Help user to become more mindful of posture habits.
Provide feedback based on measured data.
Target audience: middle-class office workers.
Methodology: Center of Gravity

## Slide 3: Specifications
The device should update the sensor input readings every 30 seconds.
The device should pair with a phone app.
The application will display posture data.
The application will provide feedback on data.
The software will store user data.
5-day standby battery life, minimum.
PCB not to exceed 230 cm squared.
Sensor array should be able to load a minimum of 100lbs (45.4kg).
Vibrate module should operate between 200-400 Hz or rpm equivalent.

## Slide 4: Overview Diagram

## Slide 5: Standards
Power Standards
  IEC-60601-1
    Electrical Shock & Fire Safety
  UL 1310
    Devices using multiple power supplies
Wireless Standards
  IEEE 802.11
Application
  Flutter Development Standards
  Distribution Standards
  User Privacy Standards

## Slide 6: Microcontroller Selection
MCU | F280049PMSR | ATMEGA 2560-16AU | PIC24FJ1024GA606-I/PT | MSP430FR2311IPW16R | ATSAMA5D21C-CUR
Manufacturer | Texas Instruments | Atmel | Microchip Technology | Texas Instruments | Microchip Technology
Program Memory (kB) | 256 | 256 | 1024 | 3.75 | 160
Data Memory (kB) | 100 | 8 | 32 | 8 | 128
Clock Frequency (MHz) | 100 | 16 | 32 | 16 | 500
GPIO | 26 | 86 | 53 | 11 | 128
Supply Voltage Range | 1.2 - 1.3V | 1.8V – 5.5V | 2 - 3.6V | 1.8V -3.6V | 1.2V
Size L x W (cm) | .072 x .072 | 1.6 x 1.6 | .07 x .07 | .05 x .04 | 1.4 x 1.4
Price (USD) | $10.81 | $12.20** | $4.41 | $1.62 | $6.71
Communication Protocols

## Slide 7: Power Supply
The system will be powered by an AC to DC adapter.
It will be operated by a voltage range from 12V to 3.3V.
The PCB will be using power 24 hours and keep it running under all conditions.
Back up power will provide to the chair by a 9V battery to allows the circuit running after it is disconnected to the wall.
The battery will take over when the main power source is unplugged.

## Slide 8: Battery Supply
9V Rating
Lithium ion composition
Rechargeable
Less Expensive
Easily substitutable

## Slide 9: Schematic Overview

## Slide 10
PCB Power Supply

## Slide 11: Overall PCB
76 x 87mm (LW)
Designed in Eagle
3 screw-holes

## Slide 12: PCB Enclosure
Wood
Laser cut in TI lab
6” x 4” x 4” (LWH)

## Slide 13: FSR Selection
 | Tekscan A502 | Tekscan A301 | SEN-09376 | FSR-406
Price per unit | $23.24 | $12.18 | $11.25 | $12.99
Surface Area(in2) | 4 | 0.375(diam) | 3.0625 | 2.25
Response time(µs) | ≤ 3 | ≤ 3 | ≤ 5 | ≤ 5
Load range(N) | 44kN max | 444N max | * | 100N max
Drive voltage(V) | Variable | Variable | * | *
Amplifier circuit | Multiple | Multiple | Volt. Div. | Multiple

## Slide 14: FSR Selection
Tighter tolerance: < 3%
Multiple integration methods
  Voltage Divider
Engineering support (Manufacturer)
Utilize MCU ADC channels to process signal

## Slide 15: Proximity Sensor
Operates within 3cm range
Located on mid-back of chair

## Slide 16: Vibrate Module
Low cost: <$1.00 per unit
Simple integration
DAC to supply pulse signal
2.8v - 5v

## Slide 17: Software Design
Wireless Communication
NoSQL Database
Application Framework

## Slide 18: Flowchart Diagram

## Slide 19: Wireless Modules
Bluetooth | Wi-Fi
Shorter Range | Longer Range
Close proximity | Remote Location
Direct Connections | Online Connection
Lower Power | Higher Power

## Slide 20: Bluetooth Specification
Hardware Features | Software Features
-80 dBm sensitivity | PIO: low-disconnect & high-connect
+4 dBm RF transmit power | Rising Pulse will disconnect
Low Power 1.8 V Operation | Auto-connect on last device
PIO Control | Pair Last Device as Default
UART Interface | PINCODE: 0000 / 1234

## Slide 21: Wi-Fi Specification
Hardware Features | Software Features
CPU: Tensilla L 106 32-bit | Security: WPA / WPA2
Integrated Memory (SRAM) | Encryption: WEP/TKIP/AES
SPI External Flash | Firmware: OTA Network
RF 2.4 GHz Receive/Transmit | SDK: Supports Cloud Server
Adjustable Power Mode | Network Protocol: TCP/UDP/HTTP

## Slide 22: Wireless Module
Wi-Fi vs Bluetooth
Wi-fi can store value into database
Bluetooth has no storage
Bluetooth lack of Full Duplex support
ESP8266
Breadboard testing
Surface mount
Antenna RF optimization

## Slide 23: ESP8266 Schematic
Main Aspects
Power Supply
Power-on sequence and reset
Flash
Crystal oscillator
RF
External resistor
UART

## Slide 24: ESP8266 Pros and Cons
Pros
Compatibility with IDE
Multiple GPIO pins
Powerful capabilities
Cons
Difficult to start working
Requires multiple libraries

## Slide 25: Wireless Communication
Sensor data
Wi-Fi Transmission
Send data through cloud
Database Receive data
Firebase

## Slide 26: Purpose of Application
To allow the user to view posture data.
To provide feedback on posture data to the user.
To allow the user to alter settings.

## Slide 27: Application Design
Technologies Used:
  Firebase serves as the back-end.
    User Accounts
    NoSQL Database
  Flutter serves as the front-end framework.
    Developed by Google
    Dart Language
    Hot reload

## Slide 28: NoSQL Database Design
Provides support for offline data persistence.
Each data entry contains the center of gravity on the left-to-right axis and the front-to-back axis and the timestamp.
This is subject to change during the process of integrating the legitimate sensor data into the software.

## Slide 29: User Interface Design

## Slide 30: User Interface Design

## Slide 31: Application Completion Status
Complete:
  Firebase authentication
  Firebase database (including read/write)
  Basic Layout
  Basic navigation
Pending:
  Settings / User Preferences
  Posture data represented in graphical format
  Recommend Stretches/Yoga poses
  Swipe navigation
  Color Theming

## Slide 32: PROGRESS GRAPH
Chart: 
| Research | Low level software implementation | High Level software Implementation | PCB | Sensor integration | Total
 | 0.9 | 0.25 | 0.56 | 0.52 | 0.5 | 0.546

## Slide 33: Roles
Task | Primary | Secondary | Status
Wireless Communication | Thien | Annavay | proto
Database Development | Annavay | Thien | proto
Mobile Application | Annavay | Thien | Proto
Microcontroller | Rudy | Mackenson | Ordered
Power Supply | Mackenson | Rudy | proto
Rechargeable Battery | Mackenson | Rudy | Received
Force Sensor Integration | Rudy | Thien | proto
Vibration Module | Rudy | Thien | Received
User Interface | Annavay | Thien | In development
PCB Design | Mackenson | Rudy | 2nd iteration

## Slide 34: BUDGET SHEET
Item | Description | Quantity | Cost | Total | Estimated Cost
Tekscan A301 | round force sensors - 4 pk | 1 | $53.60 | $53.60 | $150.00
Tekscan A502 | Larg square force sensors - 4 pk | 1 | $108.25 | $108.25 | 
556-ATMEGA2560-16AU | Microcontroller | 3 | $12.20 | $36.60 | $40.00
Chair | Office chair, cloth, rolling | 2 | 0 | 0 | $75.00
Eleego Mega 2560 R3 | ATmega Dev board | 1 | $13.99 | $13.99 | $16.00
HC-SR04 | ultrasonic proximity sensor | 1 | 0 | 0 | $10.00
Mircrochip ATMega2560 | microcontroller samples from OEM | 5 | 0 | 0 | -
Final Paper | printing and binding | 1 | $27.98 | $27.98 | $30.00
System Enclosure | Housing for PCB |  |  |  | 
PCB surface components | PCB resistors, caps, etc. | Multiple |  | 34.17 | $50.00
Firebase | Backend manager | 1 | - | - | -
ESP8266 | Wi-Fi Module | 4 | $19.99 | $19.99 | $40.00
Total |  |  |  | $291.33 | $840.00

## Slide 35: Implementation Challenges
Software-Hardware Integration
  Proper data transmission
  Formatting data
Foam of chair (Sensors)
  Reduce thickness of foam
    Partition foam
  Add barrier between sensors and foam

## Slide 36: Q&A