## Slide 1: Electric Blind​ Group 13
Ryan Meinke (Computer Engineering)
Joshua Forrest (Electrical Engineering)
Tien Tran (Electrical Engineering)
Adedoyin Adepegba (Computer and Electrical Engineering)

## Slide 2: Project Motivation​
Create a cost-efficient and energy saving product
Automated blinds on the market presently do not allow multiple activation methods
Current automated blinds do not also give high energy efficiency
Create a low-cost, energy efficient electric blind that:
  Can be activated using multiple activation methods

## Slide 3: Goals and Objectives​
Cheap electric blind
Low activation time
Low power consumption
Multiple activation methods for automating the process of interacting with a window
  Switch
  Human presence
  Digital Application
​

## Slide 4: Requirement Specifications​
​

## Slide 5: Overall Block Diagram

## Slide 6: Hardware

## Slide 7: Power Design
Components | Operating Voltage (V) | Operating Current (mA) | Power Consumption (W)
PIR sensor | 5 | 32 | 0.160
MCU | 3.3 | 80 | 0.264
PDLC Film | 30 | 12.4 | 0.372
Relay (Dissipation power) |  |  | 1.350
Transformer | 12 | 500 | 6
Total Power Consumption |  |  | 8.146

## Slide 8: Proximity Sensing Technology
Inductive Proximity Sensor
Capacitive Proximity Sensor
Magnetic Proximity Sensor
Ultrasonic Proximity Sensor
Photoelectric Proximity Sensor
    Thru-Beam Mode
    Retroreflective Mode
    Diffused Mode

## Slide 9: Different Modes for Photoelectric Proximity Sensing Technology

## Slide 10: MCM 287-18001 PIR Sensor
Specifications | Value
Input voltage | 5-20 V
Power Consumption | 32 mA
Output voltage | High: 3.3 V Low: 0V
Sensing Range | 7 m
Angle | < 110 degree Cone Anglee
Repeatable Mode | Y
Range Adjustment | Y

## Slide 11: PIR Proximity Sensor

## Slide 12: Voltage Regulator
 | XRP7659 | LM2575-ADJ
Input Range | 4.5 V – 18 V | 1.2 V – 37 V
Output Voltage | 3.3, 5, 12 V | 3.3, 5, 12 V
Output Current | 1.5 A | 1 A
Efficiency | Up to 92 % | 87.5 %
Operating Switching Frequency | 1.4 MHz | 52 kHz
Cost | $ 0.8 | $ 3.70
Dimension | 2.82 x 2.65 x 1.45 mm (with distance between 2 pins is 0.95 mm) | 10.67 x 4.83 x 30.84 mm (with distance between 2 pins is 1.7 mm)

## Slide 13: Testing Circuit

## Slide 14: Software​

## Slide 15: Software Core Functionalities​
Control Smart Glass​
Manage Input and Output​

## Slide 16: Control Smart Glass Functionality​
Simple​
Send signal to relay​
Binary Choice​
Send the signal​
Don't send the signal​
​
​

## Slide 17: Manage Input/Output Functionality​
A bit more complicated​
Multiple Types on Input/Output​
Sensors​
Network​
​

## Slide 18: Software Diagram​

## Slide 19: Modularization​
Configurability​
Continual Feature Development​
Permissions​
​

## Slide 20: Proximity Sensor Input​
Check sensor value​
Set Glass State Accordingly​
​

## Slide 21: IPv4 Network Input​
Listen on IP address/port combination for new packet​
Parse packet in accordance with custom protocol​
Process any work needed​
Send custom protocol compliant response packet​
​

## Slide 22: Custom Protocol​
What's the need?​
Computer Networks are imperfect​
Reliability vs Speed​
Modularization Standard​
Will likely make changes during testing​
​

## Slide 23: Code Quality Controls​
What's the need?​
Version Control​
git​
Code Linting​
Style Guideline​
Documentation​
Comments​
Markdown docs​
Rigorous Code Review​

## Slide 24: Work Completed vs Work Remaining​
Need to run code​
One of the last things to be completed​
Work Completed​
Overall Code Design​
Code Proof of Concepts​
"untested" Code​
Work Remaining​
Finish Development​
Rigorous Testing / Software Corrections as Needed​
Documentation​
Additional Features Development​

## Slide 25: Arduino​
Well Established Standard​
Abstraction​

## Slide 26: Microcontroller Unit

## Slide 27: MCU Choice – ESP32​
​ESP32-WROOM on ESP32 Koala Development Board
  Dual-core CPU
  Operating voltage/Power Supply of 3.0 – 3.6V
  Operating current ~ 80mA
  4Mb flash

## Slide 28: Inner workings of the MCU​

## Slide 29: Administrative Content​

## Slide 30: Work Distribution​
Team Members | Hardware | Software | MCU
Ryan Meinke |  |  | 
Tien Tran |  |  | 
Joshua Forrest |  |  | 
Adedoyin Adepegba |  |  | 

## Slide 31: Budget​

## Slide 32: Work Progress​
Chart: 
| Total | Testing | Prototyping | Design | Research
Progress | 53.75 | 25 | 40 | 55 | 95

## Slide 33: Questions???