## Slide 1: TubeSat Attitude Determination and Control System
Mark Barbaro Electrical Engineering
Daniel Cadena Electrical Engineering
Andy Garcia-Marquez Electrical Engineering
Islam Aly Electrical Engineering
Group 21

## Slide 2: What is an ADCS?
Main Uses
Orienting solar panels
Orienting thermal radiators
Orienting thrustors
Utilizing optical instruments
Optimizing antenna gain
Notes: Atittude refers to the angular orientation of a body with respect to an external reference frame. “the steering wheel of space”

## Slide 3: Project Goals
Implement the first Attitude Determination and Control System on a TubeSat (nanosatellite)
Maximize the efficiency of the system
Ensure all requirements are met for space deployment
Act as technological trailblazers for The Collegiate Space Foundation at UCF

## Slide 4: Project Impact
The ability to determine how long an ADCS can operate for in Space without power loss
The first ADCS system on a TubeSat
Future potential project platform
Launch the Universities' first student-built nanosatellite to orbit
Notes: Most systems need an ADCS system – communication +
Our project impact is based around the ADCS system and how key it is for nano-satellite use. Most projects need the stabilization and orientation that an ADCS system can provided to maximize communications and is even a key component for project success. We are looking to benefit our partners at Interorbital systems (the creators of the tubesat) as well as future UCF projects by providing them with a tested and proven ADCS model.

## Slide 5: Project Testing Requirements
Specification | Requirement | Test
Maximum Current Draw (System) | 1,912.5mA | Power Budget Test
Motor Frequency Range | 16.5 - 250.9 Hz | Individual Motor Test Simultaneous Motor Test
Axial Stability | 0°/s ± 0.1°/s | ADCS Reaction Test

## Slide 6: Project Specifications
Specification | Project Area | Priority | Validated
ASTM – E1548 | EHS | High | Yes
Lead-Free Solder | Material Selection | N/A | No*
AIA – FOD Prevention | EHS | High | Yes
IEC 62281 | Logistics | High | Yes
NASA: NESC-RP-08-75 UL 1642 | Quality | High | Yes
IEEE 830 | Software Reliability | High | Yes
Nanosatellite Standards: Allen Space | Overall Scope | Critical | Yes
Nanosatellite Standards: Interorbital Systems | Overall Scope | Critical | Yes
IEEE Industry Application Society | Part Selection | Medium | Yes
Energy Management and ADCS using flywheels by IEEE 2012 | Part Selection | Medium | Yes
SBSP IEEE (2012) | Part Validation | Low | Yes
IEEE 370-20202 | PCB Design/Testing | High | Yes
Notes: Just like our requirements, our project specifications were also meant for space-bound systems. At this point of the project all of specifications have been validated. We opted out of using lead-free solder as a project decision, due to the fact that it is more fragile as it is more suseptable to mechanical shock, and higher heat dissipation. This would pose a greater risk to the project, than the benefit from implementing this specification, so we decided to go with lead-based solder

## Slide 7
Overall Project Design and Implementation

## Slide 8
Overall Project Design and Approach
Overall Project Design
Mechanical | Sensor / Software | Electrical
Servo Motors (3) | C & C++ | Microcontroller
Reaction Wheels (3) | Inertial Measurement Module | Voltage Regulators
Attitude Determination and Control System (ADCS) Mounting Structure | ADCS Algorithm | Motor Controllers
 |  | Power Supply

## Slide 9
Overall Project Design

## Slide 10
Project Design
Mechanical

## Slide 11: Brushless DC electric motor (BLDC)
In order of the operation BLDC is more reliable
BLDC is lighter compared to other motors
Benefits to BLDC Motors
  Better Performance
  Long operating life
  Low heat dissipation
  Higher torque
  Perfect shaft size for a reaction wheel design
  To fit in our TubeSat, we are cutting the shaft smaller; the shaft will be 3.3 mm from the front plate
15mm Brushless Motor
PARAMETER | SPECIFICATION
Rated Load Speed | 14,000 rpm
Rated Operating Voltage | 5V
Shaft size | 21 mm
Commutation | Sensorless
Max. Output Power | 900 mW

## Slide 12: How does Brushless DC electric motor work ?
Rotor is a permanent magnet
Stator has a coil arrangement
When DC electricity is applied to the coil, it will activate and form an electromagnet.
Each phase of a three-phase motor is linked via a wire.
When one coil is energized, the opposite poles of the rotor and the stator are attracted to each other, causing the motor to begin spinning

## Slide 13: Reaction Wheel
A piece of hardware is also known as a momentum wheel which is the most important component in this design. We would not be able to create angular momentum to counterbalance the satellite's angular momentum without it
Reaction wheel do not consume fuel and high pointing accuracy
The operation of the reaction wheel is based on newton’s third law
The third restriction is the total angular momentum required for the wheel to be effective

## Slide 14: Reaction Wheel Specification
Pure Lead was chosen to be the optimum material for the response wheel by the team
The periodic table number 82 is pure lead, which has a density of 11.35 g/cm^3
Pure lead is low cost and machinable
Manufactured in UCF at the CECS machine lab
The thickness of design reaction wheel is 1/8 inch
Mass = 11.30 grams

## Slide 15: Satellite Stabilization and Moment of Inertia
Principal axes of inertia and principal moments of inertia : ( grams * square millimeters) | 
Px | 287.98
Py | 287.98
Pz | 556.98
Principal axes of inertia and principal moments of inertia : ( grams * square millimeters) | 
Px | 1160000
Py | 1400000
Pz | 1540000
Angular momentum calculation to stabilize the satellite:
 556.98 * 14,000 = 7797720
 7797720 / 1540000 = 5 RPM
Reaction Wheel Measurements
TubeSat Measurements

## Slide 16: Mounting Structure
The ADCS Mounting Structure is used by connecting the BLDC motors and Reaction Wheels to the ADCS PCB in all three axes.
Manufactured in UCF at the Texas Instruments Innovation Lab
40.94 mm x 40.94 mm square, placed on the bottom of our PCB
Benefits of the designed mounting structure
  Stabilization and isolation between the three motors on the three- axis
  Prevent any loss of frictions
  Motors will be more fixed to avoid any loss of energy

## Slide 17
Project Design
Software

## Slide 18
Sensor/Microcontroller
Inertial Measurement Unit
BMX 160
Collects gyroscope, acceleration, and magnetic readings
Feeds data to MCU
Microcontroller Unit
Arduino ATmega 2560
        Responsible for running software.
  Collect sensor data.
Adjust system accordingly.
3.3V logic

## Slide 19
BMX 160
Features
Low power 9-axis sensor
16-bit digital triaxial accelerometer, gyroscope, and geomagnetic sensor
I2C or SPI support
Built-in power management unit
Specific method of sensing axes orientation

## Slide 20
Arduino ATmega 2560
Features
9 timer modules with PWM support
8-bit AVR based CPU, 3.3 V, 8 MHz
Wide range of pins
Power saving modes
Sleep modes

## Slide 21
Software Design
Arduino IDE
Use C/C++
Ease of programming
Can write functions and libraries
Can write header and source files

## Slide 22
Software Design

## Slide 23
Software Implementation
IMU collects data and feeds to MCU
Code will activate corresponding signals on MCU
Output goes through step-up regulator
MCU will energize motors accordingly

## Slide 24
Software Test
Notes: Software functionality has to be tested for complications
Devised a test/checklist
Due to constraints, there has to be little room for error

## Slide 25
Project Design
Electrical

## Slide 26: IOS Main Board
Contents
Microcontroller - ATmega2560
IMU – BMX160
4-Mbit FRAM – CY15B104Q
Transceiver – Si4464
Amplifier – RFFM6406
Li-Ion Battery Charger
Solar Panel Connectors

## Slide 27: ADCS Prototype
3-Phase Motor Controller | Voltage Regulator | Microcontroller | Motor
TI DRV10964 | Pololu U3V12F5 (5V Boost) | Arduino Mega2560 Dev Board | Precision Microdrives 712-100.001 BLDC Motor
*Connections and Vise were for initial product testing purposes only; not included in final design

## Slide 28: Printed Circuit Board (PCB)

## Slide 29: Schematic (Eeschema)
Components | Use
TPS61232 | 5V Boost Converter
DRV10964 | 3-Phase BLDC Motor Controller
Resistor | CONFIG Voltage Divider
Inductor | Energy Storage
Capacitor | Bypass

## Slide 30: PCB Layout (Pcbnew)

## Slide 31: PCB Test

## Slide 32
Project Difficulties
Mechanical
Machining Lead Reaction Wheels
Electrical
Voltage Regulator Part Shortage
CONFIG PIN Handoff Threshold
Software
Bootloader Configuration Change
Modification of Timer Control Register Frequency
Stakeholder Management
NASA FSGC Grant Administration
Partnership with Interorbital Systems
Partnership with UCF / CSF
Notes: An overview of some of the hurdles we went through in our project.
Starting with our mechanical design - Lead wheels are brittle when compared to the standard aluminum alloy wheels, but in order to increase the inertia we are generating we needed a more dense material than the standard aluminum wheels. This lead a more intricate machining process than expected.
With the electrical design we had a part shortage overall for for regulators due to manufacturing delays and closing due to covid.
In order to get the correct voltage in our CONFIG pin we actually needed to put in a voltage divider to match the Back EMF that it was expecting to receive.
//CONFIG PIN – prob: getting 5V, but the Back EMF is 240hz//1.4V so we needed to put in a voltage divider – integration issue
For software it was mainly dealing with system integration, where we needed to Modify upload speed and frequency of the CPU in the bootloader data fand we needed to change the analog frequency of our Arduino in order to satisfy the MC frequency of 25KHz.
For stakeholder management, it has been an extremely involved effort as just getting a faculty member to sign on and process the application took three months and multiple escalations
Our partnerships with Interorbital systems and CSF were key with feedback and expectations especially when we were finalizing our design or missing information that proved necessary for integration.
Bootloader – Modify upload speed and frequency of the CPU in the bootloader data
TCRF – MC requires 25kHz, Arduino defaults Anaolog frequency 490Hz, which needed to be modified to satisfy MC

## Slide 33: Project Finalization
Project Budget
Project Responsibilities/ Complexity Overview
Future Plan

## Slide 34
Project Expenditures
Type | Description | QTY | Cost
Fund Expense | GoFundMe (withdraw fee) | 1.00 | -$95.52
Material Cost | TubeSat 2.0 kit | 1.00 | -$5,620.60
Material Cost | Torx screwdrivers set | 1.00 | -$17.17
Material Cost | Sony/Murata VTC6 15A-30A 3000mAh Flat Top 18650 Battery | 6.00 | -$48.72
Material Cost | BMX160 Shuttle Board | 1.00 | -$32.99
Material Cost | DEYUE 3 Set Standard Jumper Wires Plus 3 Set of Solderless Prototype Breadboard 830 tie Points Breadboard | 1.00 | -$8.99
Material Cost | Arduino Mega 2560 | 2.00 | -$31.98
Material Cost | Brushless 4 click | 1.00 | -$30.20
Material Cost | Pololu 5V Step-Up Voltage Regulator U3V12F5 | 1.00 | -$7.32
Material Cost | 12mm Brushless Motor - 15mm Type (1 Motors + Shipping) [Prototype] | 1.00 | -$117.11
Material Cost | 12mm Brushless Motor - 15mm Type (3 Motors + Shipping) [Final] | 1.00 | -$232.89
Material Cost | PCB Production Costs [Prototype] | 1.00 | -$30.00
Material Cost | Wheel Machining Costs [Prototype] | 1.00 | -$212.91
Material Cost | Hook Screw Set | 1.00 | -$5.00
Material Cost | PCB Production Costs [Final] | 1.00 | -$40.24
Material Cost | Wheel Machining Costs [Final] | 1.00 | $0.00
Material Cost | Pick and Pluck - Pre-Cubed Foam Tray 300 mm x 300 mm x 25 mm (11.8 inch x 11.8 inch x 1 inch) Plus Free Bottom | 1.00 | -$15.99
Material Cost | Pelican Air 1507 Case with Foam (2020 Edition with Push Button Latches) - Black (015070-0001-110) | 1.00 | -$176.95
Material Cost | Sea Striker Monofilament Fishing Line | 1.00 | -$8.64
Material Cost | Loctite 1330585 263 Thread Locker, 50 mL | 1.00 | -$14.22
Material Cost | BSTEAN Syringe Blunt Tip Needle and Cap - 10ml, 5ml, 3ml, 1ml Syringes 14ga 16ga 18ga 20ga Blunt Needles - Oil or Glue Applicator (Pack of 10) | 1.00 | -$7.89
Material Cost | Gorilla 2 Part Epoxy, 5 Minute Set, .85 Ounce Syringe, Clear, (Pack of 1) | 1.00 | -$6.95
Material Cost | DRV10964EVM | 1.00 | -$49.00
Material Cost | ADCS Mounting Structure 3D Print | 1.00 | -$9.26

## Slide 35: $6,820.54 2.6%
Total Expenses (Finalized)
Project Savings (Finalized)
Amount Fundraised/Granted
Project Expenditures
$7,000

## Slide 36
Project Sponsors

## Slide 37: Project Schedule
 | Senior Design 1 |  |  |  |  | Senior Design 2 |  |  | 
 | DEC20 | JAN21 | FEB21 | MAR21 | APR21 | MAY21 | JUN21 | JUL21 | AUG21
Mechanical Design |  | A |  |  |  |  |  |  | 
Electrical Design |  |  |  | A |  |  |  |  | 
Procurement |  |  |  |  |  |  | A |  | 
Software Design |  |  |  |  |  |  | A |  | 
Testing (Reaction Wheel) |  |  |  |  |  |  | A |  | 
Assembly |  |  |  |  |  |  |  | A | 
Testing (Reactive) |  |  |  |  |  |  |  | A | 

## Slide 38: Project Responsibility Matrix
KEY |  |  | Designed | 
 |  |  | Integrated | 
MCU
PCB
Radio
Amplifier
Antenna
Inertial Measurement Unit
Step Up Regulator
Mounting Structure
Step-Up Regulator
Motor Controller
Motor
Reaction Wheel
Power Supply
Solar Panels
Software
Daniel Cadena
Islam Aly
Mark Barbaro
Andy Garcia
Notes: components

## Slide 39: Future Plans
1
3
5
6
4
2
Demo the System with Reactive Software Test
Lessons Learned Workshop with CSF
Launch
Handoff to The Collegiate Space Foundation
Flight Readiness Review
Obtain Performance Information
SD Project Completion Benchmark

## Slide 40: THANKS!
Any questions?
Mark Barbaro Electrical Engineering
Daniel Cadena Electrical Engineering
Andy Garcia Electrical Engineering
Islam Aly Electrical Engineering