## Slide 1: UCF Rain Simulator “ ” Project
Group 10:
Luke Falls
Adam Cutting
David Levy
Brenda Garcia
R

## Slide 2: Introduction
Largest rain simulator of its kind in North America
Trouble with existing control system
Need a fix for the existing problems

## Slide 3: Introduction

## Slide 4: Introduction

## Slide 5: Introduction

## Slide 6: Introduction

## Slide 7: Introduction

## Slide 8: Existing Control System Overview
Communication to laptop is unreliable
Power supply is intermittent
Problems hinder their ability to meet simulation deadlines
Very Expensive: Approximately $ 5,000.00 for control system.
Far more capable than what is necessary for the application
Inefficient Design

## Slide 9: Motivation
Fixing the existing problems is not sufficient
  Power supply
  Hub-444 communication module
Avoid ruining the existing system
Project benefits another UCF department
To gain experience with motor control systems

## Slide 10: Goals & Objectives
Provide a reliable control system that can accurately deliver the desired amount of rain
Make new control system interchangeable with the existing system
Water resistant enclosure
Keep the design simple
  User friendly interface
  Eliminate the need for a computer

## Slide 11: Specifications & Requirements
Two user inputs: Intensity and Duration
  0.5 in/hr of rainfall accuracy (max 12 in/hr)
  1 minute duration accuracy
The microcontroller needs to have 2 serial communication modules and 60 GPIO pins
Rain sensors need to be accurate within 0.25 inches
Each motor driver needs to be able to handle at least 5.66 amps per phase
Stepper motor power supply rating of 65 Watts.

## Slide 12: Overall Control System Design

## Slide 13: User Interface Components
Storm-Interface Display Bezel
  Impact Resistant
  4x20 Character LCD
  3 Navigation Buttons
  Weather Sealed for outdoor use
Storm-Interface Keypad
  Vandal and impact resistant
  Weather, water, and dust resistant (IP65)
  -40ºC to 100ºC Operating Temperature
  Operating Life of at least 4 million
  cycles per key
4.20”
3.40”
3.90”
4.70”

## Slide 14: Low Voltage Power Supply Design

## Slide 15: Low Voltage Thermal Design
= 5.8C/W
= 138.3C < 150
12 Volt Regulator
= 53C/W
= 126.2C < 150
5 Volt Regulator
= 5.8C/W
= 84.1C < 150
3.3 Volt Regulator

## Slide 16: TI DRV8432 Motor Driver
Operating Supply Voltage – up to 52VDC
Continuous Output Current – 2 @ 7A
Transient Peak Output Current – 2 @ 16A
Integrated self protection from undervoltage, overtemperature, overcurrent, and short circuit
Up to 97% efficient
Each IC contains two full H-Bridges with 12 VDC gate supply voltage

## Slide 17: TI DRV8432 Motor Driver

## Slide 18: Motor Driver PCB Considerations
2 oz copper on both top and bottom layers for improved thermal performance and lower noise
Short and wide ground traces with multiple vias to ground plane to reduce noise
Clear space around IC to improve heat sinking
Separate PCB for each motor driver

## Slide 19: Microcontroller Schematic

## Slide 20: Microcontroller Schematic

## Slide 21: Microcontroller Selection
Launchpad
MSP430F5435
MSP430F5438a
 | GPIO | Communication Modules | RTC | External Interrupts | PWM Outputs | Free Target Board
G2452 | 14 | SPI, I2C | No | 16 | 3 | No
F5435 | 67 | SPI, I2C, UART | Yes | 16 | 15 | No
F5438a | 87 | SPI, I2C, UART | Yes | 16 | 15 | Yes

## Slide 22: Software Design Approach
Make the system interrupt driven
Simplify code using interrupt vectors
Utilize the MCU’s built-in peripheral modules
Modularize the software
Verify desired functionality of all software on the target board
Write all code in C using TI’s Code Composer Studio IDE
Implement a software state machine

## Slide 23: Software Design

## Slide 24: User Input Software Routine

## Slide 25: Microcontroller I/O

## Slide 26: “ ” Issues
PWM Frequency = 40 kHz
PWM Duty Cycle = 7%
Motor Speed = 50 steps/sec
PWM Frequency = 40 kHz
PWM Duty Cycle = 25%
Motor Speed = 330 steps/sec
PWM Frequency = 40 kHz
PWM Duty Cycle =
85%, then 7%
Motor Speed = 330 steps/sec
R

## Slide 27: High Voltage Power Supply
Provides power to the stepper motors via the drivers
Simple unregulated power supply
  Handles back EMF better than a SMPS
Difficulty in determining the voltage and current ratings

## Slide 28: Enclosure

## Slide 29: Enclosure

## Slide 30: Wireless Rain Sensor
Uses:
  Measure rainfall for duration of the simulation
  To check calibration of nozzle sweep-stop frequency
  To indirectly check the water pressure of the rain nozzles

## Slide 31: Wireless Rain Sensor- PCB Design
Open Circuit without any water in the gauge

## Slide 32: Wireless Rain Sensor- PCB Design
1st Level-
Water conducts current and acts as a single resistor

## Slide 33: Wireless Rain Sensor- PCB Design
2nd Level-
Water conducts current and acts as two resistors in parallel

## Slide 34: Wireless Rain Sensor- PCB Design
At the nth level of water, there are ‘n’ equivalent resistors in parallel

## Slide 35: Wireless Rain Sensor- Block Diagram
LDO
3.3 volt
regulator

## Slide 36: Wireless Rain Sensor- PCB Simulation
The Sense Resistor Value greatly impacts the linearity of the input voltage to ADC
Rsense = 1.0 kΩ

## Slide 37: Wireless Rain Sensor- PCB Simulation
Rsense = 100Ω

## Slide 38: Wireless Rain Sensor- PCB Simulation
Rsense = 10Ω

## Slide 39: Wireless Rain Sensor- XBee 2.4GHz
6 Built-In 10-bit ADC
Requires 3.3v Input
On-Chip antenna
Easy to Integrate to PCB
Serial Communication to MCU

## Slide 40: “ ” Issues
Wireless Rain Sensor
  Resistance of copper changes with oxidation due to electrolysis
Potential Solution
  Use different material  Stainless Steel
  Use lower voltage  3.3-4.5 volts
  Pulsed readings
R

## Slide 41: Budget & Financing - Development
Development Costs |  |  |  |  | 
 | Item | Quantity | Price/Unit | Projected Cost | Actual Cost
1 | Small Scale Model | 1 | $150.00 | $150.00 | $82.84
2 | MSP430 Development Board | 2 | $4.30 | $8.60 | $8.60
3 | Motor Driver Dev Kit | 2 | $175.00 | $350.00 | FREE
4 | MSP430F5438A Target Board | 1 | $149.00 | $149.00 | FREE
 |  |  |  | $657.60 | $91.44
Team Budget |  | $200.00 |  |  | 
Rev1
Rev2

## Slide 42: Budget & Financing - Deliverable
Costs for Rain Simulator |  |  |  |  | 
 | Item | Quantity | Price/Unit | Projected Cost | Actual Cost
1 | Motor Drivers | 2 | $14.26 | $28.52 | FREE
2 | Custom Stainless Steel Enclosure | 1 | $500.00 | $500.00 | FREE
3 | Amphenol Receptacles | 2 | $33.75 | $67.50 | $67.50
4 | Rain Gauges | 1 | $65.00 | $65.00 | $65.00
5 | Microcontroller | 1 | $11.67 | $11.67 | FREE
6 | PCBs | 2 | $50.99 | $101.98 | $102.00
7 | Storm-Interface LCD | 1 | $92.53 | $92.53 | FREE
8 | Storm-Interface Keypad | 1 | $64.72 | $64.72 | FREE
9 | Circuit Components | 1 | $40.00 | $40.00 | $40.00
10 | High Voltage Power Supply | 1 | $500.00 | $500.00 | $24.00
11 | Low Voltage Power Supply | 1 | $35.00 | $35.00 | $13.41
 |  |  |  | $1,466.92 | $206.91
Team Budget |  | $600.00 |  |  | 
Sponsorship |  | $200.00 |  |  | 

## Slide 43: Current Progress
Chart: 
| Research | Software testing | PCB development | Parts acquistion | Design/Build Enclosure | Prototype | Hardware Testing | Overall
"R" Progress | 0.95 | 0.5 | 0.33 | 0.7 | 0.45 | 0.9 | 0.2 | 0.57571

## Slide 44: Final Steps
 | 7-Oct | 15-Oct | 21-Oct | 30-Oct | 7-Nov | 14-Nov | 21-Nov | 30-Nov
Replace 5v regulator on LV power supply |  |  |  |  |  |  |  | 
Order motor driver and MCU PCBs |  |  |  |  |  |  |  | 
Order PCB components |  |  |  |  |  |  |  | 
Assemble/Test PCBs |  |  |  |  |  |  |  | 
Build the enclosure |  |  |  |  |  |  |  | 
Determine step speed/pause times |  |  |  |  |  |  |  | 
Build/Test the rain gauge |  |  |  |  |  |  |  | 
Final assembly |  |  |  |  |  |  |  | 
Verify simulations |  |  |  |  |  |  |  | 

## Slide 45: Questions about “ ” Project?
R