## Slide 1: Interactive Automated Chess Set
Group 4:
Brett Rankin
Paul Conboy
Samantha Lickteig
Stephen Bryant

## Slide 2: Goals
To create a portable interactive chess board where gameplay will be fully automated.
Each piece will be moved by a claw suspended above the board
Person vs. Computer game play

## Slide 3: Specifications
90% chess piece movement accuracy
Total weight <100 lbs
  Able to be lifted by two people
12”x12” playing grid

## Slide 4: Features and Functions
LED lights will be used to light up the squares on the board
  Individual squares, communication with the user(s)

## Slide 5: Features and Functions
Player modes:
  1.) Player vs. Computer
  2.) Player vs. Player
  3.) Computer vs. Computer

## Slide 6: Block Diagram

## Slide 7: Physical Chess Table

## Slide 8: Mechanical
Three Motion Axis
One Gripper
Sliding A Frame Structure
Overhead Gantry
Stability and Consistent Repeatable Motion Control Needed

## Slide 9: Gripper Claw
Purchase gripper and servo this was not a design item
One Micro Controller I/O output to command gripper open and closed
Pulse width command signal with a 20 ms period. The pulse on time will vary to open and close the gripper.
Modified gripper, added fingers and memory foam.

## Slide 10: Stepper Motors
Three 12 Volt Bi-polar Stepper Motors.
Torque Value for X,Y,& Z Axes rated at 2.4Kg*cm
The Y Axis (moves the A frame structure) needed more torque, so we set it the full step mode.
The X and Z axes are set for half step mode. This is a trade off for smother quieter operation.

## Slide 11: Motor Control
Design Goals
  Single Modular Design for all Three Axes
  Easy to bread board Avoid surface mount technology
  Must be practical to install heat sink
  Minimize micro controller I/O count. Three outputs per controller.
  Based on proven reference design

## Slide 12: Motor Control Schematic
L297
L298

## Slide 13: Stepper Resolution
Each step equals 1.8 degrees of angular displacement.
200 steps per revolution
No feedback needed with stepper motors
X and Y axes have the same size spur and rack gears, so the scaling is the same
Z axis needs 1½ revolution of the large gear.
Calculated 1REV = 1.978in 1Step ≈ .01in
Measured (Y axis) 124 steps = 1.5 inches

## Slide 14: Motion Control Circuits
X and Y Axes Over travel switches in the E-Stop chain.
E-Stop Switch
X,Y and Z Axes Home limit switches to provide the micro controller with a starting reference.
The gripper did not need position sensing due to mechanical design. No signal = Open position.

## Slide 15: LED Grid
Purpose:
    The grid of LEDs have a dual function, to add a lighting aesthetic to the board and visual cues for the player based on what is happening in the game.
    The board itself does not have painted on black and white squares, like most chess boards, but rather it has the LEDs under the board turn on or off in a checkerboard pattern to make the distinction between squares.
    The LEDs blink to indicate the position of where the piece is coming from and heading to.

## Slide 16: LED Grid
Parts to use:
    MAX7219 24Pin DIP 8X8 grid LED Driver
    Standard 20mA LEDs

## Slide 17: LED Grid

## Slide 18: User Interface
Displays messages
  Prompts the user
  Informs the user
Serial LCD Module 20x4 Blue with White Backlight for Arduino

## Slide 19: User Interface
Has buttons for input selections

## Slide 20: Microcontroller Requirements
Must run an onboard minimalist chess engine
Large development community
Easy access to dev tools.

## Slide 21: Microcontroller Specifications
60 I/O pins
4 hardware timers
4 USART
60 KB flash
4 KB SRAM

## Slide 22: Microcontroller Schematic

## Slide 23: Xmega128A1
8KB SRAM
78 I/O pins
8 UART for Serial
8 Timers for PWM
128KB Flash memory
AVRFreaks support community
Atmel Tutorials, Atmel software suite

## Slide 24: Development Tools
A1Xplained Board
For testing individual components
Atmel Studio
USB gateway
Had to program using Atmel FLIP
No debugging

## Slide 25: In System Programming
Ordered an AVR-ISP-MK2
Program in system with PDI

## Slide 26: Software

## Slide 27: Main Module

## Slide 28: Main Module
Use only high level method calls
Describes high level gameplay process
Orchestrates interaction between I/O and Engine
Translates “moves” between chess engine and I/O module representations

## Slide 29: Chess Module

## Slide 30: Chess Module
Contains internal state of chess game
Accepts player moves and creates AI moves
Should use < 4 KB RAM
Micro-Max open source chess engine
Smallest chess engine in the world
Our goal was not to understand, but to interface.

## Slide 31: I/O Module

## Slide 32: I/O Module
Contains functions to interface with individual I/O devices
Exposes high level interface to main module

## Slide 33: Motor Controller
All motor I/O functions grouped together
High level interface including “move piece”

## Slide 34: Test Framework
Created test suite
Unit tests
  LCD test
  LED grid test
  Individual Motor tests
Integration tests
  HMI integration test
  AI Integration test
  Full play test

## Slide 35: Test Plan
We developed a written test plan to check everything against
  Acceptance Test Plan (ATP) where the Acceptance Test Results (ATR) are the final test results

## Slide 36: Problems that Occurred
Wiring the LED lighting grid
Eccentric gear concept
  Replaced with a spool for Z axis
Vibration
LCD screen
Repeatability
Binding
Integration issues
  Actually putting everything on/beneath the board

## Slide 37: What Didn’t Make It: Hall Effect Sensor Grid
Original Purpose:
    For the microcontroller to understand where the chess pieces are Hall Effect sensors would have been placed under the board and grave yard.
    The sensors would read whether or not the chess piece, which originally had a magnet embedded into it, is on particular squares.

## Slide 38: Budget

## Slide 39: Budget

## Slide 40: Total Spent
$544.80

## Slide 41: Sponsors
Igus
Allied Electronics

## Slide 42: Work Distribution
Chart: 
| Hall Effect | LED Grid | Mechanical Assmbly | Enclosure | Motor Control | MCU Design | Software | Integration | Administration | HMI
Brett | 1 | 0.7 | 0 | 0.2 | 0 | 0.9 | 0 | 0.25 | 0.05 | 0.2
Paul | 0 | 0 | 1 | 0.8 | 0.7 | 0 | 0 | 0.25 | 0.05 | 0.2
Samantha | 0 | 0.3 | 0 | 0 | 0 | 0 | 0 | 0.25 | 0.85 | 0.6
Stephen | 0 | 0 | 0 | 0 | 0.3 | 0.1 | 1 | 0.25 | 0.05 | 0