## Slide 1: Small Projector Array System
Group #7
Nicholas Futch
Ryan Gallo
Chris Rowe
Gilbert Duverglas Sponsor: Q4 Services LLC

## Slide 2
Project Motivation
Problems:
High cost of current projector systems
Degradation of image quality due to image warping
Time loss due to image correcting
Maintenance cost and time associated with lamp based projectors

## Slide 3: Our Solution
Implement an array of low cost pico projectors
Lowers degradation of image due to the curvature of the screen
Internal image warping to save time on installs
LED projectors with extremely high life cycles

## Slide 4: Specifications
Low cost solution
Easy implementation with existing simulators
Longer MTBF (Mean Time Between Failure)
Lower amount of pixel loss due to image warping

## Slide 5: System Block Diagrams

## Slide 6: Graphics Cards
AMD (formerly known as ATI)
NVidia
Proprietary Crossfire Technology
Significantly better multi-monitor Support
Currently supports projector overlap
Warping and edge blending support soon
Proprietary SLI Technology
Slightly better overall Graphics

## Slide 7: Projector Box Control System
Microcontroller system
Low power
Must accept RS-232 data from host computer
Must accept TTL data from the light sensor array
Digital outputs for control of various other parts

## Slide 8: Program Flow Chart

## Slide 9: Schematic
Atmega 328 microcontroller
MAX232 chip for TTL to RS-232 signal conversion
Two 2 to 1 Multiplexors to route Serial data to either the light sensor or the host computer system

## Slide 10: Light Sensor Array Control System
Must accept TTL data from projector box
Must accept Analog signals from light sensor array

## Slide 11: Program Flow Chart

## Slide 12: Schematic
Atmega 328 Microcontroller
16 to 1 Multiplexor to switch between analog outputs
Low pass filter for filtration of light sensor signals

## Slide 13: Human Interface Specifications
Easy to use user interface
Ability to send data up to 50 feet
Independent interface for the light sensor array
Low power consumption
Cross-platform

## Slide 14: Projectors Specifications
Requirements
Solutions
Low Cost
High Pixel Count
LED
Low Power
High MTBF
High Brightness and Contrast
Low Noise
Variable Focus Control
Pico Projectors
1280 x 800 Resolution
DLP LED
< 120 watts
20,000+ lamp liftime

## Slide 15: Pico Projector Comparison
Projector | Contrast | Focus Control | Brightness | Noise | Overall Image
Acer K11 | 6.5 | 8 | 7 | 4 | 6
Acer K130 | 9 | 6 | 6 | 7 | 7
Acer K330 | 8 | 8 | 10 | 7 | 8
ViewSonic PLED | 4 | 8 | 5 | 3 | 4
Vivitek Qumi Q2 | 8 | 3 | 7 | 7 | 7.5

## Slide 16: Acer K330
Device Type | DLP
Native Resolution | WGXA(1280x800)
Maximum Resolution | 1600x1200
Projector Distance | 35.43 in – 9.83 ft
Throw Ratio | .85
Display Size | 30 in – 8.33 ft
ANSI Lumens | 500
Contrast | 4000:1
Lamp | LED
Aspect Ratio | Native: 16:10 Supported: 16:9, 4:3
Power supply | 100-240V AC 50/60 Hz
Power Consumption | 120w
Video Inputs | D-Sub, HDMI, Composite
Dimensions | 8.6 x 6.6 x 1.8 in
Weight | 2.73 lbs

## Slide 17: Projector Orientation and Overlap
The 4 projector layout with an aspect ratio of 1:1
Resolution of 2600 x 1600 for a total of over 4.5M pixels
Almost identical to the latest WQXGA format at a fraction of the cost.
Will make the most use out of the usable area of the screen.

## Slide 18: Analog Light Sensor
Used to get measurements from the single projector and the projector array for comparison.
Readings will be read by microcontroller and displayed on a GUI on the host computer

## Slide 19: Light Sensor Specifications
PCB form factor no greater than 1in^2
Low power consumption (less than .5 mW)
Max input voltage @ 5V (provided by microcontroller)
Analog output less than 5V
Range of illuminance between 0 and 100k lx
Maximum photosensitivity @ 550nm to mimic human eye

## Slide 20: SFH 5711 by Osram
Opto hybrid (photodiode with an integrated circuit)
Mimics the human eye almost exactly
Very low power consumption
Logarithmic current output (High accuracy over wide illumination range)
Surface mount

## Slide 21: SFH 5711 Specifications
Parameter | Symbol | Value |  |  | Unit
 |  | Minimum | Typical | Maximum | 
Supply Voltage | VCC | 2.5 |  | 5.5 | V
Illuminance TA= -30oC to 70oC TA= -40oC to 100oC | EV |  | 3 to 80k |  | lx
 |  |  | 10 to 80k |  | 
Spectral Range Sensitivity | λ10% | 475 |  | 650 | nm
Wavelength of Max Photosensitivity | λs max | 540 | 555 | 570 | nm
Output Current @ EV= 1000 lx | Iout | 27 |  | 32 | μA
Current Consumption VCC= 2.5 V VCC= 5.0 V @ EV= 0 lx | ICC |  | 410 | 500 | μA
 |  |  | 420 |  | 
Current Consumption VCC= 2.5 V VCC= 5.0 V @ EV= 1000 lx | ICC |  | 460 | 550 | μA
 |  |  | 470 |  | 

## Slide 22: SFH 5711 vs. Human eye

## Slide 23: SFH 5711 vs. Human eye cont.

## Slide 24: Light Sensor Circuit Diagrams
Illuminance: 0 - 10k lx
Output voltage: 0 - 3V

## Slide 25: Maximum detectable light level

## Slide 26: Light Sensor Array
Find a way to arrange light sensor in an array setup in front of projector screen
Must be easily stable, lightweight, and easily portable
Wires must not be obstructed so communication with projector box can happen
Solution: use a PVC pipe structures as array to house light sensors

## Slide 27: ANSI Lumens Test
Describes the standard method for testing the brightness of projectors.
Method involves measuring brightness of a projector screen at 9 specific points using light sensors and finding average value between these points.

## Slide 28: ANSI Lumens Test

## Slide 29: Light Sensor Array

## Slide 30: Light Sensor Array Testing
Warped image will be projected onto BP dome screen.
PVC light sensor array will be placed in front of screen facing projector box.
The wires coming from the array will be connected to the microcontroller in the projector box.
Lumens rating will be displayed on computer host system from each sensor and total lumens will also be displayed.

## Slide 31: Light Sensor Array Considerations
Make array 3 x 6 instead of 3 x 3 so that array can cover and measure whole BP screen at once without physically moving array.
Automated light sensor array

## Slide 32: Automated Light Sensor Array
Automatically move the PVC light sensor on top of BP projector screen
Use of stepper motor and gears to apply rotational movement of array
Clamp will be used to hold the array
Array will be moved manually side to side to compare both projector systems

## Slide 33: Motor and Motor Drive
Arduino Motor Shield
  Capable of driving one stepper
  Operates at 5-12V, 2A per channel 4A total
  Allows easy control for motor direction and speed
Unipolar Stepper Motor
  Operates at 4V at 1.2A per channel
  Torque 27 lb/ft

## Slide 34: Power System
Requirements:
  Capable of powering following devices
    4 Pico Projectors (120 VAC)
    2 Microcontrollers (3.3 – 5 VDC)
    1 Servo Motor (4 VDC @ 2.4 A)
    Host Computer System (120 VAC)
  Power system should be capable of providing power to all these components from a single point or “power box” and only receiving the standard main power signal from a traditional wall outlet

## Slide 35: Power System
Specifications
  Input: Should be able to take incoming power signal from any outlet (100-240 VAC 50/60 Hz)
  Output: Independent from incoming signal, will output regulated 3.3 – 5 VDC signal to microcontrollers and 4 VDC signal to servo motor, as well as remaining circuit components
  Size: will be housed within the “power box” enclosure

## Slide 36: Power System
Design Options:
  4 options considered that all met our power system design requirements.
Design | Efficiency | Design Difficulty | Cost | Electronic Noise
Linear Power Supply | ~ 58 – 70% | Moderate | ~ $20-30 | Low
Switched Mode Power Supply | ~ 79 – 90% | High | ~ $60-75 | High
Step Down DC to DC Converter | ~ 70 – 78% | Moderate | ~ $35 | Low
AC to DC Converter | ~ 74 – 85% | Low | ~ $15-30 | Low

## Slide 37: Power System
Power Flow Diagram

## Slide 38: Power System
Power Flow Diagram for components that require DC Power

## Slide 39: Power System
KMS40-12 AC to DC Converter:
  Input: 90-264 VAC
  Output: 12 VDC
  Current: 3.33 A
  Power: 40 W
  Type: Switching (Closed Frame)
  Efficiency: 83%
  Through Hole Board Mount
  Load Regulation: ± 1%

## Slide 40: Power System

## Slide 41: Distribution of Work
 | Programming | Control System Schematics | Sensor Array Mechanics | Sensor Array Schematics | Power | Projector Array
Nick | 85% | 40% | 10% | 10% | 5% | 25%
Chris | 5% | 10% | 10% | 70% | 5% | 25%
Ryan | 5% | 40% | 10% | 10% | 85% | 25%
Gilbert | 5% | 10% | 70% | 10% | 5% | 25%

## Slide 42: Budget
Part | Price per Unit | Quantity | Total
Projectors | $549 | 4 | $2169
Host Computer | $1399 | 1 | $1399
Graphics Card | $550 | 1 | $550
Warping Software | $191.95 (per channel) | 4 | $767.80
PCB parts | $450 | 1 | $450
Box PCB | $100 | 1 | $100
Sensor Array PCB | $75 | 1 | $75
Sensor PCB | $30 | 9 | $270
TOTAL |  |  | $5780.80

## Slide 43: Project Accomplishments to Date

## Slide 44: Potential Issues
Alignment of Projectors
Single Stepper Motor torque
Sensitivity of Light Sensors
Overall Projected Image