## Slide 1: Small Projector Array System
Group #7
Nicholas Futch
Ryan Gallo
Chris Rowe
Gilbert Duverglas Sponsor: Q4 Services LLC

## Slide 2: Introduction to Collimated Display Systems

## Slide 4
Project Motivation
Problems:
High cost of current projector systems
Degradation of image quality due to image warping
Time loss due to image correcting
Maintenance cost and time associated with lamp based projectors

## Slide 5: Our Solution
Implement an array of low cost pico projectors
Lowers degradation of image due to the curvature of the screen
Internal image warping to save time on installs
LED projectors with extremely high life cycles

## Slide 6: Specifications
Low cost solution
Easy implementation with existing simulators
Longer MTBF (Mean Time Between Failure)
Lower amount of pixel loss due to image warping

## Slide 7: System Block Diagrams

## Slide 8: Graphics Cards
AMD (formerly known as ATI)
NVidia
Proprietary Crossfire Technology
Significantly better multi-monitor Support
Currently supports projector overlap
Warping and edge blending support soon
Proprietary SLI Technology
Slightly better overall Graphics

## Slide 9: Projectors Specifications
Requirements
Solutions
Low Cost
High Pixel Count
LED
Low Power
High MTBF
High Brightness and Contrast
Low Noise
Variable Focus Control
Pico Projectors
1280 x 800 Resolution
DLP LED
< 120 watts
20,000+ lamp liftime

## Slide 10: Pico Projector Comparison
Projector | Contrast | Focus Control | Brightness | Noise | Overall Image
Acer K11 | 6.5 | 8 | 7 | 4 | 6
Acer K130 | 9 | 6 | 6 | 7 | 7
Acer K330 | 8 | 8 | 10 | 7 | 8
ViewSonic PLED | 4 | 8 | 5 | 3 | 4
Vivitek Qumi Q2 | 8 | 3 | 7 | 7 | 7.5

## Slide 11: Acer K330
Device Type | DLP
Native Resolution | WGXA(1280x800)
Maximum Resolution | 1600x1200
Projector Distance | 35.43 in – 9.83 ft
Throw Ratio | .85
Display Size | 30 in – 8.33 ft
ANSI Lumens | 500
Contrast | 4000:1
Lamp | LED
Aspect Ratio | Native: 16:10 Supported: 16:9, 4:3
Power supply | 100-240V AC 50/60 Hz
Power Consumption | 120w
Video Inputs | D-Sub, HDMI, Composite
Dimensions | 8.6 x 6.6 x 1.8 in
Weight | 2.73 lbs

## Slide 12: Projector Orientation and Overlap
The 4 projector layout with an aspect ratio of 1:1
Resolution of 2600 x 1600 for a total of over 4.5M pixels
Almost identical to the latest WQXGA format at a fraction of the cost.
Will make the most use out of the usable area of the screen.

## Slide 13: Light Sensor Array
Find a way to arrange light sensor in an array setup in front of projector screen
Must be easily stable, lightweight, and easily portable
Wires must not be obstructed so communication with projector box can happen
Solution: use a PVC pipe structures as array to house light sensors

## Slide 14: ANSI Lumens Test
Describes the standard method for testing the brightness of projectors.
Method involves measuring brightness of a projector screen at 9 specific points using light sensors and finding average value between these points.

## Slide 15: ANSI Lumens Test

## Slide 16: Light Sensor Array

## Slide 17: Analog Light Sensor
Used to get measurements from the projector array.
Readings will be read by microcontroller and displayed on a GUI on the host computer

## Slide 18: Light Sensor Specifications
PCB form factor no greater than 1in^2
Low power consumption (less than .5 mW)
Max input voltage @ 5V (provided by microcontroller)
Analog output less than 5V
Range of illuminance between 0 and 100k lx
Maximum photosensitivity @ 550nm to mimic human eye

## Slide 19: SFH 5711 by Osram
Opto hybrid (photodiode with an integrated circuit)
Mimics the human eye almost exactly
Very low power consumption
Logarithmic current output (High accuracy over wide illumination range)
Surface mount

## Slide 20: SFH 5711 Specifications
Parameter | Symbol | Value |  |  | Unit
 |  | Minimum | Typical | Maximum | 
Supply Voltage | VCC | 2.5 |  | 5.5 | V
Illuminance TA= -30oC to 70oC TA= -40oC to 100oC | EV |  | 3 to 80k |  | lx
 |  |  | 10 to 80k |  | 
Spectral Range Sensitivity | λ10% | 475 |  | 650 | nm
Wavelength of Max Photosensitivity | λs max | 540 | 555 | 570 | nm
Output Current @ EV= 1000 lx | Iout | 27 |  | 32 | μA
Current Consumption VCC= 2.5 V VCC= 5.0 V @ EV= 0 lx | ICC |  | 410 | 500 | μA
 |  |  | 420 |  | 
Current Consumption VCC= 2.5 V VCC= 5.0 V @ EV= 1000 lx | ICC |  | 460 | 550 | μA
 |  |  | 470 |  | 

## Slide 21: SFH 5711 vs. Human eye

## Slide 22: SFH 5711 vs. Human eye cont.

## Slide 23: Light Sensor Circuit Diagrams
Illuminance: 0 - 100k lx
Output voltage: 0 – 4.8V

## Slide 24: Maximum detectable light level

## Slide 25: Projector Box Control System
Microcontroller system
Low power
Must accept RS-232 data from host computer
Must accept TTL data from the light sensor array
Digital outputs for control of various other parts

## Slide 26: Program Flow Chart

## Slide 27: Schematic
Atmega 328 microcontroller
MAX232 chip for TTL to RS-232 signal conversion
Two 2 to 1 Multiplexors to route Serial data to either the light sensor or the host computer system

## Slide 28: Full Schematic Used for PCB

## Slide 29: Light Sensor Array Control System
Must accept TTL data from projector box
Must accept Analog signals from light sensor array

## Slide 30: Program Flow Chart

## Slide 31: Schematic
Atmega 328 Microcontroller
16 to 1 Multiplexor to switch between analog outputs
Low pass filter for filtration of light sensor signals

## Slide 32: Full Schematic Used for PCB

## Slide 33: Human Interface Specifications
Easy to use user interface
Ability to send data up to 50 feet
Independent interface for the light sensor array
Low power consumption
Cross-platform

## Slide 34: GUI

## Slide 35: Power System
Requirements:
  Capable of powering following devices
    4 Pico Projectors (120 VAC)
    2 Microcontrollers (3.3 – 5 VDC)
    16:1 Multiplexer
    2:1 Multiplexer
    1:2 De-multiplexer
    MAX232 Chip
  Power system should be capable of providing power to all these components from a single point or “power box” and only receiving the standard main power signal from a traditional wall outlet

## Slide 36: Power System
Specifications
  Input: Should be able to take incoming power signal from any outlet (100-240 VAC 50/60 Hz)
  Output: Independent from incoming signal, will output regulated 3.3 – 5 VDC signal to microcontrollers and 5 VDC signal to remaining circuit components
  Size: will be housed within the projector box enclosure

## Slide 37: Power System
Design Options:
  4 options considered that all met our power system design requirements.
Design | Efficiency | Design Difficulty | Cost | Electronic Noise
Linear Power Supply | ~ 58 – 70% | Moderate | ~ $20-30 | Low
Switched Mode Power Supply | ~ 79 – 90% | High | ~ $60-75 | High
Step Down DC to DC Converter | ~ 70 – 78% | Moderate | ~ $35 | Low
AC to DC Converter | ~ 74 – 85% | Low | ~ $15-30 | Low

## Slide 38: Power System
Power Flow Diagram

## Slide 39: Power System
DPP25-5 AC to DC Converter:
  Input: 85-264 VAC
  Output: 5 VDC
  Current: 5 A
  Power: 25 W
  Type: Switching (Closed Frame)
  Efficiency: 78%
  DIN Rail
  Load Regulation: ± 0.5%

## Slide 40: Projector Box
Must house all four projectors in a level and aligned configuration
Must house the power supply and terminal block for power distribution
Must house the PCB
Must take AC Power in from a standard wall outlet
Must take 4 DVI cables from Host computer to projectors
Must take 2 DB9 serial connections

## Slide 41: Projector Box Dimensions (Front)

## Slide 42: Projector Box Dimensions (Side)

## Slide 43: Projector Box Dimensions (Back)

## Slide 44: Projector Box Model and Exploded View

## Slide 45: Image Correction
Warping, edge blending and color correcting is handled with a software solution called Warpalizer.
Depends on Windows Aeroglass and the AMD Driver Suite

## Slide 46: Edge Blending
Technique used to create a single seamless image between two or more projectors.
Slowly fades the light intensity approaching the edge of a single projector channel
Eliminates “Hot Spots”

## Slide 47: Unwarped Image Warped Image

## Slide 48: Distribution of Work
 | Programming | Control System Schematics | Sensor Array Mechanics | Sensor Array Schematics | Power | Projector Array
Nick | 85% | 40% | 10% | 10% | 5% | 25%
Chris | 5% | 10% | 10% | 70% | 5% | 25%
Ryan | 5% | 40% | 10% | 10% | 85% | 25%
Gilbert | 5% | 10% | 70% | 10% | 5% | 25%

## Slide 49: Budget
Part | Price per Unit | Quantity | Total
Projectors | $549 | 4 | $2169
Host Computer | $1399 | 1 | $1399
Graphics Card | $550 | 1 | $550
Warping Software | $191.95 (per channel) | 4 | $767.80
PCB parts | $450 | 1 | $450
Box PCB | $44.50 | 2 | $89
Sensor Array PCB | $36 | 2 | $72
Sensor PCB | $15 | 10 | $150
TOTAL |  |  | $5646.80

## Slide 50: Problems Encountered
Ground wires for serial communications
Projector placement within projector box
Failure of internal clock of Microcontroller for serial communications
Warpalizer incompatibility with AMD driver update
Initial size of projector box
Projector overlap “dead zone”

## Slide 51: Project Conclusion
A Small Projector Array System is a feasible concept. It provides similar image quality to full scale projectors at a fraction of the cost. The only downside being a lack of brightness in the current market. While being feasible, the idea of a Small Projector Array System must wait until the market advances the brightness of Pico Projectors.