## Slide 1: Surveillance Bot
Group 9
Charlie Grubbs
Daniel Lanzone
Mike Roosa
Ryan Tochtermann

## Slide 2: Overview
Goals
Motivation
To create a scalable all-terrain remote surveillance system with stabilization platform
Audio detection capable of monitoring stereo sound levels
Real-time video link
Intuitive user-interface
Robotics
Systems Integration
Scalability

## Slide 3: Objectives
Vehicle can operate at a minimum of 4 MPH for at least 30 minutes
Camera stabilization platform capable of correction at a rate of 50 Hz
  Pitch and roll correction of 45 deg. and a minimum of 60 deg/s correction rate
Stereo audio detection up to 10kHz
Wireless communication of at least 100 yards outdoors

## Slide 5: Vehicle Chassis Overview
Capable of moving over semi-rugged terrain (unlevel, rocky, grassy)
Capable of overcoming ramped obstacles (< 35˚)
Moderate suspension for Z-axis stabilization
4 mph
Low profile for stability

## Slide 6: Vehicle Chassis : Suspension
Two passive shock absorbers on each front wheel
One passive shock absorber for rear axis

## Slide 7: Vehicle Chassis: Motors
Steering Motor
50 RPM
12 VDC rating
High torque gear box
Built-in potentiometer for position sensing
Drive Motor
2500 RPM No Load
12 VDC rating
Direct drive

## Slide 8: Vehicle Chassis: Motor Controller
Two bidirectional motor ports
Driver: L298 Dual H-Bridge IC
Control: 3 digital pins per motor: 1 for enable, and 2 for motor direction
6- 35 VDC Regulation
Up to 2A Output

## Slide 9: Stabilization Platform

## Slide 10: Stabilization Requirements
Pitch and Roll Correction rate of 50 Hz
10 W peak power consumption (pitch and roll servos)

## Slide 11: Inertial Measurement Unit (IMU)
Sensitivity ±250, ±500, ±1000, and ±2000dps
Small form-factor (4x4x0.9mm QFN)
Low power consumption
Low drift
Part Number | Axes | Type | Size | Price
ITG-3200 | 3 | Gyroscope | Small | $24.95
ITG-3200 BO | 3 | Gyroscope | Large | $49.95
MPU-6050 | 3 | Accelerometer/Gyroscope | Large | $39.95
9DOF Razor | 3 | Accelerometer/Gyroscope/ Magnetometer | Large | $124.95
IDG1215 | 2 | Gyroscope | Small | $24.50

## Slide 12: Stabilization
Uses accelerometer and gyroscope
Kalman filter
  Accelerometer data is good for long time periods
  Gyroscope is good for short time periods

## Slide 14: Microcontroller Decision
Model | Input Voltage | I/O Pins | Frequency | CPU | Flash
ATmega2560 | 1.8-5.5V | 86 | 16MHz (Max) | 8-bits | 256KB
ATmega16U2 | 2.7-5.5V | 22 | 16MHZ (Max) | 8-bits | 16KB
ATmega328 | 1.8-5.5V | 23 | 20MHZ (Max) | 8-bits | 32KB

## Slide 16: Stabilization Software
ATmega328 – C/C++ libraries
Microcontroller will be used to implement software
  Reading of IMU sensor via I2C bus
  Kalman filter
  Controlling servos

## Slide 18: Hitec HS-5485 Servo motors
Controls:
  Pitch
  Roll
3.3 V to 6 V
60 deg in .18 seconds (no load)
Mass: 59.82g
Dimensions: 40.39mm x 19.56mm x 37.59mm
180 degree resolution

## Slide 19: Wireless camera
Camera requirements
Cisco-Linksys Wireless-N
320x240 resolution
IP camera
15 FPS
640x480 max resolution
MJPEG stream
Microphone
30 FPS
5V Barrel-jack input

## Slide 20: Camera Testing
Camera tested at a peak bandwidth 1.2 Mbps with highest image quality setting and 30 FPS
Configured as an Ad-hoc network, the latency was reduced significantly

## Slide 21: Audio Detection System

## Slide 22: Overview
Detects close-range audible events that occur outside the camera’s field of view
Audio detection from 70 Hz – 12,000 Hz
Stereo detection
  Two microphones mounted to chassis, facing east and west
One stage signal amplification chain
DSP on ATmega328
Wireless communication via Xbee
User alerted via the GUI

## Slide 23: Microphone Specs
Audio Technica dynamic instrument microphone
Generates peak of ~5mV
Modifications

## Slide 24: Analog Onboard Audio Signal Processing
Microphone connection to PCB
Amplifier LM386
One gain stage
  Gain of 50

## Slide 25
Output to microcontroller

## Slide 27: GUI
Visual Design

## Slide 28: SPL Input / Output Voltage Correspondence
SPL Input (dB ) | Voltage Output (mV) | Gain Adjusted Voltage Output (V)
0 | ~ 0 | 2.27
10 | ~ 0 | 2.27
20 | ~ 0 | 2.27
30 | ~ 0 | 2.27
40 | 0.14 | 2.29
50 | 0.86 | 2.32
60 | 1.96 | 2.38
70 | 4.65 (Max Sensitivity) | 2.51
80 | 4.65 | 2.51

## Slide 29: SPL Input / Output Voltage Correspondence
SPL Input (dB)
Gain
Adj.
Voltage
(V)
Chart: 
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80
Sound | 2.27 | 2.27 | 2.27 | 2.27 | 2.29 | 2.32 | 2.38 | 2.51 | 2.51

## Slide 30: Sound Level / Notification Correspondence
Chart: 
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80
Sound | 2.27 | 2.27 | 2.27 | 2.27 | 2.29 | 2.32 | 2.38 | 2.51 | 2.51
Gain
Adj.
Voltage
(V)
SPL Input (dB)
Level 0
0V to 0.353V

## Slide 31: Sound Level / Notification Correspondence
Chart: 
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80
Sound | 2.27 | 2.27 | 2.27 | 2.27 | 2.29 | 2.32 | 2.38 | 2.51 | 2.51
Gain
Adj.
Voltage
(V)
SPL Input (dB)
Level 1
0.353V to 1.061V

## Slide 32: Sound Level / Notification Correspondence
Chart: 
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80
Sound | 2.27 | 2.27 | 2.27 | 2.27 | 2.29 | 2.32 | 2.38 | 2.51 | 2.51
Gain
Adj.
Voltage
(V)
SPL Input (dB)
Level 2
1.061V to 3.535V

## Slide 33: Sound Level / Notification Correspondence
Chart: 
| 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80
Sound | 2.27 | 2.27 | 2.27 | 2.27 | 2.29 | 2.32 | 2.38 | 2.51 | 2.51
Gain
Adj.
Voltage
(V)
SPL Input (dB)
Level 3
3.353V

## Slide 34: Microcontroller Interfacing
analogRead()
  Maps input voltages from 0 V to 5 V
  Will use full resolution of 4.8 mV (10 bit)
Software/Programming
  Loop that constantly checks input voltage from microphone
  Changes output based on notification level

## Slide 35: Communication Systems

## Slide 36: Communications System Overview
  Capable of reliable and accurate data transmission
  Relatively long range (100+ yards)
  Low power consumption
  Relatively simple setup and configuration
  Low cost

## Slide 37: Communications System Overview
The goal is to create a network between the PC and the vehicle in order to send control and sensor data between them.
It will feature a PC-side and embedded-side system, each consisting of a wireless RF module and a regulated serial interface between the module and the PC or onboard microcontroller.

## Slide 38: XBee Series 2 RF Modules
Key Features:
  3.3V @ 40mA operation
  Data rates up to 250 kb/s
  400 ft (133.33 yd) range
Pros:
  Long range
  Low power consumption
  Low cost
Cons:
  For Series 2 modules; difficult to configure for point-to-point communication
Xbee Series 2 Module – 2mW Antenna Model

## Slide 39: Embedded-Side Interfacing
Because the XBee operates at 3.3 V and the AtMega328 operates at 5 V, a voltage regulator is required for VCC input.
A level-shifting diode is also required on the Xbee’s Data In line to account for this voltage difference.
Other pins are connected to the microcontroller accordingly.

## Slide 40: Embedded-Side Development
The Arduino XBee Shield is a simple interface between wireless module and microcontroller
Takes care of all voltage regulation, I/O connections, and status LEDs
Still allows access to all other Arduino pins
Development/Testing using Arduino’s XBee Shield

## Slide 41: PC-Side Interfacing
An XBee Explorer USB will be used to connect the other XBee module to the PC.
The device uses an FT232RL USB to RS-232 serial UART to interface between the XBee and the PC.
Takes care of voltage regulation and I/O connections for easy development and testing.
RS-232 to USB connection via XBee Explorer

## Slide 42: Successes and Difficulties
Difficulties:
Getting the Series 2 XBee modules to talk quickly and reliably.
  Solution: Module is configured to broadcast mode for mesh networks by default. Must be changed to have only one destination node every time it is powered up.
Successes:
Established a reliable wireless network.
Sent and received messages between microcontroller and PC
Wireless drive control of surveillance vehicle for over 100 yards.
Sensor data acquired for over 100 yards.

## Slide 43: Control Software Overview
Embedded-Side Software
  Must receive user control data and respond accordingly
  Must relay sensor data to PC-side software
PC-Side Software
  Simple GUI for complete control and current status of surveillance vehicle
  Must receive sensor data and display it in a simple format
  Must transmit user control data quickly

## Slide 44: PC-Side Software: GUI
Features:
  Centered image of IP webcam feed
  Sound detection indicators on left and right side of image
  Vehicle drive controls
  Camera positioning controls
  Enable/disable stabilization option
Sketch of a desired GUI Layout

## Slide 45: PC-Side Software: Processing IDE
High-compatibility with Arduino platform
Simple graphical user interface design
Useful libraries:
  Controlp5 library for GUI components
  Video library for webcam stream
  Serial library for communications
Sample GUI written in Processing

## Slide 46: PC-Side Software: UML Diagram

## Slide 47: Embedded-Side Software
Will be programmed in the Arduino IDE
Will utilize the Serial library for read/write communications
Will have the following functionality:
  Read input values and send control data to the motor controller
  Write sensor data to the PC-side software to be displayed on the GUI

## Slide 48: Power System

## Slide 49: Power Overview
Device | Voltage | Current Draw | Power | Quantity
ATmega328 | 5V | 9mA | 900mW | 2
MPU-6050 | 3.3V | 3.9mA | 12.87mW | 1
Servo Motors | 5V | 1A | 15W | 3
XBee | 3.3V | 40mA | 132mW | 
Amplifiers | 5V |  |  | 4
Camera | 5V | 1A | 5W | 1
Motor Controller | 11.1V | 2A /Channel | 22.2W /Channel | 1

## Slide 50: Power Supply
Tenergy 11.1V LIPO Battery Pack
5500mAh
148 x 52 x 23 mm
333 grams

## Slide 51: 5V Voltage Regulation
≥75% Efficiency
3A output
4V to 40V input range
5-pin through-hole
LM2576

## Slide 52: 3.3V Voltage Regulation
LM109 Linear Regulator
TL2575 Buck Converter
Pros:
  Easy to use
  Small PCB footprint
  Additional components unnecessary
Cons:
  High heat generation
  Low efficiency
Pros:
  88% Efficiency
  Low heat generation
  Higher output current
Cons:
  Requires additional components
  Cost

## Slide 53: Voltage Regulation
Linear
Switching

## Slide 54: Current Sensing
ISL28006 used in conjunction with .0002Ω, 5W shunt resistor

## Slide 55: Current Sensing
ISL28006 Specs
60 uA current draw
Power supply range from 2.7V to 28V
100V/V Gain
Uni-directional

## Slide 56: Voltage Sensing
ATmega328 10-bit ADC pin
Scale input voltage to 5V

## Slide 57: Budget
Part | Qty | Projected Cost | Actual Cost
Chassis | 1 | $85.00 | $0.00
Arduino Uno Dev Board | 2 | $59.90 | $29.95
MPU-6050 | 1 | $39.95 | $39.95
XBee Explorer USB | 1 | $24.95 | $24.95
XBee Shield | 1 | $29.95 | $29.95
XBee Series 2 | 2 | $50.90 | $25.95
Motor Controller | 1 | $34.95 | $34.95
Battery /Charger | 1 | $79.94 | $79.94
PCB | 3 | $160.00 | $160.00
Bracket set | 1 | $19.00 | $19.00
HiTech 5845 servos | 3 | $137.85 | $0.00
Voltage regulators | 2 | $10.00 | $10.00
Current sensors | 2 | $6.00 | $0.00
Audio components | 1 | $50.0 | $50.00
Microphone | 2 | $16.00 | $16.00
Cisco IP Camera | 1 | $100.00 | $100.00
TOTAL |  | $904.39 | 675.54

## Slide 58
Chart: Progress
| Power | Chassis | Motor Control | Wireless | Audio | Stabilization | Software
Completed | 0.7 | 1 | 0.7 | 0.9 | 0.5 | 0.2 | 0.4

## Slide 59: Questions?