## Slide 1: Group 18: Disaster Zone Emergency Response Vehicle
Marcial (T.J.) Rosario, EE
Michael Lopez, CpE
Robert Smith, EE

## Slide 2: Motivation
Keeping search and rescue crew members safe.
Exploring the field of robotics.
Gaining insight into real-world engineering design, prototyping, and testing processes.

## Slide 3: Goals
To create a low-power, low-cost, easy-to-use mobile module to allow search and rescue crews to safely carry out their duties without unnecessarily putting themselves in danger.
Creating a simple graphical user interface which will allow them to do so.

## Slide 4: Specifications
Max wireless range of 275 ft.
Power Consumption of < 10 W
Final weight of < 10 lbs.
Operational battery life of at least 30 min.
All sensors accurate to within 10%

## Slide 5: Hardware Block Diagram

## Slide 6: Chassis

## Slide 7: Chassis Modifications
Wheels, motors and base of car will remain stock
Yellow covering will be removed and replaced with a raised platform to allow for more area for components
Batteries will be stored below this platform on plastic base in order to save space and account for heat from batteries

## Slide 8: Wireless Communication

## Slide 9: XBee Wireless Starter Kit
Includes 2 Xbee 1 mW communication modules
XBee Explorer USB
XBee Explorer Regulated
Mini USB cable
$79.99

## Slide 10: Wireless Flowchart

## Slide 11: Motor Controller

## Slide 12: Pololu Qik Dual Serial Motor Controller (qik 2s9v1)
Controls 2 DC brush motors
4.5-13.5 V motor supply range
2.7-5.5 V logic supply
Automatic baud rate detection (up to 38400 bps)
Supports daisy-chaining the qik to other qiks and Pololu serial motor and servo controllers with 1 serial line

## Slide 13: Motor Controller Pin Layout
Regulated 5 V will be connected to Vcc
Rx and Tx pins will be routed to our XBee module
Motors will be connected to M0 and M1
12 V supply will be connected to the VMOT pin

## Slide 14: Sensors

## Slide 15: Rangefinder
Efficiently navigate through search and rescue path
Detect and avoid obstacles which could impede the vehicle’s movement or damage it.
Detect possible injured life forms unable to communicate

## Slide 16: Ultrasonic or Infrared?
Ultrasonic Range Finder
Accurate distance
Can be used indoors or out
Sound absorbing materials affect accuracy
Can be costly >$25
Infrared Range Finder
Inexpensive <$20
Not as accurate
Cannot be used in the sun
Narrow beam width

## Slide 17: Obstacle Detection
Maxbotix LV-MaxSonar-EZ1 mounted on front of vehicle
2.5V – 5.5V supply with typical 2mA draw
Pulse Width output detection range of 6” – 254”
Beam width of about 45°

## Slide 18: Maxbotix LV-MaxSonar-EZ1
We will utilize three pins
  +5 (Vcc)
  GND
  PW (Output)
Pulse Width Output
  Will output a PW representation of the range
  Detection Formula: calcInches = PW/Vi
    calcInches: measure distance in inches
    PW: pulse width output
    Vi : Volts/inch; scaling factor of 147 μS/inch

## Slide 19: Atmospheric Pressure Detection

## Slide 20: Atmospheric Pressure Detection
Detect sudden changes in altitude
Detect dangerous explosive atmospheres
Detect changes in weather

## Slide 21: Pressure Sensor Selection
Part Number | MPL115A1 | BMP085
Brand | Freescale | Bosch
Operating Voltage | 2.375V – 5.5V | 1.8V – 3.6V
Power | 10 μA @ 1 sample/sec. | 5 μA @ 1 sample/sec.
Interface | SPI | I2C
Accuracy | ±1 kPa | ±0.1 kPa
Range | 50 – 115 kPa | 30 – 110 kPa
Price | $24.95 | $19.95

## Slide 22: Atmospheric Pressure Detection
Freescale MPL115A1 Miniature SPI Digital Barometer
50 kPa – 115 kPa absolute pressure
Integrated ADC
SPI interface

## Slide 23: MPL115A1 Pressure Sensor
We will utilize all the pins on the chip
  VDD, GND, SHDN, SCLK, DIN, DOUT, CS
Formula: Pcomp = a0 + (b1+c12*Tadc) * Padc + b2 * Tadc
  Padc: 10b pressure ADC output
  Tadc: 10b temp. ADC output
  a0: pressure offset coefficient
  b1: pressure sensitivity coefficient
  b2: temp. coefficient of offset
  c12: temp. coefficient of sensitivity
  Pressure(kPa) = Pcomp * [115 - 50/1023] + 50

## Slide 24: Temperature and Humidity Sensor

## Slide 25: Temperature and Humidity Sensor
Gain a better sense of surrounding environment
Be able to detect extreme heat or cold
  Can injure both survivors and vehicle
Detect levels of humidity
  Gather level of comfort of area

## Slide 26: Sensor Selection
Part Number | SHT15 | HTM1735LF | SHT10
Brand | Sensiron | Measurement Specialties | Sensiron
Operating Voltage | 2.4V-5.5V | 2.5V – 7V | 2.4V – 5.5V
Power | 150 μW | 20 mW | 90 μw
Interface | I2C | Analog Output | I2C
Accuracy | ±2% RH ±0.3 C | ±3% RH ±3% C | ±3% RH ±0.4 C
Range | 0 – 100% RH -40 – 123.8 C | 0 – 100% RH -30 – 80 C | 0 – 100% RH -40 – 125 C
Price | $28.95 | $14.95 | $15.00

## Slide 27: Temperature and Humidity Sensor
Measurement Specialties HTM1735LF Temperature and Relative Humidity Module
Direct interface with μC with humidity linear V and direct NTC output
Typical 1 – 3.6V output for 0 – 100% RH
Temp. measurement through NTC 10kΩ ±3% direct output

## Slide 28: HTM1735LF Sensor
We will utilize all 4 pins on board
  NTC (Temp.), GND, VCC, Vout (Hum.)
Humidity Formula:
Vout = 25.68RH + 1079
  RH = 0.03892Vout – 41.98
Temperature Formula:
  RT = RN * eβ[1/T – 1/Tn ]
  RT: NTC resistance (Ω) at temp. T (K)
  RN: NTC resistance (Ω) at temp. T (K)
  T, TN: Temperature (K)
  β: Material specific constant of NTC

## Slide 29: Vehicle Vision

## Slide 30: Vehicle Vision
Necessary to navigate over various types of terrain
Help operator detect obstacles the obstacle detection system might miss
Help operator locate victims or survivors in need of aid

## Slide 31: Linksys WVC54GC Wireless-G
Integrated web server; view from browsers via PC/phone
Simple to set up
320x240 pixel resolution
5V power barrel jack does not require outlet

## Slide 32: Live Video Stream
In order to lead effective mission, video stream must be live
Processing Sketchbook will be software of choice
IPCapture libraries to capture feed
Will be integrated with operator GUI

## Slide 33: Vehicle Illumination

## Slide 34: Vehicle Illumination
Robot must be able to navigate under lowlight conditions
Be able to view camera feed at all times
Search for survivors in all conditions

## Slide 35: Vehicle Illumination
LED Bar
Pre-Packaged, ready to go
Inexpensive
Simple to interface
Will drain power from our battery (30mA @ 12V)
Needs some kind of control to know when to run
Dark-Detecting Circuit
Inexpensive, Simple
Will not drain power from main battery
Automatically turns on in dark lighting situations
Needs a separate power source

## Slide 36: Dark-Detecting Circuit
Simple and automatic circuit utilizing a phototransistor
NPNs to drive the LEDs
Will utilize separate AA batteries
Only draws about 35mA

## Slide 37: Microcontroller

## Slide 38: Microcontroller
Part | ATmega1280 | ATmega328 | PIC16F886
Flash Memory | 128 KB | 32 KB | 14 KB
Pin Count | 100 | 32 | 28
CPU | 8-bit AVR | 8-bit AVR | 5 MIPS
Frequency | 16 MHz | 20 MHz | 8 MHz
EEPROM | 4096 B | 1024 B | 256 B
ADC | 16 ch, 10-bit | 8 ch, 10-bit | 11 ch, 10-bit
Price | Chip: Sampled Dev Board: $28.00 | Chip: Sampled Dev Board: $29.95 | Chip: Sampled Dev Board: $28.95

## Slide 39: ATmega328
Atmel ATmega328 offers enough computational power for out application
Tied to sensors and TX/RX module for data communication
32 total pins, with 23 I/O pins
Programmed with Arduino IDE/Bootloader

## Slide 40: Arduino Uno
For testing purposes, we will use Uno Dev. Board
14 digital I/O pins (6 PWM), 6 analog input pins
SPI communication
Serial RX and TX pins for TTL serial data
Abundance of code examples, libraries

## Slide 41: ATmega328 Schematic

## Slide 42: Software

## Slide 43: Software Overview
Operator Software
Operator Control
Operator Interface
Sensor Data Receive
Live Camera Feed
Vehicle Software
System Initialization
Sensor Polling/Reading
Sensor Data Transmit
Navigation/Motor Control

## Slide 44: Operator Software

## Slide 45: Operator Software
Written using Processing and Arduino
Displays camera feed and sensor data
Allows for on-screen control of vehicle

## Slide 46: Vehicle Software
Must handle all sensor polling and incoming sensor readings
Must handle live camera feed
Must be capable of controlling rear drive and front steering motors
Must communicate with XBee modules to send/receive data

## Slide 47: System Class Diagram

## Slide 48: Power Supplies

## Slide 49: Power Supply
Will be used to power electronics
Needs to be powerful enough to run electronics for at least 30 minutes
Must be relatively compact in order to save space on chassis
Minimal memory effect
Low cost is crucial

## Slide 50: What kind of battery suits us best?
 | NiMH | NiCd
Brand | Tenergy | Battery Space Custom
Voltage Provided | 12 V | 12 V
Current Rating | 2000 mAh | 1000 mAh
Dimensions | 50 mm (W) x 29 mm (H) x 72 mm (L) | 51 mm (W) x 32 mm (H) x 76.2 mm (L)
Memory Effect | Very Little (Provides 3000 cycles before deterioration) | Very Little (Amount of cycles not specified)
Cost | $21.99 | $21.99

## Slide 51: Battery Charger

## Slide 52: Charger Details
Charges both NiCd and NiMH batteries
7.2 – 12 V Selector Switch
Light indicator when charging
Charges our battery in less than 2 hours
Costs $10.05

## Slide 53: Voltage Regulation
Due to using a supply with more voltage than our parts are rated for, it is necessary to regulate our supply’s voltage.
Two options: linear regulators and switching regulators

## Slide 54: Voltage Regulation
Due to using a supply with more voltage than our parts are rated for, it is necessary to regulate our supply’s voltage.
Two options: linear regulators and switching regulators

## Slide 55: Linear vs. Switching Regulators
Linear Regulators
Easy to use
Available in popular three-terminal T0-220 package as seen in the 78xx and 79xx family of regulators, or as a surface mount part.
Very inefficient, 15%-40% in some cases.
Switching Regulators
Easy to implement, circuit becomes slightly more complex
Available in 5-terminal TO-220 package, as well as a surface mount part.
Highly efficient, some as high as 90%

## Slide 56
Need to regulate down to 5 V from 12V power supply.
Due to the need for such heavy regulation, a switching regulator would better suit our needs in terms of efficiency and power losses due to heat.

## Slide 57: LM2576
Previous experience
Simple setup.
77% efficiency for 5V model, 75% for 3.3V model.
Free samples readily available from Texas Instruments
Sampled both through-hole and surface-mount parts.

## Slide 59: Power Consumption
Component |  | Max Current | Input Voltage | Power
Camera (WVC54GC) |  | 1 A | 5 V | 5 W
Range Finder (LV-EZ1) |  | 2 mA | 5 V | 10 mW
Pressure Sensor (MPL115A1) |  | 10 μA | 5 V | 50 μW
Temp/Humidity Sensor (HTM1735LF) |  | 4 mA | 5 V | 20 mW
Dark Detecting Circuit |  | 35 mA | 5 V | 0.175 W
Microcontroller |  | 0.5 mA | 5 V | 2.5 mW
XBee |  | 50 mA | 3.3 V | 0.165 W
Total |  |  |  | 5.395 W

## Slide 60: Project Milestones
Chart: 
| Research | Design | Material | Prototype | Integrate | Test
Percent Complete | 90 | 85 | 95 | 70 | 30 | 15
Percent Remaining | 10 | 15 | 5 | 30 | 70 | 85

## Slide 61: Division of Labor
Chart: 
| Testing | Base Computer Software | Wireless Control | Chassis | PCB | Circuit Design | Power | Camera | Microcontroller | Sensors
Michael | 33 | 60 | 40 | 20 | 20 | 20 | 20 | 33 | 33 | 40
Marcial | 33 | 20 | 30 | 20 | 40 | 60 | 20 | 33 | 33 | 35
Robert | 33 | 20 | 30 | 60 | 40 | 20 | 60 | 33 | 33 | 25

## Slide 62: Finances

## Slide 63: Possible Problems / Concerns
Issuing commands to the vehicle while transmitting/receiving data from the sensors.
Incorporating all data into our GUI
Temperature Sensor Issues
Motor control issues

## Slide 64
QUESTIONS?