## Slide 1: M.A.S.S. (Mobile Aerial Security System)
Group 6
Derrick Shrock
Henry Chan
Eric Hernandez
Sanjay Yerra

## Slide 2: Motivation
Experience with Aviation work
Extra protection at public events
Doubles as an advertising system

## Slide 3: Goals and Objectives
Personal Surveillance System
Autonomous Blimp System
  Basic aviation functions
Camera System
  Stabilization System
  Video Recognition
GPS
  Enter waypoints into system
  Record Flight Path
Long Range Control

## Slide 4: Components of Blimp Design
7 Feet
3.5 Feet

## Slide 6: Blimp Design Structure

## Slide 7: Section Design
Typical non-rigid ellipses design
The envelope is made up of six different sections
Each section follows the overall profile measurements
Using the arc length and the radius of the envelope profile each section was measured out accordingly

## Slide 8: Joining the Sections
There are good and bad ways to join the sections
Sections will were joined with a tool using the same profile as the envelope
Overlapping Technique
Webbing Technique

## Slide 9: Gondola
The Gondola houses the controls system (includes: microcontroller, GPS, IMU, etc.)
Material: Balsa Wood; lightweight and inexpensive
The rear view of the gondola shows the camera wireless system attached as well as the camera system fused to the bottom side.
Side View

## Slide 10: Motor Mount
The motor mount houses the servo gear used for pitch control, the gears to drive the pitch axel with the motors attached at either end, and is made of light-weight Balsa wood.

## Slide 11: Weight Considerations
One cubic foot of helium will lift about 28.2 grams
Our Blimp size: ~70 - 90 cubic feet
Projected Lift: ~ 1,900- 2,500 grams

## Slide 12: Blimp Motors and Servos

## Slide 14: Pitch Axel Servo Motor (S3004)
Control System: +Pulse Width Control
360 Modifiable: Yes
Required Pulse: 3-5 Volt Peak to Peak Square Wave
Operating Voltage: 4.8-6.0 Volts
Operating Speed (4.8V): 0.23sec/60 degrees at no load
Stall Torque (4.8V): 44 oz/in. (3.2kg.cm)
Current Drain (4.8V): 7.2mA/idle
Weight: 1.3oz. (37.2g)
mm
mm
mm
mm

## Slide 15: Brushless Outrunner 2217-4 Motor
Battery Requirement:
  2 – 3 Cell Li-Poly
  6 – 10 Cell NiCd/NiMH
Kv: 950 RPM/V
Max Efficiency: 80%
Max Efficiency Current: 5 - 15A (>75%)
No Load Current: 0.9A @10V
Max Current: 18A for 60S
Max Watts: 200W
Weight: 73.4 g / 2.59 oz
Size: 27.8 mm x 34 mm
Shaft Diameter: 4mm
Running at lower speed: 2-3 MPH
Propeller
Model: LP 06040E
Dimensions: 6 x 4 inches / 15cm x 10cm
Material: Plastic

## Slide 16: BP 30 AMP Brushless Electronic Speed Controller (ESC)
Max Continuous Current: 30A on 3 Cells
Input Voltage: 2-3 Lithium Polymer
4-10 NiCD/NiMH
Resistance: 0.0050 ohm
Lithium Cut-Off Voltage: 3.0V / cell
Size: 45 x 24 x 9mm
Temperature Protection: 110C
PWM: 8kHz
  Needs “Arming Sequence” before controlling to set propeller position and then the motors start spinning.
Max Rotation Speed: 40,000 RPM for 14 pole motor

## Slide 17: Blimp Control System

## Slide 19: Microprocessor on the Blimp
AVR Atmega328 microprocessor (ATMEGA328-PwB)
  Up to 20 MIPS Throughput at 20MHz
  Low power settings
  SPI, I2C, and UART serial communication ports
  Six PWM Channels
  23 Programmable I/O Pins
  5 Volts operating voltage
  DIP packaging
Cost: $5.21

## Slide 20: Sensors (IMU) Comparison
Design | Own IMU | AVR IMU
Cost | 14.60 | 24.99
Accelerometer G Values | 2,4,6,8 | 2,4,6,8
DOF | 9 | 9
Advantages | Parts are already in. Familiar with parts. | All parts are on same board. Noise Regulators included.
Disadvantages | Would have to buy separate breakout boards for programming. Several comments complained about sensor flaws due to noise. | Spend more money. Have to wait for parts.

## Slide 21: Inertial Measurement Unit-ATAVRSBIN2
IMU 3000 Gyroscope
  X,Y,Z axis
  I2C Serial Output
  ±250, ±500, ±1000, and ±2000 degrees/sec
  1MHz clock output to synchronize with digital 3-axis accelerometer
KXTF9 Accelerometer
  ±2g, ±4g or ±8g
  I2C interface
HMC5883L Magnetometer
  s 1° to 2° compass heading accuracy
  I2C interface
  Wide Magnetic Field Range (+/-8 Oe)
14 mm
58 mm

## Slide 22: Logic Level Converter
Due to using an ATMEL sensor board with an Arduino development board modifications had to be made
The Arduino Uno board runs at 5.0 volts while the IMU runs at 3.3 volts.
This logic level converter correctly adjusts the voltages
.6”
.5”

## Slide 23: Transmission Comparison
 | Frequency | Antenna | Weight | Power Consumption | Max Range | Data Rate | Price
nRF24L01+ | 2.4Ghz | External SMA | 4.3 grams (no Antenna) | 11.3mA TX Mode 13.3mA RX Mode | 1000 meters | 250kbps, 1Mbps or 2Mbps | $19.84
XBee 60 mW PRO | 2.4Ghz | On-Chip | 5.7 grams | 3.3V @ 250mA | 1500 Meters | 250kbps Max data rate with 128-bit encryption | $ 37.95

## Slide 24: Transmitter/Receiver Module (XBEE PRO)
2.4 GHz ISM Band
250 kbps Max Data Rate
6o mW output Power
UART serial communication
Weight: 39g
Cost: $37.95

## Slide 25: GPS MODULE- LOCOSYS LS20031
66 Channel
10 Hz update rate
Built in micro battery to
preserve system data
Precision: ~2-3 m
Cost: $59.95
3.3V @ 41 mA
15X15(mm)

## Slide 26: NMEA Codes
NMEA Codes will use
  GGA
    Longitude
    Latitude
    Altitude
  GSA (confirmation of satellite connections)
    A,2 – Only Longitude and Latitude Confirmation
    A,3 – Longitude, Latitude, Altitude Confirmation
Name | Example Data | Description
Sentence Identifier | $GPGGA | Global Positioning System Fix Data
Time | 170834 | 17:08:34 Z
Latitude | 4124.8963, N | 41d 24.8963' N or 41d 24' 54" N
Longitude | 08151.6838, W | 81d 51.6838' W or 81d 51' 41" W
Fix Quality: - 0 = Invalid - 1 = GPS fix - 2 = DGPS fix | 1 | Data is from a GPS fix
Number of Satellites | 05 | 5 Satellites are in view
Horizontal Dilution of Precision (HDOP) | 1.5 | Relative accuracy of horizontal position
Altitude | 280.2, M | 280.2 meters above mean sea level
Height of geoid above WGS84 ellipsoid | -34.0, M | -34.0 meters
Time since last DGPS update | blank | No last update
DGPS reference station id | blank | No station id
Checksum | *75 | Used by program to check for transmission errors
Example:
  $GPGSA,A,3,,,,,,16,18,,22,24,,,3.6,2.1,2.2*3C
,A,3

## Slide 27: Camera System

## Slide 29: Camera Qualifications
Lightweight
Crisp Picture and High Resolution
Inexpensive
Limited Video Feed Delay

## Slide 30: Camera Comparison
Camera | GoPro Hero 3 Black Edition | SC2000 Sony CCD Video Camera
Weight | 204g | 35g
Price | $240 | $32.76
Resolution | 1080p | 540TV
Wifi Compatible | Yes | No
Power Supply | Battery included | 12V with 150 mA current draw
Flight Time | 90 minutes | Completely dependent on size of external battery
Delay for Stream of Video | 3 seconds | Delay of Transceiver <1s
Selected |  | This one!!! (It is all about the money)

## Slide 31: SC2000 Sony CCD Video Camera
Pixels 752 X 582
Internal Synchronization
Horizontal Resolution is 540 TV Lines
Lens is 3.6 mm
Power Supply: 12V/150 mA
Net weight 14 grams

## Slide 32: Camera Feed Transmitter/Receiver
Video Camera will have a 5.8 GHz AV Transceiver
Choose 5.8 GHz in order to not cross signals with 2.4 GHz Transceiver
200m range
Power Regulation:
  5 Volt, 1A
Uses RCA adapter from Camera
3” x 4” x 1”

## Slide 33: Camera Mount
Lightweight 19g
This particular mount was made for our specific camera
Gives complete 180 degree pan & full tilt
Uses two 9.5g (Torque rating) servos

## Slide 34: Servo Motor Turnigy TG9e
Dimension: 23x12.2x29mm
Torque: 1.5kg/cm (4.8V)
Operating speed:
0.10sec/60 degree
Operating voltage: 4.8V

## Slide 35: LiPo 2200mAh 3s Battery
Minimum Capacity: 2200mAh
11.1v
3cell
Constant Discharge: 25C
Peak Discharge (10sec): 35C
Pack Weight: 188g
Pack Size: 105 x 33 x 24mm

## Slide 36: Blimp Functionality & Microcontroller Program

## Slide 37: Blimp Control Flowchart

## Slide 38: Camera System Program

## Slide 39: Camera System Explained
Camera system has two modes
  User control
    The user can control at which view to see from the camera
    Controlled by the Graphic User Interface
  Auto control
    The blimp will stabilize the camera through 2 servo motors which get data from the IMU
    Auto-corrects for turbulence be it wind or debris

## Slide 40: Camera Servo Controls
The commands sent from the computer GUI through the XBee to the Blimp
Camera11-camera up tilt
Camera22-camera down tilt
Camera33-camera left pan
Camera44-camera right pan

## Slide 41: Servo Control Commands
Servo motors will be used to turn the blimp system and the camera system
Each button press will turn the servo approximately 30 degrees.

## Slide 42: Motor controls and User interface

## Slide 43: Motor control System Explained
Motor control system has 2 modes
  User control
    The user can control how the blimp will move
    Controlled by the Graphic User Interface
  Auto control
    The blimp will read in the GPS coordinates of the starting location and fly around
    The blimp automatic flight path will determined by the Graphic User Interface

## Slide 44: Motor Control Commands
Some basic controls for the blimp
There will be 5 speeds on 2 rear motors
Speed111, speed222, speed333 and so on
The speed555 will set the limit of max speed possible
For directional control of the blimp, the speed’s of the individual motors are manipulated

## Slide 45: Blimp Ground Station

## Slide 47: Ground Station Schematic

## Slide 49: Ground Station Microcontroller (atmega328)
 | Atmega 328
Speed | 16 MHz
Package | 28-pin DIP
Program Flash Memory | 32KB
Data EEPROM | 32 kBytes
Voltage Operation Range | 1.8 to 5.5 V
Digital Communication | UART SPI I2C
Cost | $ 5.25
Software UART
Hardware UART Pins

## Slide 50: Ground Station Schematic

## Slide 51: Ground Station Schematic

## Slide 52: Ground Station USB Connector (CP2102)
UART Connection.
5 Volts
No need for external crystal for full USB speed (48Mhz).
Cheap Solution for USB Connection
  $7.50

## Slide 53: Ground Station Schematic

## Slide 54: Graphical User Interface

## Slide 55: C++ GUI On Computer
Connected to Ground Station. (2.4GHz Transmitter)
Connected to Video Decoder. (5.8GHz Transmitter)
Provides
  OpenCV Video Feed
    Person Detection (HOG Descriptor)
    Tracking and Follow (Template Matching)
  Drawing Automatic Patrol Path (OpenStreetMap)
  Display of IMU and GPS Data.

## Slide 57: OpenCV (Computer Visions) – HOG Descriptor
Full body person detection.
Large Amount of Processing Power
  Takes time for detection to converge.
Works on each frame of video.
  Limit: 15-20 frames per second

## Slide 58: OpenCV HOG Algorithm (Added Implementation)
Add Overhead View to HOG
Create custom blob for detection
Or find shirt Colors and Shape
Fix Size Limitation (Default 128x64)
Change based on Blimp Current Altitude

## Slide 59: OpenCV – Custom Blob Detection and Color Detection
Create Custom Blob and Look for it in Picture.
  High False Positive Rate
Need to Combine with Color Detection for shirt and hair.

## Slide 60: OpenCV (Computer Visions) – Template Matching
Used for Tracking and Following System.
Select Target (Person) found using HOG.
Move Camera and/or
motors so person is in
Center of View.
Blimp will be in
autonomous mode.
Template

## Slide 61
Here is Sanjay being detected from the Third floor of HEC

## Slide 62: Map Patrol Path (OpenStreetMap)
Enables the user to setup a automatic path for the Blimp to Patrol.
Set Altitude on GUI before able to Start a Patrol. (Minimum of 100 meters).
Maximum Distance Determined by Transmission Range.
Reason why we didn’t use Google Maps:
  Against Terms of Service to use in
  applications. (Can only use API in Public
  Websites)
1000 Meters Around Memory Mall
Formula for Heading (Between 2 GPS Coordinates):
θ = atan2( sin(Δλ).cos(φ2), cos(φ1).sin(φ2) − sin(φ1).cos(φ2).cos(Δλ) )

## Slide 64: Administrative Content

## Slide 65: Division of Task
Tasks | Power | Blimp Controller | Camera System | Blimp Structure | Ground Station | C++ GUI
Henry | X |  |  |  | X | X
Eric | X | X | X |  |  | 
Derrick | X |  |  | X |  | 
Sanjay |  | X | X |  |  | 

## Slide 66: Cost of Design
Predicted Project Cost: $1063.00
Actual Project Cost: $952.64

## Slide 67: Issues and Troubleshooting
Communication between Pic and Atmel
Burnt out transmitters
Logic Level Problems
Structure Design
Delay in communications
Financial Difficulties

## Slide 68
Questions???