## Slide 1
Eco-Sense
Group 7:
Neil Northcutt
Jamie Olheiser Daniel Haggerty

## Slide 2: Eco-Sense
System to automate the lawn watering process through the use of
  Climate sensors
  Ground sensors
  Weather prediction
Three subsystems
  Sensor subsystem
  Central HUB subsystem
  Solenoid subsystem

## Slide 3: Goals/Motivation
Conserve water by reducing the wasteful watering of traditional watering methods
  Hand watering
  General sprinkler system
  Timer, automated system
Promote a healthier, greener lawn

## Slide 4: Hardware Specifications
Component | Parameter | Specification
Wireless Module | Range | 20ft to 1 mile
Sensors | Voltage | 3.3 or 5 V
Microcontroller | Power consumption Storage RAM/Flash Clock Speed I/O Pins | <10mW sleeping, <50mW on 128B+, 8kB+ 8 MHz 4+ Analog, 5+ Digital
Sensor Node | Power consumption | <50mW sleeping, <300mW on
Temperature Sensor | Sensing Range | 0°F to 120°F.
Humidity Sensor | Accuracy | <± 5%
Pressure Sensor | Accuracy | <± 5 hPa (mB)

## Slide 5: Water Efficiency

## Slide 6: Water Efficiency
Primary goal of Eco-Sense
Reduce the waste of water by not watering under certain climate conditions
  Soil Moisture
  Temperature
  Humidity
Allows watering only when rain is not predicted

## Slide 7: When to Water Algorithm
Within USWT limits?
Temperature above 32˚C
Raining/Rain detected soon?
Soil Field Capacity below 75%?
Temperature above 25˚C?
Humidity below 50%?
Temperature below 5˚C?
Do Not Water
Water
Sensor Data
Yes
No
No
Yes
No
Yes
Yes
Yes
Yes
Yes
No
No
No
No
USWT: User Specified watering times.

## Slide 8: Weather Prediction
Not an exact science
Uses barometric pressure, temperature, and humidity sensors
Most weather prediction algorithms are proprietary so we had to create our own

## Slide 9: Weather Prediction - Temperature
Generally, temperature increases before the onset of rain (red lines)

## Slide 10: Weather Prediction - Humidity
Generally, relative humidity rises before the onset of rain

## Slide 11: Weather Prediction - Pressure
Generally, barometric pressure drops before the onset of rain

## Slide 12: Weather Prediction Algorithm
When Rain is above 0.4 a rain storm is predicted in the next hour
  70% rain prediction
  15% false prediction of rain
This algorithm was developed from over 200hrs of Orlando weather data
Notes: After several attempts to create an algorithm to detect the onset of rain, we eventually settled on an algorithm that assigns weighted values on the slope or change of each of the three parameters measured.

## Slide 13: Hardware

## Slide 14
Barometric Pressure Sensor
Ground Moisture Sensor
Transmitter Receiver
Micro-Controller
Power Source
Ambient Temp. Sensor
Rain Detection Sensor
Humidity Sensor
Power Source
Micro-Controller
LCD Display
User Interface
Transmitter Receiver
Solenoid
Transmitter Receiver
Micro-Controller
Power Source
Sensors S.S.
Central HUB S.S.
Solenoid S.S.

## Slide 15: Humidity Sensor
Measures the absolute humidity of the surroundings.
Used for weather prediction and when to water algorithms
Needs to be exposed to the elements for accurate readings

## Slide 16: Humidity Sensor
Part | Supply Voltage | Current | Humidity Range | Accuracy | Shutdown Current | Cost
DHT11 | 3 to 5.5 V | 0.5 to 2.5mA | 20 - 90% | ± 5% | 100μA | $5
DHT22 | 3 to 5 V | 0.5 to 2.5mA | 0 to 100% | ± 2% | 40-50μA | $15
SHT10 | 2.4 to 5.5 V | 28μA | 0 to 100% | ± 4.5% | 1 to 2μA | $20
SHT11 | 2.4 to 5.5 V | 28μA | 0 to 100% | ± 3% | 1 to 2μA | $30
SHT15 | 2.4 to 5.5 V | 28μA | 0 to 100% | ± 2% | 1 to 2μA | $35
HH10D | 2.7 to 3.3 V | 120 to 180μA | 0 to 99% | ± 3% | - | $10
HIH-4000 | 4 to 5.8 V | 200 to 500μA | 0 to 100% | ± 3.5% | - | $20
HIH-4030 | 4 to 5.8 V | 200 to 500μA | 0 to 100% | ± 3.5% | - | $18

## Slide 17: Humidity Sensor
Inexpensive breakout board
Good power usage
Reasonable sensor accuracy
HIH-4030
.75 inch
.3 inch

## Slide 18
Barometric Pressure Sensor
Ground Moisture Sensor
Transmitter Receiver
Micro-Controller
Power Source
Ambient Temp. Sensor
Rain Detection Sensor
Humidity Sensor
Power Source
Micro-Controller
LCD Display
User Interface
Transmitter Receiver
Solenoid
Transmitter Receiver
Micro-Controller
Power Source
Sensors S.S.
Central HUB S.S.
Solenoid S.S.

## Slide 19: Rain Detection Sensor
Detects the presence of rain
Used for when to water algorithm and shutting off watering if rain starts
Uses a PCB board and resistivity properties
2 Inch
3 Inch

## Slide 20
Barometric Pressure Sensor
Ground Moisture Sensor
Transmitter Receiver
Micro-Controller
Power Source
Ambient Temp. Sensor
Rain Detection Sensor
Humidity Sensor
Power Source
Micro-Controller
LCD Display
User Interface
Transmitter Receiver
Solenoid
Transmitter Receiver
Micro-Controller
Power Source
Sensors S.S.
Central HUB S.S.
Solenoid S.S.

## Slide 21: Barometric Pressure Sensor
Measures ambient pressure caused by weather patterns
Used with the weather prediction algorithm
Needs to be exposed to the elements
Part | Supply Voltage | Average Current | Pressure Range | Accuracy | Shutdown Current | Cost
BMP085 | 1.8 to 3.6 V | 3 to 12μA | 300 to 1100hPa | ±1hPa | 0.1μA | $20
MPL115A1 | 2.4 to 5.5 V | 5μA | 500 to 1150hPa | ±10hPa | 1μA | $25
HP03M | 2.2 to 3.6 V | - | 300 to 1100hPa | ±3hPa | 1μA | $30

## Slide 22: Barometric Pressure Sensor
Low current
Breakout board
Contains a thermometer used as the ambient temperature sensor needed
for the sensor system
I2C connection
BMP085
.65 inch
.65 inch

## Slide 23
Barometric Pressure Sensor
Ground Moisture Sensor
Transmitter Receiver
Micro-Controller
Power Source
Ambient Temp. Sensor
Rain Detection Sensor
Humidity Sensor
Power Source
Micro-Controller
LCD Display
User Interface
Transmitter Receiver
Solenoid
Transmitter Receiver
Micro-Controller
Power Source
Sensors S.S.
Central HUB S.S.
Solenoid S.S.

## Slide 24: Ground Moisture Sensor
Used to measure the water content in soil.
Necessary for the when to water algorithm.
General resistive method

## Slide 25
Barometric Pressure Sensor
Ground Moisture Sensor
Transmitter Receiver
Micro-Controller
Power Source
Ambient Temp. Sensor
Rain Detection Sensor
Humidity Sensor
Power Source
Micro-Controller
LCD Display
User Interface
Transmitter Receiver
Solenoid
Transmitter Receiver
Micro-Controller
Power Source
Sensors S.S.
Central HUB S.S.
Solenoid S.S.

## Slide 26: Wireless Communication
Transmission Range: > 20 feet
Low power consumption: < 100mW (on)
Concurrent transmissions without interference

## Slide 27: Wireless Communication
 | Xbee | Xbee pro | Zigbee 802.15.4 | Bluetooth 802.15.1 | WIFI b/g 802.11b/g
Battery Days |  |  | 100-1000 | 1-7 | .1-5
Power transmitting | 1mW | 63mW | 100 mW | 160 mW | 1600 mW
Current sleeping | <1uA | <1uA | .3 mA | .2 mA | 20 mA
Nodes/Network |  |  | 255/65K+ | 7 | 30
Bandwidth | 250 kbps | 250 kbps | 20-250 kbps | 720 kbps | 11-54 mbps
Range (m) | 30(indoor) 90(outdoor) | 90(indoor) 1600(outdoor) | 75+ | 10+ | 100
Key attribute | Low cost, Low power | Low power | Low power, reliable | convenience | speed

## Slide 28: Xbee
Inexpensive $17
Transmission Range: 400 ft
Data Rate: 250 kbps
Transmit Power: 1.25 to 2 mW
Voltage: 2.1 - 3.6 VDC
1.25 inch
1 inch

## Slide 29
Barometric Pressure Sensor
Ground Moisture Sensor
Transmitter Receiver
Micro-Controller
Power Source
Ambient Temp. Sensor
Rain Detection Sensor
Humidity Sensor
Power Source
Micro-Controller
LCD Display
User Interface
Transmitter Receiver
Solenoid
Transmitter Receiver
Micro-Controller
Power Source
Sensors S.S.
Central HUB S.S.
Solenoid S.S.

## Slide 30: Microcontroller
Low power consumption
Communicates with the computer via serial connection
Inexpensive
Easily programmable
I/O for all sensors

## Slide 31: Microcontrollers
Item | AT90L S8535 | Atmega 103L | PIC16F8X | MSP430 F149 | StrongARM SA-1100 | At91M 42800A | MC68HC05PV8A | 80C51RD | EM6603 | MC9328MX1 | ATMega328
Bits | 8 | 8 | 8 | 16 | 32 | 16 | 8 | 8 | 4 | 16 | 8
Flash kB | 8 | 128 | 68 | 60 |  |  |  | 64 |  |  | 32
RAM B | 512 | 4k | 1 | 2k |  | 8k | 192 | 1k | 96x4 | 128k | 2k
ADC bits | 10 | 10 |  | 12 |  | 08 |  |  |  | 13 | 2x8
Timers | 3 | 3 | 1 | 3 |  | 6 | 1 | 1 | 1 | 2 | 2+1
Operating Voltage | 4-6v | 2.7-3.6v | 2-6v | 1.8-3.6v | 3-3.6v | 2.7-3.6v | 3.3-5v | 2.7-5.5v | 1.2-3.6v | 1.62-3.3v | 1.8-5.5v
Current Active | 6.4 mA | 5.5 mA | 2 mA | .4 mA | 230 mA |  | 4.4 mA | 16 mA | 1.8 μA | 90 mA | .2 mA
Current Idle Mode | 1.9 mA | 1.6 mA |  | 1.3 μA | 50 mA |  | 1.95 mA | 4 mA | .35 μA | .16 mA | .75 μA
Powered Down Current | 1 μA | 1 μA | 1 μA | .1 μA | 25 μA |  | 485 μA | 50 μA | .1 μA |  | .1 μA

## Slide 32: ATmega 328P
Inexpensive $4
14 digital I/O pins
6 Analog I/O pins
Programmable over serial using USB to serial converter
Has I2C capability
Low power
Different power modes
1.32 inch
.28 inch

## Slide 33
Barometric Pressure Sensor
Ground Moisture Sensor
Transmitter Receiver
Micro-Controller
Power Source
Ambient Temp. Sensor
Rain Detection Sensor
Humidity Sensor
Power Source
Micro-Controller
LCD Display
User Interface
Transmitter Receiver
Solenoid
Transmitter Receiver
Micro-Controller
Power Source
Sensors S.S.
Central HUB S.S.
Solenoid S.S.

## Slide 34: LCD Module
The LCD module that fits Eco-Sense:
Low power mode
LED backlighting GDM1602K
16x2 character display
Image provided under Creative Commons (CC) by Sparkfun

## Slide 35
Barometric Pressure Sensor
Ground Moisture Sensor
Transmitter Receiver
Micro-Controller
Power Source
Ambient Temp. Sensor
Rain Detection Sensor
Humidity Sensor
Power Source
Micro-Controller
LCD Display
User Interface
Transmitter Receiver
Solenoid
Transmitter Receiver
Micro-Controller
Power Source
Sensors S.S.
Central HUB S.S.
Solenoid S.S.

## Slide 36: Power
High efficiency: > 70%
DC-DC from 7.4 volts to 3.3 volts and 5 volts
Low Cost
Rechargeable, high energy density battery

## Slide 37: Power- Battery
Specification | Ni-Cad | Ni-MH | Li-ion / Li-poly | Rechargeable Alkaline | Lead Acid
Charge/Discharge life cycles | 500-700 | 300-400 | 300-1000 | 100+ | 500-800
Memory Effect | High effect | Little effect | No effect |  | 
Operating Temperature | -22 to +140°F | -4 to +122°F | +14 to +140°F | -20º F to 130º F | -85º F to 149º F
Self-Discharge | 20% loss of charge/ month at 77°F | 30% loss of Charge/ month at 77°F | Self-discharge 3% loss of charge/ month at 77°F | (5/12)% loss per month | 
Energy density (Wh/kg) | 40-60 | 30-80 | 150-250 (Li-poly 130-200) |  | 30-40
Power W/kg | 150 | 250-1000 | 1800 (Li-poly 3000+) |  | 180

## Slide 38: Batteries
Turnigy 1000mAh Lipo Pack
2-Cell, 7.4V output
Sensor and Solenoid sub-systems contain batteries

## Slide 39: AC Adapter
AC wall adapter
4.6V Output
Central HUB uses wall adapter

## Slide 40: Regulators
Linear Regulators
Easy to use
Heat sink usually required
50% efficiency
Clean voltage
Switching Regulators
  Requires more components
  Smaller heat sink required
  80% efficiency
  Some ripple voltage on the output

## Slide 41: Switching Regulator Circuit

## Slide 42
Barometric Pressure Sensor
Ground Moisture Sensor
Transmitter Receiver
Micro-Controller
Power Source
Ambient Temp. Sensor
Rain Detection Sensor
Humidity Sensor
Power Source
Micro-Controller
LCD Display
User Interface
Transmitter Receiver
Solenoid
Transmitter Receiver
Micro-Controller
Power Source
Sensors S.S.
Central HUB S.S.
Solenoid S.S.

## Slide 43: Water Solenoid
Used to control distribution of water
GHT (Garden Hose Threaded) for US standards
Operates with minimum power

## Slide 44: Water Solenoid
AQT15SP
12V water solenoid valve
Operates on 7.4V to 12V
Non-Latching solenoid allows for fail-safe condition
CC BY-NC-SA 3.0

## Slide 45: Sub-System Circuits

## Slide 46: Sensor Subsystem Schematic

## Slide 47: Solenoid Subsystem Schematic

## Slide 48: Central HUB Schematic

## Slide 49: Central Hub Schematic - UI

## Slide 50: Subsystem Software

## Slide 51: Subsystem Software Design
2 different approaches, one for each subsystem
Each Sub-System can communicate to and from the central HUB
Minimal memory usage for code

## Slide 52: Subsystem Software Design
Sensor Subsystem
Solenoid Subsystem
Central Subsystem

## Slide 53: Sensor Software
Read Moisture
Read Temperature
Read Humidity
Convert / Compress
Transmit Data
Receive Data
Read Pressure
Read Rain Status
Memory Store
System Timer
Fetch Memory
Clear Memory
Reset Timer
Sensor Data
Collection
Data Transfer
Data Storage

## Slide 54: Subsystem Software Design
Sensor Subsystem
Solenoid Subsystem
Central Subsystem

## Slide 55: Central Software
Extract Data
Moisture Flag
Transmit Data
Receive Data
Temp Flag
Humidity Flag
Pressure Flag
Rain Flag
Sum Flags
Water Signal
Display Statistics
System Timer
Override
Store in Memory
Button Input
Data Transfer
Water Algorithm
Manual Input

## Slide 56: Subsystem Software Design
Sensor Subsystem
Solenoid Subsystem
Central Subsystem

## Slide 57: Solenoid Software
Receive Signal
Open Valve
Countdown Timer
Close Valve
Data Transfer
Solenoid Controller

## Slide 58: Software Design Overview
Sensor subsystem collects data at set intervals
Central subsystem requests data, computes water signal, transmits water signal to solenoid
Solenoid subsystem controls the operation of the valve and water distribution

## Slide 59
Barometric Pressure Sensor
Ground Moisture Sensor
Transmitter Receiver
Micro-Controller
Power Source
Ambient Temp. Sensor
Rain Detection Sensor
Humidity Sensor
Power Source
Micro-Controller
LCD Display
User Interface
Transmitter Receiver
Solenoid
Transmitter Receiver
Micro-Controller
Power Source
Sensors S.S.
Central HUB S.S.
Solenoid S.S.

## Slide 60: User Interface
The user interface (UI) allows the user to access the system in an efficient manner
Provides overriding actions for user
Provides data feedback to the user
Displays system status
Provides users with the ability to enter in allowed watering times

## Slide 61: User Interface
The UI includes the following:
LCD module
Pushbuttons
Protective box

## Slide 62: UI Model
3.5 inches
6.5 inches

## Slide 63: Work Distribution
 | Neil (EE) | Jamie (CpE) | Daniel (CpE)
Sensor Configuration | X |  | 
Sub-System’s Circuitry | X | X | X
Weather/Water Algorithms | X |  | 
Wireless Communications |  |  | X
Power System |  | X | X
Housing Assembly | X | X | X
User Interface |  | X | X
Solenoid Controller | X | X | 
PCB Design | X |  | 
PCB Assembly |  | X | X

## Slide 64: Bill of Materials

## Slide 65: Demonstration

## Slide 69
Test
Score
Did it rain?
Test
Score
Did it rain?
1
0.0%
No
21
33.0%
Yes
2
75.0%
Yes
22
4.0%
No
3
0.0%
No
23
4.0%
No
4
74.0%
Yes
24
0.0%
No
5
0.0%
No
25
38.0%
Yes
6
87.0%
Yes
26
0.0%
No
7
20.0%
No
27
30.0%
No
8
40.0%
Yes
28
0.0%
No
9
13.0%
No
29
12.0%
No
10
42.0%
Yes
30
33.0%
No
11
13.0%
No
31
30.0%
No
12
52.0%
Yes
32
4.0%
No
13
42.0%
Yes
33
30.0%
No
14
83.0%
Yes
34
61.0%
No
15
30.0%
No
35
42.0%
No
16
0.0%
No
36
30.0%
No
17
91.0%
Yes
37
48.0%
No
18
42.0%
Yes
38
30.0%
No
19
56.0%
Yes
39
12.0%
No
20
12.0%
Yes
40
30.0%
No