## Slide 1
Eco-Sense
Group 7:
Neil Northcutt
Jamie Olheiser Daniel Haggerty

## Slide 2: Eco-Sense
System to automate the lawn watering process through the use of
  Climate sensors
  Ground sensors
  Weather prediction
Three subsystems
  Sensor subsystem
  Central HUB subsystem
  Solenoid subsystem

## Slide 3: Goals/Motivation
Conserve water by reducing wasteful watering of traditional watering methods.
  Hand watering
  General sprinkler system
  Timer, automated system
Promote a healthier, greener lawn.

## Slide 4: Hardware Specifications
Component | Parameter | Specification
Wireless Module | Range | 20ft to 1 mile
Sensors | Voltage | 3.3 or 5
Microcontroller | Power consumption Storage RAM/Flash Clock Speed I/O Pins | <10mW sleeping, <50mW on 128B+, 8kB+ 8 MHz 4+ Analog, 5+ Digital
Sensor Node | Power consumption | <50mW sleeping, <300mW on
Temperature Sensor | Sensing Range | 0°F to 120°F.

## Slide 5: Water Efficiency

## Slide 6: Water Efficiency
Primary goal of Eco-Sense
Reduce the waste of water by not watering under certain climate conditions.
  Soil Moisture
  Temperature
  Humidity
Allow watering only when rain is not predicted.

## Slide 7: When to Water Algorithm
Within USWT limits?
Temperature above 32˚C
Temperature below dew point?
Soil Field Capacity below 75%?
Temperature above 25˚C?
Humidity below 50%?
Temperature below 5˚C?
Do Not Water
Water
Sensor Data
Yes
No
No
Yes
No
Yes
Yes
Yes
Yes
Yes
No
No
No
No
USWT: User Specified watering times.

## Slide 8: Weather Prediction
Not an exact science
Use of the barometric pressure, temperature, and humidity sensors.
Most weather prediction algorithms are proprietary, have to create our own.
    Not yet completed

## Slide 9: Weather Prediction - Temperature
Generally, temperature increases before the onset of rain (red lines).

## Slide 10: Weather Prediction - Humidity
Generally, relative humidity rises before the onset of rain.

## Slide 11: Weather Prediction - Pressure
Generally, barometric pressure drops before the onset of rain.

## Slide 12: Hardware

## Slide 13
Barometric Pressure Sensor
Ground Moisture Sensor
Transmitter Receiver
Micro-Controller
Power Source
Ground Temp. Sensor
Ambient Temp. Sensor
Rain Detection Sensor
Humidity Sensor
Power Source
Micro-Controller
LCD Display
User Interface
Transmitter Receiver
Solenoid
Transmitter Receiver
Micro-Controller
Power Source
Sensors S.S.
Central HUB S.S.
Solenoid S.S.

## Slide 14: Humidity Sensor
Measures the absolute humidity of the surroundings.
Used for weather prediction and when to water algorithms.
Needs to be exposed to the elements for accurate readings.

## Slide 15: Humidity Sensor
Part | Supply Voltage | Current | Humidity Range | Accuracy | Shutdown Current | Cost
DHT11 | 3 to 5.5 V | 0.5 to 2.5mA | 20 - 90% | ± 5% | 100μA | $5
DHT22 | 3 to 5 V | 0.5 to 2.5mA | 0 to 100% | ± 2% | 40-50μA | $15
SHT10 | 2.4 to 5.5 V | 28μA | 0 to 100% | ± 4.5% | 1 to 2μA | $20
SHT11 | 2.4 to 5.5 V | 28μA | 0 to 100% | ± 3% | 1 to 2μA | $30
SHT15 | 2.4 to 5.5 V | 28μA | 0 to 100% | ± 2% | 1 to 2μA | $35
HH10D | 2.7 to 3.3 V | 120 to 180μA | 0 to 99% | ± 3% | - | $10
HIH-4000 | 4 to 5.8 V | 200 to 500μA | 0 to 100% | ± 3.5% | - | $20
HIH-4030 | 4 to 5.8 V | 200 to 500μA | 0 to 100% | ± 3.5% | - | $18

## Slide 16: Humidity Sensor
Inexpensive breakout board.
Good power usage.
Reasonable sensor accuracy.
HIH-4030
.75 inch
.3 inch

## Slide 17
Barometric Pressure Sensor
Ground Moisture Sensor
Transmitter Receiver
Micro-Controller
Power Source
Ground Temp. Sensor
Ambient Temp. Sensor
Rain Detection Sensor
Humidity Sensor
Power Source
Micro-Controller
LCD Display
User Interface
Transmitter Receiver
Solenoid
Transmitter Receiver
Micro-Controller
Power Source
Sensors S.S.
Central HUB S.S.
Solenoid S.S.

## Slide 18: Rain Detection Sensor
Detects the presence of rain.
Used for when to water algorithm and shutting off watering if rain starts.
Uses a PCB board and resistivity properties.
2 Inch
3 Inch

## Slide 19: Rain Detection Sensor

## Slide 20
Barometric Pressure Sensor
Ground Moisture Sensor
Transmitter Receiver
Micro-Controller
Power Source
Ground Temp. Sensor
Ambient Temp. Sensor
Rain Detection Sensor
Humidity Sensor
Power Source
Micro-Controller
LCD Display
User Interface
Transmitter Receiver
Solenoid
Transmitter Receiver
Micro-Controller
Power Source
Sensors S.S.
Central HUB S.S.
Solenoid S.S.

## Slide 21: Barometric Pressure Sensor
Measures ambient pressure caused by weather patterns.
Used with the weather prediction algorithm
Needs to be exposed to the elements.
Part | Supply Voltage | Average Current | Pressure Range | Accuracy | Shutdown Current | Cost
BMP085 | 1.8 to 3.6 V | 3 to 12μA | 300 to 1100hPa | ±1hPa | 0.1μA | $20
MPL115A1 | 2.4 to 5.5 V | 5μA | 500 to 1150hPa | ±10hPa | 1μA | $25
HP03M | 2.2 to 3.6 V | - | 300 to 1100hPa | ±3hPa | 1μA | $30

## Slide 22: Barometric Pressure Sensor
Low current
Breakout board
Contains a thermometer used as the ambient temperature sensor needed
for the sensor system.
I2C connection
BMP085
.65 inch
.65 inch

## Slide 23
Barometric Pressure Sensor
Ground Moisture Sensor
Transmitter Receiver
Micro-Controller
Power Source
Ground Temp. Sensor
Ambient Temp. Sensor
Rain Detection Sensor
Humidity Sensor
Power Source
Micro-Controller
LCD Display
User Interface
Transmitter Receiver
Solenoid
Transmitter Receiver
Micro-Controller
Power Source
Sensors S.S.
Central HUB S.S.
Solenoid S.S.

## Slide 24: Ground Moisture Sensor
Used to measure the water content in soil.
Necessary for the when to water algorithm.
General resistive method.

## Slide 25
Barometric Pressure Sensor
Ground Moisture Sensor
Transmitter Receiver
Micro-Controller
Power Source
Ground Temp. Sensor
Ambient Temp. Sensor
Rain Detection Sensor
Humidity Sensor
Power Source
Micro-Controller
LCD Display
User Interface
Transmitter Receiver
Solenoid
Transmitter Receiver
Micro-Controller
Power Source
Sensors S.S.
Central HUB S.S.
Solenoid S.S.

## Slide 26: Ground Temperature Sensor
Necessary for accuracy of ground moisture sensor.
Needs to be exposed to the elements.
Used under the Creative Commons Attribution-Share Alike 3.0 Unported. Created by Danieleccc

## Slide 27: Ground Temperature Sensor
.5 inch
.21 inch
.2 inch
Small, basic transistor package.
Created into a probe style sensor.
Part | Supply Voltage | Average Current | Temperature Range | Accuracy | Cost
AD22103 | 2.7 to 3.6V | 350 to 600μA | 0 to 100⁰C | ±0.5⁰C | $3.50
TMP36 | 2.7 to 5.5V | 50μA | -40 to 125⁰C | ±1.0⁰C | $0.80 to $1.50
LM45 | 4.0 to 10.0V | 10μA | -20 to 100⁰C | ±3.0⁰C | $2.50
AD22100K | 4.0 to 6.5 V | 500μA to 650μA | -50 to 150⁰C | ±2.0⁰C | $1.90
TMP36

## Slide 28
Barometric Pressure Sensor
Ground Moisture Sensor
Transmitter Receiver
Micro-Controller
Power Source
Ground Temp. Sensor
Ambient Temp. Sensor
Rain Detection Sensor
Humidity Sensor
Power Source
Micro-Controller
LCD Display
User Interface
Transmitter Receiver
Solenoid
Transmitter Receiver
Micro-Controller
Power Source
Sensors S.S.
Central HUB S.S.
Solenoid S.S.

## Slide 29: Wireless Communication
Transmission Range: > 20 feet.
Low power consumption: < 100mW (on)
Concurrent transmissions without interference.

## Slide 30: Wireless Communication
 | Xbee | Xbee pro | Zigbee 802.15.4 | Bluetooth 802.15.1 | WIFI b/g 802.11b/g
Battery Days |  |  | 100-1000 | 1-7 | .1-5
Power transmitting | 1mW | 63mW | 100 mW | 160 mW | 1600 mW
Current sleeping | <1uA | <1uA | .3 mA | .2 mA | 20 mA
Nodes/Network |  |  | 255/65K+ | 7 | 30
Bandwidth | 250 kbps | 250 kbps | 20-250 kbps | 720 kbps | 11-54 mbps
Range (m) | 30(indoor) 90(outdoor) | 90(indoor) 1600(outdoor) | 75+ | 10+ | 100
Key attribute | Low cost, Low power | Low power | Low power, reliable | convenience | speed

## Slide 31: Xbee
Inexpensive $17
Transmission Range: 400 ft
Data Rate: 250 kbps
Transmit Power: 1.25 to 2 mW
Voltage: 2.1 - 3.6 VDC
1.25 inch
1 inch

## Slide 32
Barometric Pressure Sensor
Ground Moisture Sensor
Transmitter Receiver
Micro-Controller
Power Source
Ground Temp. Sensor
Ambient Temp. Sensor
Rain Detection Sensor
Humidity Sensor
Power Source
Micro-Controller
LCD Display
User Interface
Transmitter Receiver
Solenoid
Transmitter Receiver
Micro-Controller
Power Source
Sensors S.S.
Central HUB S.S.
Solenoid S.S.

## Slide 33: Microcontroller
Low power consumption.
Communicates with the computer via serial connection.
Inexpensive.
Easily programmable.
I/O for all sensors.

## Slide 34: Microcontrollers
Item | AT90L S8535 | Atmega 103L | PIC16F8X | MSP430 F149 | StrongARM SA-1100 | At91M 42800A | MC68HC05PV8A | 80C51RD | EM6603 | MC9328MX1 | ATMega328
Bits | 8 | 8 | 8 | 16 | 32 | 16 | 8 | 8 | 4 | 16 | 8
Flash kB | 8 | 128 | 68 | 60 |  |  |  | 64 |  |  | 32
RAM B | 512 | 4k | 1 | 2k |  | 8k | 192 | 1k | 96x4 | 128k | 2k
ADC bits | 10 | 10 |  | 12 |  | 08 |  |  |  | 13 | 2x8
Timers | 3 | 3 | 1 | 3 |  | 6 | 1 | 1 | 1 | 2 | 2+1
Operating Voltage | 4-6v | 2.7-3.6v | 2-6v | 1.8-3.6v | 3-3.6v | 2.7-3.6v | 3.3-5v | 2.7-5.5v | 1.2-3.6v | 1.62-3.3v | 1.8-5.5v
Current Active | 6.4 mA | 5.5 mA | 2 mA | .4 mA | 230 mA |  | 4.4 mA | 16 mA | 1.8 μA | 90 mA | .2 mA
Current Idle Mode | 1.9 mA | 1.6 mA |  | 1.3 μA | 50 mA |  | 1.95 mA | 4 mA | .35 μA | .16 mA | .75 μA
Powered Down Current | 1 μA | 1 μA | 1 μA | .1 μA | 25 μA |  | 485 μA | 50 μA | .1 μA |  | .1 μA

## Slide 35: ATmega 328P
Inexpensive $4
14 digital I/O pins
6 Analog I/O pins
Programmable over serial using USB to serial converter
Has I2C capability
Low power
Different power modes
1.32 inch
.28 inch

## Slide 36: ATmega 328P to Xbee Module

## Slide 37
Barometric Pressure Sensor
Ground Moisture Sensor
Transmitter Receiver
Micro-Controller
Power Source
Ground Temp. Sensor
Ambient Temp. Sensor
Rain Detection Sensor
Humidity Sensor
Power Source
Micro-Controller
LCD Display
User Interface
Transmitter Receiver
Solenoid
Transmitter Receiver
Micro-Controller
Power Source
Sensors S.S.
Central HUB S.S.
Solenoid S.S.

## Slide 38: LCD Module
The LCD module that will fit Eco-Sense:
Low power mode
LED backlighting GDM1602K
16x2 character display
Image provided under Creative Commons (CC) by Sparkfun

## Slide 39: LCD Display

## Slide 40
Barometric Pressure Sensor
Ground Moisture Sensor
Transmitter Receiver
Micro-Controller
Power Source
Ground Temp. Sensor
Ambient Temp. Sensor
Rain Detection Sensor
Humidity Sensor
Power Source
Micro-Controller
LCD Display
User Interface
Transmitter Receiver
Solenoid
Transmitter Receiver
Micro-Controller
Power Source
Sensors S.S.
Central HUB S.S.
Solenoid S.S.

## Slide 41: Power
High efficiency: > 70%
DC-DC from 7.4 volts to 3.3 volts and 5 volts.
Low Cost
Rechargeable, high energy density battery.

## Slide 42: Power- Battery
Specification | Ni-Cad | Ni-MH | Li-ion / Li-poly | Rechargeable Alkaline | Lead Acid
Charge/Discharge life cycles | 500-700 | 300-400 | 300-1000 | 100+ | 500-800
Memory Effect | High effect | Little effect | No effect |  | 
Operating Temperature | -22 to +140°F | -4 to +122°F | +14 to +140°F | -20º F to 130º F | -85º F to 149º F
Self-Discharge | 20% loss of charge/ month at 77°F | 30% loss of Charge/ month at 77°F | Self-discharge 3% loss of charge/ month at 77°F | (5/12)% loss per month | 
Energy density (Wh/kg) | 40-60 | 30-80 | 150-250 (Li-poly 130-200) |  | 30-40
Power W/kg | 150 | 250-1000 | 1800 (Li-poly 3000+) |  | 180

## Slide 43: Regulators
Linear Regulators
Easy to use
Heat sink usually required
50% efficiency
Clean voltage
Switching Regulators
  Requires more components
  Smaller heat sink required
  80% efficiency
  Some ripple voltage on the output

## Slide 44: Switching Regulator Circuit

## Slide 45
Power
Communication
Display
Microcontroller

## Slide 46
Barometric Pressure Sensor
Ground Moisture Sensor
Transmitter Receiver
Micro-Controller
Power Source
Ground Temp. Sensor
Ambient Temp. Sensor
Rain Detection Sensor
Humidity Sensor
Power Source
Micro-Controller
LCD Display
User Interface
Transmitter Receiver
Solenoid
Transmitter Receiver
Micro-Controller
Power Source
Sensors S.S.
Central HUB S.S.
Solenoid S.S.

## Slide 47: Water Solenoid
Used to control distribution of water
Must be GHT (Garden Hose Threaded) for US standards
Must operate with minimum power

## Slide 48: Water Solenoid
Orbit Yard Watering Valve
Operates +/- 24V
Water flows +24V, stops -24V
Uses latch solenoid, power is only supplied during solenoid state transitions

## Slide 49: Water Solenoid
Arduino to Orbit Watering Valve
Schematic created by Rui Wang
as an open source project

## Slide 50: Subsystem Software

## Slide 51: Subsystem Software Design
3 different approaches, one for each subsystem
Must be able to communicate to each other
Minimal memory usage for code
Sleep mode would be ideal

## Slide 52: Subsystem Software Design
Sensor Subsystem
Solenoid Subsystem
Central Subsystem

## Slide 53: Sensor Software
Read Moisture
Read Temperature
Read Humidity
Convert / Compress
Transmit Data
Receive Data
Read Pressure
Read Rain Status
Memory Store
System Timer
Fetch Memory
Clear Memory
Reset Timer
Sensor Data
Collection
Data Transfer
Data Storage

## Slide 54: Subsystem Software Design
Sensor Subsystem
Solenoid Subsystem
Central Subsystem

## Slide 55: Central Software
Extract Data
Moisture Flag
Transmit Data
Receive Data
Temp Flag
Humidity Flag
Pressure Flag
Rain Flag
Sum Flags
Water Signal
Display Statistics
System Timer
Override
Store in Memory
Button Input
Data Transfer
Water Algorithm
Manual Input

## Slide 56: Subsystem Software Design
Sensor Subsystem
Solenoid Subsystem
Central Subsystem

## Slide 57: Solenoid Software
Receive Signal
Open Valve
Countdown Timer
Close Valve
Data Transfer
Solenoid Controller

## Slide 58: Software Design Overview
Sensor subsystem collects data at set intervals
Central subsystem requests data, computes water signal, transmits water signal to solenoid
Solenoid subsystem controls the operation of the valve and water distribution

## Slide 59
Barometric Pressure Sensor
Ground Moisture Sensor
Transmitter Receiver
Micro-Controller
Power Source
Ground Temp. Sensor
Ambient Temp. Sensor
Rain Detection Sensor
Humidity Sensor
Power Source
Micro-Controller
LCD Display
User Interface
Transmitter Receiver
Solenoid
Transmitter Receiver
Micro-Controller
Power Source
Sensors S.S.
Central HUB S.S.
Solenoid S.S.

## Slide 60: User Interface
The user interface (UI) is for allowing the user to access to the system in an efficient manner
Provide overriding actions for user
Provide data feedback to the user
Display system status

## Slide 61: User Interface
The UI will include the following:
LCD module
Pushbuttons
Protective box

## Slide 62: UI Model
3.5 inches
6.5 inches

## Slide 63: Progress
Chart: 
| Overall | Testing | Prototype | Programming | Part Testing | Part Acquisition | Design | Research
Series 1 | 30 | 5 | 5 | 5 | 10 | 70 | 85 | 90

## Slide 64: Work Distribution
 | Neil (EE) | Jamie (CpE) | Daniel (CpE)
Sensor Configuration | X |  | 
Sensor Subsystem Circuitry | X | X | X
Weather Algorithms | X |  | 
Wireless Communications |  |  | X
Power Management | X |  | X
Solenoid Subsystem Circuitry | X | X | X
Watering Algorithms |  | X | 
User Interface |  | X | 
Central Subsystem Circuitry | X | X | X
Solenoid Controller |  | X | X

## Slide 65: Bill of Materials
Part | Buy from where? | How many | Price | Extended Price
Mini Push Button Switch | Sparkfun | 4 | $0.35 | $1.40
LCD Module | Sparkfun | 1 | $13.95 | $13.95
Orbit Watering Valve | Home Depot | 1 | $15.97 | $15.97
Orbit Spike Sprinkler | Lowe's | 1 | $8.98 | $8.98
Custom Housing Estimate | SkyCraft | 3 | $10.00 | $30.00
Miscellaneous Electrical Components | N/A | 1 | $5.00 | $5.00
Atmega 328 DIP Socket Low Power Version | Sparkfun | 3 | $4.30 | $12.90
PCB | 4PCB | 3 | $33.00 | $99.00
Xbee Series 2 | Digikey | 3 | $17.00 | $51.00
HIH-4030 Hygrometer | Sparkfun | 1 | $16.95 | $16.95
BMP085 Barometer/Thermometer | Sparkfun | 1 | $19.95 | $19.95
12 Gauge Galvanied Steel Wire (2 feet) | N/A | 1 | $5.00 | $5.00
Black Electrical Tape | N/A | 1 | $5.00 | $5.00
4" x 4" x 4" Packing Foam Block | N/A | 1 | $5.00 | $5.00
Rain Detection PCB board | Baaqii | 1 | $3.01 | $3.01
LM339N Comparator | Jameco | 1 | $0.25 | $0.25
TIP120 transistor for solenoid | Jameco | 1 | $0.39 | $0.39
LM2592HV 3.3v (input 4.5-60v) | Jameco | 3 | $1.95 | $5.85
1000mAh 2S 20C Lipo Pack | HobbyKing | 3 | $4.62 | $13.86
Battery Charger (Owned) | HobbyKing | 1 | $0.00 | $0.00
 |  |  | Total | $313.46

## Slide 66: Issues
Housing material
Time for testing

## Slide 67: Project Completion
To complete this project, the following work needs to be finished:
PCB layout and purchase
Decide on housing material and design
Prototype each subsystem
Testing, testing, testing

## Slide 68: Questions?

## Slide 69: Complaints?