## Slide 1: LED Globe
Group #8
Viet Nguyen | Omar Vazquez | Rhonal Soto

## Slide 2: Motivations
To create an Innovative and attractive means of displaying information via a lighting system which allows the information to be displayed in the dark.
To display images on a 360 degree angular sphere with different sequences.
To be able to control displays through wireless communication.

## Slide 3: Goals and Objectives
Display images using different algorithms
Energy efficient
Wireless interface
Entertainment Light source

## Slide 4: Specifications
Component | Design Specification
Motor | 12 V DC brushless
Microcontroller | ATMEGA328
LED | 3.5 V; 20 mA
Shift register 74HC595 | 5 V; 35 mA Max
JY-MCU Bluetooth Module | 5 V
Power supply | 120/36V DC, 36 V Max; 10 A Max; 360W Max
Voltage regulators | 36V/12V; 36V/5V DC; 36V/adjustable voltage up to 24V

## Slide 5: 3 Output Modes
Pac-Man
Names
Random

## Slide 6: Overall Block Diagram

## Slide 7: Mechanical Materials

## Slide 8: LED Globe Motor
Fasco 7103.0113 Brushless DC motor
0-24volts
5.2A
124.8w Max
8,000RPM max
3.32in wide, 3.15Long, 1.8pounds
5/16 in shaft

## Slide 9
LED Ring Structure
Inner Diameter: 252mm
Outer Diameter: 255mm
Width (Outer and Inner Surface): 30 mm
Thickness: 3mm
97 holes
Diameter: 5 mm each
Holes location: at 15 mm from the edge
Separation hole to hole: 8.0 mm center to center

## Slide 10: Ring Support Shaft
15in long, .5in outer diameter, .4in inner diameter hollow aluminum tube
Two .5 in long, .75 outer diameter, .5in inner diameter hollow copper slip rings to provide power to the microcontroller
Two ball bearings for rotational support. .63in by 1.13in diameter ball bearing at the bottom and .6in by .62in diameter ball bearing at the top.
Three wire holes.

## Slide 12: Slip Ring Voltage Terminals
Two Copper braided mesh clamped around
.56 Copper hollow tubes insulated over the ring support shaft.
The top braid is set to a positive potential of five volts
and the bottom is set to ground.
Two holes are drilled into the support shaft, one over the positive terminal and the other over the negative terminal. The holes are for the positive and negative wires to be inserted into the support shaft and fed to the micro controller.

## Slide 13: Wood Housing
Housing for the motor and the power supply.
Stability for the support bar and motor due to vibrations.

## Slide 14: PCB Mount
Used for mounting the microcontroller and the shift registers.
Two 5in by 2in by .027in aluminum sheets
Secured by four .5in by .15in diameter threaded hollow rods on each corner
Ring support shaft

## Slide 15: Support Bar
To support the ring support shaft and stabilize due to vibration.
The vertical piece is 24 in x 1.5 in x .127 in L shape bar.
Top piece is a 10 in x 1.5 in x .127 in L bar with a .63in circle cut out for fitting top RSS ball bearing.

## Slide 16: Electric Motor
Testing configuration to reduce shaft oscillation

## Slide 17: Electronics

## Slide 18: Electronic Block Diagram

## Slide 19: LED Globe Power Supply
120Vac
Rectifier
Smoothing Capacitor
12V Regulator
36V
10A max
5V Regulator
Motor cooling fan
Micro controller and LED’s
Adjustable Voltage Regulator
Motor

## Slide 21: Motor Power Supply
36V
5.2A
Adjustable Voltage Regulator
187.2Watts
Motor
62.4Watts

## Slide 22: Motor Voltage Regulator

## Slide 23: Microcontroller Power Supply
36V
4.8A
5V Regulator
172.8Watts
Microcontroller
18Watts

## Slide 24: Microcontroller Voltage Regulator

## Slide 25: Microcontrollers
 | ATMEGA328 | MSP430G2553 | ATMEGA2560
Development Board | $27.19 | $10.99 | $46.29
Microcontroller | $2.88 | $2.35 | $18.00
Flash Memory | 32 Kb | 16 Kb | 256 Kb
I/O Pins | 20 | 14 | 70
Surface Mounted | No | No | Yes
$7.26 =
+
+

## Slide 26: 90-92 RGB Ultra-Bright Diffused LED
Specifications | 
Red (Luminous Intensity) | 1200 mcd max
Green (Luminous Intensity) | 5000 mcd max
Blue (Luminous Intensity) | 3000 mcd max
Voltage | 5 V max
Current | 25 mA

## Slide 27: Configuration I2C vs. Shift Registers Charlieplex vs. Shift Registers
Number of Pins | Outputs
3 | 6
4 | 12
5 | 20
6 | 30
10 | 90
17 | 270
Charlieplex

## Slide 28: I2C

## Slide 29: Configuration
I2C
Complex circuitry
Complex Algorithm

## Slide 30: Configuration 34 Shift Registers 74HC595
90 RGB LEDs = 270 Outputs
270/8 = 33.75
≈ 34 SR

## Slide 31: Configuration Shift Register
Less complex circuitry
Less complex algorithm

## Slide 32: LEDs Configuration
Q0-Q7 – Outputs
Pin 11 – Clock
Pin 12 – Latch
Pin 13 – Low
Pin 10 – High

## Slide 33: MCU-JY Bluetooth Module
Lack of documentation
After testing the device:
  Slave
  Serial communication UART
  Baud rate 9600
  Connect after uploading the sketch
  It does not work with apple devices
26.9 mm
13 mm

## Slide 34: MCU-JY Bluetooth Module
One command for each sequence
  P: Pac-Man
  N: Names
  L: Random

## Slide 37: Algorithm
3 Pins from the microcontroller
  Data (8- bits hexadecimal values )
  Clock pin toggles after each bit is taken
  Latch pin goes high when the sequence is completed

## Slide 38: Algorithm

## Slide 39: Software
Include the SPI library for use
  SPI = Serial Peripheral Interface
Set the latch pin as an output
Declare time variables

## Slide 40: Software
Bitmap array is declared above
Set up the serial communication Baud rate
Declare output latch pin
Initialize SPI

## Slide 41: Software
For Loop:
  Self-correcting delay using micros()
  Latch pin goes high to display the sequence
  Pgm_read_byte_near to read bitmap array

## Slide 42: Bitmap Array

## Slide 43: Budget
Part | Cost
Mechanical Parts | $42.30
Power Supply Parts | $321.21
Electronic Parts | $77.10
Other/Miscellaneous | $100.00
Total | $540.61

## Slide 44: Work Distribution
Name | Electronics | Mechanical and Power Supply | Coding/PCB Design
Rhonal Soto | X |  | 
Omar Vazquez |  | X | 
Viet Nguyen |  |  | X

## Slide 45: Prior Issues:
Machine Shop Price for Ring
Motor Voltage Regulator getting too hot
Motor to Shaft Coupling
Software

## Slide 46: Solutions

## Slide 47: Questions?