## Slide 1: KnightCop
Group 11
Elean Atencio CpE
Nitin Kundra CpE

## Slide 2
The Project
Remote controlled scout robot to aid police in hazardous situations
Onboard manipulator arm for interacting with objects
Environment sensors
Video feedback
Autonomous behavior

## Slide 3
Goals and Objectives
Navigate across urban terrain
Wireless control and data transmission (Video + sensors)
Prefer dexterity (degrees of freedom) over strength in robot arm
Intuitive UI
Reliable and robust

## Slide 4
Specifications
Max Dimensions | l x b x h | 30 x 30 x 30 in
Operating Range |  | 50 m
Power Supply Voltage |  | 12 V
Minimum Speed |  | 1 m/s
Max Robot Weight |  | 50 kg
Video Feed | 30 fps | 640 x 480 px
Arm | Lifting Capacity | 100 g
 | Rotation Span | 120°

## Slide 5
Robot Schematic

## Slide 6
Hardware Block Diagram
User Interface
Robot
Android
Phone
Laptop
Wifi
Router
Wifi T/R
MCU
ARM
Chassis
Motor Control
Obstacle
Detection
Motor Control
Video Feedback
Elean
Nitin
Pan & Tilt
Cam
Integrated Wifi
Power
Night
Vision
ENVIROMENT
Ambient Light
Temperature
Battery Level

## Slide 7
Microcontroller

## Slide 8
Microcontroller
 | MSP430G2553 | ATmega328 | ATmega2560 | PIC16F886 | PIC18F47J53
Architecture (bits) | 16 | 8 | 8 | 16 | 8
Frequency (MHz) | 16 | 20 | 16 | 8 | 8
Max Voltage (V) | 3.6 | 5.5 | 5.5 | 5.5 | 3.6
Program Memory (KB) | 16 | 32 | 256 | 14 | 128
RAM (KB) | 0.5 | 2 | 8 | 0.359 | 3.71
USART/SPI | 1/1 | 1/2 | 4/5 | 1/1 | 2/2
I/O Pins | 24 | 23 | 86 | 25 | 44
ADC (channels, bits) | 8, 10 | 8, 10 | 16, 10 | 11, 10 | 13, 12

## Slide 9
Mobile Base
User Interface
Robot
Android
Phone
Laptop
Integrated
Wi-Fi
Wi-Fi T/R
MCU
Potentiometers
Limit Switches
ARM
Mobile Base
Motor Control
Power Unit
Obstacle
Detection
Motor Control
AV Feedback
Elean
Nitin
Wesley
Flashlight
Mic/Speaker
Cam
Integrated Wi-Fi
Environment Sensors

## Slide 10
Mobile Base

## Slide 11
Drive Base
Design and built by us
Footprint: 12”H x 18”W x 25.5”L
Pre-drilled aluminum
6 inch threaded wheels
Gear ratio: 30:1
Tank drive configuration

## Slide 12
Drive Motors
CIM Motor (AM802-001A)
12V DC Brushed
No Load RPM: 5310
Max Power: 337 W
Footprint: 2.5” diameter, 4.3” long

## Slide 13
Drive Motor Controllers
Victor 888 Motor Controller
Supply voltage: 6-15 V
Continuous supply current: 60A
Surge supply current: 150A
PWM control
Break and coast modes
Footprint: 2”H x 2.7”W x 2.3”L

## Slide 14
Proximity Technology
Infrared Sensors
  Cheap: $10-$15
  Narrow beam width
  Problems in direct sunlight
Ultrasonic Sensors
  About double the price of infrared
  Poor detection of absorbent materials
  Wider beam width
  Detects items as close as 2 cm

## Slide 15
Ultrasonic Sensors
 | Parallax PING))) | HC-SR04 | Maxbotix LV-EZ1 | SRF04
Supply Voltage (V) | 5 | 5 | 2.5-5 | 5
Supply Current (mA) | 30 | 2 | 3 | 30
Range (cm) | 2-300 | 2-50 | 0-645 | 3-300
Frequency (kHz) | 40 kHz | 40 kHz | 42 kHz | 40 kHz
size (mm) | 22x46x16 | 20x43x15 | 20x22x16 | 20x43x17
Price | $29.99 | $5.99 | $29.95 | $29.50
Cascade feature | No | No | Yes | No

## Slide 16
Arm System
User Interface
Robot
Android
Phone
Laptop
Integrated
Wi-Fi
Wi-Fi T/R
MCU
Potentiometers
Limit Switches
ARM
Mobile Base
Motor Control
Power Unit
Obstacle
Detection
Motor Control
AV Feedback
Elean
Nitin
Wesley
Flashlight
Mic/Speaker
Cam
Integrated Wi-Fi
Environment Sensors

## Slide 17
Arm System

## Slide 18
Manipulator
OWI-535 Robotic Arm
Robotic Kit (easier to modify)
9”L x 6”W x 15” H
Lifting capacity 100 gram
5 Degrees of motion
Price: $45

## Slide 19
Arm Motor Controllers
DRV8833PWPR Dual bridge motor driver
Supply voltage: up to 11 V per channel
Supply current: up to 1.5A per channel
Over-current, under-voltage, over-temperature protection and Energy savings mode
PWM/Digital Control
Footprint: ~.25 inch2
Price: ~$1.50

## Slide 20
Com Systems
User Interface
Robot
Android
Phone
Laptop
Integrated
Wi-Fi
Wi-Fi T/R
MCU
Potentiometers
Limit Switches
ARM
Mobile Base
Motor Control
Power Unit
Obstacle
Detection
Motor Control
AV Feedback
Elean
Nitin
Wesley
Flashlight
Mic/Speaker
Cam
Integrated Wi-Fi
Environment Sensors

## Slide 21
Com Systems

## Slide 22
Communications

## Slide 23
Communication Technology
 | Bluetooth 2.1 | ZigBee S2 | Wi-Fi
Peak Range (m) | 30 | 120 | 100
Frequency (GHz) | 2.4 | 2.4 | 2.4
Bandwidth (Mbps) | 2.1 | 0.25 | 11
Encryption | Yes | Yes | Yes
Interface | UART/USB | UART/USB | UART/SPI/USB
Cost ($) | 29.91 | 21 | 35

## Slide 24
Communication Device
Wi-Fi Module | Bluegiga Technologies | Texas Instruments | Roving Networks
Model | WF111-A | CC3000MOD | RN171XVW-I/RM
Protocol (802.11) | b/g/n | b/g | b/g
Max Data Rate (Mbps) | 72.2 | 54 | 54
Interface | UART/USB/CSPI | SPI | UART
Antenna Type | Integrated | U.FL | Wire
Transmit Power (dBm) | 12 | 18 | 17
Security | WPA, WPA2, WEP, CCMP, TKIP, WPS | WEP, WPA, WPA2 | WEP, WPA, WPA2
Mounting | Surface Mount | Surface Mount | Through Hole
Cost ($) | 28.16 | 23.56 | 37.48

## Slide 25
Protocol

## Slide 26
A/V System
User Interface
Robot
Android
Phone
Laptop
Integrated
Wi-Fi
Wi-Fi T/R
MCU
Potentiometers
Limit Switches
ARM
Mobile Base
Motor Control
Power Unit
Obstacle
Detection
Motor Control
AV Feedback
Elean
Nitin
Wesley
Flashlight
Mic/Speaker
Cam
Integrated Wi-Fi
Environment Sensors

## Slide 27
A/V System

## Slide 28
Camera
Make | HackHD SEN-11418 | Foscam FI8910W | D-Link DCS-932L
NightVision | No | Yes | No
Resolution | 1920 * 1080 | 640 * 480 | 640 * 480
FPS | 30 | 30 | 20
Microphone | No | Yes | No
Encoding | H.264 | MJPEG | MJPEG
Video Output | Composite | MJPEG Stream | MJPEG Stream
Pan / Tilt | No | 300° / 120° | No
Cost ($) | 159.95 | 65.00 | 69.70

## Slide 29
Environment Peripherals
User Interface
Robot
Android
Phone
Laptop
Integrated
Wi-Fi
Wi-Fi T/R
MCU
Potentiometers
Limit Switches
ARM
Mobile Base
Motor Control
Power Unit
Obstacle
Detection
Motor Control
AV Feedback
Elean
Nitin
Wesley
Flashlight
Mic/Speaker
Cam
Integrated Wi-Fi
Environment Sensors

## Slide 30
Environment Peripherals

## Slide 31
Ambient Light Sensors
Make | Vishay | SEN-09088 Photo Cell | ROHM Semiconductors
Part # | TEPT4400 | 09088 | BH1603FVC-TR
Peak Wavelength (nm) | 570 | 550 | 560
Operating Temp (°C) | -40 to +85 | -30 to +70 | -40 to +85
Mounting | Through Hole | Through Hole | Surface Mount
Peak Supply Voltage (V) | 6 | 150 | 5.5
Power Dissipation (mW) | 100 | 100 | 260
Cost ($) | 0.62 | 1.50 | 1.15

## Slide 32
Interfacing Light Sensor
Output current directly proportional to illuminance:
0 µA = 0 lux (dark)
48 µA = 1000 lux (typical indoor lighting)
480 µA = 10000 lux (daylight)

## Slide 33
Temperature Sensors
Make | Dallas Semiconductor | Analog Devices | Maxim Integrated
Base Part | DS18B20 | TMP36 | DS18B20
Max Voltage Supply (V) | 5.5 | 5.5 | 5.5
Min Temperature (°C) | -55 | -40 | -55
Max Temperature (°C) | +125 | +125 | +125
Accuracy (°C) | 0.5 | 2 | 0.5
Output | digital | analog | digital
Cost ($) | 4.25 | 1.5 | 9.95

## Slide 34
Interfacing Temperature Sensor
One digital line for input/output
Temperature reading corresponds to value in Temperature Register:
    0° C = 0x0000
125° C = 0x07D0
hex_value / 16 = temperature in °C
Image by Sparkfun.com under Creative Commons

## Slide 35
ATmega2560 Code

## Slide 36
Java Code

## Slide 37
Navigation Example

## Slide 38
Light Check Example

## Slide 39
PC UI
image from Wikipedia under CC

## Slide 40
Android UI

## Slide 41
Work Distribution
 | Elean | Nitin
Chassis Design and Construction | X | 
Communications |  | X
PC + Android Apps |  | X
Obstacle Detection | X | X
Microcontroller Programming | X | X
PCB Design | X | 
Power | X | 

## Slide 42
Spending
Thus
Far
Part | Manufacturer | Quantity | Unit Price | Net Price
Ultrasonic Sensors | Maxbotix | 4 | $25.95 | $103.80
Potentiometer | 中国制造 | 1 | $1.95 | $1.95
Drive Motors | CIM | 4 | $25.00 | $100.00
Manipulator | OWI Robots | 1 | $45.00 | $45.00
Arm Motor Controllers | Texas Instruments | 3 | $2.00 | $6.00
Drive Motor Controllers | Vex Robotics | 4 | $69.99 | Donated
Micro Switch | Sparkfun | 2 | $0.95 | $1.50
RN-XV Wi-Fi Module | Roving Networks | 1 | $34.94 | $34.94
Temperature Sensor | Maxim Integrated | 1 | $4.25 | $4.25
Ambient Light Sensor | Sharp Electronics | 1 | $0.81 | $0.81
IP Camera | Foscam | 1 | $65.00 | $65.00
AVR ISP | Atmel | 1 | $34.00 | $34.00
Arduino Mega 2560 | Arduino | 1 | $45.95 | $45.95
ATmega2560 | Atmel | 1 | $18.00 | Sampled
MiniBoards | ExpressPCB | 3 | $33.00 | $99.00
72’’ Aluminium Angle | Vex Robotics | 3 | $29.95 | $89.85
Sensor Brackets | Vex Robotics | -- | -- | 50.00
Trimpot 10K with Knob | Sparkfun | 4 | $0.95 | $3.80
ToughBox Nano 500 Hex Shaft | AndyMark | 4 | $78.00 | Donated
6” Plaction Wheel w/ Tread | AndyMark | 4 | $29.00 | Donated
Hex Wheel Hub | AndyMark | 4 | $10.00 | Donated
Misc Mechanical Parts | -- | -- | -- | 50.00
Misc Electrical Supplies (Resistors, Capacitors, Wires etc) | -- | -- | -- | 50.00
TOTAL |  |  |  | $785.85

## Slide 43
Questions?