## Slide 1
Group 2
Chris Britt – Electrical Engineering
Francisco Tirado Perez – Computer Engineering
David Simoneau – Computer Engineering
Anthony Hunter Hinnant – Computer Engineering

## Slide 2: Motivation
Severe lack of open source VR controllers
Existing options are expensive, controllers, or outdated
The project is an excellent avenue to showcase practical engineering skills

## Slide 3: Goals and Objectives
    Enhance the virtual experience by providing touch and temperature feedback
    Create a cheaper experience to current VR users
    Provide a basis for simple open source hardware and software
    Design a product that can be used for most VR applications

## Slide 4: Specifications
General Type | Specific Type | Design Specification
Immersiveness | Frame Rate | > 30 FPS
Battery | Use Life | > 30 min
Safety | Thermal/Electrical | Reasonably Safe
Arm Strain | Weight | < 2 kgs

## Slide 5: Expected Budget
Item | Quantity | Price (rough estimate)
Glove | 2 | $20
PCB Design ~ Processor Board | 4 | $150
PCB Design ~ Glove | 4 | $150
Electrical Components on PCBs | ? | $200
Bluetooth modules | 2 | $40
Peltier Devices | 10 | $50
Power Supply | 2 | $20
Vibrational Motors | 10 | $50
Gyroscope Sensor | 2 | $50
Room for Error | ? | $270
Total |  | $1000

## Slide 6: Current Expenditures
Part | Description | Supplier | Amount Ordered | Cost Per Unit | Total
C0720B015F | Vibrational Motor | Digi-Key | 7 | 3.354 | 23.48
MAX6897 | IC Sequencer | Digi-Key | 3 | 1.38 | 4.14
TSV321 | Op Amp | Digi-Key | 15 | 0.494 | 7.41
NX3008CBKS | Dual Fet | Digi-Key | 25 | 0.467 | 11.53
AD5248 | Digital Potentiometer | Digi-Key | 15 | 2.525 | 37.88
TPS62823 | Power Regulator | Mouser | 3 | 1.63 | 4.89
TCA954A | I2C Mux | Mouser | 3 | 1.51 | 4.53
MMA8451 | Accelerometer Breakout | Adafruit | 2 | 10.51 | 21.02
MMA8451 | Accelerometer | Digi-Key | 0 |  | 
1N4148 | Switching Diode | Digi-Key | 20 | 0.067 | 1.34
NXRT15XH103FA1B040 | Thermister | Digi-Key | 10 | 0.58 | 5.8
WP154A4SEJ3VBDZGW/CA | RGB LED | Mouser | 3 | 2.05 | 6.15
CM23-1.9 | Peltier Device | Digi-Key | 5 | 10.404 | 52.2
DRV8836 | H-bridge | Digi-Key | 5 | 1.49 | 7.45
Inductor | 470 nH Inductor | Arrow | 5 | 0.378 | 1.89
Surfance Mount to DIP converters | Various | Various |  |  | 101.8
Total |  |  |  |  | 291.51

## Slide 7: Division of Labor
    Chris – Hardware
    David – Embedded Systems
    Francisco – Interface Driver
    Hunter – Virtual Environment and API

## Slide 8: Hardware Design
Christopher Benjamin Turner Britt – Primary
David Simoneau- Secondary

## Slide 9
Diagram of Accelerometer Placements
Diagram of Placements of Peltier Devices and Vibrational Motors

## Slide 11
TPS62823DLC
  Chosen with TI Testbench
  High Efficiency Switching Reg
  3.3 Volts and 3 Amps
  QFN
  $1.63 per Unit
ICR18650
  Lithium Ion Battery
  6600 mAh at 3.7V
  $29.5 per Unit
  69mm x 54mm x 18mm
  1.25A discharge rate

## Slide 12
WP154A4SEJ3VBDZGW/CA
  RGB Common Anode LED
  2.2V Red, 3.3V Green, 3.3V Blue
  $2.46 per Unit
BSS138
  Switching NFET
  220mA
  $0.32 per Unit
  SOT-23-3
  Used Before

## Slide 13
  CM23-1.9-01AC
    300 to 350 mA Usuable Range
    1.9A Max Current
    $11.08 per Unit
    Cooling Not an Option

## Slide 14
NX3008CBKSRGB
  N/P Channel Dual FET
  P Channel 200 mA
  N channel 350 mA
  Used Before
  $0.467 per Unit
  Used for N/P Switch to avoid 3rd State

## Slide 15
  DRV8836
    2 Channel Low Voltage H-Bridge
    1.5 Amp Max Drive Current
    Phase/Enable vs PWM
    WSON 2mm x 3mm
    Dedicated Sleep Pin
    $1.49 per Package
    3.3V Operable

## Slide 16
  C0720B015F
    "Coin" Form ERM
    3.3 Volt Operable
    80 mA Max
    $3.54 per Unit

## Slide 17
TSV321
  General Purpose Rail to Rail Op Amp
  80 mA Max Output Current
  3.3 Operable
  $0.494

## Slide 18
  AD5248
    2 Channel 256 bit I2C Potentiometer
    100k Max Resistance
    ~50 Min Resistance
    3.3V Operable
    2 Addressable Pins
    No Connect 3rd Terminal
    10 MSOP
    $2.525 per Unit

## Slide 19
  MMA8451
    Triple Axis 14 Bit Accelerometer
    2/4/8 Capable
    3.3V Operable
    I2C interface
    800 Hz Data Output
    2 Possible Addresses
    Cheap Adafruit Breakout Board
    16 Pin QFN 3mm x 3mm x 1 mm

## Slide 20
Inner
Middle
Outer
26mm x 18mm
20mm x 17mm
45mm x 60mm

## Slide 21
  TCA9548A
    1 to 8 Bidirectional I2C Switch
    3.3V Operable
    Adafruit Tutorial
    TSSOP 24
    $1.51 per Unit

## Slide 22
  STM32F030C8 LQFP48
    32 Bit
    48 MHz
    256 Kbytes Flash
    2 I2C Channels
    6 UART Channels
    12 bit ADC
    3.3 Operable
    32 I/O Pins
    Serial Wire Debug (SWD)
    Internal Oscillators
    Reset Pin
    $2.02 per Unit

## Slide 23
  BL652
    Bluetooth Module
    3.3V Operable
    $7.45 per Unit
    VSP Mode

## Slide 24: Embedded Systems
David Simoneau- Primary
Christopher Benjamin Turner Britt – Secondary

## Slide 25: The Other Guys
VRGluv
  Force-feedback system
    Pulley-like technology
    5 pounds of force

## Slide 26: The Other Guys
HAPTX
  Microfluidic technology
    Shape, movement, texture and temperature
    5 pounds of force feedback

## Slide 27: Processing Information
Handle data between sensors and software

## Slide 28: Processor Choices
ATMega
MSP430
STM32 *

## Slide 29: Processor Choices Comparisons
Cheaper with more I/O

## Slide 30: Processor Choices Comparisons
More memory

## Slide 31: Processor Choices Comparisons
Faster

## Slide 32: I2C
Using an I2C bus.
Multiplexer for polling
Device addresses minimize lines

## Slide 33: Processing Information
Handle data between sensors and software

## Slide 34: Wireless Communication
Infrared, satellite, radio, Bluetooth, wifi.

## Slide 35: Bluetooth Module Choices
Keeping it modern. Bluetooth choices are 1.x, 2.x, 3.x, 4.x, and 5.x
RN4871-V/RM118
BL652-SC-01 *
BM62SPKS1MC2-0001AA

## Slide 36: Bluetooth Comparison
Cheaper

## Slide 37: Bluetooth Comparison
Cheaper
Bigger

## Slide 38: Bluetooth Comparison
Cheaper
Bigger
Less Power

## Slide 39: Bluetooth Regulations
This device may not cause harmful interference
device must accept any interference received, including interference that may cause undesired operation.”

## Slide 40: UART
Method used with Bluetooth
Internal clocks ensure proper timing instead of clock line
HAL library handles most of specific technical details e.g start bits, stop bits, baud rate, and parity bits.

## Slide 41: PCB Design
Flexible PCB?
Small and Secure

## Slide 42: PCB Design Tools
KiCAD
  Free
  Plethora of documentation
SOLIDWORKS PCB
  Better for more complex designs
DesignSpark PCB
  Less documentation

## Slide 43: PCB Fabrication Companies
PCBWay
  Cheap and easy
4pcb
  More expensive
PCBgogo
  Boasts 12-24-hour production
  Reliable
JLCPCB
  Popular
  Cheapest
  Largest in China

## Slide 44: System Startup Procedure
Initialize
Loop
  I2CReads
  UARTSend
  UARTReceive
  I2CSend

## Slide 45: Programming the Chip
Complexities in Datasheet
  Register addresses
  I2C pins and other pinouts
  How to Flash
  power modes

## Slide 46: Configuration Utility
Francisco Tirado Perez – Primary
Anthony Hunter Hinnant - Secondary

## Slide 47: Goals
System Isolation
  Separate the Blender 3D environment from the Hardware Glove
Scalable
  Can Coordinate multiple hardware gloves for use in the 3D environment
Debugging Platform
  Aids in debugging by providing a real-time data viewing interface.

## Slide 48
Windows 10 Operation System
Microsoft Visual Studio 2015 Community edition
C# Programing language
  C# forms API
  Windows Bluetooth API
Development

## Slide 49
3 Actors
  User
    Initiates the system
    Manages stored profiles
    Sets operating mode of the syste
  Blender
    Receives updated positional data
    Provides updated sensory data
  Hardware Glove
    Provides Updated positional data
    Receives updated sensory data
Use Case Diagram

## Slide 50
GUI
  Visual Tool interface
Process I/O
  Tool to Blender communication
Serial I/O
  Tool to BlueTooth communication
Data Packager
  Coordination of data
Liner Interpolator
  Scaling of hardware limits
Debugger
  Real-time debugging interface
Profile Manager
  Persistent data storage management
System Architecture

## Slide 51
Class Diagram
Util Core
  Serial Comm
    Establishes Bluetooth Connection with the Hardware Glove
  Process Comm
    Establishes interprocess communication with Blender
  Glove
    Storage unit for a gloved device
  Electric Device
    Storage unit for an electric Device (accelerometers, Plteir, vibration motors)
  Interpolator
    Provides the Logic for the interpolation routines

## Slide 52
Input/Ouput Scheme
Utility <-> Blender
I/O using files
  2 files
  Util_to_Blender – Utility writes, Blender reads
  Blender_to_Util – Blender writes, Utility reads
Utility <-> Hardware Glove
I/O Bluetooth
  Utility leverages Windows Bluetooth API
  Hardware Glove has a Bluetooth Module

## Slide 53
UI Design

## Slide 54: Blender & 3D Environment
Anthony Hunter Hinnant - Primary
Francisco Tirado Perez – Secondary

## Slide 55: Blender
Blender is a professional open-source 3D graphics toolset used for modeling, animation, and interactive 3D applications.
Free and open source.
Flexible enough to fulfill many of our project requirements at once.

## Slide 56: 3D Modeling
Blender is used to build 3D models for our hand to interact with.
We make a table with 5 cubes, a plane for a ground, and a few other objects

## Slide 57: Hand
“Realistic Hand 3d model” from user “mohammadalizadeh” on free3d.com.
Textured, rigged, animating, and scripted in blender

## Slide 58: Animation & Rigging
Blender allows us to create animation skeletons to rig our models with.
This is how we set up the hand to animate and change based on the input from the dvice

## Slide 59: Physics
Blender has a built in physics engine that we can modify for our use
This allows us to set collision boundaries, and physics behaviors independently for each object.

## Slide 60: Logic Scripting
Blender incorporates logic bricks that are associated with objects, allowing us to incorporate basic scripting behaviors like camera movement and key presses.
It also allows us to associate integer properties with our objects.

## Slide 61: Python Scripting
Blender allows for python scripts to be associated with objects and applications
This allows us to use scripts to perform more complex actions
This Is also how we incorporate the file i/o to communicate with the device driver

## Slide 62: Texturing
We can edit textures on objects to give a better look.

## Slide 63: HTC Vive
The program is also made to interact with the HTC vive headset
The vive can track the users head using two beacons that come packed with it, allowing the user to see the hand relative to them

## Slide 64: Virtual Reality
The user will be able to move the hand and interact with objects in the application with the device and virtual reality headset

## Slide 65: Demonstration

## Slide 66
Chart: Progress
| Overall | Hardware | Embedded Systems | Utility Software | 3D Environment
Prototyping | 60 | 80 | 3.5 | 40 | 90
Testing | 40 | 80 | 20 | 30 | 80
Implementation | 40 | 30 | 50 | 40 | 80

## Slide 67: Questions Curiosities Queries Comments